replacemsg alertmail

The FortiGate unit adds the alert mail replacement messages listed to alert email messages sent to administrators. For more information about alert email, see “system email-server” on page 509.

Alert mail replacement messages are text messages. These are HTML messages with HTTP headers.

Syntax

config system replacemsg alertmail alert_msg_type set buffer <message>

set format <format>

set header <header_type>

end

| Variable | Description | Default |
| --- | --- | --- |
| alert_msg_type | FortiGuard replacement alertmail message type. See Table 3. | No default. |
| buffer <message> | Type a new replacement message to replace the current replacement message. Maximum length 8 192 characters. | Depends on message type. |
| format <format> | Set the format of the message: html text none | No default. |
| header <header_type> | Set the format of the message header: 8bit http none | Depends on message type. |

If you enable Send alert email for logs based on severity for alert email, whether or not replacement messages are sent by alert email depends on how you set the alert email Minimum log level.

Table 3: alertmail message types

| Message Type | Description |
| --- | --- |
| alertmail-block | Virus detected must be enabled for alert email. Antivirus File Filter must be enabled in an antivirus profile, and it must block a file that matches an entry in a selected file filter list. |
| alertmail-crit-event | Whenever a critical level event log message is generated, this replacement message is sent unless you configure alert email to enable Send alert email for logs based on severity and set the Minimum log level to Alert or Emergency. |

Table 3: alertmail message types

| alertmail-disk-full | Disk usage must be enabled, and disk usage reaches the percent full amount configured for alert email. For more information, see “system email-server” on page 509. |
| --- | --- |
| alertmail-nids-event | Intrusion detected must be enabled for alert email. When an IPS Sensor or a DoS Sensor detects an attack, this replacement message will be sent. |
| alertmail-virus | Virus detected must be enabled for alert email. Antivirus Virus Scan must be enabled in an antivirus profile and detect a virus. |

Replacement messages can include replacement message tags. When users receive the replacement message, the replacement message tag is replaced with content relevant to the message.

Table 4: Replacement message tags

| Tag | Description |
| --- | --- |
| %%FILE%% | The name of a file that has been removed from a content stream. This could be a file that contained a virus or was blocked by antivirus file blocking. %%FILE%% can be used in virus and file block messages. |
| %%VIRUS%% | The name of a virus that was found in a file by the antivirus system. %%VIRUS%% can be used in virus messages |
| %%URL%% | The URL of a web page. This can be a web page that is blocked by web filter content or URL blocking. %%URL%% can also be used in http virus and file block messages to be the URL of the web page from which a user attempted to download a file that is blocked. |
| %%CRITICAL_EVENT%% | Added to alert email critical event email messages. %%CRITICAL_EVENT%% is replaced with the critical event message that triggered the alert email. |
| %%PROTOCOL%% | The protocol (HTTP, FTP, POP3, IMAP, SMTP) in which a virus was detected. %%PROTOCOL%% is added to alert email virus messages. |
| %%SOURCE_IP%% | IP address of the email server that sent the email containing the virus. |
| %%DEST_IP%% | IP address of the user’s computer that attempted to download the message from which the file was removed. |
| %%EMAIL_FROM%% | The email address of the sender of the message from which the file was removed. |
| %%EMAIL_TO%% | The email address of the intended receiver of the message from which the file was removed. |
| %%NIDS_EVENT%% | The IPS attack message. %%NIDS_EVENT%% is added to alert email intrusion messages. |

replacemsg auth

The FortiGate unit uses the text of the authentication replacement messages listed in Table 6 for various user authentication HTML pages that are displayed when a user is required to authenticate because a firewall policy includes at least one identity-based policy that requires firewall users to authenticate.

These pages are used for authentication using HTTP and HTTPS. Authentication replacement messages are HTML messages. You cannot customize the firewall authentication messages for FTP and Telnet.

The authentication login page and the authentication disclaimer include replacement tags and controls not found on other replacement messages.

Users see the authentication login page when they use a VPN or a firewall policy that requires authentication. You can customize this page in the same way as you modify other replacement messages,

Administrators see the authentication disclaimer page when logging into the FortiGate

web-based manager or CLI. The disclaimer page makes a statement about usage policy to which the user must agree before the FortiGate unit permits access. You should change only the disclaimer text itself, not the HTML form code.

There are some unique requirements for these replacement messages:

•  The login page must be an HTML page containing a form with ACTION="/" and

METHOD="POST"

•  The form must contain the following hidden controls:

| • <INPUT | TYPE="hidden" | NAME="%%MAGICID%%" | VALUE="%%MAGICVAL%%"> |
| --- | --- | --- | --- |
| • <INPUT | TYPE="hidden" | NAME="%%STATEID%%" | VALUE="%%STATEVAL%%"> |
| • <INPUT | TYPE="hidden" | NAME="%%REDIRID%%" | VALUE="%%PROTURI%%"> |

•  The form must contain the following visible controls:

• <INPUT TYPE="text" NAME="%%USERNAMEID%%" size=25>

• <INPUT TYPE="password" NAME="%%PASSWORDID%%" size=25>

These are HTML messages with HTTP headers.

Syntax

config system replacemsg auth auth_msg_type set buffer <message>

set format <format>

set header <header_type>

end

| Variable | Description | Default |
| --- | --- | --- |
| auth_msg_type | FortiGuard replacement message type. See Table 5 on page 602. | No default |
| buffer <message> | Type a new replacement message to replace the current replacement message. Maximum length 8 192 characters. | Depends on message type. |

| Variable | Description | Default |
| --- | --- | --- |
| format <format> | Set the format of the message: html text none | No default |
| header <header_type> | Set the format of the message header: 8bit http none | Depends on message type. |

Table 5: auth message types

| Message Type | Description |
| --- | --- |
| auth-challenge-page | This HTML page is displayed if firewall users are required to answer a question to complete authentication. The page displays the question and includes a field in which to type the answer. This feature is supported by RADIUS and uses the generic RADIUS challenge-access auth response. Usually, challenge-access responses contain a Reply- Message attribute that contains a message for the user (for example, “Please enter new PIN”). This message is displayed on the login challenge page. The user enters a response that is sent back to the RADIUS server to be verified. The Login challenge page is most often used with RSA RADIUS server for RSA SecurID authentication. The login challenge appears when the server needs the user to enter a new PIN. You can customize the replacement message to ask the user for a SecurID PIN. This page uses the %%QUESTION%% tag. |
| auth-disclaimer[1¦2¦3] | Prompts user to accept the displayed disclaimer when leaving protected network. The web-based manager refers to this as User Authentication Disclaimer, and it is enabled with a firewall policy that also includes at least one identity-based policy. When a firewall user attempts to browse a network through the FortiGate unit using HTTP or HTTPS this disclaimer page is displayed. The extra pages seamlessly extend the size of the page from 8 192 characters to 16 384 and 24 576 characters respectively. |

Table 5: auth message types

| auth-keepalive-page | The HTML page displayed with firewall authentication keepalive is enabled using the following CLI command: config system global set auth-keepalive enable end Authentication keepalive keeps authenticated firewall sessions from ending when the authentication timeout ends. In the web-based manager, go to User > Options to set the Authentication Timeout. This page includes %%TIMEOUT%%. |
| --- | --- |
| auth-login-failed-page | The HTML page displayed if firewall users enter an incorrect user name and password combination. This page includes %%FAILED_MESSAGE%%, %%USERNAMEID%%, and %%PASSWORDID%% tags. |
| auth-login-page | The authentication HTML page displayed when firewall users who are required to authenticate connect through the FortiGate unit using HTTP or HTTPS. Prompts the user for their username and password to login. This page includes %%USERNAMEID%% and %%PASSWORDID%% tags. |
| auth-reject-page | The Disclaimer page replacement message does not re-direct the user to a redirect URL or the firewall policy does not include a redirect URL. When a firewall user selects the button on the disclaimer page to decline access through the FortiGate unit, the Declined disclaimer page is displayed. |
| auth-token-login-page | The authentication HTML page displayed when firewall users who are required to use two-factor authentication connect through the FortiGate unit using HTTP or HTTPS. Prompts the user for their username, password and two-factor authentication credentials. This page includes %%USERNAMEID%%, %%PASSWORDID%%, and %%TOKENCODE%% tags. |
| auth-token-login- failed-page | The HTML page displayed if firewall users performing two-factor authentication enter an incorrect credentials. This page includes %%USERNAMEID%%, %%PASSWORDID%%, and %%TOKENCODE%% and %%EXTRAINFO%% tags. |

Replacement messages can include replacement message tags. When users receive the replacement message, the replacement message tag is replaced with content relevant to the message.

Table 6: Replacement message tags

| Tag | Description |
| --- | --- |
| %%AUTH_REDIR_URL%% | Link to open a new window. (optional). |
| %%AUTH_LOGOUT%% | Immediately close the connection policy. |

Table 6: Replacement message tags

| Tag | Description |
| --- | --- |
| %%EXTRAINFO%% | Provide extra help on two-factor authentication. |
| %%FAILED_MESSAGE%% | Message displayed on failed login page after user login fails. |
| %%KEEPALIVEURL%% | URL the keep alive page connects to that keeps the connection policy alive. Connects every %%TIMEOUT%% seconds. |
| %%QUESTION%% | The default login and rejected login pages use this text immediately preceding the username and password fields. The default challenge page uses this as the challenge question. These are treated as two different variables by the server. If you want to use different text, replace %%QUESTION%% with the text that you prefer. |
| %%TIMEOUT%% | Configured number of seconds between %%KEEPALIVEURL%% connections. |
| %%TOKENCODE%% | The FortiToken authentication code. Used for two-factor authentication. |
| %%USERNAMEID%% | Username of the user logging in. This tag is used on the login and failed login pages. |
| %%PASSWORDID%% | Password of the user logging in. This tag is used on the challenge, login and failed login pages. |

Requirements for login page

The authentication login page is linked to FortiGate functionality and you must construct it according to the following guidelines to ensure that it will work.

•  The login page must be an HTML page containing a form with ACTION="/" and

METHOD="POST"

•  The form must contain the following hidden controls:

| • <INPUT | TYPE="hidden" | NAME="%%MAGICID%%" | VALUE="%%MAGICVAL%%"> |
| --- | --- | --- | --- |
| • <INPUT | TYPE="hidden" | NAME="%%STATEID%%" | VALUE="%%STATEVAL%%"> |
| • <INPUT | TYPE="hidden" | NAME="%%REDIRID%%" | VALUE="%%PROTURI%%"> |

•  The form must contain the following visible controls:

• <INPUT TYPE="text" NAME="%%USERNAMEID%%" size=25>

• <INPUT TYPE="password" NAME="%%PASSWORDID%%" size=25>

replacemsg ec

The endpoint control (ec) replacement messages format the portal pages that the FortiGate unit sends to non-compliant users who attempt to use a firewall policy in which Endpoint NAC (endpoint-check) is enabled.

There are two Endpoint NAC portals:

•  Endpoint NAC Download Portal — The FortiGate unit sends this page if the Endpoint NAC profile has recommendation-disclaimer disabled. In the web-based manager, this is the Quarantine Hosts to User Portal (Enforce compliance) option. The user can download the FortiClient Endpoint Security application installer. If you modify this replacement message, be sure to retain the %%LINK%% tag which provides the download URL for the FortiClient installer.

•  Endpoint NAC Recommendation Portal — The FortiGate unit sends this page if the Endpoint NAC profile has recommendation-disclaimer enabled. In the web-based manager, this is the Notify Hosts to Install FortiClient (Warn only) option. The user can either download the FortiClient Endpoint Security application installer or select the Continue to link to access their desired destination. If you modify this replacement message, be sure to retain both the

%%LINK%% tag which provides the download URL for the FortiClient installer and the

%%DST_ADDR%% link that contains the URL that the user requested.

Message format is HTML by default.

Syntax

config system replacemsg ec endpt-download-portal set buffer <message>

set format <format>

set header <header_type>

end

config system replacemsg ec endpt-recommendation-portal set buffer <message>

set format <format>

set header <header_type>

end

| Variable | Description | Default |
| --- | --- | --- |
| endpt-download-portal | The Endpoint NAC Download Portal. The FortiGate unit sends this message to non-compliant users if recommendation-disclaimer is disabled in the Endpoint Control profile. The user can download the FortiClient Endpoint Security application installer. | No default |
| endpt-recommendation-portal | The Endpoint NAC Recommendation Portal. The FortiGate unit sends this message to non- compliant users if recommendation- disclaimer is enabled in the Endpoint Control profile. The user can either download the FortiClient Endpoint Security application installer or select the Continue to link to access their desired destination. | No default |

| Variable | Description | Default |
| --- | --- | --- |
| buffer <message> | Type a new replacement message to replace the current replacement message. Maximum length 8 192 characters. | Depends on message type. |
| format <format> | Set the format of the message: html text none |
| header <header_type> | Set the format of the message header: 8bit http none |

The endpoint control replacement messages include the following replacement message tags. When users receive the replacement message, the replacement message tag is replaced with the appropriate content.

Table 7: Replacement message tags

| Tag | Description |
| --- | --- |
| %%LINK%% | The download URL for the FortiClient installer. |
| %%DST_ADDR%% | The destination URL that the user entered. This is used in the endpt-recommendation-portal message only. |

replacemsg fortiguard-wf

Use this command to change the default messages that replace a web pages that FortiGuard web filtering has blocked.

The FortiGate unit sends the FortiGuard Web Filtering replacement messages listed in Table 8 to web browsers using the HTTP protocol when FortiGuard web filtering blocks a URL, provides details about blocked HTTP 4xx and 5xx errors, and for FortiGuard overrides. FortiGuard Web Filtering replacement messages are HTTP pages.

If the FortiGate unit supports SSL content scanning and inspection these replacement messages can also replace web pages downloaded using the HTTPS protocol.

By default, these are HTML messages.

Syntax

config system replacemsg fortiguard-wf <fortiguard_msg_type>

set buffer <message>

set format <format>

set header <header_type>

end

| Variable | Description | Default |
| --- | --- | --- |
| <fortiguard_msg_type> | FortiGuard replacement message type. See Table 8. | No default. |
| buffer <message> | Type a new replacement message to replace the current replacement message. Maximum length 8 192 characters. | Depends on message type. |
| format <format> | Set the format of the message: html text none | No default |
| header <header_type> | Set the format of the message header: 8bit http none | Depends on message type. |

Table 8: FortiGuard Web Filtering replacement messages

| Message name | Description |
| --- | --- |
| ftgd-block | Enable FortiGuard Web Filtering is enabled in a web filter profile for HTTP or HTTPS, and blocks a web page. The blocked page is replaced with the ftgd-block web page. |
| ftgd-ovrd | Override selected filtering for a FortiGuard Web Filtering category and FortiGuard Web Filtering blocks a web page in this category. displays this web page. Using this web page users can authenticate to get access to the page. Go to UTM > Web Filter > Override to add override rules. For more information, see “webfilter override” on page 846. The %%OVRD_FORM%% tag provides the form used to initiate an override if FortiGuard Web Filtering blocks access to a web page. Do not remove this tag from the replacement message. |
| http-err | Provide details for blocked HTTP 4xx and 5xx errors is enabled in a web filter profile for HTTP or HTTPS, and blocks a web page. The blocked page is replaced with the http-err web page. |

replacemsg ftp

The FortiGate unit sends the FTP replacement messages to FTP clients when an event occurs such as antivirus blocking a file that contains a virus in an FTP session.

By default, these are text-format messages with no header.

Syntax

config system replacemsg ftp <message-type>

set buffer <message>

set format <format>

set header <header_type>

end

| Variable | Description | Default |
| --- | --- | --- |
| <message-type> | FTP replacement message type. See Table 9. | No default. |
| buffer <message> | Type a new replacement message to replace the current replacement message. Maximum length 8 192 characters. | Depends on message type. |
| format <format> | Set the format of the message: html text none | No default |
| header <header_type> | Set the format of the message header: 8bit http none | Depends on message type. |

Table 9: FTP replacement messages

| Message name | Description |
| --- | --- |
| explicit-banner | Greeting banner for explicit FTP proxy. |
| ftp-dl-archive-block | FTP file transfer for DLP archiving was blocked. In DLP archiving, the DLP engine examines email, FTP, IM, NNTP, and web traffic. When enabled, the FortiGate unit records all occurrences of these traffic types when they are detected by the sensor. |
| ftp-dl-blocked | Antivirus File Filter enabled for FTP in an antivirus profile blocks a file being downloaded using FTP that matches an entry in the selected file filter list and sends this message to the FTP client. |
| ftp-dl-dlp-ban | In a DLP sensor, a rule with action set to Ban blocks an FTP session and displays this message. This message is displayed whenever the banned user attempts to access until the user is removed from the banned user list. |

Replacement messages can include replacement message tags. When users receive the replacement message, the replacement message tag is replaced with content relevant to the message.

Table 10: Replacement message tags

| Tag | Description |
| --- | --- |
| %%FILE%% | The name of a file that has been removed from a content stream. This could be a file that contained a virus or was blocked by antivirus file blocking. %%FILE%% can be used in virus and file block messages. |
| %%VIRUS%% | The name of a virus that was found in a file by the antivirus system. %%VIRUS%% can be used in virus messages |
| %%QUARFILENAME%% | The name of a file that has been removed from a content stream and added to the quarantine. This could be a file that contained a virus or was blocked by antivirus file blocking. %%QUARFILENAME%% can be used in virus and file block messages. Quarantining is only available on FortiGate units with a local disk. |
| %%URL%% | The URL of a web page. This can be a web page that is blocked by web filter content or URL blocking. %%URL%% can also be used in http virus and file block messages to be the URL of the web page from which a user attempted to download a file that is blocked. |
| %%PROTOCOL%% | The protocol (HTTP, FTP, POP3, IMAP, SMTP) in which a virus was detected. %%PROTOCOL%% is added to alert email virus messages. |
| %%SOURCE_IP%% | The IP address from which a virus was received. For email this is the IP address of the email server that sent the email containing the virus. For HTTP this is the IP address of the web page that sent the virus. |
| %%DEST_IP%% | The IP address of the computer that would have received the blocked file. For email this is the IP address of the user’s computer that attempted to download the message from which the file was removed. |

replacemsg http

Use this command to change default replacement messages added to web pages when the antivirus engine blocks a file in an HTTP session because of a matching file pattern or because a virus is detected; or when web filter blocks a web page.

The FortiGate unit sends the HTTP replacement messages listed to web browsers using the HTTP protocol when an event occurs such as antivirus blocking a file that contains a virus in an HTTP session. HTTP replacement messages are HTML pages.

If the FortiGate unit supports SSL content scanning and inspection these replacement messages can also replace web pages downloaded using the HTTPS protocol.

Syntax

config system replacemsg http <message-type>

set buffer <message>

set format <format>

set header <header_type>

end

| Variable | Description | Default |
| --- | --- | --- |
| <message-type> | HTTP replacement message type. See Table 11. | No default. |
| buffer <message> | Type a new replacement message to replace the current replacement message. Maximum length 8 192 characters. | Depends on message type. |
| format <format> | Set the format of the message: html text none | No default |
| header <header_type> | Set the format of the message header: 8bit http none | Depends on message type. |

Table 11: HTTP replacement messages

| Message name | Description |
| --- | --- |
| bannedword | Web content blocking is enabled in a web filter profile, and blocks a web page being downloaded with an HTTP GET that contains content matching an entry in the selected Web Content Block list. The blocked page is replaced with the bannedword web page. |
| http-archive-block | A transfer contained a blocked DLP archive. In DLP archiving, the DLP engine examines email, FTP, IM, NNTP, and web traffic. When enabled, the FortiGate unit records all occurrences of these traffic types when they are detected by the sensor. |

Table 11: HTTP replacement messages

| Message name | Description |
| --- | --- |
| http-block | Antivirus File Filter is enabled for HTTP or HTTPS in a web filter profile, and blocks a file being downloaded using an HTTP GET that matches an entry in the selected file filter list. The file is replaced with the http- block web page that is displayed by the client browser. |
| http-client-archive- block | The user is not allowed to upload the file. |
| http-client- bannedword | Web content blocking enabled in a web filter profile blocks a web page being uploaded with an HTTP PUT that contains content that matches an entry in the selected Web Content Block list. The client browser displays the http-client-bannedword web page. |
| http-client-block | Antivirus File Filter is enabled for HTTP or HTTPS in an antivirus profile blocks a file being uploaded by an HTTP POST that matches an entry in the selected file filter list and replaces it with the http-client-block web page that is displayed by the client browser. |
| http-client-filesize | Oversized File/Email is set to Block for HTTP or HTTPS and an oversized file that is being uploaded with an HTTP PUT is blocked and replaced with the http-client-filesize web page. |
| http-contenttype- block | When a specific type of content is not allowed, it is replaced with the http-contenttype-block web page. |
| http-dlp-ban | In a DLP sensor, a rule with action set to Ban replaces a blocked web page or file with the http-dlp-ban web page. This web page also replaces any additional web pages or files that the banned user attempts to access until the user is removed from the banned user list. |
| http-filesize | Antivirus Oversized File/Email is set to Block for HTTP or HTTPS and blocks an oversized file being downloaded using an HTTP GET. The file is replaced with the http-filesize web page that is displayed by the client browser. |
| http-post-block | HTTP POST Action is set to Block and the FortiGate unit blocks an HTTP POST and displays the http-post-block web page. |
| https-invalid-cert- block | When an invalid security certificate is detected, the https-invalid- cert-block page is displayed. |
| infcache-block | Client comforting is enabled and the FortiGate unit blocks a URL added to the client comforting URL cache. It replaces the blocked URL with the infcache-block web page. For more information about the client comforting URL cache, see“firewall policy, policy46, policy6, policy64” on page 162. |
| url-block | Web URL filtering is enabled and blocks a web page with a URL that matches an entry in the selected URL Filter list. The blocked page is replaced with the url-block web page. |

Replacement messages can include replacement message tags. When users receive the replacement message, the replacement message tag is replaced with content relevant to the message.

Table 12: Replacement message tags

| Tag | Description |
| --- | --- |
| %%FILE%% | The name of a file that has been removed from a content stream. This could be a file that contained a virus or was blocked by antivirus file blocking. %%FILE%% can be used in virus and file block messages. |
| %%VIRUS%% | The name of a virus that was found in a file by the antivirus system. %%VIRUS%% can be used in virus messages |
| %%QUARFILENAME%% | The name of a file that has been removed from a content stream and added to the quarantine. This could be a file that contained a virus or was blocked by antivirus file blocking. %%QUARFILENAME%% can be used in virus and file block messages. Quarantining is only available on FortiGate units with a local disk. |
| %%URL%% | The URL of a web page. This can be a web page that is blocked by web filter content or URL blocking. %%URL%% can also be used in http virus and file block messages to be the URL of the web page from which a user attempted to download a file that is blocked. |
| %%PROTOCOL%% | The protocol (HTTP, FTP, POP3, IMAP, SMTP) in which a virus was detected. %%PROTOCOL%% is added to alert email virus messages. |
| %%SOURCE_IP%% | The IP address of the web page from which a virus was received. |
| %%DEST_IP%% | The IP address of the computer that would have received the blocked file. For email this is the IP address of the user’s computer that attempted to download the message from which the file was removed. |

replacemsg im

Use this command to change default replacement messages added to instant messaging and peer-to-peer sessions when either file-transfer or voice-chat is blocked.

By default, these are text messages with an 8-bit header.

Syntax

config system replacemsg im <message-type>

set buffer <message>

set format <format>

set header <header_type>

end

| Variable | Description | Default |
| --- | --- | --- |
| <message-type> | im replacement message type. See Table 13. | No default. |
| buffer <message> | Type a new replacement message to replace the current replacement message. Maximum length 8 192 characters. | Depends on message type. |
| format <format> | Set the format of the message: html text none | No default |
| header <header_type> | Set the format of the message header: 8bit http none | Depends on message type. |

Table 13: Instant messaging (IM) and peer to peer (P2P) message types

| Message name | Description |
| --- | --- |
| im-dlp | In a DLP sensor, a rule with action set to Block replaces a blocked IM or P2P message with this message. |
| im-dlp-ban | In a DLP sensor, a rule with action set to Ban replaces a blocked IM or P2P message with this message. This message also replaces any additional messages that the banned user sends until they are removed from the banned user list. |
| im-file-xfer-block | Antivirus File Filter enabled for IM deletes a file that matches an entry in the selected file filter list and replaces it with this message. |
| im-file-xfer-infected | Antivirus Virus Scan enabled for IM deletes an infected file from and replaces the file with this message. |
| im-file-xfer-name | Antivirus File Filter enabled for IM deletes a file with a name that matches an entry in the selected file filter list and replaces it with this message. |

Table 13: Instant messaging (IM) and peer to peer (P2P) message types

| Message name | Description |
| --- | --- |
| im-file-xfer-size | Antivirus Oversized File/Email set to Block for IM removes an oversized file and replaces the file with this message. |
| im-long-chat-block | In an Application Control list, the block-long-chat CLI field is enabled for AIM, ICQ, MSN, or Yahoo. You enable blocking oversized chat messages from the CLI. |
| im-photo-share-block | In an Application Control list, the block-photo CLI field is enabled for MSN, or Yahoo. You enable photo blocking from the CLI. |
| im-voice-chat-block | In an Application Control list, the Block Audio option is selected for AIM, ICQ, MSN, or Yahoo!. |
| im-video-chat-block | In an Application Control list, the block-video CLI field is enabled for MSN. You enable video chat blocking from the CLI. |

Replacement messages can include replacement message tags. When users receive the replacement message, the replacement message tag is replaced with content relevant to the message.

Table 14: Replacement message tags

| Tag | Description |
| --- | --- |
| %%FILE%% | The name of a file that has been removed from a content stream. This could be a file that contained a virus or was blocked by antivirus file blocking. %%FILE%% can be used in virus and file block messages. |
| %%VIRUS%% | The name of a virus that was found in a file by the antivirus system. %%VIRUS%% can be used in virus messages |
| %%QUARFILENAME%% | The name of a file that has been removed from a content stream and added to the quarantine. This could be a file that contained a virus or was blocked by antivirus file blocking. %%QUARFILENAME%% can be used in virus and file block messages. Quarantining is only available on FortiGate units with a local disk. |
| %%PROTOCOL%% | The protocol (HTTP, FTP, POP3, IMAP, SMTP) in which a virus was detected. %%PROTOCOL%% is added to alert email virus messages. |
| %%SOURCE_IP%% | The IP address from which a virus was received. For email this is the IP address of the email server that sent the email containing the virus. For HTTP this is the IP address of the web page that sent the virus. |
| %%DEST_IP%% | The IP address of the computer that would have received the blocked file. For email this is the IP address of the user’s computer that attempted to download the message from which the file was removed. |

replacemsg mail

Use this command to change default replacement messages added to email messages when the antivirus engine blocks a file either because of a matching file pattern or because a virus is detected; or when spam filter blocks an email.

By default, these are text messages with an 8-bit header.

Syntax

config system replacemsg mail <message-type>

set buffer <message>

set format <format>

set header <header_type>

end

| Variable | Description | Default |
| --- | --- | --- |
| <message-type> | mail replacement message type. See Table 15. | No default. |
| buffer <message> | Type a new replacement message to replace the current replacement message. Maximum length 8 192 characters. | Depends on message type. |
| format <format> | Set the format of the message: html text none | No default |
| header <header_type> | Set the format of the message header: 8bit http none | Depends on message type. |

Table 15: mail message types

| Message name | Description |
| --- | --- |
| email-block | The antivirus File Filter is enabled for an email protocol deletes a file that matches an entry in the selected file filter list. The file is blocked and the email is replaced with the email-block message. |
| email-dlp-ban | In a DLP sensor, a rule with action set to Ban replaces a blocked email message with this message. This message also replaces any additional email messages that the banned user sends until they are removed from the banned user list. |
| email-dl-ban-sender | In a DLP sensor, a rule with action set to Ban Sender replaces a blocked email message with this message. The email-dlp-ban message also replaces any additional email messages that the banned user sends until the user is removed from the banned user list. |

Table 15: mail message types

| Message name | Description |
| --- | --- |
| email-dlp-subject | The email-dlp-subject message is added to the subject field of all email messages replaced by the DLP sensor Block, Ban, Ban Sender, Quarantine IP address, and Quarantine interface actions. |
| email-filesize | When the antivirus Oversized File/Email is set to Block for an email protocol removes an oversized file from an email message, the file is replaced with the email-filesize message. |
| partial | Antivirus Pass Fragmented Emails is not enabled so a fragmented email is blocked. The partial message replaces the first fragment of the fragmented email. |
| smtp-block | Splice mode is enabled and the antivirus file filter deleted a file from an SMTP email message. The FortiGate unit aborts the SMTP session and returns a 554 SMTP error message to the sender that includes the smtp-block replacement message. |
| smtp-filesize | Splice mode is enabled and antivirus Oversized File/Email is set to Block. When the FortiGate unit blocks an oversize SMTP email message, the FortiGate unit aborts the SMTP session and returns a 554 SMTP error message to the sender that includes the smtp- filesize replacement message. |

Replacement messages can include replacement message tags. When users receive the replacement message, the replacement message tag is replaced with content relevant to the message.

Table 16: Replacement message tags

| Tag | Description |
| --- | --- |
| %%FILE%% | The name of a file that has been removed from a content stream. This could be a file that contained a virus or was blocked by antivirus file blocking. %%FILE%% can be used in virus and file block messages. |
| %%VIRUS%% | The name of a virus that was found in a file by the antivirus system. %%VIRUS%% can be used in virus messages |
| %%QUARFILENAME%% | The name of a file that has been removed from a content stream and added to the quarantine. This could be a file that contained a virus or was blocked by antivirus file blocking. %%QUARFILENAME%% can be used in virus and file block messages. Quarantining is only available on FortiGate units with a local disk. |
| %%PROTOCOL%% | The protocol (HTTP, FTP, POP3, IMAP, SMTP) in which a virus was detected. %%PROTOCOL%% is added to alert email virus messages. |
| %%SOURCE_IP%% | IP address of the email server that sent the email containing the virus. |
| %%DEST_IP%% | IP address of the user’s computer that attempted to download the message from which the file was removed. |

Table 16: Replacement message tags

| Tag | Description |
| --- | --- |
| %%EMAIL_FROM%% | The email address of the sender of the message from which the file was removed. |
| %%EMAIL_TO%% | The email address of the intended receiver of the message from which the file was removed. |

replacemsg mm1

Use this command to change default replacement messages added to messages sent by FortiOS Carrier on the MM1 network when the antivirus engine blocks a file either because of a matching file pattern or because a virus is detected; or when spam filter blocks an email.

Syntax

config system replacemsg mm1 <message_type>

set add-smil {enable | disable}

set charset <character_set>

set class <class>

set format <format>

set from <from_address>

set from-sender {enable | disable}

set header <header_type>

set image <string>

set message <message_text>

set priority <priority>

set rsp-status <rsp_status>

set rsp-text <response_text>

set sender-visibility <sender_vis>

set smil-part <string>

set subject <subject_text>

end

| Variable | Description | Default |
| --- | --- | --- |
| <message_type> | MM1 replacement message types, one of: mm1-retr-conf-block mm1-retr-conf-bword mm1-retr-conf-sis-block mm1-retr-conf-virus mm1-send-conf-block mm1-send-conf-bword mm1-send-conf-sis-block mm1-send-conf-virus mm1-send-req-block mm1-send-req-bword mm1-send-req-sis-block mm1-send-req-virus | No default. |

| add-smil {enable ¦ disable} | Enable to add SMIL content to the message. SMIL content can include images. This field is available for the following message types: mm1-send-req-block mm1-send-req-bword mm1-send-req-sis-block mm1-send-req-virus | disable |
| --- | --- | --- |
| charset <character_set> | Character encoding used for replacement message, one of: us-ascii utf-8 | utf-8 |
| class <class> | The message can be classified as one of: advertisement automatic informational not-included personal | automatic |
| format <format> | Set the format of the message, one of: html none text wml Not all formats are supported by all message types. | text |
| from <from_address> | Address the message is from. | null |
| from-sender {enable ¦ disable} | Enable for the notification message to be sent from the recipient. This is to avoid billing problems. | disable |
| header <header_type> | Set the format of the message header, one of: 8bit http none | http |
| image <string> | Enter the name of the image to include in the SMIL message part. Using ‘?’ will show the list of available image names. This is only available when add-smil is enabled. |  |
| message <message_text> | Text of the replacement message. | Depends on message type. |

Fortinet Technologies Inc.                                                                Page 620                                     FortiOS™ - CLI Reference for FortiOS 5.0

| priority <priority> | Priority of the message, one of: high low normal not included | normal |
| --- | --- | --- |
| rsp-status <rsp_status> | Response status code, one of: err-content-not-accepted err-msg-fmt-corrupt err-msg-not-found err-net-prob err-snd-addr-unresolv err-srv-denied err-unspecified err-unsupp-msg ok | err-content-not- accepted |
| rsp-text <response_text> | Response text. | Depends on message type. |
| sender-visibility <sender_vis> | Sender visibility, one of: hide not-specified show | not-specified |
| smil-part <string> | Enter the SMIL part of the replacement message. |  |
| subject <subject_text> | Subject text string. | Depends on message type. |

Fortinet Technologies Inc.                                                                Page 621                                     FortiOS™ - CLI Reference for FortiOS 5.0

replacemsg mm3

Use this command to change default replacement messages added to messages sent by FortiOS Carrier on the MM3 network when the antivirus engine blocks a file either because of a matching file pattern or because a virus is detected; or when spam filter blocks an email.

Syntax

config system replacemsg mm3 <message_type>

set charset <character_set>

set format <format>

set from <from_address> set header <header_type> set message <message_text> set priority <priority>

set subject <subject_text>

end

| Variable | Description | Default |
| --- | --- | --- |
| <message_type> | MM3 replacement message types, one of: mm3-block mm3-block-notif mm3-bword mm3-bword-notif mm3-sis-block mm3-sis-block-notif mm3-sis-block-notif mm3-virus mm3-virus-block | No default. |
| charset <character_set> | Character encoding used for replacement messages, one of: us-ascii utf-8 | utf-8 |
| format <format> | Replacement message format flag, one of: html none text wml | text |
| from <from_address> | Address the message is from. | null |
| header <header_type> | Set the format of the message header, one of: 8bit http none | none |

Fortinet Technologies Inc.                                                                Page 622                                     FortiOS™ - CLI Reference for FortiOS 5.0

| message <message_text> | Text of the replacement message. | Depends on message type. |
| --- | --- | --- |
| priority <priority> | Priority of the message, one of: high low normal not included | normal |
| subject <subject_text> | Subject text string. | Depends on message type. |

Fortinet Technologies Inc.                                                                Page 623                                     FortiOS™ - CLI Reference for FortiOS 5.0

replacemsg mm4

Use this command to change default replacement messages added to messages sent by FortiOS Carrier on the MM4 network when the antivirus engine blocks a file either because of a matching file pattern or because a virus is detected; or when spam filter blocks an email.

Syntax

config system replacemsg mm4 <message_type>

set charset <character_set>

set class <class>

set domain <address_domain>

set format <format>

set from <from_address>

set from-sender {enable | disable}

set header <header_type>

set image <string>

set message <message_text>

set priority <priority>

set rsp-status <rsp_status>

set smil-part <string>

set subject <subject_text>

end

| Variable | Description | Default |
| --- | --- | --- |
| <message_type> | MM4 replacement message types, one of: mm4-block mm4-block-notif mm4-bword mm4-bword-notif mm4-sis-block mm4-sis-block-notif mm4-virus mm4-virus-block | No default. |
| add-smil {enable ¦ disable} | Enable to add SMIL content to the message. SMIL content can include images. This field is available for the following message types: mm4-block-notif mm4-bword-notif mm4-sis-block-notif | disable |
| charset <character_set> | Character encoding used for replacement messages: us-ascii or utf-8. | utf-8 |

Fortinet Technologies Inc.                                                                Page 624                                     FortiOS™ - CLI Reference for FortiOS 5.0

| class <class> | The message can be classified as one of: advertisement automatic informational not-included personal | automatic |
| --- | --- | --- |
| domain <address_domain> | The from address domain. | null |
| format <format> | Replacement message format flag, one of: html none text wml | text |
| from <from_address> | Address the message is from. | null |
| from-sender {enable ¦ disable} | Enable for the notification message to be sent from the recipient. This is to avoid billing problems. | disable |
| header <header_type> | Set the format of the message header: 8bit, http, or none. | none |
| image <string> | Enter the name of the image to include in the SMIL message part. Using ‘?’ will show the list of available image names. This is only available when add-smil is enabled. |  |
| message <message_text> | Text of the replacement message. | Depends on message type. |
| priority <priority> | Priority of the message, one of: high low normal not included | normal |
| rsp-status <rsp_status> | Response status codes, one of: err-content-not-accepted err-msg-fmt-corrupt err-net-prob err-snd-addr-unresolv err-srv-denied err-unspecified err-unsupp-msg ok | err-content-not- accepted |
| smil-part <string> | Enter the SMIL part of the replacement message. |  |
| subject <subject_text> | Subject text string. | Depends on message type. |

Fortinet Technologies Inc.                                                                Page 625                                     FortiOS™ - CLI Reference for FortiOS 5.0

replacemsg mm7

Use this command to change default replacement messages added to messages sent by FortiOS Carrier on the MM7 network when the antivirus engine blocks a file either because of a matching file pattern or because a virus is detected; or when spam filter blocks an email.

Syntax

config system replacemsg mm7 <mm7message_type>

set add-smil {enable | disable}

set addr_type <addr_type> set charset <character_set> set class <class>

set format <format>

set from <from_address>

set from-sender {enable | disable}

set header <header_type>

set image <string>

set message <message_text>

set priority <priority>

set rsp-status <rsp_status>

set smil-part <string>

set subject <subject_text>

end

| Variable | Description | Default |
| --- | --- | --- |
| <mm7message_type> | MM7 replacement message types, one of: mm7-block mm7-block-notif mm7-bword mm7-bword-notif mm7-sis-block mm7-sis-block-notif mm7-virus mm7-virus-block | No default. |
| add-smil {enable ¦ disable} | Enable to add SMIL content to the message. SMIL content can include images. This field is available for the following message types: mm7-block-notif mm7-bword-notif mm7-sis-block-notif | disable |
| addr_type <addr_type> | From address types, one of: number rfc2882-addr short-code | number |

Fortinet Technologies Inc.                                                                Page 626                                     FortiOS™ - CLI Reference for FortiOS 5.0

| charset <character_set> | Character encoding used for replacement messages, one of: us-ascii utf-8 | utf-8 |
| --- | --- | --- |
| class <class> | The message can be classified as one of: advertisement automatic informational not-included personal | automatic |
| format <format> | Replacement message format flag, one of: html none text wml | text |
| from <from_address> | Address the message is from. | null |
| from-sender {enable ¦ disable} | Enable for the notification message to be sent from the recipient. This is to avoid billing problems. | disable |
| header <header_type> | Set the format of the message header, one of: 8bit http none | none |
| image <string> | Enter the name of the image to include in the SMIL message part. Using ‘?’ will show the list of available image names. This is only available when add-smil is enabled. |  |
| message <message_text> | Text of the replacement message. | Depends on message type. |
| priority <priority> | Priority of the message, one of: high low normal not included | normal |

Fortinet Technologies Inc.                                                                Page 627                                     FortiOS™ - CLI Reference for FortiOS 5.0

| rsp-status <rsp_status> | Response status codes, one of: addr-err addr-not-found app-addr-not-supp app-denied app-id-not-found client-err content-refused gen-service-err improper-ident link-id-not-found msg-fmt-corrupt msg-id-not-found msg-rejected multiple-addr-not-supp not-possible oper-restrict partial-success repl-app-id-not-found service-denied service-err service-unavail srv-err success unsupp-oper unsupp-ver validation-err | Depends on message type. |
| --- | --- | --- |
| smil-part <string> | Enter the SMIL part of the replacement message. |  |
| subject <subject_text> | Subject text string. | Depends on message type. |

Fortinet Technologies Inc.                                                                Page 628                                     FortiOS™ - CLI Reference for FortiOS 5.0

replacemsg-group

Use this command to define replacement messages for your VDOM, overriding the corresponding global replacement messages.

Syntax

To create a VDOM-specific replacement message:

config system replacemsg-group edit default

config <msg_category>

edit <msg_type>

set buffer <message>

set format <format>

set header <header_type>

end end

To remove a VDOM-specific replacement message, restoring the global replacement message:

config system replacemsg-group edit default

config <msg_category>

delete <msg_type>

end

| Variable | Description | Default |
| --- | --- | --- |
| buffer <message> | Type a new replacement message to replace the current replacement message. Maximum length 8 192 characters. | Depends on message type. |
| comment <comment_str> | Optionally, enter a descriptive comment. | No default |
| format <format> | Set the format of the message: html text none | No default |
| header <header_type> | Set the format of the message header: 8bit http none | Depends on message type. |

Fortinet Technologies Inc.                                                                Page 629                                     FortiOS™ - CLI Reference for FortiOS 5.0

| Variable | Description | Default |
| --- | --- | --- |
| <msg_category> | The category of replacement message. This corresponds to the field following replacemsg in the global system replacemsg command. For example, the http category includes the messages defined globally in the system replacemsg http command. | No default |
| <msg_type> | The message type. This corresponds to the final field in the global system replacemsg command. For example, to create a new login message for your SSL VPN, you would set <msg_category> to sslvpn and <msg_type> to sslvpn-login. | No default |

Fortinet Technologies Inc.                                                                Page 630                                     FortiOS™ - CLI Reference for FortiOS 5.0

replacemsg-group

Replacement messages can be created and applied to specific profile groups. This allows the customization of messages for specific users or user groups.

If a user is not part of a custom replacement message group, their replacement messages come from the ‘default’ group. The ‘default’ group always exists, and cannot be deleted. All additional replacement message groups inherit from the default group. Any messages in custom groups that have not been modified, inherit any changes to those messages in the default group.

The only replacement messages that can not be customized in groups are administration related messages, which in the following categories:

•  Alert Mail

•   Administration

•   Authentication

•  IM and P2P

•  SSL VPN

Except for mm1, mm3, mm4, mm7 which use the message field, all replacement message types use the buffer field to refer to the body of the message.

Syntax

config system replacemsg-group edit <groupname_string>

set comment <string>

set group-type {auth | captive-portal | ec | utm}

config {auth | ec | fortiguard-wf | ftp | http | mail | mm1

| mm3 | mm4 | mm7 | nntp | spam}

edit <msgkey_integer> set msg-type <type> set buffer <string>

set header <header_flag> set format <format_flag> set message <string>

end

end

| Variable | Description | Default |
| --- | --- | --- |
| edit <groupname_string> | Create or edit a replacement message group. Use a groupname of default to configure per-vdom replacement messages. Only valid when VDOMs are enabled. |  |
| comment <string> | Enter a descriptive comment for this replacement message group. |  |

Fortinet Technologies Inc.                                                                Page 631                                     FortiOS™ - CLI Reference for FortiOS 5.0

| Variable | Description | Default |
| --- | --- | --- |
| group-type {auth ¦ captive-portal ¦ ec ¦ utm} | Enter the type of replacement message group this is. auth — for use with authentication pages in firewall policies captive-portal — for use with captive-portal configurations ec — for use with endpoint-control profiles utm — for use with UTM settings in firewall policies default — used to configure per-vdom replacement messages, only available when group name is set to default | utm |
| config {auth ¦ ec ¦ fortiguard-wf ¦ ftp ¦ http ¦ mail ¦ mm1 ¦ mm3 ¦ mm4 ¦ mm7 ¦ nntp ¦ spam} | Select a replacement message type to add or edit. These types or protocols, match with the existing replacemsg commands, and determine which msg- types are available. For more information on these replacement message types see: • “system replacemsg auth” on page 601 • “system replacemsg ec” on page 605 • “replacemsg fortiguard-wf” on page 607 • “replacemsg ftp” on page 609 • “replacemsg http” on page 611 • “replacemsg mail” on page 616 • “replacemsg mm1” on page 619 • “replacemsg mm3” on page 622 • “replacemsg mm4” on page 624 • “replacemsg mm7” on page 626 • “replacemsg nntp” on page 637 • “replacemsg spam” on page 639 Note: mm1,mm3,mm4,and mm7 are FortiOS Carrier only. |  |
| edit <msgkey_integer> | Create or edit a message entry in the table. Enter the key of the entry. Using ‘?’ will show you the existing message type as well as the msgkey entries in the table. |  |
| msg-type <type> | Select the message type for this message entry. Valid message types vary according to which replacement message table you are editing. For a list of valid message types for this table, refer to the CLI replacemsg command of the same name. |  |

Fortinet Technologies Inc.                                                                Page 632                                     FortiOS™ - CLI Reference for FortiOS 5.0

| Variable | Description | Default |
| --- | --- | --- |
| buffer <string> | Enter the replacement message for this message type. Enclose the message in quotes. This field is used with the following replacement messages: fortiguard-wf ftp http mail nntp spam Other replacement messages use the message field. |  |
| header <header_flag> | Select the header for this message. Valid types include: 8bit http none |  |
| format <format_flag> | Select the format of this message. Valid formats include: html none text wml (FortiOS Carrier only) |  |
| message <string> | Enter the replacement message for this message type. Enclose the message in quotes. This field is used with the following replacement messages: mm1 (FortiOS Carrier only) mm3 (FortiOS Carrier only) mm4 (FortiOS Carrier only) mm7 (FortiOS Carrier only) Other replacement messages use the buffer field. |  |

Fortinet Technologies Inc.                                                                Page 633                                     FortiOS™ - CLI Reference for FortiOS 5.0

replacemsg-image

Use this command to add, edit, or delete images to be used in HTTP replacement messages and for the SMIL parts of FortiOS Carrier replacement messages. Both image-base64 and image-type must be present for a valid entry.

Syntax

config system replacemsg-image edit <image_name>

set image-base64 <image_data>

set image-type <format>

end

| Variable | Description | Default |
| --- | --- | --- |
| edit <image_name> | Enter the name or tag to use for this image | none. |
| image-base64 <image_data> | Enter the image in base64 encoding. You can also use the graphical interface to add images by browsing to their location. | none. |
| image-type <format> | Select the format of the image. Available formats include: gif jpeg png tiff | none. |

replacemsg nac-quar

Use this command to change the NAC quarantine pages for data leak (DLP), denial of service

(DoS), IPS, and virus detected.

These are HTML messages with HTTP headers.

Syntax

config system replacemsg nac-quar nac-quar_msg_type set buffer <message>

set format <format>

set header <header_type>

end

| Variable | Description | Default |
| --- | --- | --- |
| nac-quar_msg_type | Replacement message type. See Table 17. | No default |
| buffer <message> | Type a new replacement message to replace the current replacement message. Maximum length 8 192 characters. | Depends on message type. |
| format <format> | Set the format of the message: html text none | No default |
| header <header_type> | Set the format of the message header: 8bit http none | Depends on message type. |

Table 17: nac-quar message types

| Message name | Description |
| --- | --- |
| nac-quar-dlp | Action set to Quarantine IP address or Quarantine Interface in a DLP sensor and the DLP sensor adds a source IP address or a FortiGate interface to the banned user list. The FortiGate unit displays this replacement message as a web page when the blocked user attempts to connect through the FortiGate unit using HTTP on port 80 or when any user attempts to connect through a FortiGate interface added to the banned user list using HTTP on port 80. |
| nac-quar-dos | For a DoS Sensor the CLI quarantine option set to attacker or interface and the DoS Sensor added to a DoS firewall policy adds a source IP, a destination IP, or FortiGate interface to the banned user list. The FortiGate unit displays this replacement message as a web page when the blocked user attempts to connect through the FortiGate unit using HTTP on port 80 or when any user attempts to connect through a FortiGate interface added to the banned user list using HTTP on port 80. This replacement message is not displayed if quarantine is set to both. |

Table 17: nac-quar message types

| Message name | Description |
| --- | --- |
| nac-quar-ips | Quarantine Attackers enabled in an IPS sensor filter or override and the IPS sensor adds a source IP address, a destination IP address, or a FortiGate interface to the banned user list. The FortiGate unit displays this replacement message as a web page when the blocked user attempts to connect through the FortiGate unit using HTTP on port 80 or when any user attempts to connect through a FortiGate interface added to the banned user list using HTTP on port 80. This replacement message is not displayed if method is set to Attacker and Victim IP Address. |
| nac-quar- virus | Antivirus Quarantine Virus Sender adds a source IP address or FortiGate interface to the banned user list. The FortiGate unit displays this replacement message as a web page when the blocked user attempts to connect through the FortiGate unit using HTTP on port 80 or when any user attempts to connect through a FortiGate interface added to the banned user list using HTTP on port 80. |

replacemsg nntp

Use this command to change the net news transfer protocol (NNTP) download pages. These are HTML messages with HTTP headers.

Syntax

config system replacemsg nntp auth_msg_type set buffer <message>

set format <format>

set header <header_type>

end

| Variable | Description | Default |
| --- | --- | --- |
| auth_msg_type | FortiGuard replacement alertmail message type. See Table 18. | No default |
| buffer <message> | Type a new replacement message to replace the current replacement message. Maximum length 8 192 characters. | Depends on message type. |
| format <format> | Set the format of the message: html text none | No default |
| header <header_type> | Set the format of the message header: 8bit http none | Depends on message type. |

Table 18: net news transfer protocol (NNTP) message types

| Message name | Description |
| --- | --- |
| nntp-dl-blocked | Antivirus File Filter is enabled for NNTP blocks a file attached to an NNTP message that matches an entry in the selected file filter list. The FortiGate unit sends the nntp-dl-blocked message to the FTP client. |
| nntp-dl-filesize | Antivirus Oversized File/Email is set to Block for NNTP. The FortiGate unit removes an oversized file from an NNTP message and replaces the file with the nntp-dl-filesize message. |
| nntp-dlp-ban | In a DLP sensor, a rule with action set to Ban replaces a blocked NNTP message with this message. The nntp-dlp-ban message also replaces any additional NNTP messages that the banned user sends until they are removed from the banned user list. |
| nntp-dlp-subject | The nntp-dlp-subject message is added to the subject field of all NNTP messages replaced by the DLP sensor Block, Ban, Quarantine IP address, and Quarantine interface actions. |

Replacement messages can include replacement message tags. When users receive the replacement message, the replacement message tag is replaced with content relevant to the message.

Table 19: Replacement message tags

| Tag | Description |
| --- | --- |
| %%FILE%% | The name of a file that has been removed from a content stream. This could be a file that contained a virus or was blocked by antivirus file blocking. The file may have been quarantined if a virus was detected. %%FILE%% can be used in virus and file block messages. |
| %%QUARFILENAME%% | The name of a file that has been removed from a content stream and added to the quarantine. This could be a file that contained a virus or was blocked by antivirus file blocking. %%QUARFILENAME%% can be used in virus and file block messages. Quarantining is only available on FortiGate units with a local disk. |
| %%VIRUS%% | The name of a virus that was found in a file by the antivirus system. %%VIRUS%% can be used in virus messages |

replacemsg spam

The FortiGate unit adds the Spam replacement messages listed in Table 20 to SMTP server responses if the email message is identified as spam and the spam action is discard. If the FortiGate unit supports SSL content scanning and inspection these replacement messages can also be added to SMTPS server responses.

By default, these are text messages with an 8-bit header.

Syntax

config system replacemsg spam <message-type>

set buffer <message>

set format <format>

set header <header_type>

end

| Variable | Description | Default |
| --- | --- | --- |
| <message-type> | Spam replacement message type. See Table 20. | No default. |
| buffer <message> | Type a new replacement message to replace the current replacement message. Maximum length 8 192 characters. | Depends on message type. |
| format <format> | Set the format of the message, one of: html text none | text |
| header <header_type> | Set the format of the message header, one of: 8bit http none | 8bit |

Table 20: spam message types

| Message name | Description |
| --- | --- |
| ipblocklist | Spam Filtering IP address BWL check enabled for an email protocol identifies an email message as spam and adds this replacement message. |
| reversedns | Spam Filtering Return e-mail DNS check enabled for an email protocol identifies an email message as spam and adds this replacement message. |
| smtp-spam-ase | The FortiGuard Antispam Engine (ASE) reports this message as spam. |
| smtp-spam- bannedword | Spam Filtering Banned word check enabled for an email protocol identifies an email message as spam and adds this replacement message. |

Table 20: spam message types

| Message name | Description |
| --- | --- |
| smtp-spam-dnsbl | From the CLI, spamrbl enabled for an email protocol identifies an email message as spam and adds this replacement message. |
| smtp-spam-emailblack | The spam filter email address blacklist marked an email as spam. The smtp-spam-emailblack replaces the email. |
| smtp-spam-feip | FortiGuard Antispam IP address checking identifies an email message as spam and adds this replacement message to the server response. |
| smtp-spam-helo | Spam Filtering HELO DNS lookup enabled for SMTP identifies an email message as spam and adds this replacement message. HELO DNS lookup is not available for SMTPS. |
| smtp-spam- mimeheader | From the CLI, spamhdrcheck enabled for an email protocol identifies an email message as spam and adds this replacement message. |
| submit | Any Spam Filtering option enabled for an email protocol identifies an email message as spam and adds this replacement message. Spam Filtering adds this message to all email tagged as spam. The message describes a button that the recipient of the message can select to submit the email signatures to the FortiGuard Antispam service if the email was incorrectly tagged as spam (a false positive). |

Replacement messages can include replacement message tags. When users receive the replacement message, the replacement message tag is replaced with content relevant to the message.

Table 21: Replacement message tags

| Tag | Description |
| --- | --- |
| %%QUARFILENAME%% | The name of a file that has been removed from a content stream and added to the quarantine. This could be a file that contained a virus or was blocked by antivirus file blocking. %%QUARFILENAME%% can be used in virus and file block messages. Quarantining is only available on FortiGate units with a local disk. |
| %%SOURCE_IP%% | The IP address from which a virus was received. For email this is the IP address of the email server that sent the email containing the virus. For HTTP this is the IP address of the web page that sent the virus. |
| %%DEST_IP%% | The IP address of the computer that would have received the blocked file. For email this is the IP address of the user’s computer that attempted to download the message from which the file was removed. |

Table 21: Replacement message tags

| Tag | Description |
| --- | --- |
| %%EMAIL_FROM%% | The email address of the sender of the message from which the file was removed. |
| %%EMAIL_TO%% | The email address of the intended receiver of the message from which the file was removed. |

replacemsg sslvpn

The SSL VPN login replacement messages are HTML replacement messages. The sslvpn-logon message formats the FortiGate SSL VPN portal login page.

The sslvpn-limit message formats the web page that appears if a user attempts to log into

SSL VPN more than once.

You can customize these replacement messages according to your organization’s needs. The pages are linked to FortiGate functionality and you must construct them according to the following guidelines to ensure that it will work.

These are HTML messages with HTTP headers.

Syntax

config system replacemsg sslvpn {sslvpn-limit | sslvpn-logon}

set buffer <message>

set format <format>

set header <header_type>

end

| Variable | Description | Default |
| --- | --- | --- |
| buffer <message> | Type a new replacement message to replace the current replacement message. Maximum length 8 192 characters. | Depends on message type. |
| format <format> | Set the format of the message: html text none | No default |
| header <header_type> | Set the format of the message header: 8bit http none | Depends on message type. |

Replacement messages can include replacement message tags. When users receive the replacement message, the replacement message tag is replaced with content relevant to the message.

replacemsg traffic-quota

When user traffic through the FortiGate unit is blocked by traffic shaper quota controls, users see the Traffic shaper block message or the Per IP traffic shaper block message when they attempt to connect through the FortiGate unit using HTTP.

This is an HTML message with an HTTP header.

Syntax

config system replacemsg traffic-quota {per-ip-shaper-block |

traffic-shaper-block}

set buffer <message>

set format <format>

set header <header_type>

end

| Variable | Description | Default |
| --- | --- | --- |
| buffer <message> | Type a new replacement message to replace the current replacement message. Maximum length 8 192 characters. | Depends on message type. |
| format <format> | Set the format of the message: html text none | No default |
| header <header_type> | Set the format of the message header: 8bit http none | Depends on message type. |

Replacement messages can include replacement message tags. When users receive the replacement message, the replacement message tag is replaced with content relevant to the message.

Requirements for traffic quota pages

The traffic quota HTTP pages should contain the %%QUOTA_INFO%% tag to display information about the traffic shaping quota setting that is blocking the user.

replacemsg utm

When data leaks or viruses are detected, these messages are substituted for the blocked item.

Syntax

config system replacemsg utm <message_type>

set buffer <message>

set format <format>

set header <header_type>

end

| Variable | Description | Default |
| --- | --- | --- |
| buffer <message> | Type a new replacement message to replace the current replacement message. Maximum length 8 192 characters. | Depends on message type. |
| format <format> | Set the format of the message: html text none | No default |
| header <header_type> | Set the format of the message header: 8bit http none | Depends on message type. |

| dlp-text | An email message is blocked because it appears to contain a data leak. |
| --- | --- |
| dlp-html | An HTTP transfer is blocked because it appears to contain a data leak. |
| virus-html | A virus was detected in a file being downloaded using an HTTP GET. |
| virus-text | A virus was detected in a file attachment. The file was removed. |

Table 22: Replacement message tags

| Tag | Description |
| --- | --- |
| %%FILE%% | The name of a file that has been removed from a content stream. This could be a file that contained a virus or was blocked by antivirus file blocking. %%FILE%% can be used in virus and file block messages. |
| %%VIRUS%% | The name of a virus that was found in a file by the antivirus system. %%VIRUS%% can be used in virus messages |

Table 22: Replacement message tags

| Tag | Description |
| --- | --- |
| %%QUARFILENAME%% | The name of a file that has been removed from a content stream and added to the quarantine. This could be a file that contained a virus or was blocked by antivirus file blocking. %%QUARFILENAME%% can be used in virus and file block messages. Quarantining is only available on FortiGate units with a local disk. |
| %%PROTOCOL%% | The protocol (HTTP, FTP, POP3, IMAP, SMTP) in which a virus was detected. %%PROTOCOL%% is added to alert email virus messages. |

replacemsg webproxy

The web proxy returns messages for user authentication failures and HTTP errors.

Syntax

config system replacemsg webproxy {auth-authorization | auth- challenge | auth-login | deny | http-err | user-limit}

set buffer <message>

set format <format>

set header <header_type>

| Variable | Description | Default |
| --- | --- | --- |
| buffer <message> | Type a new replacement message to replace the current replacement message. Maximum length 8 192 characters. | Depends on message type. |
| format <format> | Set the format of the message: html text none | html |
| header <header_type> | Set the format of the message header: 8bit http none | http |

The http-err replacement message requires the following tags:

Table 23: Web proxy http-err replacement message tags

| Tag | Description |
| --- | --- |
| %%HTTP_ERR_CODE%% | The returned HTTP error code, “404” for example. |
| %%HTTP_ERR_DESC%% | The returned HTTP error message, “Not Found” for example. |
| %%PROTOCOL%% | The protocol that applies to the traffic, “http://” for example. |
| %%URL%% | The URL (not including protocol) that caused the error. |

resource-limits

Use this command to configure resource limits that will apply to all VDOMs. When you set a global resource limit, you cannot exceed that resource limit in any VDOM. For example, enter the following command to limit all VDOMS to 100 VPN IPSec Phase 1 Tunnels:

config global

config system resource-limits set ipsec-phase1 100

end end

With this global limit set you can only add a maximum of 100 VPN IPSec Phase 1 Tunnels to any

VDOM.

You can also edit the resource limits for individual VDOMs to further limit the number of resources that you can add to individual VDOMs. See “system vdom-property” on page 683.

A resource limit of 0 means no limit. No limit means the resource is not being limited by the resource limit configuration. Instead the resource is being limited by other factors. The FortiGate unit limits dynamic resources by the capacity of the FortiGate unit and can vary depending on how busy the system is. Limits for static resources are set by limitations in the FortiGate configuration as documented in the FortiGate Maximum Values Matrix document.

The default maximum value for each resource depends on the FortiGate model. Dynamic resources (Sessions, Dial-up Tunnels, and SSL VPN) do not have default maximums so the default maximum for dynamic resources is always 0 (meaning unlimited). Static resources may have a limit set or many be set to 0 meaning they are limited by the resource limit configuration.

If you set the maximum resource usage for a VDOM you cannot reduce the default maximum     global limit for all VDOMs below this maximum.

This command is available only when VDOMs are enabled.

Syntax

config global

config system resource-limits set custom-service <max_int> set dialup-tunnel <max_int>

set firewall-address <max_int> set firewall-addrgrp <max_int> set firewall-policy <max_int> set ipsec-phase1 <max_int>

set ipsec-phase2 <max_int> set log-disk-quota <max_int> set onetime-schedule <max_int> set proxy <max_int>

set recurring-schedule <max_int>

set service-group <max_int>

set session <max_int>

set sslvpn <max_int>

set user <max_int>

set user-group <max_int>

end end

| Variable | Description | Default |
| --- | --- | --- |
| custom-service <max_int> | Enter the maximum number of firewall custom services. |  |
| dialup-tunnel <max_int> | Enter the maximum number of dialup-tunnels. |  |
| firewall-address <max_int> | Enter the maximum number of firewall addresses. |  |
| firewall-addrgrp <max_int> | Enter the maximum number of firewall address groups. |  |
| firewall-policy <max_int> | Enter the maximum number of firewall policies. |  |
| ipsec-phase1 <max_int> | Enter the maximum number of IPSec phase1 tunnels. |  |
| ipsec-phase2 <max_int> | Enter the maximum number of IPSec phase2 tunnels. |  |
| log-disk-quota <max_int> | Enter the maximum amount of log disk space available in MBytes for global log messages. The range depends on the amount of hard disk space available. |  |
| onetime-schedule <max_int> | Enter the maximum number of onetime schedules. |  |
| proxy <max_int> | Enter the maximum number of users that can be using the explicit proxy at one time. How the number of concurrent explicit proxy users is determined depends on their authentication method: • For session-based authenticated users, each authenticated user is counted as a single user. Since multiple users can have the same user name, the proxy attempts to identify users according to their authentication membership (based upon whether they were authenticated using RADIUS, LADAP, FSSO, local database etc.). If a user of one session has the same name and membership as a user of another session, the explicit proxy assumes this is one user. • For IP Based authentication, or no authentication, or if no explicit proxy security policy has been added, the source IP address is used to determine a user. All sessions from a single source address are assumed to be from the same user. |  |
| recurring-schedule <max_int> | Enter the maximum number of recurring schedules. |  |
| service-group <max_int> | Enter the maximum number of firewall service groups. |  |
| session <max_int> | Enter the maximum number of sessions. |  |
| sslvpn <max_int> | Enter the maximum number of sessions. |  |
| user <max_int> | Enter the maximum number of users. |  |
| user-group <max_int> | Enter the maximum number of user groups. |  |

server-probe

Use this command to configure server probing.

Syntax

config system server-probe edit <id>

set interval <seconds_int>

set port <port_int>

set protocol {ping | http-get}

set response-value <str>

set retry <tries-Int>

set server <server_addr>

set srcintf <interface_name> set status {enable | disable} set url <url_str>

end

| Variable | Description | Default |
| --- | --- | --- |
| interval <seconds_int> | Enter the period in seconds between probe attempts. | 60 |
| port <port_int> | Enter the TCP port for HTTP-Get protocol probe. | 80 |
| protocol {ping ¦ http-get} | Select the protocol to use when probing. | ping |
| response-value <str> | Enter the expected server response. This is available when protocol is http-get. | No default. |
| retry <tries-Int> | Enter the number of times to retry unsuccessful probe. | 5 |
| server <server_addr> | Enter the server IP address or FQDN to probe. | No default. |
| srcintf <interface_name> | Enter the interface to which the server is connected. | No default. |
| status {enable ¦ disable} | Enable or disable probe. | enable |
| url <url_str> | Enter the URL for HTTP-Get protocol probe. | No default. |

session-helper

FortiGate units use session helpers to process sessions that have special requirements. Session helpers function like proxies by getting information from the session and performing support functions required by the session. For example:

•  The SIP session helper looks inside SIP messages and performs NAT (if required) on the IP addresses in the SIP message and opens pinholes to allow media traffic associated with the SIP session to pass through the FortiGate unit.

•  The FTP session helper can keep track of multiple connections initiated from a single FTP session. The session helper can also permits an FTP server to actively open a connection back to a client program.

•  The TNS session helper sniffs the return packet from an initial 1521 SQLNET exchange and then uses the port and session information uncovered in that return TNS redirect packet to add a temporary firewall policy that accepts the new port and IP address supplied as part of the TNS redirect.

The session helper configuration binds a session helper to a TCP or UDP port and protocol. When a session is accepted by a firewall policy on that port and protocol the FortiGate unit passes the session to the session helper configured with this command. The session is processed by the session helper.

If your FortiGate unit accepts sessions that require a session helper on different ports than those defined by the session-helper configuration, then you can add more entire to the session helper configuration. Its OK to have multiple session helper configurations for a given protocol because only the matching configuration is used.

Use the show system session-helper command to view the current session helper configuration.

FortiGate units include the session helpers listed in Table 24:

Table 24: FortiGate session helpers

| Session helper name | Description |
| --- | --- |
| dcerpc | Distributed computing environment / remote procedure calls protocol (DCE/RPC). |
| dns-tcp | Domain name service (DNS) using the TCP protocol. |
| dns-udp | Domain name service (DNS) using the UDP protocol. |
| ftp | File transfer protocol (FTP). |
| h245I | H.245 I call-in protocol. |
| h245O | H.256 O call-out protocol. |
| h323 | H.323 protocol. |
| mgcp | Media gateway control protocol (MGCP). |
| mms | Multimedia message service (MMS) protocol |
| pmap | Port mapper (PMAP) protocol. |
| pptp | Point to point tunneling protocol (PPTP). |

Table 24: FortiGate session helpers

| Session helper name | Description |
| --- | --- |
| ras | Remote access service (RAS) protocol. |
| rsh | Remote shell protocol (RSH). |
| sip | Session initiation protocol (SIP). |
| tftp | Trivial file transfer protocol (TFTP). |
| tns | Oracle transparent network substrate protocol (TNS or SQLNET). |

Syntax

config system session-helper edit <helper-number>

set name {dcerpc | dns-tcp | dns-udp | ftp | h245I | H2450

| h323 | mgcp | mms | pmap | pptp | ras | rsh | sip | tftp

| tns}

set port <port_number>

set protocol <protocol_number>

end

| Variable | Description | Default |
| --- | --- | --- |
| <helper-number> | Enter the number of the session-helper that you want to edit, or enter an unused number or 0 to create a new session-helper. | No default. |
| name {dcerpc ¦ dns-tcp ¦ dns-udp ¦ ftp ¦ h245I ¦ H2450 ¦ h323 ¦ mgcp ¦ mms ¦ pmap ¦ pptp ¦ ras ¦ rsh ¦ sip ¦ tftp ¦ tns} | The name of the session helper to configure. | No default. |
| port <port_number> | Enter the port number to use for this protocol. | No default. |
| protocol <protocol_number> | The protocol number for this service, as defined in RFC 1700. | No default. |

session-sync

Use this command to configure TCP session synchronization between two standalone FortiGate units. You can use this feature with external routers or load balancers configured to distribute or load balance TCP sessions between two peer FortiGate units. If one of the peers fails, session failover occurs and active TCP sessions fail over to the peer that is still operating. This failover occurs without any loss of data. As well the external routers or load balancers will detect the failover and re-distribute all sessions to the peer that is still operating.

TCP session synchronization between two standalone FortiGate units is also sometimes called standalone session synchronization or session synchronization between non-HA FortiGate units.

You cannot configure standalone session synchronization when HA is enabled.

Syntax

config system session-sync edit <sync_id>

set peerip <peer_ipv4> set peervd <vd_name> set syncvd <vd_name> config filter

set dstaddr <dst_ip_ipv4> <dst_mask_ipv4>

set dstaddr6 <dst_ip_ipv6> set dstintf <interface_name> set service <string>

set srcaddr <src_ip_ipv4> <src_mask_ipv4>

set srcaddr6 <src_ip_ipv6>

set srcintf <interface_name>

end end

| Variable | Description | Default |
| --- | --- | --- |
| <sync_id> | Enter the unique ID number for the session synchronization configuration to edit. The session synchronization configuration ID can be any number between 1 and 200. The session synchronization configuration IDs of the peers do not have to match. | No default. |
| peerip <peer_ipv4> | Enter the IP address of the interface on the peer unit that is used for the session synchronization link. | 0.0.0.0 |
| peervd <vd_name> | Enter the name of the virtual domain that contains the session synchronization link interface on the peer unit. Usually both peers would have the same peervd. Multiple session synchronization configurations can use the same peervd. | root |
| syncvd <vd_name> | Enter the names of one or more virtual domains so that the sessions processed by these virtual domains are synchronized using this session synchronization configuration. |  |

| Variable | Description | Default |
| --- | --- | --- |
| config filter | Add a filter to a standalone session synchronization configuration. You can add a filter if you want to only synchronize some TCP sessions. Using a filter you can configure synchronization to only synchronize sessions according to source and destination address, source and destination interface, and predefined firewall TCP service. You can only add one filter to a standalone session synchronization configuration. |  |
| dstaddr <dst_ip_ipv4> <dst_mask_ipv4> dstaddr6 <dst_ip_ipv6> | Enter the destination IP address (or range) and netmask of the sessions to synchronize. For IPv4 addresses, use dstaddr. For IPv6 addresses, use dstaddr6. The default IP address and netmask (0.0.0.0 / 0.0.0.0 or ::/0) synchronizes sessions for all destination address. If you want to specify multiple IP addresses or address ranges you can add multiple standalone session synchronization configurations. | 0.0.0.0 0.0.0.0 ::/0 |
| dstintf <interface_name> | Enter the name of a FortiGate interface (this can be any interface including a VLAN interface, aggregate interface, redundant interface, virtual SSL VPN interface, or inter- VDOM link interface). Only sessions destined for this interface are synchronized. You can only enter one interface name. If you want to synchronize sessions for multiple interfaces you can add multiple standalone session synchronization configurations. The default dstintf setting synchronizes sessions for all interfaces. | (null) |
| service <string> | Enter the name of a FortiGate firewall predefined service. Only sessions that use this predefined service are synchronized. You can only enter one predefined service name. If you want to synchronize sessions for multiple services you can add multiple standalone session synchronization configurations. | (null) |
| srcaddr <src_ip_ipv4> <src_mask_ipv4> srcaddr6 <src_ip_ipv6> | Enter the source IP address and netmask of the sessions to synchronize. For IPv4 addresses, use srcaddr. For IPv6 addresses, use srcaddr6. The default IP address and netmask (0.0.0.0 / 0.0.0.0 or ::/0) synchronizes sessions for all source address. If you want to specify multiple IP addresses or address ranges you can add multiple standalone session synchronization configurations. | 0.0.0.0 0.0.0.0 ::/0 |
| srcintf <interface_name> | Enter the name of a FortiGate interface (this can be any interface including a VLAN interface, aggregate interface, redundant interface, virtual SSL VPN interface, or inter- VDOM link interface). Only sessions from this interface are synchronized. You can only enter one interface name. If you want to synchronize sessions for multiple interfaces you can add multiple standalone session synchronization configurations. The default srcintf setting synchronizes sessions for all interfaces. | (null) |

Fortinet Technologies Inc.                                                                Page 653                                     FortiOS™ - CLI Reference for FortiOS 5.0

session-ttl

Use this command to configure port-range based session timeouts by setting the session time to live (ttl) for multiple TCP, UDP, or SCTP port number ranges. The session ttl is the length of time a TCP, UDP, or SCTP session can be idle before being dropped by the FortiGate unit. You can add multiple port number ranges. For each range you can configure the protocol (TCP, UDP, or SCTP) and start and end numbers of the port number range.

Syntax

config system session-ttl set default <seconds> config port

edit <entry_id>

set end-port <port_number_int>

set protocol <protocol_int>

set start-port <port_number_int>

set timeout {<timeout_int> | never}

end

end

| Variable | Description | Default |
| --- | --- | --- |
| default <seconds> | Enter the default session timeout in seconds. The valid range is from 300 - 604 800 seconds. | 3600 |
| <entry_id> | Enter an entry ID. Range 0-65535. This is just an identifier, and does not assign the port number. | No default. |
| end-port <port_number_int> | The end port number of the port number range. You must configure both the start-port and end-port. To specify a range, the start-port value must be lower than the end-port value. To specify a single port, the start-port value must be identical to the end-port value. The range is 0 to 65 535. | 0 |
| protocol <protocol_int> | Enter the protocol number to match the protocol of the sessions for which to configure a session ttl range. The Internet Protocol Number is found in the IP packet header. RFC 5237 describes protocol numbers and you can find a list of the assigned protocol numbers here. The range is from 0 to 255. To enter a port number range you must set protocol to 6 for TCP sessions, to 17 for UDP sessions, or to 132 for SCTP sessions. | 0 |

Fortinet Technologies Inc.                                                                Page 654                                     FortiOS™ - CLI Reference for FortiOS 5.0

| Variable | Description | Default |
| --- | --- | --- |
| start-port <port_number_int> | The start port number of the port number range. You must configure both the start-port and end-port. To specify a range, the start-port value must be lower than the end-port value. To specify a single port, the start-port value must be identical to the end-port value. The range is 0 to 65 535. | 0 |
| timeout {<timeout_int> ¦ never} | Enter the number of seconds the session can be idle for on this port. The valid range is from 1 - 604800 seconds. Optionally you can enter never instead of specifying the number of seconds if you want the session to never expire. Caution: While it is possible to set timeout to never, this is not a secure configuration and should be avoided. | 300 |

Fortinet Technologies Inc.                                                                Page 655                                     FortiOS™ - CLI Reference for FortiOS 5.0

settings

Use this command to change settings that are per VDOM settings such as the operating mode and default gateway.

When changing the opmode of the VDOM, there are fields that are visible depending on which opmode you are changing to. They are only visible after you set the opmode and before you commit the changes with either ‘end or ‘next’. If you do not set these fields, the opmode change will fail.

Table 25: Fields associated with each opmode

| Change from NAT to Transparent mode | Change from Transparent to NAT mode |
| --- | --- |
| set gateway <gw_ipv4> set manageip <manage_ipv4> | set device <interface_name> set gateway <gw_ipv4> set ip <address_ipv4> |

system settings differs from system global in that system global fields apply to the entire FortiGate unit, where system settings fields apply only to the current VDOM, or the entire FortiGate unit if VDOMs are not enabled.

Bi-directional Forwarding Detection (BFD) is a protocol used by BGP and OSPF. It is used to quickly locate hardware failures in the network. Routers running BFD communicate with each other, and if a timer runs out on a connection then that router is declared down. BFD then communicates this information to the routing protocol and the routing information is updated. BFD support was added in FortiOS v3.0 MR4, and can only be configured through the CLI.

When asymmetric routing is enabled, through the use of asymroute field, the FortiGate unit     can no longer perform stateful inspection.

Syntax

config system settings

set allow-subnet-overlap {enable | disable}

set asymroute {enable | disable} set asymroute6 {enable | disable} set bfd {enable | disable}

set bfd-desired-min-tx <interval_msec> set bfd-required-min-rx <interval_msec> set bfd-detect-mult <multiplier

set bfd-dont-enforce-src-port {enable | disable}

set deny-tcp-with-icmp {enable | disable}

set device <interface_name>

set discovered-device-timeout <days_int>

set ecmp-max-paths <max_entries>

set gateway <gw_ipv4>

set gateway6 <gw_ipv6>

set gui-default-policy-columns <column_list>

set ip <address_ipv4>

set ip6 <address_ipv6>

set mac-ttl <seconds_int> set manageip <manage_ipv4> set manageip6 <manage_ipv6>

set multicast-forward {enable | disable}

set multicast-ttl-notchange {enable | disable}

set opmode {nat | transparent}

set sccp-port <port_number>

set ses-denied-traffic {enable | disable}

set sip-helper {enable | disable}

set sip-nat-trace {enable | disable}

set sip-ssl-port <port_number>

set sip-tcp-port <port1_int> [<port2_int>]>

set sip-udp-port <port_number>

set status {enable | disable}

set strict-src-check {enable | disable}

set utf8-spam-tagging {enable | disable}

set v4-ecmp-mode {source-ip-based | usage-based | weight-based}

set vpn-stats-log {ipsec | l2tp | pptp | ssl}

set vpn-stats-period <period_int>

set wccp-cache-engine {enable | disable}

end

| Variable | Description | Default |
| --- | --- | --- |
| allow-subnet-overlap {enable ¦ disable} | Enable limited support for interface and VLAN subinterface IP address overlap for this VDOM. Use this command to enable limited support for overlapping IP addresses in an existing network configuration. Caution: for advanced users only. Use this only for existing network configurations that cannot be changed to eliminate IP address overlapping. | disable |
| asymroute {enable ¦ disable} | Enable to turn on IPv4 asymmetric routing on your FortiGate unit, or this VDOM if you have VDOMs enabled. This feature should only be used as a temporary check to troubleshoot a network. It is not intended to be enabled permanently. When it enabled, many security features of your FortiGate unit are not enabled. Note: Enabling asymmetric routing disables stateful inspection. Your FortiGate unit can only perform stateless inspection in this state. | disable |
| asymroute6 {enable ¦ disable} | Enable to turn on IPv6 asymmetric routing on your FortiGate unit, or this VDOM if you have VDOMs enabled. | disable |
| bfd {enable ¦ disable} | Enable to turn on bi-directional forwarding detection (BFD) for this virtual domain, or the whole FortiGate unit. BFD can be used with OSPF and BGP configurations, and overridden on a per interface basis. | disable |

| Variable | Description | Default |
| --- | --- | --- |
| bfd-desired-min-tx <interval_msec> | Enter a value from 1 to 100 000 msec as the preferred minimum transmit interval for BFD packets. If possible this will be the minimum used. This variable is only available when bfd is enabled. | 50 |
| bfd-required-min-rx <interval_msec> | Enter a value from 1 to 100 000 msec as the required minimum receive interval for BFD packets. The FortiGate unit will not transmit BFD packets at a slower rate than this. This variable is only available when bfd is enabled. | 50 |
| bfd-detect-mult <multiplier | Enter a value from 1 to 50 for the BFD detection multiplier. | 3 |
| bfd-dont-enforce-src-port {enable ¦ disable} | Enable to not enforce the BFD source port. | disable |
| deny-tcp-with-icmp {enable ¦ disable} | Enable to deny TCP by sending an ICMP Communication Prohibited packet. Firewall policies will enable send-deny-packet. | disable |
| device <interface_name> | Enter the interface to use for management access. This is the interface to which ip applies. This field is visible only after you change opmode from transparent to nat, before you commit the change. | No default. |
| discovered-device-timeout <days_int> | Enter the timeout for discovered devices. Range: 1 to 365 days. | 28 |
| ecmp-max-paths <max_entries> | Enter the maximum number of routes allowed to be included in an Equal Cost Multi-Path (ECMP) configuration. Set to 1 to disable ECMP routing. ECMP routes have the same distance and the same priority, and can be used in load balancing. | 10 |
| email-portal-check-dns {enable ¦ disable} | Enable to have the email collection portal verify that the domain name part of email address can be resolved using a DNS lookup. | enable |
| gateway <gw_ipv4> | Enter the default gateway IP address. This field is visible only after you change opmode from nat to transparent or from transparent to nat, before you commit the change. | No default. |
| gateway6 <gw_ipv6> | Enter the default gateway IPv6 address. This field is visible only after you change opmode from nat to transparent or from transparent to nat, before you commit the change. | No default. |

Fortinet Technologies Inc.                                                                Page 658                                     FortiOS™ - CLI Reference for FortiOS 5.0

| Variable | Description | Default |
| --- | --- | --- |
| gui-default-policy-columns <column_list> | Optionally, override the web-based manager’s default displayed column set for firewall policies. <column_list> is a space-delimited list containing any of the following column names in the desired order of appearance from left to right: #, policyid, srcintf, dstintf, srcaddr, dstaddr, schedule, service, action, logtraffic, nat, status, authentication, count, profile, vpntunnel, comments | (null) |
| ip <address_ipv4> | Enter the IP address to use after switching to nat mode. This field is visible only after you change opmode from transparent to nat, before you commit the change. | No default. |
| ip6 <address_ipv6> | Enter the IPv6 address to use after switching to nat mode. This field is visible only after you change opmode from transparent to nat, before you commit the change. | No default. |
| mac-ttl <seconds_int> | Set duration of MAC addresses during transparent mode. Range: 300 to 8 640 000 seconds (100days). | 300 |
| manageip <manage_ipv4> | Set the IP address and netmask of the Transparent mode management interface. You must set this when you change opmode from nat to transparent. | No default. |
| manageip6 <manage_ipv6> | Set the IPv6 management address prefix for Transparent mode. | No default. |
| multicast-forward {enable ¦ disable} | Enable or disable multicast forwarding to forward any multicast IP packets in which the TTL is 2 or higher to all interfaces and VLAN interfaces except the receiving interface. The TTL in the IP header will be reduced by 1. When multiple VDOMs are configured, this option is available within each VDOM. | disable |
| multicast-ttl-notchange {enable ¦ disable} | Enable to alter multicast forwarding so that it does not decrement the time-to-live (TTL) in the packet header. Disable for normal multicast forwarding behavior. In multiple VDOM mode, this option is only available within VDOMs. It is not available at the global level. | disable |
| opmode {nat ¦ transparent} | Enter the required operating mode. If you change opmode from nat to transparent, you must set manageip and gateway. If you change opmode from transparent to nat, you must set device, ip, gateway- device and gateway. | nat |

Fortinet Technologies Inc.                                                                Page 659                                     FortiOS™ - CLI Reference for FortiOS 5.0

| Variable | Description | Default |
| --- | --- | --- |
| sccp-port <port_number> | Enter the port number from 1 to 65535 of the TCP port to use to monitor Skinny Client Call protocol (SCCP) traffic. SCCP is a Cisco proprietary protocol for VoIP. | 2000 |
| ses-denied-traffic {enable ¦ disable} | Enable or disable including denied traffic in session table. | disable |
| sip-helper {enable ¦ disable} | Enable or disable the SIP session helper. The SIP session helper will process SIP sessions unless the SIP sessions are accepted by the SIP ALG. | enable |
| sip-nat-trace {enable ¦ disable} | Select enable to record the original IP address of the phone. | enable |
| sip-ssl-port <port_number> | Enter the port number from 1 to 65535 that the SIP proxy monitors for SIP traffic. | 5061 |
| sip-tcp-port <port1_int> [<port2_int>]> | Enter of one or two port numbers (range 1 to 65535) that the SIP ALG monitors for SIP TCP sessions. | 5060 |
| sip-udp-port <port_number> | Enter the port number from 1 to 65535 that the SIP ALG monitors for SIP UDP sessions. | 5060 |
| status {enable ¦ disable} | Disable or enable this VDOM. Disabled VDOMs keep all their configuration, but the resources of that VDOM are not accessible. To leave VDOM mode, all disabled VDOMs must be deleted - to leave VDOM mode there can be only the root VDOM configured. Only available when VDOMs are enabled. | enable |
| strict-src-check {enable ¦ disable} | Enable to refuse packets from a source IP range if there is a specific route in the routing table for this network (RFC 3704). | disable |
| utf8-spam-tagging {enable ¦ disable} | Enable converts spam tags to UTF8 for better non-ascii character support. | enable |

Fortinet Technologies Inc.                                                                Page 660                                     FortiOS™ - CLI Reference for FortiOS 5.0

| Variable | Description | Default |
| --- | --- | --- |
| v4-ecmp-mode {source-ip-based ¦ usage-based ¦ weight-based} | Set the ECMP route failover and load balance method, which controls how the FortiGate unit assigns a route to a session when multiple equal- cost routes to the sessions’s destination are available. You can select: source-ip-based — the FortiGate unit load balances sessions among ECMP routes based on the source IP address of the sessions to be load balanced. No other settings can be configured to support source IP load balancing. weight-based — the FortiGate unit load balances sessions among ECMP routes based on weights added to ECMP routes. More traffic is directed to routes with higher weights. Use the weight field of the config router static command to add weights to static routes. See “router static” on page 443. usage-based — the FortiGate unit distributes sessions among ECMP routes based on how busy the FortiGate interfaces added to the routes are. After selecting usage-based you use the spillover-threshold field of the config system interface command to add spillover thresholds to interfaces added to ECMP routes. The FortiGate unit sends all ECMP-routed sessions to the lowest numbered interface until the bandwidth being processed by this interface reaches its spillover threshold. The FortiGate unit then spills additional sessions over to the next lowest numbered interface. See “system interface” on page 550. | source-ip-based |
| vpn-stats-log {ipsec ¦ l2tp ¦ pptp ¦ ssl} | Enable periodic VPN log statistics for one or more types of VPN. |  |
| vpn-stats-period <period_int> | Enter the interval in seconds for vpn-stats- log to collect statistics. | 0 |
| wccp-cache-engine {enable ¦ disable} | Configure the FortiGate unit to operate as a WCCP cache engine. Use the config system wccp command to configure WCCP cache engine settings. | disable |

Fortinet Technologies Inc.                                                                Page 661                                     FortiOS™ - CLI Reference for FortiOS 5.0

sit-tunnel

Use this command to tunnel IPv6 traffic over an IPv4 network. The IPv6 interface is configured under config system interface. The command to do the reverse is system ipv6- tunnel.This command is not available in Transparent mode.

Syntax

config system sit-tunnel edit <tunnel_name>

set destination <tunnel_address>

set interface <name>

set ip6 <address_ipv6>

set source <address_ipv4>

end

| Variable | Description | Default |
| --- | --- | --- |
| edit <tunnel_name> | Enter a name for the IPv6 tunnel. | No default. |
| destination <tunnel_address> | The destination IPv4 address for this tunnel. | 0.0.0.0 |
| interface <name> | The interface used to send and receive traffic for this tunnel. | No default. |
| ip6 <address_ipv6> | The IPv6 address for this tunnel. | No default. |
| source <address_ipv4> | The source IPv4 address for this tunnel. | 0.0.0.0 |

sflow

Use this command to add or change the IP address and UDP port that FortiGate sFlow agents use to send sFlow datagrams to an sFlow collector.

sFlow is a network monitoring protocol described in http://www.sflow.org. FortiOS implements sFlow version 5. You can configure one or more FortiGate interfaces as sFlow agents that monitor network traffic and send sFlow datagrams containing information about traffic flow to an sFlow collector.

sFlow is normally used to provide an overall traffic flow picture of your network. You would usually operate sFlow agents on switches, routers, and firewall on your network, collect traffic data from all of them and use a collector to show traffic flows and patterns.

Syntax

config system sflow

set collector-ip <collector_ipv4>

set collector_port <port_int>

set source-ip <ipv4_addr>

end

| Variable | Description | Default |
| --- | --- | --- |
| collector-ip <collector_ipv4> | The IP address of the sFlow collector that sFlow agents should send sFlow datagrams to. | 0.0.0.0 |
| collector_port <port_int> | The UDP port number used for sending sFlow datagrams. Change this setting only if required by your sFlow collector or you network configuration. | 6343 |
| source-ip <ipv4_addr> | Enter the source IP address for the sFlow agent. | 0.0.0.0 |

sms-server

Use this command to configure cellphone service provider entries for use with the SMS text message option for two-factor authentication.

One option for two-factor authentication sends a token via SMS text message to a cell phone number when the user or admin attempts to log on to the FortiGate unit. This token must be entered for the user or admin to be authenticated and allowed access.

Syntax

config system sms-server edit <provider>

set mail-server <server_name>

end

| Variable | Description | Default |
| --- | --- | --- |
| edit <provider> | Enter the name of a cell phone service provider. Maximum length allowed is 32 characters. To enter a name that includes spaces enclose the name in quotes. | null |
| mail-server <server_name> | Enter the address of the mail server that will accept the email and forward the message to the destination cell phone as an SMS text message. | null |

snmp  community

Use this command to configure SNMP communities on your FortiGate unit. You add SNMP communities so that SNMP managers can connect to the FortiGate unit to view system information and receive SNMP traps. SNMP traps are triggered when system events happen such as when antivirus checking is bypassed, or when the log disk is almost full.

You can add up to three SNMP communities. Each community can have a different configuration for SNMP queries and traps. Each community can be configured to monitor the FortiGate unit for a different set of events. You can also the add IP addresses of up to 8 SNMP managers to each community.

Part of configuring an SNMP manager is to list it as a host in a community on the FortiGate unit it will be monitoring. Otherwise the SNMP monitor will not receive any traps from that FortiGate unit, or be able to query it.

Syntax

config system snmp community edit <index_number>

set events <events_list>

set name <community_name>

set query-v1-port <port_number>

set query-v1-status {enable | disable}

set query-v2c-port <port_number>

set query-v2c-status {enable | disable}

set status {enable | disable} set trap-v1-lport <port_number> set trap-v1-rport <port_number>

set trap-v1-status {enable | disable}

set trap-v2c-lport <port_number>

set trap-v2c-rport <port_number>

set trap-v2c-status {enable | disable}

config hosts

edit <host_number>

set elbc-management {enable | disable}

set ha-direct {enable | disable} set host-type {any | query | trap} set interface <if_name>

set ip <address_ipv4>

set source-ip <address_ipv4/mask>

end

config hosts6

edit <host_number>

set ha-direct {enable | disable}

set interface <if_name>

set ip6 <address_ipv6>

set source-ip6 <address_ipv6>

end

end

| Variable | Description | Default |
| --- | --- | --- |
| edit <index_number> | Enter the index number of the community in the SNMP communities table. Enter an unused index number to create a new SNMP community. |  |
| events <events_list> | Enable the events for which the FortiGate unit should send traps to the SNMP managers in this community. amc-bypass — an AMC bridge module has switched to bridge (bypass) mode. av-bypass — FortiGate unit has entered bypass mode. See “set av-failopen pass” under “global” on page 520. av-conserve — System enters conserve mode. av-fragmented — A fragmented file has been detected. av-oversize — An oversized file has been detected. av-oversize-blocked — An oversized file has been blocked. av-oversize-passed — An oversized file has passed through. av-pattern — An file matching the AV pattern is detected. av-virus — A virus is detected. cpu-high — CPU usage exceeds threshold. Default is 80%. Automatic smoothing ensures only prolonged high CPU usage will trigger this trap, not a momentary spike. ent-conf-change — entity config change (rfc4133) fan-failure — A cooling fan has failed. faz-disconnect — A FortiAnalyzer device has disconnected from the FortiGate unit. fm-conf-change — FortiGate unit is managed by FortiManager, but the FortiGate administrator has modified the configuration directly. fm-if-change — FortiManager interface changes. ha-hb-failure — The HA heartbeat interface has failed. ha-member-down — The HA cluster member stops. ha-member-up — The HA cluster members starts. ha-switch — The primary unit in a HA cluster fails and is replaced with a new HA unit. | All events enabled. |

| Variable | Description intf-ip — The IP address of a FortiGate interface changes. ips-anomaly — IPS detects an anomaly. ips-pkg-update — IPS package has been updated. ips-signature — IPS detects an attack. log-full — Hard drive usage exceeds threshold. Default is 90%. mem-low — Memory usage exceeds threshold. Default is 80%. power-supply-failure — Power outage detected on monitored power supply. Available only on some models. vpn-tun-down — A VPN tunnel stops. vpn-tun-up — A VPN tunnel starts. | Default |
| --- | --- | --- |
| name <community_name> | Enter the name of the SNMP community. | No default. |
| query-v1-port <port_number> | Enter the SNMP v1 query port number used for SNMP manager queries. | 161 |
| query-v1-status {enable ¦ disable} | Enable or disable SNMP v1 queries for this SNMP community. | enable |
| query-v2c-port <port_number> | Enter the SNMP v2c query port number used for SNMP manager queries. | 161 |
| query-v2c-status {enable ¦ disable} | Enable or disable SNMP v2c queries for this SNMP community. | enable |
| status {enable ¦ disable} | Enable or disable the SNMP community. | enable |
| trap-v1-lport <port_number> | Enter the SNMP v1 local port number used for sending traps to the SNMP managers. | 162 |
| trap-v1-rport <port_number> | Enter the SNMP v1 remote port number used for sending traps to the SNMP managers. | 162 |
| trap-v1-status {enable ¦ disable} | Enable or disable SNMP v1 traps for this SNMP community. | enable |
| trap-v2c-lport <port_number> | Enter the SNMP v2c local port number used for sending traps to the SNMP managers. | 162 |
| trap-v2c-rport <port_number> | Enter the SNMP v2c remote port number used for sending traps to the SNMP managers. | 162 |
| trap-v2c-status {enable ¦ disable} | Enable or disable SNMP v2c traps for this SNMP community. | enable |
| hosts, hosts6 variables |
| edit <host_number> | Enter the index number of the host in the table. Enter an unused index number to create a new host. |  |
| elbc-management {enable ¦ disable} | Enable to allow use of snmp over the base channel and front panel ports in ELBC mode. |  |
| ha-direct {enable ¦ disable} | Enable direct management of cluster members. | disable |

Fortinet Technologies Inc.                                                                Page 667                                     FortiOS™ - CLI Reference for FortiOS 5.0

| Variable | Description | Default |
| --- | --- | --- |
| host-type {any ¦ query ¦ trap} | Set permitted actions for this host: query—make queries only trap—receive traps only any—any SMTP action | any |
| interface <if_name> | Enter the name of the FortiGate interface to which the SNMP manager connects. | No default. |
| ip <address_ipv4> | Enter the IPv4 IP address of the SNMP manager (for hosts). | 0.0.0.0 |
| ip6 <address_ipv6> | Enter the IPv6 IP address of the SNMP manager (for hosts6). | :: |
| source-ip <address_ipv4/mask > | Enter the source IPv4 IP address for SNMP traps sent by the FortiGate unit (for hosts). | 0.0.0.0/ 0.0.0.0 |
| source-ip6 <address_ipv6> | Enter the source IPv6 IP address for SNMP traps sent by the FortiGate unit (for hosts6). | :: |

Fortinet Technologies Inc.                                                                Page 668                                     FortiOS™ - CLI Reference for FortiOS 5.0

snmp  sysinfo

Use this command to enable the FortiGate SNMP agent and to enter basic system information used by the SNMP agent. Enter information about the FortiGate unit to identify it. When your SNMP manager receives traps from the FortiGate unit, you will know which unit sent the information. Some SNMP traps indicate high CPU usage, log full, or low memory.

Syntax

config system snmp sysinfo

set contact-info <info_str> set description <description> set engine-id <engine-id_str> set location <location>

set status {enable | disable}

set trap-high-cpu-threshold <percentage> set trap-log-full-threshold <percentage> set trap-low-memory-threshold <percentage>

end

| Variable | Description | Default |
| --- | --- | --- |
| contact-info <info_str> | Add the contact information for the person responsible for this FortiGate unit. The contact information can be up to 35 characters long. | No default. |
| description <description> | Add a name or description of the FortiGate unit. The description can be up to 35 characters long. | No default. |
| engine-id <engine-id_str> | Each SNMP engine maintains a value, snmpEngineID, which uniquely identifies the SNMP engine. This value is included in each message sent to or from the SNMP engine. In FortiOS, the snmpEngineID is composed of two parts: • Fortinet prefix 0x8000304404 • the optional engine-id string, 24 characters maximum, defined in this command Optionally, enter an engine-id value. | No default. |
| location <location> | Describe the physical location of the FortiGate unit. The system location description can be up to 35 characters long. Note: XSS vulnerability checking is disabled, so XSS characters such as ‘(‘ and ‘)’ are permitted. | No default. |
| status {enable ¦ disable} | Enable or disable the FortiGate SNMP agent. | disable |
| trap-high-cpu-threshold <percentage> | Enter the percentage of CPU used that will trigger the threshold SNMP trap for the high-cpu. There is some smoothing of the high CPU trap to ensure the CPU usage is constant rather than a momentary spike. This feature prevents frequent and unnecessary traps. | 80 |

Fortinet Technologies Inc.                                                                Page 669                                     FortiOS™ - CLI Reference for FortiOS 5.0

| Variable | Description | Default |
| --- | --- | --- |
| trap-log-full-threshold <percentage> | Enter the percentage of disk space used that will trigger the threshold SNMP trap for the log-full. | 90 |
| trap-low-memory-threshold <percentage> | Enter the percentage of memory used that will be the threshold SNMP trap for the low-memory. | 80 |

Fortinet Technologies Inc.                                                                Page 670                                     FortiOS™ - CLI Reference for FortiOS 5.0

snmp  user

Use this command to configure an SNMP user including which SNMP events the user wants to be notified about, which hosts will be notified, and if queries are enabled which port to listen on for them.

FortiOS implements the user security model of RFC 3414. You can require the user to authenticate with a password and you can use encryption to protect the communication with the user.

Syntax

config system snmp user edit <username>

set auth-proto {md5 | sha}

set auth-pwd <password>

set events <event_string>

set ha-direct {enable | disable} set notify-hosts <hosts_string> set notify-hosts6 <hosts_string> set priv-proto {aes | des}

set priv-pwd <key>

set queries {enable | disable}

set query-port <port_int>

set security-level <slevel>

end

| Variable | Description | Default |
| --- | --- | --- |
| edit <username> | Edit or add selected user. | No default. |
| auth-proto {md5 ¦ sha} | Select authentication protocol: md5 — use HMAC-MD5-96 authentication protocol. sha — use HMAC-SHA-96 authentication protocol. This is only available if security-level is auth-priv or auth-no-priv. | sha |
| auth-pwd <password> | Enter the user’s password. Maximum 32 characters. This is only available if security-level is auth-priv or auth-no-priv. | No default. |

Fortinet Technologies Inc.                                                                Page 671                                     FortiOS™ - CLI Reference for FortiOS 5.0

| Variable | Description | Default |
| --- | --- | --- |
| events <event_string> | Select which SNMP notifications to send. Select each event that will generate a notification, and add to string. Separate multiple events by a space. Available events include: amc-bypass — an AMC bridge module has switched to bridge (bypass) mode. av-bypass — AV bypass happens av-conserve — AV system enters conserve mode av-fragmented — AV detected fragmented file av-oversize — AV detected oversized file av-oversize-blocked — AV oversized files blocked av-oversize-passed — AV oversized files passed av-pattern — AV detected file matching pattern av-virus — AV detected virus cpu-high — cpu usage too high ent-conf-change — entity config change (rfc4133) fan-failure — A cooling fan has failed. faz-disconnect — FortiAnalyzer unit disconnected fm-conf-change — config change (FM trap) fm-if-change — interface IP change (FM trap) ha-hb-failure — HA heartbeat interface failure ha-member-down — HA cluster member down ha-member-up — HA cluster member up ha-switch — HA cluster status change intf-ip — interface IP address changed ips-anomaly — ips detected an anomaly ips-pkg-update — ips package updated ips-signature — ips detected an attack log-full — available log space is low mem-low — available memory is low power-supply-failure — power supply failure vpn-tun-down — VPN tunnel is down vpn-tun-up — VPN tunnel is up Note: On the events field, the unset command clears all options. | No default. |
| ha-direct {enable ¦ disable} | Enable direct management of cluster members. | disable |
| notify-hosts <hosts_string> | Enter IPv4 IP addresses to send SNMP notifications (SNMP traps) to when events occur. Separate multiple addresses with a space. | No default. |

Fortinet Technologies Inc.                                                                Page 672                                     FortiOS™ - CLI Reference for FortiOS 5.0

| Variable | Description | Default |
| --- | --- | --- |
| notify-hosts6 <hosts_string> | Enter IPv6 IP addresses to send SNMP notifications (SNMP traps) to when events occur. Separate multiple addresses with a space. | No default. |
| priv-proto {aes ¦ des} | Select privacy (encryption) protocol: aes — use CFB128-AES-128 symmetric encryption. des — use CBC-DES symmetric encryption. This is available if security-level is auth-priv. | aes |
| priv-pwd <key> | Enter the privacy encryption key. Maximum 32 characters. This is available if security-level is auth-priv. | No default. |
| queries {enable ¦ disable} | Enable or disable SNMP v3 queries for this user. Queries are used to determine the status of SNMP variables. | enable |
| query-port <port_int> | Enter the number of the port used for SNMP v3 queries. If multiple versions of SNMP are being supported, each version should listen on a different port. | 161 |
| security-level <slevel> | Set security level to one of: no-auth-no-priv — no authentication or privacy auth-no-priv — authentication but no privacy auth-priv — authentication and privacy | no-auth-no-priv |

Fortinet Technologies Inc.                                                                Page 673                                     FortiOS™ - CLI Reference for FortiOS 5.0

sp

Use this command to configure offloading traffic to a FortiASIC Security Processing (SP) Module. Fortinet security processing modules provide multi-gigabit throughput increases for intrusion prevention, firewall, and IP multicast applications. All models are based on the carrier- class Advanced Mezzanine Card™ (AMC) specification.

FortiGate units that support these modules offer a third action. Legitimate connections are allowed while an attack is blocked.

This command is only available on models with one or more AMC slots and a FortiASIC Security

Processing Module installed. When VDOMs are enabled, this is a global command.

Syntax

config system sp

set name <string>

set ips-weight {less-fw | balanced | all-ips}

set fp-disable {all | ips | ipsec | multicast | DoS | none}

set ipsec-inb-optimization {enable | disable}

set syn-proxy-client-timer <sec_int>

set syn-proxy-server-timer <sec_int>

end

| Variable | Description | Default |
| --- | --- | --- |
| name <string> | Maximum of 31 characters. |  |
| ips-weight {less-fw ¦ balanced ¦ all-ips} | Select the weighting method for IPS sessions. Default is less-fw. • less-fw • balanced • all-ips | less-fw |
| fp-disable {all ¦ ips ¦ ipsec ¦ multicast ¦ DoS ¦ none} | Select one or more types of traffic to exclude from file processing. Security processing modules can accelerate different security features such as firewall, IPS, multicast, and DoS. By default the modules will accelerate all those types of traffic, but you can disable acceleration of one or more of those types of traffic with this command. Any one or more types of traffic listed will not be accelerated, and will be handled by the FortiOS system. | none |
| ipsec-inb-optimization {enable ¦ disable} | Select to enable inbound IPsec optimization. | enable |

Fortinet Technologies Inc.                                                                Page 674                                     FortiOS™ - CLI Reference for FortiOS 5.0

| Variable | Description | Default |
| --- | --- | --- |
| syn-proxy-client-timer <sec_int> | Set the number of seconds for the client side timer for the three-way handshake. If the timer expires and the handshake is not complete, the connection is discarded. Range is 1 to 255. Default is 3. For the tcp_syn_flood threshold, in addition to Block and Pass, you can choose to Proxy connect attempts when their volume exceeds the threshold value. When the tcp_syn_flood threshold action is set to Proxy, incomplete TCP connections are allowed as normal as long as the configured threshold is not exceeded. If the threshold is exceeded, the FortiGate unit will intercept incoming SYN packets with a hardware accelerated SYN proxy to determine whether the connection attempts are legitimate or a SYN flood attack. | 3 |
| syn-proxy-server- timer <sec_int> | Set the number of seconds for the server side timer for the three-way handshake. If the timer expires and the handshake is not complete, the connection is discarded. Range is 1 to 255. Default is 3. | 3 |

Fortinet Technologies Inc.                                                                Page 675                                     FortiOS™ - CLI Reference for FortiOS 5.0

storage

Use this command to add and edit local disk storage settings.

Syntax

config system storage edit <storage_name>

set media-type <name>

set partition <partition_ref_int>

end

| Variable | Description | Default |
| --- | --- | --- |
| <storage_name> | The name for this storage. |  |
| media-type <name> | The type of disk. You cannot configure or change this setting. |  |
| partition <partition_ref_int> | The partition reference number. See “execute disk” on page 904. |  |

stp

Use this command to configure Spanning Tree Protocol on an Internal interface switch in switch mode.

Syntax

config system stp

set config-revision <int>

set forward-delay <secs_int>

set hello-time <secs_int>

set max-age <secs_int>

set max-hops <hops_int>

set region-name <name_str>

set status {enable | disable}

set switch-priority <prio_int>

end

| Variable | Description | Default |
| --- | --- | --- |
| config-revision <int> | Set the configuration revision. Range 0-65535. | 0 |
| forward-delay <secs_int> | Set forwarding delay. Range 4 to 30. | 15 |
| hello-time <secs_int> | Set hello time. Range 1 to 10. | 2 |
| max-age <secs_int> | Set maximum packet age. Range 6 to 40. | 20 |
| max-hops <hops_int> | Set maximum number of hops. Range 1 to 40. | 20 |
| region-name <name_str> | Set region name. | null |
| status {enable ¦ disable} | Enable or disable STP. | enable |
| switch-priority <prio_int> | Set priority. Permitted values: 0, 4096, 8192, 12288, 16384, 20480, 24576, 28672, 32768, 36864, 40960, 45056, 49152, 53248, 57344, 61440. | 32768 |

switch-interface

Use this command to group physical and wifi interfaces into a software switch interface (also called a softswitch, soft-switch or soft switch). A software switch is a virtual switch that is implemented in software instead of hardware. When you add interfaces to a software switch the interfaces all share one IP address and become a single entry on the interface list. As a result, all of the interfaces are on the same subnet and traffic between devices connected to each interface of the software switch cannot be filtered by firewall policies.

Adding a software switch can be used to simplify communication between devices connected to different FortiGate interfaces. For example, using a software switch you can place the FortiGate interface connected to an internal network on the same subnet as your wireless interfaces. Then devices on the internal network can communicate with devices on the wireless network without any additional configuration on the FortiGate unit.

The physical and WiFi interfaces added to a software switch interface cannot be used in any other configurations. The wifi interfaces can be implemented on the FortiWiFi unit or on remote FortiWiFi units of FortiAP units controlled by the wireless controller feature. Interfaces in a software switch cannot be monitored by HA or used as heart beat devices.

This command can be used at the Global or VDOM level.

Syntax

config system switch-interface edit <group_name>

set member <iflist>

set span {enable | disable}

set span-dest-port <portnum>

set span-direction {rx | tx | both}

set span-source-port <portlist>

set type {hub | switch | hardware-switch}

set vdom <vdom_name>

end

| Variable | Description | Default |
| --- | --- | --- |
| <group_name> | The name for this software switch. Cannot be in use by any other interfaces, vlans, or inter- VDOM links. | No default. |
| member <iflist> | Enter a list of the interfaces that will be part of this software switch. Separate interface names with a space. Use <tab> to advance through the list of available interfaces. | No default. |
| span {enable ¦ disable} | Enable or disable port spanning. This is available only when type is switch. Port spanning echoes traffic received by the software switch to the span destination port. Port spanning can be used to monitor all traffic passing through the soft switch. You can also configure the span destination port and the span source ports., which are the switch ports for which traffic is echoed. | disable |
| span-dest-port <portnum> | Enter the span port destination port name. All traffic on the span source ports is echoed to the span destination port. Use <tab> to advance through the list of available interfaces. Available when span is enabled. | No default. |

| Variable | Description | Default |
| --- | --- | --- |
| span-direction {rx ¦ tx ¦ both} | Select the direction in which the span port operates: rx — Copy only received packets from source SPAN ports to the destination SPAN port. tx — Copy only transmitted packets from source SPAN ports to the destination SPAN port. both — Copy both transmitted and received packets from source SPAN ports to the destination SPAN port. span-direction is available only when span is enabled. | both |
| span-source-port <portlist> | Enter a list of the interfaces that are span source ports. Separate interface names with a space. Port spanning echoes all traffic on the span source ports to the span destination port. Use <tab> to advance through the list of available interfaces. Available when span is enabled. | No default. |
| type {hub ¦ switch ¦ hardware-switch} | Select the type of switch functionality: hub — duplicates packets to all member ports switch — normal switch functionality (available in NAT mode only) | switch |
| vdom <vdom_name> | Enter the VDOM to which the software switch belongs. | No default. |

Fortinet Technologies Inc.                                                                Page 679                                     FortiOS™ - CLI Reference for FortiOS 5.0

tos-based-priority

Use this command to prioritize your network traffic based on its type-of-service (TOS).

IP datagrams have a TOS byte in the header (as described in RFC 791). Four bits within this field determine the delay, the throughput, the reliability, and cost (as described in RFC 1349) associated with that service. There are 4 other bits that are seldom used or reserved that are not included here. Together these bits are the tos variable of the tos-based-priority command.

The TOS information can be used to manage network traffic and its quality based on the needs of the application or service. TOS application routing (RFC 1583) is supported by OSPF routing.

For more information on TOS in routing, see “policy, policy6” on page 414.

Syntax

config system tos-based-priority edit <name>

set tos <ip_tos_value>

set priority [high | medium | low]

end

| Variable | Description | Default |
| --- | --- | --- |
| edit <name> | Enter the name of the link object to create | No default. |
| tos <ip_tos_value> | Enter the value of the type of service byte in the IP datagram header: 8 -- minimize delay 4 -- maximize throughput 2 -- maximize reliability 1 -- minimize monetary cost 0 -- default service | 0 |
| priority [high ¦ medium ¦ low] | Select the priority of this type of service as either high, medium, or low priority. These priority levels conform to the firewall traffic shaping priorities. | high |

vdom-dns

Use this command to configure DNS servers for a non-management VDOM. This command is only available from a non-management VDOM

DNS settings such as dns-cache-limit and set globally. See “system dns” on page 504.

Syntax

config system vdom-dns

set ip6-primary <dns_ipv6> set ip6-secondary <dns_ip6> set primary <dns_ipv4>

set secondary <dns_ip4>

set source-ip <ipv4_addr>

set vdom-dns {disable | enable}

end

| Variable | Description | Default |
| --- | --- | --- |
| ip6-primary <dns_ipv6> | Enter the primary IPv6 DNS server IP address. | :: |
| ip6-secondary <dns_ip6> | Enter the secondary IPv6 DNS server IP address. | :: |
| primary <dns_ipv4> | Enter the primary DNS server IP address. | 0.0.0.0 |
| secondary <dns_ip4> | Enter the secondary DNS IP server address. | 0.0.0.0 |
| source-ip <ipv4_addr> | Enter the source IP for communications to DNS server. | 0.0.0.0 |
| vdom-dns {disable ¦ enable} | Enable configuring DNS servers for the current VDOM. | disable |

vdom-link

Use this command to create an internal point-to-point interface object. This object is a link used to join virtual domains. Inter-VDOM links support BGP routing, and DHCP.

Creating the interface object also creates 2 new interface objects by the name of <name>0 and

<name>1. For example if your object was named v_link, the 2 interface objects would be named v_link0 and v_link1. You can then configure these new interfaces as you would any other virtual interface using config system interface.

When using vdom-links in HA, you can only have vdom-links in one vcluster. If you have vclusters defined, you must use the vcluster field to determine which vcluster will be allowed to contain the vdom-links.

A packet can pass through an inter-VDOM link a maximum of three times. This is to prevent a loop. When traffic is encrypted or decrypted it changes the content of the packets and this resets the inter-VDOM counter. However using IPIP or GRE tunnels do not reset the counter.

Syntax

config system vdom-link edit <name>

set type {ppp | ethernet}

set vcluster {1|2}

end

| Variable | Description | Default |
| --- | --- | --- |
| edit <name> | Enter the name of the link object to create. You are limited to 8 characters maximum for the name. | No default. |
| type {ppp ¦ ethernet} | Select type of VDOM link: PPP or Ethernet. | ppp |
| vcluster {1¦2} | Select vcluster 1 or 2 as the only vcluster to have inter- VDOM links. This option is available only when HA and vclusters are configured, and there are VDOMs in both vclusters. |  |

vdom-property

Use this command to enter a description of a VDOM and to configure resource usage for the

VDOM that overrides global limits and specifies guaranteed resource usage for the VDOM.

When configuring resource usage for a VDOM you can set the Maximum and Guaranteed value for each resource.

•  The Maximum value limits the amount of the resource that can be used by the VDOM. When you add a VDOM, all maximum resource usage settings are 0 indicating that resource limits for this VDOM are controlled by the global resource limits. You do not have to override the maximum settings unless you need to override global limits to further limit the resources available for the VDOM. You cannot set maximum resource usage higher in a VDOM than the corresponding global resource limit. For each resource you can override the global limit to reduce the amount of each resource available for this VDOM. The maximum must the same as or lower than the global limit. The default value is 0, which means the maximum is the same as the global limit.

Use the command “system resource-limits” on page 647 to set global resource limits.

•  The Guaranteed value represents the minimum amount of the resource available for that VDOM. Setting the guaranteed value makes sure that other VDOMs do not use all of a resource. A guaranteed value of 0 means that an amount of this resource is not guaranteed for this VDOM. You only have to change guaranteed settings if your FortiGate may become low on resources and you want to guarantee that a minimum level is available for this VDOM. For each resource you can enter the minimum amount of the resource available to this VDOM regardless of usage by other VDOMs. The default value is 0, which means that an amount of this resource is not guaranteed for this VDOM.

Syntax

config global

config system vdom-property edit <vdom_name>

set custom-service <max_int> [<guaranteed_int>]

set description <description_str>

set dialup-tunnel <max_int> [<guaranteed_int>] set firewall-policy <max_int> [<guaranteed_int>] set firewall-profile <max_int> [<guaranteed_int>] set firewall-address <max_int> [<guaranteed_int>] set firewall-addrgrp <max_int> [<guaranteed_int>] set ipsec-phase1 <max_int> [<guaranteed_int>]

set ipsec-phase2 <max_int> [<guaranteed_int>]

set log-disk-quota <max_int>

set onetime-schedule <max_int> [<guaranteed_int>] set recurring-schedule <max_int> [<guaranteed_int>] set service-group <max_int> [<guaranteed_int>]

set session <max_int> [<guaranteed_int>]

set user <max_int> [<guaranteed_int>]

set user-group <max_int> [<guaranteed_int>]

set web-proxy <max_int>

end end

| Variable | Description | Default |
| --- | --- | --- |
| edit <vdom_name> | Select the VDOM to set the limits for. |  |
| custom-service <max_int> [<guaranteed_int>] | Enter the maximum and guaranteed number of firewall custom services. | 0 0 |
| description <description_str> | Enter a description of the VDOM. The description can be up to 63 characters long. |  |
| dialup-tunnel <max_int> [<guaranteed_int>] | Enter the maximum and guaranteed number of dialup- tunnels. | 0 0 |
| firewall-policy <max_int> [<guaranteed_int>] | Enter the maximum and guaranteed number of firewall policies. | 0 0 |
| firewall-profile <max_int> [<guaranteed_int>] | Enter the maximum and guaranteed number of firewall profiles. | 0 0 |
| firewall-address <max_int> [<guaranteed_int>] | Enter the maximum and guaranteed number of firewall addresses. | 0 0 |
| firewall-addrgrp <max_int> [<guaranteed_int>] | Enter the maximum and guaranteed number of firewall address groups. | 0 0 |
| ipsec-phase1 <max_int> [<guaranteed_int>] | Enter the maximum and guaranteed number of IPSec phase1 tunnels. | 0 0 |
| ipsec-phase2 <max_int> [<guaranteed_int>] | Enter the maximum and guaranteed number of IPSec phase2 tunnels. | 0 0 |
| log-disk-quota <max_int> | Enter the maximum amount of log disk space available in MBytes for log messages for this VDOM. The range depends on the amount of hard disk space available. | 0 0 |
| onetime-schedule <max_int> [<guaranteed_int>] | Enter the maximum and guaranteed number of onetime schedules. | 0 0 |
| recurring-schedule <max_int> [<guaranteed_int>] | Enter the maximum and guaranteed number of recurring schedules. | 0 0 |
| service-group <max_int> [<guaranteed_int>] | Enter the maximum and guaranteed number of firewall service groups. | 0 0 |
| session <max_int> [<guaranteed_int>] | Enter the maximum and guaranteed number of sessions. | 0 0 |
| user <max_int> [<guaranteed_int>] | Enter the maximum and guaranteed number of users. | 0 0 |

| Variable | Description | Default |
| --- | --- | --- |
| user-group <max_int> [<guaranteed_int>] | Enter the maximum and guaranteed number of user groups. | 0 0 |
| web-proxy <max_int> | Enter the maximum number of users that can be using the explicit web proxy at one time from this VDOM. How the number of concurrent explicit proxy users is determined depends on their authentication method: • For session-based authenticated users, each authenticated user is counted as a single user. Since multiple users can have the same user name, the proxy attempts to identify users according to their authentication membership (based upon whether they were authenticated using RADIUS, LADAP, FSSO, local database etc.). If a user of one session has the same name and membership as a user of another session, the explicit proxy assumes this is one user. • For IP Based authentication, or no authentication, or if no web-proxy firewall policy has been added, the source IP address is used to determine a user. All sessions from a single source address are assumed to be from the same user. | 0 0 |

Fortinet Technologies Inc.                                                                Page 685                                     FortiOS™ - CLI Reference for FortiOS 5.0

vdom-radius-server

Use this command to specify the dynamic profile RADIUS server for each VDOM. This command is available only if VDOMs are enabled (vdom-admin is enabled in config system global).

Syntax

config system vdom-radius-server edit vdom_name <name_str>

set status {enable | disable}

set radius-server-vdom <vdom_name_str>

end

| Variable | Description | Default |
| --- | --- | --- |
| vdom_name <name_str> | Enter the VDOM name. | No default. |
| status {enable ¦ disable} | Enable or disable this VDOM RADIUS server entry. | disable |
| radius-server-vdom <vdom_name_str> | Enter the VDOM of the dynamic profile radius server to use for dynamic profile traffic in the current vdom. | No default. |

vdom-sflow

Use this command to add or change the IP address and UDP port that FortiGate sFlow agents operating on interfaces in a non-management VDOM use to send sFlow datagrams to an sFlow collector.

Syntax

config system sit-tunnel

set collector-ip <collector_ipv4> set collector-ip <collector_ipv4> set vdom-sflow {enable | disable}

end

| Variable | Description | Default |
| --- | --- | --- |
| collector-ip <collector_ipv4> | The IP address of the sFlow collector that sFlow agents added to interfaces in this VDOM should send sFlow datagrams to. | 0.0.0.0 |
| collector_port <port_int> | The UDP port number used for sending sFlow datagrams. Change this setting only if required by your sFlow collector or you network configuration. | 6343 |
| vdom-sflow {enable ¦ disable} | Enable configuring sFlow settings for the current VDOM. | enable |

virtual-switch

Use this command to configure virtual switch interfaces on the FortiGate models that support this feature.

Syntax

config system virtual-switch edit <vswitch_name>

set set physical-switch <switch_name>

config port

edit <port_name>

set duplex {full | half}

set speed <interface_speed>

set status {up | down}

end end

| Variable | Description | Default |
| --- | --- | --- |
| <vswitch_name> | Enter a name for the virtual switch. | No default. |
| set physical-switch <switch_name> | Enter the hardware switch name, sw0 for example. |  |
| config port | Create an entry for each member interface. |  |
| <port_name> | Enter the interface name. |  |
| duplex {full ¦ half} | Select duplex setting. | full |
| speed <interface_speed> | Set the interface speed: auto — the default speed. The interface uses auto- negotiation to determine the connection speed. Change the speed only if the interface is connected to a device that does not support auto-negotiation. 10full — 10 Mbps, full duplex 10half — 10 Mbps, half duplex 100full — 100 Mbps, full duplex 100half — 100 Mbps, half duplex 1000full — 1000 Mbps, full duplex 1000half — 1000 Mbps, half duplex Speed options vary for different models and interfaces. Enter and a set speed ? to display a list of speeds available for your model and interface. | auto |
| status {up ¦ down} | Select up or down status for this member interface. | up |

wccp

Configure settings for Web Cache Communication Protocol (WCCP).

You can configure a FortiGate unit to operate as a WCCP router or client.

•  A FortiGate unit operating as a WCCP router can intercept HTTP and HTTPS sessions and forward them to a web caching engine that caches web pages and returns cached content to the web browser.

•  A FortiGate unit operating as a WCCP client can accept and forward WCCP sessions and use firewall policies to apply NAT, UTM, and other FortiGate security features to them. A FortiGate unit operates as a WCCP client only in NAT/Route mode (and not in Transparent mode)

Enter the following command to configure a FortiGate unit to operate as a WCCP router (this is the default FortiGate WCCP configuration):

config system settings

set wccp-cache-engine disable end

Enter the following command to configure a FortiGate unit to operate as a WCCP client:

config system settings

set wccp-cache-engine enable end

When you enter this command an interface named w.<vdom_name> is added to the FortiGate configuration (for example w.root). All WCCP sessions received by a FortiGate unit operating as a WCCP client are considered to be received at this interface and you can enter firewall policies for the WCCP traffic.

Syntax (WCCP router  mode)

config system wccp edit <service-id>

set router-id <interface_ipv4>

set group-address <multicast_ipv4>

set server-list <router1_ipv4> [<router2_ipv4> ...

<router4_ipv4>]

set authentication {disable | enable} set forward-method {GRE | L2 | any} set return-method {GRE | L2 | any}

set assignment-method {HASH | MASK | any}

set password <password_str>

next end

Syntax (WCCP client mode)

config system wccp edit <service-id>

set cache-id <cache_engine_ip4>

set group-address <multicast_ipv4>

set router-list <server_ipv4mask>

set authentication {disable | enable}

set service-type {auto | dynamic | standard}

set assignment-weight <weight_int>

set assignment-bucket-format {cisco-implementation | wccp-v2}

set password <password_str>

next end

| Variable | Description | Default |
| --- | --- | --- |
| <service-id> | Valid ID range is from 0 to 255. 0 for HTTP. | 1 |
| router-id <interface_ipv4> | An IP address known to all cache engines. This IP address identifies a FortiGate interface IP address to the cache engines. If all cache engines connect to the same FortiGate interface, then <interface_ipv4> can be 0.0.0.0, and the FortiGate unit uses the IP address of that interface as the router-id. If the cache engines can connect to different FortiGate interfaces, you must set router-id to a single IP address, and this IP address must be added to the configuration of the cache engines that connect to that interface. | 0.0.0.0 |
| cache-id <cache_engine_ip4> | The IP address of the cache engine if its IP address is not the same as the IP address of a FortiGate interface. If the IP address of the cache engine is the same as the IP address of the FortiGate interface on which you have enabled WCCP, the cache-id should be 0.0.0.0. | 0.0.0.0 |
| group-address <multicast_ipv4> | The IP multicast address used by the cache routers. 0.0.0.0 means the FortiGate unit ignores multicast WCCP traffic. Otherwise, group-address must be from 224.0.0.0 to 239.255.255.255. | 0.0.0.0 |
| server-list <router1_ipv4> [<router2_ipv4> ... <router4_ipv4>] | The IP address and net mask of up to four WCCP routers. | 0.0.0.0 0.0.0.0 |
| router-list <server_ipv4mask> | IP addresses of one or more WCCP routers that can communicate with a FortiGate unit operating as a WCCP cache engine. Separate multiple addresses with a space. |  |
| authentication {disable ¦ enable} | Enable or disable using use MD5 authentication for the WCCP configuration. | disable |
| service-type {auto ¦ dynamic ¦ standard} | Set the WCCP service type used by the cache server. | auto |
| forward-method {GRE ¦ L2 ¦ any} | Specifies how the FortiGate unit forwards traffic to cache servers. If forward-method is any the cache server determines the forward method. | GRE |

| Variable | Description | Default |
| --- | --- | --- |
| return-method {GRE ¦ L2 ¦ any} | Specifies how a cache server declines a redirected packet and returns it to the FortiGate unit. If return- method is any the cache server determines the return method. | GRE |
| assignment-method {HASH ¦ MASK ¦ any} | Specifies which assignment method the FortiGate unit prefers. If assignment-method is any the cache server determines the assignment method. | HASH |
| assignment-weight <weight_int> | Set the assignment weight for the WCCP cache engine. The range is 0 to 255. | 0 |
| assignment-bucket- format {cisco- implementation ¦ wccp-v2} | Set the assignment bucket format for the WCCP cache engine. | cisco- implementation |
| password <password_str> | The authentication password. Maximum length is 8 characters. | No default. |

Fortinet Technologies Inc.                                                                Page 691                                     FortiOS™ - CLI Reference for FortiOS 5.0

zone

Use this command to add or edit zones.

In NAT/Route mode, you can group related interfaces or VLAN subinterfaces into zones. Grouping interfaces and subinterfaces into zones simplifies policy creation. For example, if you have two interfaces connected to the Internet, you can add both of these interfaces to the same zone. Then you can configure policies for connections to and from this zone, rather than to and from each interface.

In Transparent mode you can group related VLAN subinterfaces into zones and add these zones to virtual domains.

Syntax

config system zone edit <zone_name>

set interface <name_str>

set intrazone {allow | deny}

end

| Variable | Description | Default |
| --- | --- | --- |
| edit <zone_name> | Enter the name of a new or existing zone. |  |
| interface <name_str> | Add the specified interface to this zone. You cannot add an interface if it belongs to another zone or if firewall policies are defined for it. | No default. |
| intrazone {allow ¦ deny} | Allow or deny traffic routing between different interfaces in the same zone. | deny |

Fortinet Technologies Inc.                                                                Page 692                                     FortiOS™ - CLI Reference for FortiOS 5.0

user

This chapter covers:

•  configuration of the FortiGate unit to use external authentication servers, including

Windows Active Directory or other Directory Service servers

•  configuration of user accounts and user groups for firewall policy authentication, administrator authentication and some types of VPN authentication

•  configuration of peers and peer groups for IPSec VPN authentication and PKI user authentication

This chapter contains the following sections:

Configuring users for authentication

ban device

device-access-list device-category device-group fortitoken

fsso

fsso-polling group

ldap

local

password-policy peer

peergrp radius setting tacacs+

Configuring users  for authentication

This chapter covers two types of user configuration:

•  users authenticated by password

•  users, sites or computers (peers) authenticated by certificate

Configuring users for password authentication

You need to set up authentication in the following order:

1.  If external authentication is needed, configure the required servers.

•  See “user radius” on page 720.

•  See “user ldap” on page 711.

•  See “user tacacs+” on page 727

•  For Directory Service, see “user fsso” on page 703.

Page 693

2.  Configure local user identities.

For each user, you can choose whether the FortiGate unit or an external authentication server verifies the password.

•  See “user local” on page 714.

3.  Create user groups.

Add local users to each user group as appropriate. You can also add an authentication server to a user group. In this case, all users in the server’s database can authenticate to the FortiGate unit.

•  See “user group” on page 707.

•  For Directory Service, also see “user ban” on page 695.

Configuring peers for certificate authentication

If your FortiGate unit will host IPSec VPNs that authenticate clients using certificates, you need to prepare for certificate authentication as follows:

1.  Import the CA certificates for clients who authenticate with a FortiGate unit VPN using certificates.

•  See “vpn certificate ca” on page 742.

2.  Enter the certificate information for each VPN client (peer).

•  See “user peer” on page 717.

3.  Create peer groups, if you have VPNs that authenticate by peer group. Assign the appropriate peers to each peer group.

•  See “user peergrp” on page 719.

ban

The FortiGate unit compiles a list of all users, IP addresses, or interfaces that have a quarantine/ban rule applied to them. The Banned User list in the FortiGate web-based interface shows all IP addresses and interfaces blocked by NAC (Network Access Control) quarantine, and all IP addresses, authenticated users, senders and interfaces blocked by DLP (Data Leak Prevention). All users or IP addresses on the Banned User list are blocked until they are removed from the list, and all sessions to an interface on the list are blocked until the interface is removed from the list. Each banned user configuration can have an expiry time/date to automatically remove it from the Banned User list, or the user must be removed from the list manually by the system administrator.

You cannot configure items in the Banned user list with the CLI, you must use the web-based manager. In the CLI, you can display the list items in the Banned User list using get user ban, and remove items from the list using the following command:

config user ban

delete banid <ban_int>

end

Syntax (view only, cannot be configured)

config user ban

edit banid <ban_int>

set source {dlp-rule | dlp-compound | IPS | AV | DoS}

set type {quarantine-src-ip | quarantine-dst-ip

| quarantine-src-dst-ip | quarantine-intf | dlp-user

| dlp-ip | dlp-sender | dlp-im}

set cause {IPS (Intrusion Protection Sensor) | Antivirus (AV)

| Data Leak Prevention (DLP)}

set src-ip-addr <src_ip_addr>

set protocol {smtp | pop3 | imap | http-post | http-get | ftp- put | ftp-get | nntp | aim | icq | msn | ym | smtps | pop3s

| imaps | https-post | https_get}

set dst-ip-addr <dst_ip_addr> set interface <interface_name> set ip-addr <ip_addr>

set user <user_name>

set sender <sender_name>

set im-type {aim | icq | msn | yahoo}

set im-name <im_name>

set expires <ban_expiry_date>

set created <system_date>

end end

| Variable | Description | Default |
| --- | --- | --- |
| banid <ban_int> | Enter the unique ID number of the banned user configuration. | No default. |

| Variable | Description | Default |
| --- | --- | --- |
| source {dlp-rule ¦ dlp-compound ¦ IPS ¦ AV ¦ DoS} | The source of the ban: • dlp-rule — a DLP rule configured by the system administrator • dlp-compound — a DLP compound rule configured by the system administrator • IPS — FortiGate unit IPS • AV — FortiGate unit IPS • DoS — DoS sensor | dlp-rule |
| type {quarantine-src-ip ¦ quarantine-dst-ip ¦ quarantine-src-dst-ip ¦ quarantine-intf ¦ dlp-user ¦ dlp-ip ¦ dlp-sender ¦ dlp-im} | The type of ban: • quarantine-src-ip — Complete quarantine based on source IP address • quarantine-dst-ip — Complete quarantine based on destination IP address • quarantine-src-dst-ip — Block all traffic from source to destination address • quarantine-intf — Block all traffic on the banned interface (port quarantine) • dlp-user — Ban based on user • dlp-ip — Ban based on IP address of user • dlp-sender — Ban based on email sender • dlp-im — Ban based on IM user | quarantine-src-ip |
| cause {IPS (Intrusion Protection Sensor) ¦ Antivirus (AV) ¦ Data Leak Prevention (DLP)} | FortiGate function that caused ban: • IPS (Intrusion Protection Sensor) • Antivirus (AV) — virus detected • Data Leak Prevention (DLP) | (null) |
| src-ip-addr <src_ip_addr> | The banned source IP address. | 0.0.0.0 |
| protocol {smtp ¦ pop3 ¦ imap ¦ http-post ¦ http-get ¦ ftp-put ¦ ftp-get ¦ nntp ¦ aim ¦ icq ¦ msn ¦ ym ¦ smtps ¦ pop3s ¦ imaps ¦ https-post ¦ https_get} | The protocol used by the user or IP addresses added to the Banned User list. | No default. |
| dst-ip-addr <dst_ip_addr> | The destination IP address quarantined or banned. This applies to ban types quarantine- dst-ip and quarantine-src-dst-ip. |  |
| interface <interface_name> | The interface that was quarantined or banned. This applies to ban type quarantine-intf. | null |
| ip-addr <ip_addr> | The banned IP address (ban type dlp-ip). | 0.0.0.0 |
| user <user_name> | The name of the banned user (ban type dlp- user). | null |
| sender <sender_name> | The name of the banned sender (ban type dlp-sender). | null |

Fortinet Technologies Inc.                                                                Page 696                                     FortiOS™ - CLI Reference for FortiOS 5.0

| Variable | Description | Default |
| --- | --- | --- |
| im-type {aim ¦ icq ¦ msn ¦ yahoo} | The type of instant messenger that was banned. This applies to ban type dlp-im: • aim — AOL instant messenger • icq — ICQ • msn — MSN messenger • yahoo — Yahoo! messenger | aim |
| im-name <im_name> | The name of the banned instant messenger (ban type dlp-im). | null |
| expires <ban_expiry_date> | Date and Time when the FortiGate unit will lift the ban. Date and time <yyyy/mm/dd hh:mm:ss>. Range from 5 minutes to 365 days or indefinite. If set to indefinite, the ban must be manually removed from the Banned User list. | indefinite |
| created <system_date> | System-generated time that the ban was created by the system administrator. Format Wed Dec 31 16:00:00 1969. | No default. |

Fortinet Technologies Inc.                                                                Page 697                                     FortiOS™ - CLI Reference for FortiOS 5.0

device

Use this command to define host devices.

Syntax

config user device edit <device_alias>

set comment <comment_str>

set mac <mac_addr>

set type { Android Phone | Android Tablet | BlackBerry Phone

| BlackBerry PlayBook | Fortinet Device | Gaming Console

| IP Phone | Linux PC | Mac | Media Streaming

| Other Device | Windows PC | Windows Phone | iPad

| iPhone}

set user <username_str>

end

| Variable | Description | Default |
| --- | --- | --- |
| <device_alias> | Enter a name for the device. Device, device type and device group names must be unique. | No default. |
| comment <comment_str> | Optionally, enter a comment up to 32 characters in length. | No default. |
| mac <mac_addr> | Enter the MAC address of the device. | 00:00:00:00:00:00 |
| type { Android Phone ¦ Android Tablet ¦ BlackBerry Phone ¦ BlackBerry PlayBook ¦ Fortinet Device ¦ Gaming Console ¦ IP Phone ¦ Linux PC ¦ Mac ¦ Media Streaming ¦ Other Device ¦ Windows PC ¦ Windows Phone ¦ iPad ¦ iPhone} | Select the device type. | Null |
| user <username_str> | Enter the name of the device’s user. | Null |

device-access-list

Use this command to configure device lists for use on interfaces with device identification enabled.

Syntax

config user device-access-list edit <devlist_name>

set default-action {accept | deny}

config device-list edit <id>

set action {accept | deny}

set device <dev_name>

end

end

| Variable | Description | Default |
| --- | --- | --- |
| <devlist_name> | Enter a name for this device list. |  |
| action {accept ¦ deny} | Select whether to accept or deny this device. |  |
| default-action {accept ¦ deny} | Select whether to allow or deny unknown devices. | accept |
| device <dev_name> | Enter the device name. | No default. |

device-category

Use this command to provide comments for the predefined device types. You cannot create or delete device types.

Syntax

config user device-category

edit {android-phone | android-tablet | blackberry-phone

| blackberry-playbook | collected-emails | fortinet-device

| gaming-console | ip-phone | ipad | iphone | linux-pc | mac

| media-streaming | other-network-device | router-nat-device

| windows-pc | windows-phone}

set comment <comment_str>

end

| Variable | Description | Default |
| --- | --- | --- |
| comment <comment_str> | Comment (read-only). | No default. |
| desc <desc_str> | Description (read-only). | No default. |

device-group

Use this command to define device groups.

Syntax

config user device-group edit <groupname_str>

set comment <comment_str>

set member {device-1 ... device-n}

end

| Variable | Description | Default |
| --- | --- | --- |
| <groupname_str> | Enter a name for this device group. Device, device type and device group names must be unique. | No default. |
| comment <comment_str> | Optionally, enter a comment up to 32 characters in length. | No default. |
| member {device-1 ... device-n} | Enter the device names that belong to this group. | No default. |

fortitoken

This command to register FortiToken devices and FortiToken Mobile “soft token” certificates.

Syntax

config user fortitoken

edit serial-number <sn_str> set status {active | lock} set comments <comment_str> set license <license_str>

set activation-code <code_str>

set activation-expire <str>

end

| Variable | Description | Default |
| --- | --- | --- |
| serial-number <sn_str> | Enter the FortiToken device serial number. | No default. |
| status {active ¦ lock} | Activate or lock out FortiToken device. | active |
| comments <comment_str> |  | No default. |
| license <license_str> | FortiToken Mobile license. You can retrieve this using the command execute fortitoken-mobile import <activation_code> | No default. |
| activation-code <code_str> | The FortiToken activation code from the FortiToken Mobile card. | No default. |
| activation-expire <str> | Activation expiry time. Read-only. |  |

fsso

Use this command to configure the FortiGate unit to receive user group information from a Directory Service server equipped with the Fortinet Single Sign On Agent (FSSO-Agent). You can specify up to five computers on which a FSSO collector agent is installed. The FortiGate unit uses these collector agents in a redundant configuration. If the first agent fails, the FortiGate unit attempts to connect to the next agent in the list.

You can add user groups to Directory Service type user groups for authentication in firewall policies.

Syntax

config user fsso

edit <server_name>

set ldap_server <ldap-server-name>

set password <password> set password2 <password2> set password3 <password3> set password4 <password4> set password5 <password5> set port <port_number>

set port2 <port2_number> set port3 <por3_number> set port4 <port4_number> set port5 <port5_number> set server <domain>

set server2 <domain2> set server3 <domain3> set server4 <domain4> set server5 <domain5>

set source-ip <ipv4_addr>

end

| Variable | Description | Default |
| --- | --- | --- |
| edit <server_name> | Enter a name to identify the Directory Service server. Enter a new name to create a new server definition or enter an existing server name to edit that server definition. | No default. |
| ldap_server <ldap-server-name> | Enter the name of the LDAP server to be used to access the Directory Service. | No default. |
| password <password> password2 <password2> password3 <password3> password4 <password4> password5 <password5> | For each collector agent, enter the password. | No default. |

| Variable | Description | Default |
| --- | --- | --- |
| port <port_number> port2 <port2_number> port3 <por3_number> port4 <port4_number> port5 <port5_number> | For each collector agent, enter the port number used for communication with FortiGate units. | 8000 |
| server <domain> server2 <domain2> server3 <domain3> server4 <domain4> server5 <domain5> | Enter the domain name or IP address for up to five collector agents. Range from 1 to 63 characters. | No default. |
| source-ip <ipv4_addr> | Enter the source IP for communications to FSSO server. | 0.0.0.0 |

Fortinet Technologies Inc.                                                                Page 704                                     FortiOS™ - CLI Reference for FortiOS 5.0

fsso-polling

Use this command to configure polling of servers for Fortinet Single Sign-On.

Syntax - Global

config user fsso-polling edit <AD_id_int>

set status {enable | disable}

set server <name>

set authentication {enable | disable}

set auth-password <pwd_str> set listening-port <port_int> end

Syntax - VDOM

config user fsso-polling edit <AD_id_int>

set status {enable | disable}

set server <name>

set password <pwd_str>

set default-domain <domain_str> set ldap-server <server_name> set logon-history <hours_int> set polling-frequency <sec_int> set port <port_int>

set user <uid_str>

config adgrp

edit adgrp-name <group_name>

end end

| Variable | Description | Default |
| --- | --- | --- |
| <AD_id_int> | Enter an ID number for the Windows Active Directory (AD) server. |  |
| status {enable ¦ disable} | Enable or disable FSSO polling. | enable |
| server <name> | Enter the AD server name or IP address. | Null |
| password <pwd_str> | Enter the AD server password. | Null |
| authentication {enable ¦ disable} | Enable or disable authentication. | enable |
| auth-password <pwd_str> | Enter the AD server password. | Null |
| default-domain <domain_str> | Enter this server’s default domain name. | Null |
| ldap-server <server_name> | Enter the name of the LDAP server for group and user names. | Null |
| listening-port <port_int> | Enter the server port number. Range 1 the 65 535, | 8000 |
| logon-history <hours_int> | Enter length of logon history. Range 1 to 48 hours. | 8 |
| polling-frequency <sec_int> | Enter the polling interval. Range 1 to 30 seconds. | 10 |

Fortinet Technologies Inc.                                                                Page 705                                     FortiOS™ - CLI Reference for FortiOS 5.0

| Variable | Description | Default |
| --- | --- | --- |
| port <port_int> | Enter the server port number. Range 0 the 65 535. | 0 |
| user <uid_str> | Enter the user account name for the AD server. | Null |
| config adgrp fields |  |
| adgrp-name <group_name> | Enter a Windows AD group name for which FSSO polling will be conducted. | No default. |

Fortinet Technologies Inc.                                                                Page 706                                     FortiOS™ - CLI Reference for FortiOS 5.0

group

Use this command to add or edit user groups. User groups can include defined peer members.

Syntax

config user group edit <groupname>

set auth-concurrent-override {enable | disable}

set auth-concurrent-value <limit_int>

set authtimeout <timeout>

set company {disabled | mandatory | optional}

set email {enable | disable}

set expire <seconds_int>

set expire-type {immediately | first-successful-login} set group-type {firewall | fsso-service | rsso | guest} set http-digest-realm <realm_str>

set member <names>

set mobile-phone {enable | disable}

set multiple-guest-add {enable | disable}

set password {auto-generate | email | specify} set sponsor {disabled | mandatory | optional} set sslvpn-portal <web_portal_name>

set sso-attribute-value <string>

set user-id {auto-generate | email | specify}

set user-name {enable | disable}

config guest

edit <guest_id>

set company <company-name_str>

set email <email-addr_str>

set expiration <expire-time_str> set mobile-phone <telnumber_str> set name <name_str>

set password <pwd_str>

set sponser <sponsor-name_str>

end

config match

edit <match_id>

set group-name <gname_str> set rsso {enable | disable} set server-name <srvname_str>

end

end

| Variable | Description | Default |
| --- | --- | --- |
| edit <groupname> | Enter a new name to create a new group or enter an existing group name to edit that group. | No default. |
| auth-concurrent-override {enable ¦ disable} | Enable to override the policy-auth-concurrent setting in system global. | disable |

Fortinet Technologies Inc.                                                                Page 707                                     FortiOS™ - CLI Reference for FortiOS 5.0

| Variable | Description | Default |
| --- | --- | --- |
| auth-concurrent-value <limit_int> | Set the number of concurrent logins permitted from the same IP address. Range 1 to 100. 0 means no limit. This field is available if auth-concurrent- override is enabled. | 0 |
| authtimeout <timeout> | Enter the value in seconds of an authentication timeout for the user group. Range 1 to 480 minutes. Enter 0 to use the global authentication value. This is available if group-type is firewall or directory-service. | 0 |
| company {disabled ¦ mandatory ¦ optional} | Select the option for the guest’s company name field on the web-based manager Guest Management form: disabled, mandatory or optional. This is available if group-type is guest. | optional |
| email {enable ¦ disable} | Enable or disable the email address field in the web-based manager Guest Management form. This is available if group-type is guest. | disable |
| expire <seconds_int> | Enter the number of seconds until the guest account expires. This is available if group-type is guest. | 14400 |
| expire-type {immediately ¦ first-successful-login} | Select when expiry time countdown begins: immediately or after the user’s first successful login. This is available if group-type is guest. | immediately |
| group-type {firewall ¦ fsso-service ¦ rsso ¦ guest} | Enter the group type. <grp_type> determines the type of user: firewall - FortiGate users defined in user local, user ldap or user radius fsso-service - Single Sign On users rsso - RADIUS SSO users guest — guest users | firewall |
| http-digest-realm <realm_str> | Enter the realm attribute for MD5-digest authentication. | No default. |
| member <names> | Enter the names of users, peers, LDAP servers, or RADIUS servers to add to the user group. Separate names by spaces. To add or remove names from the group you must re-enter the whole list with the additions or deletions required. This field is available if group-type is firewall or fsso-service. | No default. |
| mobile-phone {enable ¦ disable} | Enable or disable the mobile phone number field in the web-based manager Guest Management form. This is available if group-type is guest. | disable |
| multiple-guest-add {enable ¦ disable} | Enable or disable the multiple guest add option in the web-based manager User Group form. This is available if group-type is guest. | disable |

Fortinet Technologies Inc.                                                                Page 708                                     FortiOS™ - CLI Reference for FortiOS 5.0

| Variable | Description | Default |
| --- | --- | --- |
| password {auto-generate ¦ email ¦ specify} | Select the source of the guest password: auto-generate — create a random user ID email — use the guest’s email address specify — enter a user ID string This is available if group-type is guest. | auto-generate |
| sponsor {disabled ¦ mandatory ¦ optional} | Select whether the sponsor field on the web-based manager Guest Management form should be disabled, mandatory or optional. This is available if group-type is guest. | optional |
| sslvpn-portal <web_portal_name> | Enter the name of the SSL-VPN portal for this group. This is available if group-type is sslvpn. | No default. |
| sso-attribute-value <string> | Enter the name of the RADIUS user group this local user group represents. | No default. |
| user-id {auto-generate ¦ email ¦ specify} | Select the source of the guest user ID: auto-generate — create a random user ID email — use the guest’s email address specify — enter a user ID string This is available if group-type is guest. | email |
| user-name {enable ¦ disable} | Enable or disable guest user name entry. This is available if group-type is guest. | disable |
| config guest fields | Configure guest users. This is available if group- type is guest. |  |
| <guest_id> | Enter the guest user ID. | No default. |
| company <company-name_str> | Enter the user’s company name. |  |
| email <email-addr_str> | Enter the user’s email address. |  |
| expiration <expire-time_str> | Enter the account expiration time. |  |
| mobile-phone <telnumber_str> | Enter the user’s user’s telephone number. |  |
| name <name_str> | Enter the user’s name. |  |
| password <pwd_str> | Enter the user’s password. |  |
| sponser <sponsor-name_str> | Enter the user’s sponsor. |  |
| config match fields | Specify the user group names on the authentication servers that are members of this FortiGate user group. If no matches are specified, all users on the server can authenticate. |  |
| <match_id> | Enter an ID for the entry. |  |
| group-name <gname_str> | The name of the matching group on the remote authentication server. |  |

Fortinet Technologies Inc.                                                                Page 709                                     FortiOS™ - CLI Reference for FortiOS 5.0

| Variable | Description | Default |
| --- | --- | --- |
| rsso {enable ¦ disable} | Enable or disable RADIUS single sign-on matching in this user group. | disable |
| server-name <srvname_str> | The name of the remote authentication server. |  |

Fortinet Technologies Inc.                                                                Page 710                                     FortiOS™ - CLI Reference for FortiOS 5.0

ldap

Use this command to add or edit the definition of an LDAP server for user authentication.

To authenticate with the FortiGate unit, the user enters a user name and password. The FortiGate unit sends this user name and password to the LDAP server. If the LDAP server can authenticate the user, the user is successfully authenticated with the FortiGate unit. If the LDAP server cannot authenticate the user, the connection is refused by the FortiGate unit. The maximum number of remote LDAP servers that can be configured for authentication is 10.

The FortiGate unit supports LDAP protocol functionality defined in RFC2251 for looking up and validating user names and passwords. FortiGate LDAP supports all LDAP servers compliant with LDAP v3.

FortiGate LDAP support does not extend to proprietary functionality, such as notification of password expiration, that is available from some LDAP servers. FortiGate LDAP support does not supply information to the user about why authentication failed.

LDAP user authentication is supported for PPTP, L2TP, IPSec VPN, and firewall authentication. With PPTP, L2TP, and IPSec VPN, PAP (Packet Authentication Protocol) is supported and CHAP (Challenge Handshake Authentication Protocol) is not.

Syntax

config user ldap

edit <server_name> set cnid <id> set dn <dname>

set group-member-check {user-attr | group-object}

set group-object-filter <group_filter>

set member-attr <attr_name>

set port <number>

set server <domain>

set secondary-server <domain>

set tertiary-server <domain>

set source-ip <source_ipv4addr>

set type <auth_type>

set username <ldap_username>

set password <ldap_passwd>

set password-expiry-warning {disable | enable}

set password-renewal {disable | enable}

set secure <auth_port>

set ca-cert <cert_name>

end

| Variable | Description | Default |
| --- | --- | --- |
| edit <server_name> | Enter a name to identify the LDAP server. Enter a new name to create a new server definition or enter an existing server name to edit that server definition. | No default. |

Fortinet Technologies Inc.                                                                Page 711                                     FortiOS™ - CLI Reference for FortiOS 5.0

| Variable | Description | Default |
| --- | --- | --- |
| cnid <id> | Enter the common name identifier for the LDAP server. The common name identifier for most LDAP servers is cn. However some servers use other common name identifiers such as uid. Maximum 20 characters. | cn |
| dn <dname> | Enter the distinguished name used to look up entries on the LDAP server. It reflects the hierarchy of LDAP database object classes above the Common Name Identifier. The FortiGate unit passes this distinguished name unchanged to the server. You must provide a dn value if type is simple. Maximum 512 characters. | No default. |
| group-member-check {user-attr ¦ group-object} | Select the group membership checking method: user attribute or group object. | user-attr |
| group-object-filter <group_filter> | Enter the name of the filter for group searches. The search for the group on the LDAP server is done with the following default filter configuration: (&(objectcategory=group)(member=*)) For example, to look for the group that will allow dial- in (msNPAllowDialin) set the filter to (&(uid=%u)(msNPAllowDialin=TRUE)). This field is available when group-member-check is group-object. |  |
| member-attr <attr_name> | An attribute of the group that is used to authenticate users. | null |
| port <number> | Enter the port number for communication with the LDAP server. | 389 |
| server <domain> | Enter the LDAP server domain name or IP address. The host name must comply with RFC1035. | No default. |
| secondary-server <domain> | Optionally, enter a second LDAP server name or IP address. | No default. |
| tertiary-server <domain> | Optionally, enter a third LDAP server name or IP address. | No default. |
| source-ip <source_ipv4addr> | Optionally, enter a source IP address to use for LDAP requests. | 0.0.0.0 |

Fortinet Technologies Inc.                                                                Page 712                                     FortiOS™ - CLI Reference for FortiOS 5.0

| Variable | Description | Default |
| --- | --- | --- |
| type <auth_type> | Enter the authentication type for LDAP searches. One of: • anonymous — bind using anonymous user search • regular — bind using username/password and then search • simple — simple password authentication without search You can use simple authentication if the user records are all under one dn that you know. If the users are under more than one dn, use the anonymous or regular type, which can search the entire LDAP database for the required user name. If your LDAP server requires authentication to perform searches, use the regular type and provide values for username and password. | simple |
| username <ldap_username> | This field is available only if type is regular. For regular authentication, you need a user name and password. See your server administrator for more information. | No default. |
| password <ldap_passwd> | This field is available only if type is regular. For regular authentication, you need a user name and password. See your server administrator for more information. | No default. |
| password-expiry-warning {disable ¦ enable} | Enable or disable password expiry warnings. | disable |
| password-renewal {disable ¦ enable} | Enable or disable online password renewal. | disable |
| secure <auth_port> {disable ¦ starttls ¦ ldaps} | Select the port to be used in authentication. disable — port 389 ldaps — port 636 starttls — port 389 | disable |
| ca-cert <cert_name> | This field is available when secure is set to ldaps or starttls. User authentication will take place via a CA certificate. The CA certificate will be used by the LDAP library to validate the public certificate provided by the LDAP server. | null |

Fortinet Technologies Inc.                                                                Page 713                                     FortiOS™ - CLI Reference for FortiOS 5.0

local

Use this command to add local user names and configure user authentication for the FortiGate unit. To add authentication by LDAP or RADIUS server you must first add servers using the config user ldap and config user radius commands.

Syntax

config user local edit <username>

set auth-concurrent-override {enable | disable}

set auth-concurrent-value <limit_int>

set ldap-server <servername>

set passwd <password_str>

set passwd-policy <policy_name>

set passwd-time <time_str>

set radius-server <servername> set sms-custom-server <srv_name> set sms-phone <phone_str>

set sms-server {fortiguard | custom}

set status {enable | disable}

set tacacs+-server <servername>

set two-factor {disable | fortitoken | email | sms}

set type <auth-type>

set workstation <name_str>

end

| Variable | Description | Default |
| --- | --- | --- |
| edit <username> | Enter the user name. Enter a new name to create a new user account or enter an existing user name to edit that account. |  |
| auth-concurrent- override {enable ¦ disable} | Enable to override the policy-auth-concurrent setting in system global. | disable |
| auth-concurrent- value <limit_int> | Set the number of concurrent logins permitted from the same IP address. Range 1 to 100. 0 means no limit. This field is available if auth-concurrent-override is enabled. | 0 |
| ldap-server <servername> | Enter the name of the LDAP server with which the user must authenticate. You can only select an LDAP server that has been added to the list of LDAP servers. See “ldap” on page 711. This is available when type is set to ldap. | No default. |
| passwd <password_str> | Enter the password with which the user must authenticate. Passwords at least 6 characters long provide better security than shorter passwords. This is available when type is set to password. | No default. |
| passwd-policy <policy_name> | Optionally, select a password policy to apply to this user. Use user password-policy to create password policies. | null |
| passwd-time <time_str> | The time of last password update. (Read only). | No default. |

Fortinet Technologies Inc.                                                                Page 714                                     FortiOS™ - CLI Reference for FortiOS 5.0

| Variable | Description | Default |
| --- | --- | --- |
| radius-server <servername> | Enter the name of the RADIUS server with which the user must authenticate. You can only select a RADIUS server that has been added to the list of RADIUS servers. See “radius” on page 720. This is available when type is set to radius. | No default. |
| sms-custom- server <srv_name> | Enter the custom server to use for SMS-based two-factor authentication. The server name must be defined first using the config system sms-server command. This field is available when two-factor is sms and sms-server is custom. | No default. |
| sms-phone <phone_str> | Enter the user’s phone number for SMS-based two-factor authentication. | No default. |
| sms-server {fortiguard ¦ custom} | Select FortiGuard or custom SMS server for SMS-based two- factor authentication. This field is available when two-factor is sms. | fortiguard |
| status {enable ¦ disable} | Enter enable to allow the local user to authenticate with the FortiGate unit. | enable |
| tacacs+-server <servername> | Enter the name of the TACACS+ server with which the user must authenticate. You can only select a TACACS+ server that has been added to the list of TACACS+ servers. See “tacacs+” on page 727. This is available when type is set to tacacs+. | No default. |
| two-factor {disable ¦ fortitoken ¦ email ¦ sms} | Enable two-factor authentication through FortiToken, email, or SMS. | disable |
| type <auth-type> | Enter one of the following to specify how this user’s password is verified: ldap — The LDAP server specified in ldap-server verifies the password. password — The FortiGate unit verifies the password against the value of passwd. radius — The RADIUS server specified in radius-server verifies the password. tacacs+ — The TACACS+ server specified in tacacs+-server verifies the password. | No default. |
| workstation <name_str> | Enter the user’s workstation name if you want to permit the user to authenticate only from a particular workstation. This is available when type is ldap. | null |

Fortinet Technologies Inc.                                                                Page 715                                     FortiOS™ - CLI Reference for FortiOS 5.0

password-policy

Use this command to define password policies that set user password expiry and provide expiry warnings.

Syntax

config user password-policy edit <policy_name>

set expire-days <days_int>

set warn-days <days_int>

end

| Variable | Description | Default |
| --- | --- | --- |
| <policy_name> | Enter a name for this password policy. | No default. |
| expire-days <days_int> | Set the number of days until expiry. Range 0 to 999. | 180 |
| warn-days <days_int> | Set number of days prior to expiry to provide expiry warning. Range 0 to 30. | 15 |

peer

Use this command to add or edit peer (digital certificate holder) information. You use the peers you define here in the config vpn ipsec phase1 command if you specify peertype as peer. Also, you can add these peers to peer groups you define in the config user peergrp command.

For PKI user authentication, you can add or edit peer information and configure use of LDAP

server to check access rights for client certificates.

This command refers to certificates imported into the FortiGate unit. You import CA certificates using the vpn certificate ca command. You import local certificates using the vpn certificate local command.

You can configure a peer user with no values in subject or ca. This user behaves like a user account or policy that is disabled.

If you create a PKI user in the CLI with no values in subject or ca, you cannot open the user record in the web-based manager, or you will be prompted to add a value in Subject (subject) or CA (ca).

Syntax

config user peer edit <peer_name>

set ca <ca_name> set cn <cn_name> set cn-type <type>

set ldap-mode {password | principal-name}

set ldap-password <ldap_password>

set ldap-server <ldap_server>

set ldap-username <ldap_user>

set mandatory-ca-verify {enable | disable}

set ocsp-override-server <ocsp-name>

set passwd <password_str>

set subject <constraints>

set two-factor {enable | disable}

end

| Variable | Description | Default |
| --- | --- | --- |
| edit <peer_name> | Enter the peer name. Enter a new name to create a new peer or enter an existing peer name to edit that peer’s information. |  |
| ca <ca_name> | Enter the CA certificate name, as returned by execute vpn certificate ca list. | No default. |
| cn <cn_name> | Enter the peer certificate common name. | No default. |

| Variable | Description | Default |
| --- | --- | --- |
| cn-type <type> | Enter the peer certificate common name type: FQDN — Fully-qualified domain name. email — The user’s email address. ipv4 — The user’s IP address (IPv4). ipv6 — The user’s IP address (IPv6). string — Any other piece of information. | string |
| ldap-mode {password ¦ principal-name} | Select mode for LDAP authentication. password — use user name and password. principal-name — use LDAP userPrincipalName attribute. | password |
| ldap-password <ldap_password> | Enter the login password for the LDAP server used to perform client access rights check for the defined peer. | No default. |
| ldap-server <ldap_server> | Enter the name of one of the LDAP servers defined under ‘config user ldap’ used to perform client access rights check for the defined peer. | null |
| ldap-username <ldap_user> | Enter the login name for the LDAP server used to perform client access rights check for the defined peer. | null |
| mandatory-ca-verify {enable ¦ disable} | If the CA certificate is installed on the FortiGate unit, the peer certificate is checked for validity. The mandatory- ca-verify field determines what to do if the CA certificate is not installed: enable — The peer cannot be authenticated. disable — The peer certificate is automatically considered valid and authentication succeeds. | disable |
| ocsp-override-server <ocsp-name> | Enter the OCSP server to use to retrieve certificate. This applies if OCSP is enabled in vpn certificate setting. | null |
| passwd <password_str> | Enter the password that this peer uses for two-factor authentication. The is available when two-factor is enabled. | No default. |
| subject <constraints> | Optionally, enter any of the peer certificate name constraints. | No default. |
| two-factor {enable ¦ disable} | Enable user to authenticate by password in addition to certificate authentication. Specify the password in passwd. | disable |

Fortinet Technologies Inc.                                                                Page 718                                     FortiOS™ - CLI Reference for FortiOS 5.0

peergrp

Use this command to add or edit a peer group. Peers are digital certificate holders defined using the config user peer command. You use the peer groups you define here in the config vpn ipsec phase1 command if you specify peertype as peergrp.

For PKI user authentication, you can add or edit peer group member information. User groups that use PKI authentication can also be configured using config user group.

Syntax

config user peergrp edit <groupname>

set member <peer_names>

end

| Variable | Description | Default |
| --- | --- | --- |
| edit <groupname> | Enter a new name to create a new peer group or enter an existing group name to edit that group. |  |
| member <peer_names> | Enter the names of peers to add to the peer group. Separate names by spaces. To add or remove names from the group you must re-enter the whole list with the additions or deletions required. | No default. |

radius

Use this command to add or edit the information used for RADIUS authentication.

The default port for RADIUS traffic is 1812. If your RADIUS server is using a different port you can change the default RADIUS port. You may set a different port for each of your RADIUS servers. The maximum number of remote RADIUS servers that can be configured for authentication is 10.

The RADIUS server is now provided with more information to make authentication decisions, based on values in server, use-management-vdom, nas-ip,  and the  config user group subcommand  config match. Attributes include:

•  NAS-IP-Address - RADIUS setting or IP address of FortiGate interface used to talk to

RADIUS server, if not configured

•  NAS-Port - physical interface number of the traffic that triggered the authentication

•  Called-Station-ID - same value as NAS-IP Address but in text format

•  Fortinet-Vdom-Name - name of VDOM of the traffic that triggered the authentication

•  NAS-Identifier - configured hostname in non-HA mode; HA cluster group name in HA

mode

•  Acct-Session-ID - unique ID identifying the authentication session

•  Connect-Info - identifies the service for which the authentication is being performed

(web-auth, vpn-ipsec, vpn-pptp, vpn-l2tp, vpn-ssl, admin-login, test)

You may select an alternative authentication method for each server. These include CHAP, PAP, MS-CHAP, and MS-CHAP-v2.

Syntax

config user radius edit <server_name>

set all-usergroup {enable | disable}

set auth-type {auto | chap | ms_chap | ms_chap_v2 | pap}

set nas-ip <use_ip>

set radius-port <radius_port_num>

set secret <server_password>

set server <domain>

set secondary-secret <sec_server_password> set secondary-server <sec_server_domain> set tertiary-secret <ter_server_password> set tertiary-server <ter_domain>

set source-ip <ipv4_addr>

set use-management-vdom {enable | disable}

set rsso {enable | disable}

set rsso-context-timeout <timeout_seconds>

set rsso-endpoint-attribute <RADIUS_attribute>

set rsso-endpoint-block-attribute <RADIUS_attribute>

set rsso-flush-ip-session {enable | disable}

set rsso-log-flags <lflags>

set rsso-log-period <log_time>

set rsso-radius-response {enable | disable}

set rsso-radius-server-port <RADIUS_listen_port>

set rsso-secret <server_password>

set rsso-validate-request-secret {enable | disable}

set sso-attribute <RADIUS_attribute>

set sso-attribute-key <profile_attribute_key>

end

| Variable | Description | Default |
| --- | --- | --- |
| edit <server_name> | Enter a name to identify the RADIUS server. Enter a new name to create a new server definition or enter an existing server name to edit that server definition. |  |
| all-usergroup {enable ¦ disable} | Enable to automatically include this RADIUS server in all user groups. | disable |
| auth-type {auto ¦ chap ¦ ms_chap ¦ ms_chap_v2 ¦ pap} | Select the authentication method for this RADIUS server. auto uses pap, ms_chap_v2, and chap. | auto |
| nas-ip <use_ip> | IP address used as NAS-IP-Address and Called-Station-ID attribute in RADIUS access requests. RADIUS setting or IP address of FGT interface used to talk with RADIUS server, if not configured. | No default. |
| radius-port <radius_port_num> | Change the default RADIUS port for this server. The default port for RADIUS traffic is 1812. Range is 0..65535. | 1812 |
| secret <server_password> | Enter the RADIUS server shared secret. The server secret key should be a maximum of 16 characters in length. | No default. |
| server <domain> | Enter the RADIUS server domain name or IP address. The host name must comply with RFC1035. | No default. |
| secondary-secret <sec_server_password> | Enter the secondary RADIUS server shared secret. The server secret key should be a maximum of 16 characters in length. | No default. |
| secondary-server <sec_server_domain> | Enter the secondary RADIUS server domain name or IP address. | No default. |
| tertiary-secret <ter_server_password> | Enter the tertiary RADIUS server shared secret. The server secret key should be a maximum of 16 characters in length. | No default. |
| tertiary-server <ter_domain> | Optionally, enter the secondary RADIUS server domain name or IP address. | No default. |
| source-ip <ipv4_addr> | Enter the source IP for communications to RADIUS server. | 0.0.0.0 |
| use-management-vdom {enable ¦ disable} | Enable to use the management VDOM to send all RADIUS requests. | disable |

| Variable | Description | Default |
| --- | --- | --- |
| RADIUS SSO fields |
| rsso {enable ¦ disable} | Enable RADIUS SSO to configure a RADIUS SSO agent. Then, FortiOS accepts connections on the rsso- radius-server-port. Other RSSO settings become available. | disable |

| Variable | Description | Default |
| --- | --- | --- |
| rsso-context-timeout <timeout_seconds> | When the FortiGate unit receives a RADIUS Start record, the user added to a “user context list” of logged on users. The user is considered logged on until • the FortiGate unit receives a RADIUS Stop record for the user’s end point or • this timeout period has expired with no communication from the user end point. This timeout is only required if FortiOS doesn’t receive RADIUS Stop records. However, even if the accounting system does send RADIUS Stop records, this timeout should be set in case the FortiGate unit misses a Stop record. The default timeout is 28800 seconds (8 hours). You can keep this timeout relatively high because its not usually a problem to have a long context list, but entries that are no longer used should be removed regularly. If the timeout is too short, user context entries might be removed prematurely. Set the timeout to 0 if you do not want FortiOS to remove entries from the list except in response to RADIUS Stop messages. | 28800 |
| rsso-endpoint-attribute <RADIUS_attribute> | To extract the user end point identifier from the RADIUS Start record, this field must be set to the name of the RADIUS attribute that contains the end point identifier. You can select the RADIUS_attribute from the list or enter an attribute name. The RADIUS_attribute must match one of the RADIUS attributes in the list. The RADIUS_attribute is case sensitive. | Calling- Station-Id |
| rsso-endpoint-block- attribute <RADIUS_attribute> | This field specifies a RADIUS attribute that can be used to block a user. If the attribute value is “Block”, FortiOS blocks all traffic from the user’s IP address. | Called- Station-Id |
| rsso-flush-ip-session {enable ¦ disable} | Enable to flush user IP sessions on RADIUS accounting stop messages. | disable |
| rsso-log-flags <lflags> | Enter one or more of the following options to configure FortiOS to write event log messages for RADIUS SSO events. You can enter multiple options. Separate the options with a space. none — Disable logging of RADIUS SSO events. accounting-event — Enable to write an event log message when FortiOS does not find the expected information in a RADIUS Record. For example, if a RADIUS record contains more than the expected number of addresses. accounting-stop-missed — Enable to write an event log message whenever a user context entry timeout expires indicating that FortiOS removed an entry from the user context list without receiving a RADIUS Stop message. | All options except none. |

Fortinet Technologies Inc.                                                                Page 722                                     FortiOS™ - CLI Reference for FortiOS 5.0

| Variable | Description context-missing — Enable to write an event log message whenever a user context creation timeout expires indicating that FortiOS was not able to match a communication session because a matching entry was not found in the user context list. endpoint-block — Enable to write an event log message whenever a user is blocked because the attribute specified in rsso-endpoint-block- attribute has the value “Block”. profile-missing — Enable to write an event log message whenever FortiOS cannot find a group name in a RADIUS start message that matches the name of an RSSO user group in FortiOS. protocol-error — Enable to write an event log message if RADIUS protocol errors occur. For example, if a RADIUS record contains a RADIUS secret that does not match the one added to the dynamic profile. radiusd-other — Enable to write event log messages for other events. The event is described in the log message. For example, write a log message if the memory limit for the user context list is reached and the oldest entries in the table have been dropped. | Default |
| --- | --- | --- |
| rsso-log-period <log_time> | The time in seconds to group event log messages for dynamic profile events. For example, if the log message period is 30 seconds, FortiOS Carrier generates groups of event log messages every 30 seconds instead of generating event log messages continuously. And the log messages generated each period contain a count of how many events of that type occurred. If set to 0, FortiOS Carrier generates all event log messages in real time. | 0 |
| rsso-radius-response {enable ¦ disable} | Enable if you want FortiOS Carrier to send RADIUS responses after receiving RADIUS Start and Stop records. This setting may be required by your accounting system. | disable |
| rsso-radius-server-port <RADIUS_listen_port> | If required, change the UDP port number used by the RADIUS accounting server for sending RADIUS records. FortiOS Carrier listens for RADIUS Start and Stop records on this port. | 1813 |
| rsso-secret <server_password> | Enter the RADIUS secret used by the RADIUS accounting server. | No default |
| rsso-validate-request- secret {enable ¦ disable} | Enable if you want FortiOS Carrier to verify that the RADIUS secret matches the RADIUS secret in the RADIUS Start or End record. You can verify the RADIUS secret to verify that the RADIUS record is valid. | disable |

Fortinet Technologies Inc.                                                                Page 723                                     FortiOS™ - CLI Reference for FortiOS 5.0

| Variable | Description | Default |
| --- | --- | --- |
| sso-attribute <RADIUS_attribute> | To extract a profile group name from the RADIUS Start record, this field must be set to the name of the RADIUS attribute that contains the profile group name. You can select the RADIUS_attribute from the list or enter an attribute name. The RADIUS_attribute must match one of the RADIUS attributes in the list. The RADIUS_attribute is case sensitive. | Class |
| sso-attribute-key <profile_attribute_key> | Enter a string if the profile attribute contains more data than just the profile group name. The profile key is a text string that always comes directly before the profile group name in the profile attribute. For example, if the profile group name always follows the text string profile, the class attribute could include the string: profile=<profile_name_str>. Where <profile_name_str> is the name of the profile group. Maximum 36 characters. | No default. |

Fortinet Technologies Inc.                                                                Page 724                                     FortiOS™ - CLI Reference for FortiOS 5.0

setting

Use this command to change per VDOM user settings such as the firewall user authentication time out and protocol support for firewall policy authentication.

user settings differ from system global settings in that system global settings fields apply to the entire FortiGate unit, where user settings fields apply only to the user VDOM.

Syntax

config user setting

set auth-blackout-time <blackout_time_int>

set auth-cert <cert_name>

set auth-http-basic {enable | disable}

set auth-invalid-max <int>

set auth-lockout-duration <seconds>

set auth-lockout-threshold <int>

set auth-multi-group {enable | disable}

set auth-secure-http {enable | disable}

set auth-type {ftp | http | https | telnet}

set auth-timeout <auth_timeout_minutes>

set auth-timeout-type {idle-timeout | hard-timeout | new-session}

config auth-ports

edit <auth-table-entry-id>

set port <port_int>

set type {ftp | http | https | telnet}

end

end

| Variable | Description | Default |
| --- | --- | --- |
| auth-blackout-time <blackout_time_int> | When a firewall authentication attempt fails 5 times within one minute the IP address that is the source of the authentication attempts is denied access for the <blackout_time_int> period in seconds. The range is 0 to 3600 seconds. | 0 |
| auth-cert <cert_name> | HTTPS server certificate for policy authentication. Fortinet_Factory, Fortinet_Firmware (if applicable to your FortiGate unit), and self-sign are built-in certificates but others will be listed as you add them. | self-sign |
| auth-http-basic {enable ¦ disable} | Enable or disable support for HTTP basic authentication for identity-based firewall policies. HTTP basic authentication usually causes a browser to display a pop-up authentication window instead of displaying an authentication web page. Some basic web browsers, for example, web browsers on mobile devices, may only support HTTP basic authentication. | disable |
| auth-invalid-max <int> | Enter the maximum number of failed authentication attempts to allow before the client is blocked. Range: 1-100. | 5 |

Fortinet Technologies Inc.                                                                Page 725                                     FortiOS™ - CLI Reference for FortiOS 5.0

| Variable | Description | Default |
| --- | --- | --- |
| auth-lockout-duration <seconds> | Enter the login lockout period in seconds. The lockout is imposed after too many failed login attempts, set by auth-lockout-threshold. | 0 |
| auth-lockout-threshold <int> | Enter the number of login attempts that trigger a login lockout. Range 1 to 10. | 3 |
| auth-multi-group {enable ¦ disable} | This option can be disabled if the Active Directory structure is setup such that users belong to only 1 group for the purpose of firewall authentication. | enable |
| auth-secure-http {enable ¦ disable} | Enable to have http user authentication redirected to secure channel - https. | disable |
| auth-type {ftp ¦ http ¦ https ¦ telnet} | Set the user authentication protocol support for firewall policy authentication. User controls which protocols should support the authentication challenge. |  |
| auth-timeout <auth_timeout_minutes> | Set the number of minutes before the firewall user authentication timeout requires the user to authenticate again. The maximum authtimeout interval is 1440 minutes (24 hours). To improve security, keep the authentication timeout at the default value of 5 minutes. | 5 |
| auth-timeout-type {idle-timeout ¦ hard-timeout ¦ new-session} | Set the type of authentication timeout. idle-timeout — applies only to idle session hard-timeout — applies to all sessions new-session — applies only to new sessions | idle-timeout |
| radius-ses-timeout-act {hard-timeout ¦ ignore-timeout} | Select how to use RADIUS session timeout: hard-timeout — use RADIUS timeout ignore-timeout — ignore RADIUS timeout | hard-timeout |
| config auth-ports variables |
| <auth-table-entry-id> | Create an entry in the authentication port table if you are using non-standard ports. |  |
| port <port_int> | Specify the authentication port. Range 1 to 65535. | 1024 |
| type {ftp ¦ http ¦ https ¦ telnet} | Specify the protocol to which port applies. | http |

Fortinet Technologies Inc.                                                                Page 726                                     FortiOS™ - CLI Reference for FortiOS 5.0

tacacs+

Use this command to add or edit the information used for TACACS+ authentication.

Terminal Access Controller Access-Control System (TACACS+) is a remote authentication protocol used to communicate with an authentication server. TACACS+ allows a client to accept a user name and password and send a query to a TACACS+ authentication server. The server host determines whether to accept or deny the request and sends a response back that allows or denies network access to the user.

The default port for a TACACS+ server is 49. The maximum number of remote TACACS+

servers that can be configured for authentication is 10.

You may select an alternative authentication method for each server. These include CHAP, PAP, MS-CHAP, and ASCII.

Syntax

config user tacacs+

edit <server_name>

set authen-type {ascii | auto | chap | ms_chap | pap}

set authorization {enable | disable}

set key <server_key>

set port <tacacs+_port_num>

set server <domain>

set source-ip <ipv4_addr>

end

| Variable | Description | Default |
| --- | --- | --- |
| edit <server_name> | Enter a name to identify the TACACS+ server. Enter a new name to create a new server definition or enter an existing server name to edit that server definition. |  |
| authen-type {ascii ¦ auto ¦ chap ¦ ms_chap ¦ pap} | Select the authentication method for this TACACS+ server. auto uses pap, ms_chap_v, and chap, in that order. | auto |
| authorization {enable ¦ disable} | Enable or disable TACACS+ authorization. | disable |
| key <server_key> | Enter the key to access the server. The maximum number is 16. |  |
| port <tacacs+_port_num> | Change the default TACACS+ port for this server. The default port for TACACS+ traffic is 49. Range is 0..65535. | 49 |
| server <domain> | Enter the TACACS+ server domain name or IP address. The host name must comply with RFC1035. | No default. |
| source-ip <ipv4_addr> | Enter the source IP for communications to TACACS+ server. | 0.0.0.0 |

•

Fortinet Technologies Inc.                                                                Page 727                                     FortiOS™ - CLI Reference for FortiOS 5.0

voip

Use VoIP commands to configure VoIP profiles for firewall policies. This chapter describes the following command:

profile

Page 728

profile

Use this command to add VoIP profiles for SIP, SIMPLE, and SCCP. To apply the SIP ALG, you add a VoIP profile to a firewall policy that accepts SIP sessions. All SIP sessions accepted by the firewall policy will be processed by the SIP ALG using the settings in the VoIP profile. The VoIP profile contains settings that are applied to SIP, Session Initiation Protocol for Instant Messaging and Presence Leveraging Extensions (SIMPLE) and Skinny Call Control Protocol (SCCP) sessions. You configure SIP and SCCP settings separately. SIP settings also apply to SIMPLE sessions.

Syntax

config voip profile edit <profile_name>

set comment <comment_str>

set extended-utm-log {enable | disable}

config sip

set status {enable | disable}

set rtp {enable | disable}

set open-register-pinhole {enable | disable}

set open-contact-pinhole {enable | disable}

set open-record-route-pinhole {enable | disable}

set open-via-pinhole {enable | disable} set strict-register {enable | disable} set register-rate <rate_sec_policy_int> set invite-rate <rate_sec_policy_int> set max-dialogs <max_int>

set max-line-length <length_int>

set block-long-lines {enable | disable}

set block-unknown {enable | disable} set call-keepalive <keepalive_time> set block-ack {enable | disable}

set block-bye {enable | disable}

set block-cancel {enable | disable} set block-info {enable | disable} set block-invite {enable | disable}

set block-message {enable | disable} set block-notify {enable | disable} set block-options {enable | disable} set block-prack {enable | disable} set block-publish {enable | disable} set block-refer {enable | disable}

set block-register {enable | disable} set block-subscribe {enable | disable} set block-update {enable | disable}

set reg-diff-port {enable | disable} set rfc2543-branch {enable | disable} set log-violations {enable | disable} set log-call-summary {enable | disable} set nat-trace {enable | disable}

set subscribe-rate <rate_sec_policy_int> set message-rate <rate_sec_policy_int> set notify-rate <rate_sec_policy_int>

set refer-rate <rate_sec_policy_int> set update-rate <rate_sec_policy_int> set options-rate <rate_sec_policy_int> set ack-rate <rate_sec_policy_int>

set prack-rate <rate_sec_policy_int>

set info-rate <rate_sec_policy_int>

set publish-rate <rate_sec_policy_int>

set bye-rate <rate_sec_policy_int>

set cancel-rate <rate_sec_policy_int>

set preserve-override {enable | disable}

set no-sdp-fixup {enable | disable}

set contact-fixup {enable | disable}

set max-idle-dialogs <dialogs_perpolicy_int> set block-geo-red-options {enable | disable} set hosted-nat-traversal {enable | disable} set hnt-restrict-source-ip {enable | disable} set max-body-length <size_bytes_int>

set unknown-header {discard | pass | respond}

set malformed-request-line {discard | pass | respond} set malformed-header-via {discard | pass | respond} set malformed-header-from {discard | pass | respond} set malformed-header-to {discard | pass | respond}

set malformed-header-call-id {discard | pass | respond}

set malformed-header-cseq {discard | pass | respond} set malformed-header-rack {discard | pass | respond} set malformed-header-rseq {discard | pass | respond}

set malformed-header-contact {discard | pass | respond}

set malformed-header-record-route {discard | pass | respond}

set malformed-header-route {discard | pass | respond}

set malformed-header-expires {discard | pass | respond}

set malformed-header-content-type {discard | pass | respond}

set malformed-header-content-length {discard | pass |

respond}

set malformed-header-max-forwards {discard | pass | respond}

set malformed-header-allow {discard | pass | respond}

set malformed-header-p-asserted-identity {discard | pass |

respond}

set malformed-header-sdp-v {discard | pass | respond} set malformed-header-sdp-o {discard | pass | respond} set malformed-header-sdp-s {discard | pass | respond} set malformed-header-sdp-i {discard | pass | respond} set malformed-header-sdp-c {discard | pass | respond} set malformed-header-sdp-b {discard | pass | respond} set malformed-header-sdp-z {discard | pass | respond} set malformed-header-sdp-k {discard | pass | respond} set malformed-header-sdp-a {discard | pass | respond}

set malformed-header-sdp-t {discard | pass | respond} set malformed-header-sdp-r {discard | pass | respond} set malformed-header-sdp-m {discard | pass | respond} set ips-rtp {enable | disable}

set provisional-invite-expiry-time <time_int>

set ssl-mode {off | full}

set ssl-algorithm {high | medium | low)

set ssl-auth-client <peer_group>

set ssl-auth-server <peer_group>

set ssl-client-certificate <cert_name>

set ssl-client-renegotiation {allow | deny | secure}

set ssl-min-version {ssl-3.0 | tls-1.0 | tls-1.1} set ssl-max-version {ssl-3.0 | tls-1.0 | tls-1.1} set ssl-pfs {require | allow | deny}

set ssl-send-empty-frags {enable | disable}

set ssl-server-certificate <cert_name>

end config sccp

set status {disable | enable}

set block-mcast {enable | disable}

set verify-header {enable | disable}

set log-call-summary {disable | enable} set log-violations {disable | enable} set max-calls <calls_int>

end

end

| Variable | Description | Default |
| --- | --- | --- |
| edit <profile_name> | Enter the name of a VoIP profile |  |
| comment <comment_str> | Optionally enter a description of up to 63 characters of the VoIP profile. |  |
| extended-utm-log {enable ¦ disable} | Enable or disable detailed UTM log messages. | disable |

config  sip

Configure VoIP profile settings for SIP and SIMPLE.

| Variable | Description | Default |
| --- | --- | --- |
| status {enable ¦ disable} | Enable or disable SIP for this VoIP profile. | enable |
| rtp {enable ¦ disable} | Enable or disable opening pinholes for RTP traffic to traverse FortiGate unit. | enable |
| open-register-pinhole {enable ¦ disable} | Enable or disable opening a pinhole for the port number specified in SIP REGISTER message Contact header line. | enable |
| open-contact-pinhole {enable ¦ disable} | Enable or disable opening a pinhole for the port number specified in a Contact header line in any SIP message except a SIP REGISTER message. | enable |
| open-record-route-pinhole {enable ¦ disable} | Open firewall pinhole for Record-Route port. | enable |

| Variable | Description | Default |
| --- | --- | --- |
| open-via-pinhole {enable ¦ disable} | Open firewall pinhole for Via port. | disable |
| strict-register {enable ¦ disable} | Controls how pinholes are opened to allow traffic from a SIP server to pass through the FortiGate unit. If enabled the SIP ALG opens a pinhole that only accepts sessions from a single IP address (the address of the SIP server). This option should be disabled if the SIP proxy server and SIP registrar are different entities with different IP addresses. | disable |
| register-rate <rate_sec_policy_int> | Set a rate limit (per second, per policy) for SIP REGISTER requests. Set to 0 to disable rate limiting. | 0 |
| invite-rate <rate_sec_policy_int> | Set a rate limit (per second, per policy) for SIP INVITE requests. Set to 0 to disable rate limiting. | 0 |
| max-dialogs <max_int> | Maximum number of concurrent calls (or dialogs) per policy. Set to 0 to not limit dialogs. | 0 |
| max-line-length <length_int> | Maximum SIP header line length. The range is 78-4096 characters. If a SIP message contains a line that exceeds the maximum line length a log message is recorded. If block-long-lines is enabled the message is blocked and the FortiGate unit returns a SIP 413 Request entity too large SIP response message. | 998 |
| block-long-lines {enable ¦ disable} | Enable or disable blocking SIP request messages with a header or body line that exceeds the max-line- length. | enable |
| block-unknown {enable ¦ disable} | Block unrecognized SIP request messages. | enable |
| call-keepalive <keepalive_time> | Continue tracking calls with no RTP sessions for this many minutes. Terminate the call if the time limit is exceeded. Range is 1 and 10,080 seconds. Set to 0 to disable. Call keep alive should be used with caution because enabling this feature results in extra FortiGate CPU overhead and can cause delay/jitter for the VoIP call. Also, the FortiGate unit terminates the call without sending SIP messages to end the call. And if the SIP endpoints send SIP messages to terminate the call they will be blocked by the FortiGate unit if they are sent after the FortiGate unit terminates the call. | 0 |
| block-ack {enable ¦ disable} | Enable or disable blocking SIP ACK request messages. | disable |
| block-bye {enable ¦ disable} | Enable or disable blocking SIP BYE request messages. | disable |
| block-cancel {enable ¦ disable} | Enable or disable blocking SIP CANCEL request messages. | disable |
| block-info {enable ¦ disable} | Enable or disable blocking SIP INFO request messages. | disable |
| block-invite {enable ¦ disable} | Enable or disable blocking SIP INVITE request messages. | disable |
| block-message {enable ¦ disable} | Enable or disable blocking SIP MESSAGE request messages. | disable |
| block-notify {enable ¦ disable} | Enable or disable blocking SIP NOTIFY request messages. | disable |

Fortinet Technologies Inc.                                                                Page 732                                     FortiOS™ - CLI Reference for FortiOS 5.0

| Variable | Description | Default |
| --- | --- | --- |
| block-options {enable ¦ disable} | Enable or disable blocking SIP OPTIONS request messages. | disable |
| block-prack {enable ¦ disable} | Enable or disable blocking SIP PRACK request messages. | disable |
| block-publish {enable ¦ disable} | Enable or disable blocking SIP PUBLISH request messages. | disable |
| block-refer {enable ¦ disable} | Enable or disable blocking SIP REFER request messages. | disable |
| block-register {enable ¦ disable} | Enable or disable blocking SIP REGISTER request messages. | disable |
| block-subscribe {enable ¦ disable} | Enable or disable blocking SIP SUBSCRIBE request messages. | disable |
| block-update {enable ¦ disable} | Enable or disable blocking SIP UPDATE request messages. | disable |
| reg-diff-port {enable ¦ disable} | Enable or disable opening a pinhole for the port number included in the Via SIP message header line. | disable |
| rfc2543-branch {enable ¦ disable} | Enable to support RFC 2543-complaint SIP calls involving branch commands that are missing or that are valid for RFC 2543 but invalid for RFC 3261. RFC 3261 is the most recent SIP RFC. RFC 3261 obsoletes RFC 2543. This option also allows FortiGate units to support SIP calls that include Via headers that are missing the branch parameter. | disable |
| log-violations {enable ¦ disable} | Enable or disable writing a logging message when a SIP option in a VoIP profile detects a violation in a SIP message. | disable |
| log-call-summary {enable ¦ disable} | Enable or disable summary content archiving of SIP calls. | enable |
| nat-trace {enable ¦ disable} | Enable or disable preserving the original source IP address of the SIP message in the i= line of the SDP profile. This option enables NAT with IP address conservation (also called SIP NAT tracing), which changes the contents of SIP messages by adding the source IP address of the originator of the message into the SDP i= line of the SIP message. The SDP i= line is used for free-form text. However, if your SIP server can retrieve information from the SDP i= line, it can be useful for keeping a record of the source IP address of the originator of a SIP message when operating in a NAT environment. You can use this feature for billing purposes by extracting the IP address of the originator of the message. | enable |
| subscribe-rate <rate_sec_policy_int> | Limit the number of SIP SUBSCRIBE messages per second per policy that the FortiGate unit accepts. Set to 0 to disable rate limiting. | 0 |
| message-rate <rate_sec_policy_int> | Limit the number of SIP MESSAGE messages per second per policy that the FortiGate unit accepts. Set to 0 to disable rate limiting. | 0 |

Fortinet Technologies Inc.                                                                Page 733                                     FortiOS™ - CLI Reference for FortiOS 5.0

| Variable | Description | Default |
| --- | --- | --- |
| notify-rate <rate_sec_policy_int> | Limit the number of SIP NOTIFY messages per second per policy that the FortiGate unit accepts. Set to 0 to disable rate limiting. | 0 |
| refer-rate <rate_sec_policy_int> | Limit the number of SIP REFER messages per second per policy that the FortiGate unit accepts. Set to 0 to disable rate limiting. | 0 |
| update-rate <rate_sec_policy_int> | Limit the number of SIP UPDATE messages per second per policy that the FortiGate unit accepts. Set to 0 to disable rate limiting. | 0 |
| options-rate <rate_sec_policy_int> | Limit the number of SIP OPTIONS messages per second per policy that the FortiGate unit accepts. Set to 0 to disable rate limiting. | 0 |
| ack-rate <rate_sec_policy_int> | Limit the number of SIP ACK messages per second per policy that the FortiGate unit accepts. Set to 0 to disable rate limiting. | 0 |
| prack-rate <rate_sec_policy_int> | Limit the number of SIP PRACK messages per second per policy that the FortiGate unit accepts. Set to 0 to disable rate limiting. | 0 |
| info-rate <rate_sec_policy_int> | Limit the number of SIP INFO messages per second per policy that the FortiGate unit accepts. Set to 0 to disable rate limiting. | 0 |
| publish-rate <rate_sec_policy_int> | Limit the number of SIP PUBLISH messages per second per policy that the FortiGate unit accepts. Set to 0 to disable rate limiting. | 0 |
| bye-rate <rate_sec_policy_int> | Limit the number of SIP BYE messages per second per policy that the FortiGate unit accepts. Set to 0 to disable rate limiting. | 0 |
| cancel-rate <rate_sec_policy_int> | Limit the number of SIP CANCEL messages per second per policy that the FortiGate unit accepts. Set to 0 to disable rate limiting. | 0 |
| preserve-override {enable ¦ disable} | Enable or disable adding the original o= line of a SIP message to the end of the i= line or replace the i= line in the original message with a new i= line. This command is used for SIP IP address conservation. | disable |
| no-sdp-fixup {enable ¦ disable} | Enable or disable not performing NAT on addresses in the SDP lines of the SIP message body. This option is disabled by default and the FortiGate unit performs NAT on addresses in SDP lines. Enable this option if you don’t want the FortiGate unit to perform NAT on the addresses in SDP lines. | disable |
| contact-fixup {enable ¦ disable} | Enable or disable performing NAT on the IP addresses and port numbers in the headers in SIP CONTACT messages even if they don’t match the session’s IP address and port numbers. | enable |

Fortinet Technologies Inc.                                                                Page 734                                     FortiOS™ - CLI Reference for FortiOS 5.0

| Variable | Description | Default |
| --- | --- | --- |
| max-idle-dialogs <dialogs_perpolicy_int> | Specify the maximum number of established but idle dialogs to retain (per policy). Set to 0 to disable. Idle dialogs would usually be dialogs that have been interrupted because of errors or problems or as the result of a SIP attack that opens a large number of SIP dialogs without closing them. This command provides a way to remove these dialogs from the dialog table and recover memory and resources being used by these open and idle dialogs. | 0 |
| block-geo-red-options {enable ¦ disable} | Block OPTIONS requests, but OPTIONS requests still notify for redundancy. | disable |
| hosted-nat-traversal {enable ¦ disable} | Enable or disable support for hosted NAT Traversal (HNT). HNT has different requirements for address translation. | disable |
| hnt-restrict-source-ip {enable ¦ disable} | Restrict RTP source IP to be the same as SIP source IP when HNT is enabled. | disable |
| max-body-length <size_bytes_int> | Specify the maximum size of a SIP message body in bytes that will be processed by the SIP ALG. Larger messages are discarded. Set to 0 for no limit. This option checks the value in the SIP Content-Length header line to determine body length. The Content-Length can be larger than the actual size of a SIP message if the SIP message content is split over more than one packet. SIP messages are of variable size and the message size can change with the addition of Via and Record-Route headers. | 0 |
| unknown-header {discard ¦ pass ¦ respond} | Configure deep SIP message inspection to discard, pass without changing, or discard and send a SIP response message for a SIP message with an unknown header line. Even if set to pass the SIP ALG writes a log message if an unknown header is found and log- violations is enabled. | pass |
| malformed-request-line {discard ¦ pass ¦ respond} | Configure deep SIP message inspection to discard, pass without changing, or discard and send a SIP response message for a SIP message a with a malformed request- line (the first line in a SIP request message). Even if set to pass the SIP ALG writes a log message if an unknown header is found and log-violations is enabled. | pass |
| malformed-header-via {discard ¦ pass ¦ respond} | Configure deep SIP message inspection to discard, pass without changing, or discard and send a SIP response message for a SIP message a with a malformed Via header line. Even if set to pass the SIP ALG writes a log message if an unknown header is found and log- violations is enabled. | pass |
| malformed-header-from {discard ¦ pass ¦ respond} | Configure deep SIP message inspection to discard, pass without changing, or discard and send a SIP response message for a SIP message a with a malformed From header line. Even if set to pass the SIP ALG writes a log message if an unknown header is found and log- violations is enabled. | pass |

Fortinet Technologies Inc.                                                                Page 735                                     FortiOS™ - CLI Reference for FortiOS 5.0

| Variable | Description | Default |
| --- | --- | --- |
| malformed-header-to {discard ¦ pass ¦ respond} | Configure deep SIP message inspection to discard, pass without changing, or discard and send a SIP response message for a SIP message a with a malformed To header line. Even if set to pass the SIP ALG writes a log message if an unknown header is found and log- violations is enabled. | pass |
| malformed-header-call-id {discard ¦ pass ¦ respond} | Configure deep SIP message inspection to discard, pass without changing, or discard and send a SIP response message for a SIP message a with a malformed Call ID header line. Even if set to pass the SIP ALG writes a log message if an unknown header is found and log- violations is enabled. | pass |
| malformed-header-cseq {discard ¦ pass ¦ respond} | Configure deep SIP message inspection to discard, pass without changing, or discard and send a SIP response message for a SIP message a with a malformed CSeq header line. Even if set to pass the SIP ALG writes a log message if an unknown header is found and log- violations is enabled. | pass |
| malformed-header-rack {discard ¦ pass ¦ respond} | Configure deep SIP message inspection to discard, pass without changing, or discard and send a SIP response message for a SIP message a with a malformed Rack header line. Even if set to pass the SIP ALG writes a log message if an unknown header is found and log- violations is enabled. | pass |
| malformed-header-rseq {discard ¦ pass ¦ respond} | Configure deep SIP message inspection to discard, pass without changing, or discard and send a SIP response message for a SIP message a with a malformed RSeq header line. Even if set to pass the SIP ALG writes a log message if an unknown header is found and log- violations is enabled. | pass |
| malformed-header-contact {discard ¦ pass ¦ respond} | Configure deep SIP message inspection to discard, pass without changing, or discard and send a SIP response message for a SIP message a with a malformed Contact header line. Even if set to pass the SIP ALG writes a log message if an unknown header is found and log- violations is enabled. | pass |
| malformed-header-record- route {discard ¦ pass ¦ respond} | Configure deep SIP message inspection to discard, pass without changing, or discard and send a SIP response message for a SIP message a with a malformed Record- Route header line. Even if set to pass the SIP ALG writes a log message if an unknown header is found and log- violations is enabled. | pass |
| malformed-header-route {discard ¦ pass ¦ respond} | Configure deep SIP message inspection to discard, pass without changing, or discard and send a SIP response message for a SIP message a with a malformed Route header line. Even if set to pass the SIP ALG writes a log message if an unknown header is found and log- violations is enabled. | pass |

Fortinet Technologies Inc.                                                                Page 736                                     FortiOS™ - CLI Reference for FortiOS 5.0

| Variable | Description | Default |
| --- | --- | --- |
| malformed-header-expires {discard ¦ pass ¦ respond} | Configure deep SIP message inspection to discard, pass without changing, or discard and send a SIP response message for a SIP message a with a malformed Expires header line. Even if set to pass the SIP ALG writes a log message if an unknown header is found and log- violations is enabled. | pass |
| malformed-header-content- type {discard ¦ pass ¦ respond} | Configure deep SIP message inspection to discard, pass without changing, or discard and send a SIP response message for a SIP message a with a malformed Content- Type header line. Even if set to pass the SIP ALG writes a log message if an unknown header is found and log- violations is enabled. | pass |
| malformed-header-content- length {discard ¦ pass ¦ respond} | Configure deep SIP message inspection to discard, pass without changing, or discard and send a SIP response message for a SIP message a with a malformed Content- Length header line. Even if set to pass the SIP ALG writes a log message if an unknown header is found and log-violations is enabled. | pass |
| malformed-header-max- forwards {discard ¦ pass ¦ respond} | Configure deep SIP message inspection to discard, pass without changing, or discard and send a SIP response message for a SIP message a with a malformed Max- forwards header line. Even if set to pass the SIP ALG writes a log message if an unknown header is found and log-violations is enabled. | pass |
| malformed-header-allow {discard ¦ pass ¦ respond} | Configure deep SIP message inspection to discard, pass without changing, or discard and send a SIP response message for a SIP message a with a malformed Allow header line. Even if set to pass the SIP ALG writes a log message if an unknown header is found and log- violations is enabled. | pass |
| malformed-header-p- asserted-identity {discard ¦ pass ¦ respond} | Configure deep SIP message inspection to discard, pass without changing, or discard and send a SIP response message for a SIP message a with a malformed P- Asserted-Identity header line. Even if set to pass the SIP ALG writes a log message if an unknown header is found and log-violations is enabled. | pass |
| malformed-header-sdp-v {discard ¦ pass ¦ respond} | Configure deep SIP message inspection to discard, pass without changing, or discard and send a SIP response message for a SIP message a with a malformed v= body line. Even if set to pass the SIP ALG writes a log message if an unknown header is found and log- violations is enabled. | pass |
| malformed-header-sdp-o {discard ¦ pass ¦ respond} | Configure deep SIP message inspection to discard, pass without changing, or discard and send a SIP response message for a SIP message a with a malformed o= body line. Even if set to pass the SIP ALG writes a log message if an unknown header is found and log- violations is enabled. | pass |

Fortinet Technologies Inc.                                                                Page 737                                     FortiOS™ - CLI Reference for FortiOS 5.0

| Variable | Description | Default |
| --- | --- | --- |
| malformed-header-sdp-s {discard ¦ pass ¦ respond} | Configure deep SIP message inspection to discard, pass without changing, or discard and send a SIP response message for a SIP message a with a malformed s= body line. Even if set to pass the SIP ALG writes a log message if an unknown header is found and log- violations is enabled. | pass |
| malformed-header-sdp-i {discard ¦ pass ¦ respond} | Configure deep SIP message inspection to discard, pass without changing, or discard and send a SIP response message for a SIP message a with a malformed i= body line. Even if set to pass the SIP ALG writes a log message if an unknown header is found and log- violations is enabled. | pass |
| malformed-header-sdp-c {discard ¦ pass ¦ respond} | Configure deep SIP message inspection to discard, pass without changing, or discard and send a SIP response message for a SIP message a with a malformed c= body line. Even if set to pass the SIP ALG writes a log message if an unknown header is found and log- violations is enabled. | pass |
| malformed-header-sdp-b {discard ¦ pass ¦ respond} | Configure deep SIP message inspection to discard, pass without changing, or discard and send a SIP response message for a SIP message a with a malformed b= body line. Even if set to pass the SIP ALG writes a log message if an unknown header is found and log- violations is enabled. | pass |
| malformed-header-sdp-z {discard ¦ pass ¦ respond} | Configure deep SIP message inspection to discard, pass without changing, or discard and send a SIP response message for a SIP message a with a malformed z= body line. Even if set to pass the SIP ALG writes a log message if an unknown header is found and log- violations is enabled. | pass |
| malformed-header-sdp-k {discard ¦ pass ¦ respond} | Configure deep SIP message inspection to discard, pass without changing, or discard and send a SIP response message for a SIP message a with a malformed k= body line. Even if set to pass the SIP ALG writes a log message if an unknown header is found and log- violations is enabled. | pass |
| malformed-header-sdp-a {discard ¦ pass ¦ respond} | Configure deep SIP message inspection to discard, pass without changing, or discard and send a SIP response message for a SIP message a with a malformed a= body line. Even if set to pass the SIP ALG writes a log message if an unknown header is found and log- violations is enabled. | pass |
| malformed-header-sdp-t {discard ¦ pass ¦ respond} | Configure deep SIP message inspection to discard, pass without changing, or discard and send a SIP response message for a SIP message a with a malformed t= body line. Even if set to pass the SIP ALG writes a log message if an unknown header is found and log- violations is enabled. | pass |

Fortinet Technologies Inc.                                                                Page 738                                     FortiOS™ - CLI Reference for FortiOS 5.0

| Variable | Description | Default |
| --- | --- | --- |
| malformed-header-sdp-r {discard ¦ pass ¦ respond} | Configure deep SIP message inspection to discard, pass without changing, or discard and send a SIP response message for a SIP message a with a malformed r= body line. Even if set to pass the SIP ALG writes a log message if an unknown header is found and log- violations is enabled. | pass |
| malformed-header-sdp-m {discard ¦ pass ¦ respond} | Configure deep SIP message inspection to discard, pass without changing, or discard and send a SIP response message for a SIP message a with a malformed m= body line. Even if set to pass the SIP ALG writes a log message if an unknown header is found and log- violations is enabled. | pass |
| ips-rtp {enable ¦ disable} | Enable to have RTP traffic inherit the IPS setting from the SIP firewall policy. Disable if IPS slows down RTP traffic, which might occur if there is a high volume of RTP traffic. Also if the traffic is using NP accelerated interfaces, enabling IPS means that the RTP traffic cannot be accelerated by NP interface acceleration. | enable |
| provisional-invite-expiry- time <time_int> | The expiry time in seconds to wait for provisional INVITE requests. The range is 10-3600 seconds. | 210 |
| ssl-mode {off ¦ full} | Select SSL mode: full — client-to-FortiGate and FortiGate-to-client off — no SSL | off |
| ssl-algorithm {high ¦ medium ¦ low) | Select SSL algorithm strength: high — AES or 3DES medium — AES, 3DES, RC4, or DES low — AES, 3DES, or RC4 | high |
| ssl-auth-client <peer_group> | Require a client certificate and authenticate it with the peer or peergrp. | null |
| ssl-auth-server <peer_group> | Authenticate the server certificate with the peer or peergrp. | null |
| ssl-client-certificate <cert_name> | Select the certificate to use for client authentication. | null |
| ssl-client-renegotiation {allow ¦ deny ¦ secure} | Select the client renegotiation policy: allow — allow SSL client to renegotiate deny — reject any attempt to renegotiate secure — reject any renegotiation attempt that does not offer a RFC 5746 Secure Regotiation Indication | allow |
| ssl-min-version {ssl-3.0 ¦ tls-1.0 ¦ tls-1.1} | Select the minimum SSL/TLS version to accept. | ssl-3.0 |
| ssl-max-version {ssl-3.0 ¦ tls-1.0 ¦ tls-1.1} | Select the maximum SSL/TLS version to accept. | tls-1.1 |
| ssl-pfs {require ¦ allow ¦ deny} | Set policy for Perfect Forward Secrecy (PFS). | allow |

Fortinet Technologies Inc.                                                                Page 739                                     FortiOS™ - CLI Reference for FortiOS 5.0

| Variable | Description | Default |
| --- | --- | --- |
| ssl-send-empty-frags {enable ¦ disable} | Enable sending empty fragments to avoid attack on CBC IV (SSL 3.0 & TLS 1.0 only). | enable |
| ssl-server-certificate <cert_name> | Select the certificate to use for server authentication. | null |

config  sccp

Configure VoIP profile settings for SCCP.

| Variable | Description | Default |
| --- | --- | --- |
| status {disable ¦ enable} | Enable or disable SCCP. | enable |
| block-mcast {enable ¦ disable} | Enable or disable blocking multicast RTP connections. | disable |
| verify-header {enable ¦ disable} | Enable or disable verifying SCCP header content. | disable |
| log-call-summary {disable ¦ enable} | Enable or disable summary content archiving of SCCP calls. | enable |
| log-violations {disable ¦ enable} | Enable or disable writing a logging message when a SIP option in a VoIP profile detects a violation in a SIP message. | disable |
| max-calls <calls_int> | Enter the maximum number of calls per minute per SCCP client. The range is 1 to 65535. Set to 0 to disable limiting the number of calls. | 0 |

Fortinet Technologies Inc.                                                                Page 740                                     FortiOS™ - CLI Reference for FortiOS 5.0

vpn

Use vpn commands to configure options related to virtual private networking through the

FortiGate unit, including:

•  IPSec operating parameters

•  a local address range for PPTP or L2TP clients

•  SSL VPN configuration settings

This chapter contains the following sections:

certificate ca certificate crl certificate local

certificate ocsp-server certificate remote certificate setting

ipsec concentrator ipsec forticlient ipsec manualkey

ipsec manualkey-interface ipsec phase1

ipsec phase1-interface ipsec phase2

ipsec phase2-interface

l2tp pptp

ssl settings

ssl web host-check-software ssl web portal

ssl web realm ssl web user

ssl web virtual-desktop-app-list

Page 741

certificate ca

Use this command to install Certificate Authority (CA) root certificates.

When a CA processes your Certificate Signing Request (CSR), it sends you the CA certificate, the signed local certificate and the Certificate Revocation List (CRL).

The process for obtaining and installing certificates is as follows:

1.  Use the execute vpn certificate local command to generate a CSR.

2.  Send the CSR to a CA.

The CA sends you the CA certificate, the signed local certificate and the CRL.

3.  Use the vpn certificate local command to install the signed local certificate.

4.  Use the vpn certificate ca command to install the CA certificate.

5.  Use the vpn certificate crl command to install the CRL.

Depending on your terminal software, you can copy the certificate and paste it into the command.

The CA certificate can update automatically from a Simple Certificate Enrollment Protocol

(SCEP) server.

Syntax

config vpn certificate ca edit <ca_name>

set ca <cert>

set auto-update-days <days_int>

set auto-update-days-warning <days_int>

set scep-url <URL_str>

set source-ip <ip4_addr>

end

To view all of the information about the certificate, use the get command:

get vpn certificate ca <ca_name>

| Variable | Description | Default |
| --- | --- | --- |
| edit <ca_name> | Enter a name for the CA certificate. | No default. |
| ca <cert> | Enter or retrieve the CA certificate in PEM format. | No default. |
| Fields relevant to SCEP auto-update |  |
| auto-update-days <days_int> | Enter how many days before expiry the FortiGate unit requests an updated CA certificate. Enter 0 for no auto- update. | 0 |
| auto-update-days- warning <days_int> | Enter how many days before CA certificate expiry the FortiGate generates a warning message. Enter 0 for no warning. | 0 |
| scep-url <URL_str> | Enter the URL of the SCEP server. | No default. |
| source-ip <ip4_addr> | Enter an address to verify request is send from expected IP. source-ip can be set after local Certificate is generated. | No default. |

certificate crl

Use this command to install a Certificate Revocation List (CRL).

When a CA processes your Certificate Signing Request (CSR), it sends you the CA certificate, the signed local certificate and the Certificate Revocation List (CRL).

The process for obtaining and installing certificates is as follows:

1.  Use the execute vpn certificate local command to generate a CSR.

2.  Send the CSR to a CA.

The CA sends you the CA certificate, the signed local certificate and the CRL.

3.  Use the vpn certificate local command to install the signed local certificate.

4.  Use the vpn certificate ca command to install the CA certificate.

5.  Use the vpn certificate crl command to install the CRL.

Depending on your terminal software, you can copy the certificate and paste it into the command.

The CRL can update automatically from a Simple Certificate Enrollment Protocol (SCEP) server.

Syntax

config vpn certificate crl edit <crl_name>

set crl <crl_PEM>

set ldap-server <ldap_server_name> set ldap-username <ldap_username> set ldap-password <ldap_password> set scep-cert <scep_certificate> set scep-url <scep_url>

set source-ip <ip4_addr>

set update-vdom <update_vdom>

set http-url <http_url>

set update-interval <seconds>

end

| Variable | Description | Default |
| --- | --- | --- |
| edit <crl_name> | Enter a name for the Certificate Revocation List (CRL). |  |
| crl <crl_PEM> | Enter the CRL in PEM format. |  |
| ldap-server <ldap_server_name> | Name of the LDAP server defined in config user ldap table for CRL auto-update. |  |
| ldap-username <ldap_username> | LDAP login name. |  |
| ldap-password <ldap_password> | LDAP login password. |  |
| scep-cert <scep_certificate> | Local certificate used for SCEP communication for CRL auto- update. | Fortinet- Firmware |
| scep-url <scep_url> | URL of the SCEP server used for automatic CRL certificate updates. The URL must begin with http:// or https://. |  |
| source-ip <ip4_addr> | Enter an address to verify request is send from expected IP. source-ip can be set after local Certificate is generated. | No default. |

| Variable | Description | Default |
| --- | --- | --- |
| update-vdom <update_vdom> | VDOM used to communicate with remote SCEP server for CRL auto-update. | root |
| http-url <http_url> | URL of an http server used for automatic CRL certificate updates. The URL must begin with http:// or https://. |  |
| update-interval <seconds> | Enter how frequently, in seconds, the FortiGate unit checks for an updated CRL. Enter 0 to update the CRL only when it expires. This option is available when you add a scep-url. |  |

Fortinet Technologies Inc.                                                                Page 744                                     FortiOS™ - CLI Reference for FortiOS 5.0

certificate local

Use this command to install local certificates.

When a CA processes your Certificate Signing Request (CSR), it sends you the CA certificate, the signed local certificate and the Certificate Revocation List (CRL).

The process for obtaining and installing certificates is as follows:

1.  Use the execute vpn certificate local command to generate a CSR.

2.  Send the CSR to a CA.

The CA sends you the CA certificate, the signed local certificate and the CRL.

3.  Use the vpn certificate local command to install the signed local certificate.

4.  Use the vpn certificate ca command to install the CA certificate.

5.  Use the vpn certificate crl command to install the CRL.

Depending on your terminal software, you can copy the certificate and paste it into the command.

The local certificate can update automatically from a Simple Certificate Enrollment Protocol

(SCEP) server.

Syntax

config vpn certificate local edit <cert_name>

set password <pwd>

set comments <comment_text>

set private-key <prkey> set source-ip <ip4_addr> set certificate <cert_PEM> set csr <csr_PEM>

set scep-url <URL_str>

set scep-password <password_str>

set auto-regenerate-days <days_int>

set auto-regenerate-days-warning <days_int>

end

To view all of the information about the certificate, use the get command:

get vpn certificate local [cert_name]

| Variable | Description | Default |
| --- | --- | --- |
| edit <cert_name> | Enter the local certificate name. | No default. |
| certificate <cert_PEM> | Enter the signed local certificate in PEM format. | No default. |
| comments <comment_text> | Enter any relevant information about the certificate. | No default. |
| You should not modify the following variables if you generated the CSR on this unit. |
| csr <csr_PEM> | The CSR in PEM format. | No default. |
| password <pwd> | The password in PEM format. | No default. |
| private-key <prkey> | The private key in PEM format. | No default. |
| source-ip <ip4_addr> | Enter an address to verify request is send from expected IP. source-ip can be set after local Certificate is generated. | No default. |

Fortinet Technologies Inc.                                                                Page 745                                     FortiOS™ - CLI Reference for FortiOS 5.0

| Variable | Description | Default |
| --- | --- | --- |
| Fields relevant to SCEP auto-update |  |
| scep-url <URL_str> | Enter the URL of the SCEP server. | No default. |
| scep-password <password_str> | Enter the password for the SCEP server. | No default. |
| auto-regenerate-days <days_int> | Enter how many days before expiry the FortiGate unit requests an updated local certificate. Enter 0 for no auto-update. | 0 |
| auto-regenerate-days- warning <days_int> | Enter how many days before local certificate expiry the FortiGate generates a warning message. Enter 0 for no warning. | 0 |

Fortinet Technologies Inc.                                                                Page 746                                     FortiOS™ - CLI Reference for FortiOS 5.0

certificate ocsp-server

Use this command to specify the revocation server for an OCSP (Online Certificate Status

Protocol) server certificate. You can also specify the action to take if the server is not available.

Syntax

config vpn certificate ocsp-server edit <ocsp_name>

set cert <cert_name>

set secondary-cert <cert2_name> set secondary-url <ocsp2_url> set source-ip <ip4_addr>

set url <ocsp_url>

set unavail-action <unavailable_action>

end

To view all of the information about the certificate, use the get command:

get vpn certificate ocsp [cert_name]

| Variable | Description |
| --- | --- |
| <ocsp_name> | Enter a name for this OSCP server entry. |
| cert <cert_name> | Enter the OCSP server public certificate (one of the remote certificates). |
| secondary-cert <cert2_name> | Enter the secondary OCSP server public certificate (one of the remote certificates). |
| secondary-url <ocsp2_url> | Enter the URL of the secondary OCSP server. |
| source-ip <ip4_addr> | Enter an address to verify request is send from expected IP. source-ip can be set after local Certificate is generated. |
| url <ocsp_url> | Enter the URL of the OCSP server. |
| unavail-action <unavailable_action> | Action taken on client certification when the OCSP server is unreachable. revoke or ignore. Default is revoke. |

certificate remote

Use this command to install remote certificates. The remote certificates are public certificates without a private key. They are used as OCSP (Online Certificate Status Protocol) server certificates.

Syntax

config vpn certificate remote edit cert <cert_name>

set remote <remote_cert_detail>

end

To view all of the information about the certificate, use the get command:

get vpn certificate remote [cert_name]

| Variable | Description |
| --- | --- |
| cert <cert_name> | Enter the name of the public certificate. |
| remote <remote_cert_detail> | Details/description of the remote certificate. |

certificate setting

Use this command to enable obtaining certificates by OSCP.

Syntax

config vpn certificate setting

set check-ca-cert {enable | disable} set ocsp-status {enable | disable} set oscp-default-server <ocsp_name>

end

| Variable | Description | Default |
| --- | --- | --- |
| check-ca-cert {enable ¦ disable} | Enable to check certificate and fail the authentication if the CA certificate is not found. | enable |
| ocsp-status {enable ¦ disable} | Enable or disable obtaining certificates by OCSP | disable |
| oscp-default-server <ocsp_name> | Enter the OSCP server to use by default. This is one of the servers defined in vpn certificate ocsp- server. | null |

ipsec concentrator

Use this command to add IPSec policy-based VPN tunnels to a VPN concentrator. The VPN

concentrator collects hub-and-spoke tunnels into a group.

The concentrator allows VPN traffic to pass from one tunnel to the other through the FortiGate unit. The FortiGate unit functions as a concentrator, or hub, in a hub-and-spoke network.

VPN concentrators are not available in Transparent mode.

Syntax

config vpn ipsec concentrator edit <concentrator_name>

set member <member_name> [member_name] [member_name]

set src-check {enable | disable}

end

The member field is required.

| Variable | Description | Default |
| --- | --- | --- |
| edit <concentrator_name> | Enter a name for the concentrator. | No default. |
| member <member_name> [member_name] [member_name] | Enter the names of up to three VPN tunnels to add to the concentrator. Separate the tunnel names with spaces. Members can be tunnels defined in vpn ipsec phase1 or vpn ipsec manual-key. To add or remove tunnels from the concentrator you must re-enter the whole list with the required additions or deletions. | No default. |
| src-check {enable ¦ disable} | Enable to check the source address of the phase2 selector when locating the best matching phase2 in a concentrator. The default is to check only the destination selector. | disable |

ipsec forticlient

Use this command to configure automatic VPN configuration for FortiClient Host Security application users.

The FortiClient users who will use automatic configuration must be members of a user group. The config vpn ipsec forticlient command creates a “realm” that associates the user group with the phase 2 VPN configuration. You can create multiple realms to associate different user groups with different phase 2 configurations.

The user group identifies the user name and password settings that the dialup client’s credentials must match in order for authentication to be successful. The phase 2 tunnel definition and its associated firewall encryption policy provides the configuration parameters to download to the FortiClient Host Security application.

Syntax

Set or unset VPN policy distribution parameters.

config vpn ipsec forticlient edit <realm_name>

set phase2name <tunnel_name> set status {enable | disable} set usergroupname <group_name>

end

| Variable | Description | Default |
| --- | --- | --- |
| edit <realm_name> | Enter a name for the FortiClient realm. This is also referred to as the policy name. | No default. |
| phase2name <tunnel_name> | Enter the name of the phase 2 tunnel configuration that you defined as part of the dialup-client configuration. | Null |
| status {enable ¦ disable} | Enable or disable IPSec VPN policy distribution. | enable |
| usergroupname <group_name> | Enter the name of the user group that you created for dialup clients. This group must already exist. | Null |

ipsec manualkey

Use this command to configure manual keys for IPSec tunnel-mode VPN tunnels. You configure a manual key tunnel to create an IPSec tunnel-mode VPN tunnel between the FortiGate unit and a remote IPSec VPN client or gateway that is also using manual key.

A manual key VPN tunnel consists of a name for the tunnel, the IP address of the VPN gateway or client at the opposite end of the tunnel, and the encryption and authentication algorithms to use for the tunnel. Because the keys are created when you configure the tunnel, no negotiation is required for the VPN tunnel to start. However, the VPN gateway or client that connects to this tunnel must use the same encryption and authentication algorithms and must have the same encryption and authentication keys.

Syntax

config vpn ipsec manualkey edit <tunnel_name>

set authentication <authentication_algorithm>

set authkey <authentication_key>

set encryption <method>

set enckey <encryption_key>

set interface <interface_name> set localspi <local_spi_number> set local-gw <address_ipv4>

set remote-gw <address_ipv4>

set remotespi <remote_spi_number>

end

The authentication, encryption, interface, remote-gw, localspi, and remotespi

fields are required. All other fields are optional.

| Variable | Description | Default |
| --- | --- | --- |
| edit <tunnel_name> | Enter a name for the tunnel. | No default. |
| authentication <authentication_algorithm> | Enter one of the following authentication algorithms: • md5 • null • sha1 • sha256 • sha384 • sha512 Make sure you use the same algorithm at both ends of the tunnel. Note: encryption and authentication cannot both be null. | null |

| Variable | Description | Default |
| --- | --- | --- |
| authkey <authentication_key> | This field is available when authentication is set to md5, sha1, or sha256. Enter the key in 16-digit (8-byte) segments separated by hyphens. For example (MD5): 0102030405060708-090a0b0c0d0e0f10 For a SHA1 key, the final segment is only 8 digits (4 bytes). • If authentication is md5, enter a 32-digit (16- byte) hexadecimal number. • If authentication is sha1, enter a 40-digit (20- byte) hexadecimal number. • If authentication is sha256, enter a 64-digit (32-byte) hexadecimal number. Digits can be 0 to 9, and a to f. Use the same authentication key at both ends of the tunnel. | - (No default.) |
| encryption <method> | Enter one of the following encryption algorithms: • 3des • aes128 • aes192 • aes256 • aria128 • aria192 • aria256 • des • seed • null The ARIA and seed algorithms are not available on some models. Make sure you use the same algorithm at both ends of the tunnel. Note: encryption and authentication cannot both be null. | null |

Fortinet Technologies Inc.                                                                Page 753                                     FortiOS™ - CLI Reference for FortiOS 5.0

| Variable | Description | Default |
| --- | --- | --- |
| enckey <encryption_key> | This field is available when encryption is set to 3des, aes128, aes192, aes256, or des. Enter the associated encryption key: • If encryption is des, enter a 16 digit (8 byte) hexadecimal number. • If encryption is 3des, enter a 48 digit (24 byte) hexadecimal number. • If encryption is aes128, enter a 32 digit (16 byte) hexadecimal number. • If encryption is aes192, enter a 48 digit (24 byte) hexadecimal number. • If encryption is aes256, enter a 64 digit (32 byte) hexadecimal number. Digits can be 0 to 9, and a to f. For all of the above, separate each 16 digit (8 byte) hexadecimal segment with a hyphen. Use the same encryption key at both ends of the tunnel. | - (No default.) |
| interface <interface_name> | Enter the name of the physical, aggregate, or VLAN interface to which the IPSec tunnel will be bound. The FortiGate unit obtains the IP address of the interface from system interface settings (see “interface” on page 550). You cannot change interface if a firewall policy references this VPN. | Null. |
| local-gw <address_ipv4> | Optionally, specify a secondary IP address of the interface selected in interface to use for the local end of the VPN tunnel. If you do not specify an IP address here, the FortiGate unit obtains the IP address of the interface from the system interface settings (see “interface” on page 550). | 0.0.0.0 |
| localspi <local_spi_number> | Local Security Parameter Index. Enter a hexadecimal number of up to eight digits (digits can be 0 to 9, a to f) in the range 0x100 to FFFFFFF. This number must be added to the Remote SPI at the opposite end of the tunnel. | 0x100 |
| remote-gw <address_ipv4> | The IP address of the remote gateway external interface. | 0.0.0.0 |
| remotespi <remote_spi_number> | Remote Security Parameter Index. Enter a hexadecimal number of up to eight digits in the range 0x100 to FFFFFFF. This number must be added to the Local SPI at the opposite end of the tunnel. | 0x100 |

Fortinet Technologies Inc.                                                                Page 754                                     FortiOS™ - CLI Reference for FortiOS 5.0

ipsec manualkey-interface

Use this command to configure manual keys for a route-based (interface mode) IPSec VPN tunnel. When you create a route-based tunnel, the FortiGate unit creates a virtual IPSec interface automatically. The interface can be modified afterward using the system network interface CLI command. This command is available only in NAT/Route mode.

Syntax

config vpn ipsec manualkey-interface edit <tunnel_name>

set auth-alg <authentication_algorithm>

set auth-key <authentication_key>

set enc-alg <method>

set enc-key <encryption_key> set interface <interface_name> set ip-version <4 | 6>

set local-gw <address_ipv4>

set local-gw6 <address_ipv6>

set local-spi <local_spi_number>

set remote-gw <address_ipv4>

set remote-gw6 <address_ipv6>

set remote-spi <remote_spi_number>

end

The auth-alg, enc-alg, interface, remote-gw, local-spi, and remote-spi fields are required. All other fields are optional.

| Variable | Description | Default |
| --- | --- | --- |
| edit <tunnel_name> | Enter a name for the tunnel. | No default. |
| auth-alg <authentication_algorithm> | Enter one of the following authentication algorithms: • md5 • null • sha1 • sha256 • sha384 • sha512 Make sure you use the same algorithm at both ends of the tunnel. Note: enc-alg and auth-alg cannot both be null. | null |

Fortinet Technologies Inc.                                                                Page 755                                     FortiOS™ - CLI Reference for FortiOS 5.0

| Variable | Description | Default |
| --- | --- | --- |
| auth-key <authentication_key> | This field is available when auth-alg is set to md5, sha1 or sha256. Enter the key in 16-digit (8-byte) segments separated by hyphens. For example (MD5): 0102030405060708-090a0b0c0d0e0f10 For a SHA1 key, the final segment is only 8 digits (4 bytes). • If auth-alg is md5, enter a 32-digit (16-byte) hexadecimal number. • If auth-alg is sha1, enter a 40-digit (20-byte) hexadecimal number. • If auth-alg is sha256, enter a 64-digit (32-byte) hexadecimal number. Digits can be 0 to 9, and a to f. Use the same authentication key at both ends of the tunnel. | - (No default.) |
| enc-alg <method> | Enter one of the following encryption algorithms: • 3des • aes128 • aes192 • aes256 • des • aria128 • aria192 • aria256 • seed • null The ARIA algorithm is not available on some models. Make sure you use the same algorithm at both ends of the tunnel. Note: enc-alg and auth-alg cannot both be null. | null |

Fortinet Technologies Inc.                                                                Page 756                                     FortiOS™ - CLI Reference for FortiOS 5.0

| Variable | Description | Default |
| --- | --- | --- |
| enc-key <encryption_key> | This field is available when enc-alg is set to 3des, aes128, aes192, aes256, or des. Enter the associated encryption key: • If enc-alg is des, enter a 16 digit (8 byte) hexadecimal number. • If enc-alg is 3des, enter a 48 digit (24 byte) hexadecimal number. • If enc-alg is aes128, enter a 32 digit (16 byte) hexadecimal number. • If enc-alg is aes192, enter a 48 digit (24 byte) hexadecimal number. • If enc-alg is aes256, enter a 64 digit (32 byte) hexadecimal number. Digits can be 0 to 9, and a to f. For all of the above, separate each 16 digit (8 byte) hexadecimal segment with a hyphen. Use the same encryption key at both ends of the tunnel. | - (No default.) |
| interface <interface_name> | Enter the name of the physical, aggregate, or VLAN interface to which the IPSec tunnel will be bound. The FortiGate unit obtains the IP address of the interface from system interface settings (see “interface” on page 550). | Null. |
| ip-version <4 ¦ 6> | Enter 4 for IPv4 encapsulation or 6 for IPv6 encapsulation. | 4 |
| local-gw <address_ipv4> local-gw6 <address_ipv6> | By default, the FortiGate unit determines the local gateway IP address from the interface setting. Optionally, you can specify a secondary IP address configured on the same interface. local-gw6 is available when ip-version is 6. local-gw is available when ip-version is 4. | 0.0.0.0 for IPv4 :: for IPv6 |
| local-spi <local_spi_number> | Local Security Parameter Index. Enter a hexadecimal number of up to eight digits (digits can be 0 to 9, a to f) in the range 0x100 to FFFFFFF. This number must be added to the Remote SPI at the opposite end of the tunnel. | 0x100 |
| remote-gw <address_ipv4> remote-gw6 <address_ipv6> | The IP address of the remote gateway external interface. remote-gw6 is available when ip-version is 6. remote-gw is available when ip-version is 4. | 0.0.0.0 for IPv4 :: for IPv6 |
| remote-spi <remote_spi_number> | Remote Security Parameter Index. Enter a hexadecimal number of up to eight digits in the range 0x100 to FFFFFFF. This number must be added to the Local SPI at the opposite end of the tunnel. | 0x100 |

Fortinet Technologies Inc.                                                                Page 757                                     FortiOS™ - CLI Reference for FortiOS 5.0

ipsec phase1

Use this command to add or edit IPSec tunnel-mode phase 1 configurations. When you add a tunnel-mode phase 1 configuration, you define how the FortiGate unit and a remote VPN peer (gateway or client) authenticate themselves to each other as part of establishing an IPSec VPN tunnel.

The phase 1 configuration specifies the name of a remote VPN peer, the nature of the connection (static IP, dialup, or dynamic DNS), the encryption and authentication keys for the phase 1 proposal, and the authentication method (preshared key or certificate). For authentication to be successful, the FortiGate unit and the remote VPN peer must be configured with compatible phase 1 settings.

You can change all settings except the type setting after you define the configuration: if the address type of a remote peer changes, you must delete the original phase 1 configuration and define a new one. As a general rule, create only one phase 1 configuration per remote VPN peer.

Syntax

config vpn ipsec phase1 edit <gateway_name>

set add-gw-route {enable | disable}

set authmethod <authentication_method>

set authpasswd <password>

set authusr <user_name>

set authusrgrp <group_name>

set autoconfig {client | gateway | disable}

set auto-negotiate {enable | disable}

set dhgrp {1 2 5 14}

set distance <int>

set dpd {disable | enable}

set dpd-retrycount <retry_integer>

set dpd-retryinterval <seconds> [<milliseconds>] set forticlient-enforcement {enable | disable} set fragmentation {enable | disable}

set ike-version {1 | 2}

set interface <interface_name>

set keepalive <seconds>

set keylife <seconds>

set local-gw <address_ipv4>

set localid <local_id>

set localid-type {auto | fqdn | user-fqdn | keyid | address

| asn1dn}

set mode {aggressive | main}

set nattraversal {enable | disable} set negotiate-timeout <seconds_int> set peer <CA_certificate_name>

set peerid <peer_id>

set peergrp <certificate_group_name> set peertype <authentication_method> set priority <prio>

set proposal <encryption_combination>

set psksecret <preshared_key>

set remote-gw <address_ipv4>

set remotegw-ddns <domain_name>

set rsa-certificate <server_certificate>

set type <remote_gw_type>

set usrgrp <group_name>

set xauthtype <XAuth_type>

set xauthexpire {on-disconnect | on-rekey}

end

A proposal value is required. In NAT/Route mode, you must specify interface. A

remote-gw value may be required depending on the value of the type attribute. You must also

enter a preshared key or a certificate name depending on the value of authmethod. All other

fields are optional.

| Variable | Description | Default |
| --- | --- | --- |
| edit <gateway_name> | Enter a name (maximum 35 characters) for this gateway. If type is dynamic, the maximum name length is further reduced depending on the number of dialup tunnels that can be established: by 2 for up to 9 tunnels, by 3 for up to 99 tunnels, 4 for up to 999 tunnels, and so on. | No default. |
| add-gw-route {enable ¦ disable} | Enable to automatically add a route to the remote gateway specified in remote-gw. Note: This command is deprecated. Use the dynamic-gateway {enable ¦ disable} field in config router static instead. | disable |
| authmethod <authentication_method> | Specify the authentication method: • Enter psk to authenticate using a pre-shared key. Use psksecret to enter the pre-shared key. • Enter rsa-signature to authenticate using a digital certificate. Use set rsa-certificate to enter the name of the digital certificate. You must configure certificates before selecting rsa-signature here. For more information, see “execute vpn certificate local” on page 990 and “vpn certificate ca” on page 742. | psk |
| authpasswd <password> | This field is available when xauthtype is set to client. Enter the XAuth client password for the FortiGate unit. | No default. |
| authusr <user_name> | This field is available when xauthtype is set to client. Enter the XAuth client user name for the FortiGate unit. | Null |

| Variable | Description | Default |
| --- | --- | --- |
| authusrgrp <group_name> | This field is available when xauthtype is set to auto, pap, or chap. When the FortiGate unit is configured as an XAuth server, enter the user group to authenticate remote VPN peers. The user group can contain local users, LDAP servers, and RADIUS servers. The user group must be added to the FortiGate configuration before the group name can be cross-referenced. For more information, see “user group” on page 707, “user ldap” on page 711, “user local” on page 714, and “user radius” on page 720. | Null |
| autoconfig {client ¦ gateway ¦ disable} | Select VPN auto configuration mode: VPN gateway, VPN client, or auto configuration disabled. | disable |
| auto-negotiate {enable ¦ disable} | Enable to keep trying to negotiate an IKE SA even if the link is down. The primary use of this feature is in cases where there are multiple redundant tunnels and you prefer the primary connection if it can be established. | enable |
| dhgrp {1 2 5 14} | Type 1, 2, 5 and/or 14 to select one or more Diffie- Hellman groups from DH group 1, 2, 5 and 14 respectively. At least one of the DH group settings on the remote peer or client must be identical to one of the selections on the FortiGate unit. | 5 |
| distance <int> | Configure the administrative distance for routes added when a dialup IPSec connection is established. Using administrative distance you can specify the relative priorities of different routes to the same destination. A lower administrative distance indicates a more preferred route. Distance can be an integer from 1-255. See also router static “distance <distance>” on page 444. | 1 |
| dpd {disable ¦ enable} | Enable or disable DPD (Dead Peer Detection). DPD detects the status of the connection between VPN peers. Enabling DPD facilitates cleaning up dead connections and establishing new VPN tunnels. DPD is not supported by all vendors and is not used unless DPD is supported and enabled by both VPN peers. | enable |
| dpd-retrycount <retry_integer> | This field is available when dpd is set to enable. The DPD retry count when dpd is set to enable. Set the number of times that the local VPN peer sends a DPD probe before it considers the link to be dead and tears down the security association (SA). The dpd- retrycount range is 0 to 10. To avoid false negatives due to congestion or other transient failures, set the retry count to a sufficiently high value for your network. | 3 |

Fortinet Technologies Inc.                                                                Page 760                                     FortiOS™ - CLI Reference for FortiOS 5.0

| Variable | Description | Default |
| --- | --- | --- |
| dpd-retryinterval <seconds> [<milliseconds>] | This field is available when dpd is set to enable. The DPD (Dead Peer Detection) retry interval is the time that the local VPN peer waits between sending DPD probes. Set the time in seconds plus, optionally, milliseconds. For example, for 2.5 seconds enter 2 500. The range is 1 to 60 seconds, 0 to 999 milliseconds. When the tunnel is starting, or if it has failed, a retry interval of 5 seconds is used if dpd-retryinterval is less than 5 seconds. | 5 |
| forticlient-enforcement {enable ¦ disable} | Enable to allow only FortiClient users to connect. | disable |
| fragmentation {enable ¦ disable} | Enable intra-IKE fragmentation support on re- transmission of fragmented packets. | enable |
| ike-version {1 ¦ 2} | Select whether to use IKEv1 or IKEv2 (RFC 4306). | 1 |
| interface <interface_name> | Enter the name of the physical, aggregate, or VLAN interface to which the IPSec tunnel will be bound. The FortiGate unit obtains the IP address of the interface from system interface settings (see “interface” on page 550) unless you specify a different IP address using the local-gw <address_ipv4> attribute. You cannot change interface if a firewall policy references this VPN. | Null |
| keepalive <seconds> | This field is available when nattraversal is set to enable. Set the NAT traversal keepalive frequency. This number specifies (in seconds) how frequently empty UDP packets are sent through the NAT device to make sure that the NAT mapping does not change until P1 and P2 security associations expire. The keepalive frequency can be from 10 to 900 seconds. | 10 |
| keylife <seconds> | Set the keylife time. The keylife is the amount of time (in seconds) before the phase 1 encryption key expires. When the key expires, a new key is generated without interrupting service. The range is 120 to 172,800 seconds. | 28800 |
| local-gw <address_ipv4> | Optionally, specify a secondary IP address of the interface selected in interface to use for the local end of the VPN tunnel. If you do not specify an IP address here, the FortiGate unit obtains the IP address of the interface from the system interface settings (see “interface” on page 550). | 0.0.0.0 |

Fortinet Technologies Inc.                                                                Page 761                                     FortiOS™ - CLI Reference for FortiOS 5.0

| Variable | Description | Default |
| --- | --- | --- |
| localid <local_id> | Enter a local ID if the FortiGate unit is functioning as a VPN client and will use the local ID for authentication purposes. If you want to dedicate a tunnel to a FortiGate dialup client, you must assign a unique identifier (local ID) to the FortiGate client. Whenever you configure a unique identifier (local ID) on a FortiGate dialup client, you must enable aggressive mode on the FortiGate dialup server and also specify the identifier as a peer ID on the FortiGate dialup server. | Null |
| localid-type {auto ¦ fqdn ¦ user-fqdn ¦ keyid ¦ address ¦ asn1dn} | Select the type of localid: auto — select type automatically fqdn — Fully Qualified Domain Name user-fqdn — Use User Fully Qualified Domain Name keyid — Use Key Identifier ID address — Use IP address ID asn1dn — Use ASN.1 Distinguished Name ID | auto |
| mode {aggressive ¦ main} | Enter aggressive or main (ID Protection) mode. Both modes establish a secure channel. In main mode, identifying information is hidden. Main mode is typically used when both VPN peers have static IP addresses. In aggressive mode, identifying information is exchanged in the clear. When the remote VPN peer or client has a dynamic IP address, or the remote VPN peer or client will be authenticated using an identifier (local ID), you must select Aggressive mode if there is more than one dialup phase 1 configuration for the interface IP address. | main |
| nattraversal {enable ¦ disable} | Enable NAT traversal if you expect the IPSec VPN traffic to go through a gateway that performs NAT. If no NAT device is detected, enabling NAT traversal has no effect. Both ends of the VPN must have the same NAT traversal setting. If you enable NAT traversal you can set the keepalive frequency. | enable |
| negotiate-timeout <seconds_int> | Enter how long in seconds the FortiGate unit will wait for the IKE SA to be negotiated. Range: 1 to 300 seconds. | 30 |

Fortinet Technologies Inc.                                                                Page 762                                     FortiOS™ - CLI Reference for FortiOS 5.0

| Variable | Description | Default |
| --- | --- | --- |
| peer <CA_certificate_name> | This field is available when authmethod is set to rsa-signature and peertype is set to peer. Enter the name of the peer (CA) certificate that will be used to authenticate remote VPN clients or peers. Use the command config user peer to add peer certificates. Peer certificates must be added to the FortiGate configuration before they can be cross- referenced. For more information, see “user peer” on page 717. | Null |
| peerid <peer_id> | This field is available when peertype is set to one. Enter the peer ID that will be used to authenticate remote clients or peers by peer ID. | Null |
| peergrp <certificate_group_name> | This field is available when type is set to dynamic, authmethod is set to rsa-signature, and peertype is set to peergrp. Enter the name of the peer certificate group that will be used to authenticate remote clients or peers. You must create the peer certificate group before the group name can be cross-referenced. For more information, see “user peergrp” on page 719. | Null |
| peertype <authentication_method> | The following attributes are available under the following conditions: • one is available when mode is set to aggressive or when authmethod is set to rsa-signature. • dialup is available when type is set to dynamic and authmethod is set to psk. • peer is available when authmethod is set to rsa-signature. • peergrp is available when type is set to dynamic and authmethod is set to rsa- signature. Enter the method for authenticating remote clients or peers when they connect to the FortiGate unit: • Type any to accept any remote client or peer (peer IDs are not used for authentication purposes). The mode attribute can be set to aggressive or main. You can use this option with RSA Signature authentication. But, for highest security, you should configure a PKI user/group for the peer and set Peer Options to Accept this peer certificate only. • Type one to authenticate either a remote peer or client that has a dynamic IP address and connects using a unique identifier over a dedicated tunnel, or more than one dialup client that connects through the same tunnel using the same (shared) identifier. Use the peerid field to set the peer ID. If more than one dialup client will be connecting using the same (shared) identifier, set mode to aggressive. | any |

Fortinet Technologies Inc.                                                                Page 763                                     FortiOS™ - CLI Reference for FortiOS 5.0

| Variable | Description • Type dialup to authenticate dialup VPN clients that use unique identifiers and preshared keys (or unique preshared keys only) to connect to the VPN through the same VPN tunnel. In this case, you must create a dialup user group for authentication purposes. Use the usrgrp field to set the user group name. If the dialup clients use unique identifiers and preshared keys, set mode to aggressive. If the dialup clients use preshared keys only, set mode to main. • Type peer to authenticate one (or more) certificate holders based on a particular (or shared) certificate. Use the peer field to enter the certificate name. Set mode to aggressive if the remote peer or client has a dynamic IP address. • Type peergrp to authenticate certificate holders that use unique certificates. In this case, you must create a group of certificate holders for authentication purposes. Use the peergrp field to set the certificate group name. The mode attribute can be set to aggressive or main. Set mode to aggressive if the remote peer or client has a dynamic IP address. | Default |
| --- | --- | --- |
| priority <prio> | This value is used to be break ties in selection of dialup routes. In the case that both routes have the same priority, the egress index for the routes will be used to determine the selected route. Set <prio> to a value between 0 and 4 294 967 295. | 0 |
| proposal <encryption_combination> | Select a minimum of one and a maximum of three encryption-message digest combinations for the phase 1 proposal (for example, 3des-md5). The remote peer must be configured to use at least one of the proposals that you define. Use a space to separate the combinations. You can choose any of the following abbreviated symmetric key encryption algorithms: • des — Digital Encryption Standard, a 64-bit block algorithm that uses a 56-bit key. • 3des — Triple-DES, in which plain text is encrypted three times by three keys. • aes128 — A 128-bit block algorithm that uses a 128-bit key. • aes192 — A 128-bit block algorithm that uses a 192-bit key. • aes256 — A 128-bit block algorithm that uses a 256-bit key. | aes128-sha1 3des-sha1 |

Fortinet Technologies Inc.                                                                Page 764                                     FortiOS™ - CLI Reference for FortiOS 5.0

| Variable | Description • aria128 — A 128-bit Korean block algorithm that uses a 128-bit key. • aria192 — A 128-bit Korean block algorithm that uses a 192-bit key. • aria256 — A 128-bit Korean block algorithm that uses a 256-bit key. • seed — A 128-bit Korean block algorithm that uses a 128-bit key. The ARIA and seed algorithms are not available on some models. You can select any of the following message digests to check the authenticity of messages during an encrypted session: • md5 — Message Digest 5, the hash algorithm developed by RSA Data Security. • sha1 — Secure Hash Algorithm 1, which produces a 160-bit message digest. • sha256 — Secure Hash Algorithm 2, which produces a 256-bit message digest. • sha384 — Secure Hash Algorithm 2, which produces a 384-bit message digest. • sha512 — Secure Hash Algorithm 2, which produces a 512-bit message digest. | Default |
| --- | --- | --- |
| psksecret <preshared_key> | This field is available when authmethod is set to psk. Enter the pre-shared key. The pre-shared key must be the same on the remote VPN gateway or client and should only be known by network administrators. The key must consist of at least 6 printable characters. For optimum protection against currently known attacks, the key should consist of a minimum of 16 randomly chosen alphanumeric characters. | * (No default.) |
| remote-gw <address_ipv4> | This field is available when type is set to static. Enter the static IP address of the remote VPN peer. | 0.0.0.0 |
| remotegw-ddns <domain_name> | This field is available when type is set to ddns. Enter the identifier of the remote peer (for example, a fully qualified domain name). Use this setting when the remote peer has a static domain name and a dynamic IP address (the IP address is obtained dynamically from an ISP and the remote peer subscribes to a dynamic DNS service). | Null. |
| rsa-certificate <server_certificate> | This field is available when authmethod is set to rsa-signature. Enter the name of the signed personal certificate for the FortiGate unit. You must install the server certificate before you enter the server certificate name. For more information, see “vpn certificate local” on page 990. | Null. |

Fortinet Technologies Inc.                                                                Page 765                                     FortiOS™ - CLI Reference for FortiOS 5.0

| Variable | Description | Default |
| --- | --- | --- |
| type <remote_gw_type> | Enter the connection type of the remote gateway: • If the remote VPN peer has a static IP address, type static. Use the remotegw field to enter the IP address. • If the remote VPN peer has a dynamically assigned IP address (DHCP or PPPoE), type dynamic. • If the remote VPN peer has a dynamically assigned IP address and subscribes to a dynamic DNS service, type ddns. Use the remotegw-ddns field to enter the domain name of the remote VPN peer. | static |
| usrgrp <group_name> | This field is available when type is set to dynamic, authmethod is set to psk, and peertype is set to dialup. Enter the name of the group of dialup VPN clients to authenticate. The user group must be added to the FortiGate configuration before it can be cross- referenced here. For more information, see “user group” on page 707, “user ldap” on page 711, “user local” on page 714, and “user radius” on page 720. | Null. |
| xauthtype <XAuth_type> | Optionally configure XAuth (eXtended Authentication): • Type disable to disable XAuth. • Type client to configure the FortiGate unit to act as an XAuth client. Use the authuser field to add the XAuth user name and password. • Type auto, pap, or chap to configure the FortiGate unit as an XAuth server. These options are available only when type is dynamic. Use the authusrgrp field to specify the user group containing members that will be authenticated using XAuth. | disable |
| xauthexpire {on-disconnect ¦ on-rekey} | Choose when the authentication with XAUTH expires: • on-disconnect — when the tunnel closes • on-rekey — when the phase 1 encryption key expires | on- disconnect |

Fortinet Technologies Inc.                                                                Page 766                                     FortiOS™ - CLI Reference for FortiOS 5.0

ipsec phase1-interface

Use this command to define a phase 1 definition for a route-based (interface mode) IPSec VPN tunnel that generates authentication and encryption keys automatically. A new interface of type “tunnel” with the same name is created automatically as the local end of the tunnel.

Optionally, you can create a route-based phase 1 definition to act as a backup for another

IPSec interface. See the monitor <phase1> field.

To complete the configuration of an IPSec tunnel, you need to:

•  configure phase 2 settings (see “ipsec phase2-interface” on page 788)

•  configure a firewall policy to pass traffic from the local private network to the tunnel interface

•  configure a static route via the IPSec interface to the private network at the remote end of the tunnel

•  optionally, define the IP addresses for each end of the tunnel to enable dynamic routing through the tunnel or to enable pinging of each end of the tunnel for testing

Syntax

config vpn ipsec phase1-interface edit <gateway_name>

set add-gw-route {enable | disable}

set add-route {enable | disable}

set assign-ip {enable | disable}

set assign-ip-from {range | usrgrp}

set assign-ip-type {ip | subnet}

set authmethod <authentication_method>

set authpasswd <password>

set authusr <user_name>

set authusrgrp <group_name>

set auto-negotiate {enable | disable}

set banner <string>

set client-auto-negotiate {enable | disable}

set client-keep-alive {enable | disable}

set default-gw <gw_ip>

set default-gw-priority <int>

set dhgrp {1 2 5 14}

set distance <int>

set dns-mode {auto | manual}

set domain <string>

set dpd {enable | disable}

set dpd-retrycount <retry_integer>

set dpd-retryinterval <seconds> [<milliseconds] set forticlient-enforcement {enable | disable} set fragmentation {enable | disable}

set ike-version {1 | 2}

set include-local-lan {enable | disable}

set interface <interface_name>

set ip-version <4 | 6> set ipv4-dns-server1 set ipv6-dns-server1

set ipv4-dns-server2 set ipv6-dns-server2 set ipv4-dns-server3 set ipv6-dns-server3

set ipv4-end-ip <ip4addr> set ipv6-end-ip <ip6addr> set ipv4-netmask <ip4mask>

set ipv4-split-include <address_name>

set ipv4-start-ip <ip4addr> set ipv6-start-ip <ip6addr> set ipv4-wins-server1

set ipv4-wins-server2

set ipv6-prefix <ip6prefix>

set keepalive <seconds>

set keylife <seconds>

set local-gw <address_ipv4> set local-gw6 <address_ipv6> set localid <local_id>

set localid-type {auto | fqdn | user-fqdn | keyid

| address | asn1dn}

set mode {aggressive | main}

set mode-cfg {enable | disable} set mode-cfg-ip-version {4|6} set monitor <phase1>

set monitor-hold-down-delay <seconds_int>

set nattraversal {enable | disable} set negotiate-timeout <seconds_int> set npu-offload {enable | disable} set peer <CA_certificate_name>

set peerid <peer_id>

set peergrp <certificate_group_name> set peertype <authentication_method> set priority <prio>

set proposal <encryption_combination>

set psksecret <preshared_key> set remote-gw <address_ipv4> set remote-gw6 <address_ipv6>

set remotegw-ddns <domain_name>

set rsa-certificate <server_certificate>

set save-password {enable | disable} set save-password {enable | disable} set send-cert-chain {enable | disable} set type <remote_gw_type>

set unity-support {enable | disable}

set usrgrp <group_name>

set xauthtype <XAuth_type>

set xauthexpire {on-disconnect | on-rekey}

config ipv4-exclude-range edit <entry_id>

set start-ip <ipaddr>

set end-ip <ipaddr>

end

config ipv6-exclude-range edit <entry_id>

set start-ip <ipaddr>

set end-ip <ipaddr>

end

end

You must specify values for proposal and interface. A remote-gw value may be required depending on the value of the type attribute. You must also enter a preshared key or a certificate name depending on the value of authmethod. All other fields are optional.

| Variable | Description | Default |
| --- | --- | --- |
| edit <gateway_name> | Enter a name (maximum 15 characters) for the remote gateway. If type is dynamic, the maximum name length is further reduced depending on the number of dialup tunnels that can be established: by 2 for up to 9 tunnels, by 3 for up to 99 tunnels, 4 for up to 999 tunnels, and so on | No default. |
| add-gw-route {enable ¦ disable} | Enable to automatically add a route to the remote gateway specified in remote-gw. Note: This command is deprecated. Use the dynamic-gateway {enable ¦ disable} field in config router static instead. | disable |
| add-route {enable ¦ disable} | Enable to add a route to the client’s peer destination selector. Disable if you use dynamic routing over the tunnel. This is available only when mode-cfg is enabled. | enable |
| assign-ip {enable ¦ disable} | For a client, enable to request an IP address from the server. For a server, enable to assign an IP address to a dialup client. This is available if mode-cfg (IKE Configuration Method) is enabled. | enable |

| Variable | Description | Default |
| --- | --- | --- |
| assign-ip-from {range ¦ usrgrp} | Select source of IP address assigned to an IKE Configuration Method client. range — Assign an IP address from the range defined in ipv4-start-ip and ipv4-end-ip (ipv6-start-ip and ipv4-end-ip for IPv6 clients). usrgrp — Assign the address defined in the RADIUS Framed-IP-Address for the user. This is available when the VPN is configured to authenticate clients with XAuth. xauthtype must be auto, pap, or chap. This is available only if ike-version is 1. This is available if mode-cfg (IKE Configuration Method) is enabled. | range |
| assign-ip-type {ip ¦ subnet} | Select the type of IP address assigned to an IKE Configuration Method client: ip — assign a single IP address to the client, as configured in assign-ip-from. subnet — assign an IP address to each end of the VPN tunnel, as configured in assign-ip-from. This type of IP address assignment facilitates the use of dynamic routing through the tunnel. This is available if mode-cfg (IKE Configuration Method) is enabled. | ip |
| authmethod <authentication_method> | Specify the authentication method: • Enter psk to authenticate using a pre-shared key. Use psksecret to enter the pre-shared key. • Enter rsa-signature to authenticate using a digital certificate. Use set rsa-certificate to enter the name of the digital certificate. You must configure certificates before selecting rsa-signature here. For more information, see “execute vpn certificate local” on page 990 and “vpn certificate ca” on page 742. | psk |
| authpasswd <password> | This field is available when xauthtype is set to client. Enter the XAuth client password for the FortiGate unit. | No default. |
| authusr <user_name> | This field is available when xauthtype is set to client. Enter the XAuth client user name for the FortiGate unit. | Null |

Fortinet Technologies Inc.                                                                Page 770                                     FortiOS™ - CLI Reference for FortiOS 5.0

| Variable | Description | Default |
| --- | --- | --- |
| authusrgrp <group_name> | This field is available when xauthtype is set to auto, pap, or chap. When the FortiGate unit is configured as an XAuth server, enter the user group to authenticate remote VPN peers. The user group can contain local users, LDAP servers, and RADIUS servers. The user group must be added to the FortiGate configuration before the group name can be cross- referenced. For more information, see “user group” on page 707, “user ldap” on page 711, “user local” on page 714, and “user radius” on page 720. | Null |
| auto-negotiate {enable ¦ disable} | Enable to keep trying to negotiate an IKE SA even if the link is down. The primary use of this feature is in cases where there are multiple redundant tunnels and you prefer the primary connection if it can be established. | enable |
| banner <string> | Specify a message to send to IKE Configuration Method clients. Some clients display this message to users. This is available if mode-cfg (IKE Configuration Method) is enabled. | Null |
| client-auto-negotiate {enable ¦ disable} | Enable or disable allowing the client to bring up the tunnel when there is no traffic. This is available when type is dynamic and mode-cfg is enabled. | disable |
| client-keep-alive {enable ¦ disable} | Enable or disable allowing the client to keep the tunnel up when there is no traffic. This is available when type is dynamic and mode-cfg is enabled. | disable |
| default-gw <gw_ip> | If the IPSec interface has a different default route than other traffic, enter the next hop router IP address. Be sure to set default-gw-priority to a higher priority (lower value) than the general default route. This is available when type is dynamic. The route it creates is not visible in the routing table. | 0.0.0.0 |
| default-gw-priority <int> | If you set default-gw, set the priority to a lower value (higher priority) than the general default route. | 0 |
| dhgrp {1 2 5 14} | Type 1, 2, 5, and/or 14 to select one or more Diffie-Hellman groups from DH group 1, 2, 5, and 14 respectively. At least one of the DH group settings on the remote peer or client must be identical to one of the selections on the FortiGate unit. | 5 |
| distance <int> | Configure the administrative distance for routes added when a dialup IPSec connection is established. Using administrative distance you can specify the relative priorities of different routes to the same destination. A lower administrative distance indicates a more preferred route. Distance can be an integer from 1-255. See also router static “distance <distance>” on page 444. | 1 |

Fortinet Technologies Inc.                                                                Page 771                                     FortiOS™ - CLI Reference for FortiOS 5.0

| Variable | Description | Default |
| --- | --- | --- |
| dns-mode {auto ¦ manual} | Set DNS behavior when mode-cfg is enabled. auto — assign DNS servers in the following order: 1 servers assigned to interface by DHCP 2 per-VDOM assigned DNS servers 3 global DNS server manual — use DNS servers specified in ipv4- dns-server1, ipv4-dns-server2, etc. | manual |
| domain <string> | Specify a domain name to send to IKE Configuration Method clients. This is available if mode-cfg (IKE Configuration Method) is enabled. | Null |
| dpd {enable ¦ disable} | Enable or disable DPD (Dead Peer Detection). DPD detects the status of the connection between VPN peers. Enabling DPD facilitates cleaning up dead connections and establishing new VPN tunnels. DPD is not supported by all vendors and is not used unless DPD is supported and enabled by both VPN peers. | enable |
| dpd-retrycount <retry_integer> | This field is available when dpd is set to enable. The DPD retry count when dpd is set to enable. Set the number of times that the local VPN peer sends a DPD probe before it considers the link to be dead and tears down the security association (SA). The dpd-retrycount range is 0 to 10. To avoid false negatives due to congestion or other transient failures, set the retry count to a sufficiently high value for your network. | 3 |
| dpd-retryinterval <seconds> [<milliseconds] | This field is available when dpd is set to enable. The DPD (Dead Peer Detection) retry interval is the time that the local VPN peer waits between sending DPD probes. Set the time in seconds plus, optionally, milliseconds. For example, for 2.5 seconds enter 2 500. The range is 1 to 60 seconds, 0 to 999 milliseconds. When the tunnel is starting, or if it has failed, a retry interval of 5 seconds is used if dpd- retryinterval is less than 5 seconds. | 5 |
| forticlient-enforcement {enable ¦ disable} | Enable to allow only FortiClient users to connect. | disable |
| fragmentation {enable ¦ disable} | Enable intra-IKE fragmentation support on re- transmission of fragmented packets. | enable |
| ike-version {1 ¦ 2} | Select whether to use IKEv1 or IKEv2 (RFC 4306). | 1 |
| include-local-lan {enable ¦ disable} | Allow Unity clients to access their local LAN even if they are using split tunneling. This is available when type is dynamic and mode-config is enabled. | disable |

Fortinet Technologies Inc.                                                                Page 772                                     FortiOS™ - CLI Reference for FortiOS 5.0

| Variable | Description | Default |
| --- | --- | --- |
| interface <interface_name> | Enter the name of the physical, aggregate, or VLAN interface to which the IPSec tunnel will be bound. The FortiGate unit obtains the IP address of the interface from system interface settings (see “interface” on page 550) unless you specify a different IP address using the local-gw <address_ipv4> attribute. | Null |
| ip-version <4 ¦ 6> | Enter 4 for IPv4 encapsulation or 6 for IPv6 encapsulation. | 4 |
| ipv4-dns-server1 ipv6-dns-server1 ipv4-dns-server2 ipv6-dns-server2 ipv4-dns-server3 ipv6-dns-server3 | Enter DNS server addresses to provide to IKE Configuration Method clients. If the value is 0.0.0.0, no DNS server address is provided. Either the IPv4 or IPv6 version of these fields is available, depending on mode-cfg-ip-version. | 0.0.0.0 :: |
| ipv4-end-ip <ip4addr> ipv6-end-ip <ip6addr> | Set end of IP address range to assign to IKE Configuration Method clients. This is available when mode-cfg is enabled, type is dynamic, and assign-ip-from is range. Either the IPv4 or IPv6 version of this field is available, depending on mode-cfg-ip-version. | No default. |
| ipv4-netmask <ip4mask> | Set the netmask value to pass to IKE Configuration Method clients. | No default. |
| ipv4-split-include <address_name> | Select the address or address group that the client can reach through the VPN. This information is sent to the client as part of IKE Configuration Method. This is available only if mode-cfg is set to enable. | Null. |
| ipv4-start-ip <ip4addr> ipv6-start-ip <ip6addr> | Set start of IP address range to assign to IKE Configuration Method clients. This is available when mode-cfg is enabled, type is dynamic, and assign-ip-from is range. Either the IPv4 or IPv6 version of this field is available, depending on mode-cfg-ip-version. | No default. |
| ipv4-wins-server1 ipv4-wins-server2 | Enter WINS server addresses to provide to IKE Configuration Method clients. If the value is 0.0.0.0, no WINS server address is provided. | 0.0.0.0 |
| ipv6-prefix <ip6prefix> | Specify the size, in bits, of the network portion of the subnet address for IPv6 IKE Configuration Method clients. Range is 0 to 128. This is available when mode-cfg-ip-version is 6 and assign-ip-type is subnet. | 0 |

Fortinet Technologies Inc.                                                                Page 773                                     FortiOS™ - CLI Reference for FortiOS 5.0

| Variable | Description | Default |
| --- | --- | --- |
| keepalive <seconds> | This field is available when nattraversal is set to enable. Set the NAT traversal keepalive frequency. This number specifies (in seconds) how frequently empty UDP packets are sent through the NAT device to make sure that the NAT mapping does not change until P1 and P2 security associations expire. The keepalive frequency can be from 0 to 900 seconds. | 5 |
| keylife <seconds> | Set the keylife time. The keylife is the amount of time (in seconds) before the phase 1 encryption key expires. When the key expires, a new key is generated without interrupting service. The range is 120 to 172,800 seconds. | 28800 |
| local-gw <address_ipv4> local-gw6 <address_ipv6> | Optionally, specify a secondary IP address of the interface selected in interface to use for the local end of the VPN tunnel. local-gw6 is available when ip-version is 6. local-gw is available when ip-version is 4. If you do not specify an IP address here, the FortiGate unit obtains the IP address of the interface from system interface settings (see “interface” on page 550). | 0.0.0.0 for IPv4 :: for IPv6 |
| localid <local_id> | Enter a local ID if the FortiGate unit is functioning as a VPN client and will use the local ID for authentication purposes. If you want to dedicate a tunnel to a FortiGate dialup client, you must assign a unique identifier (local ID) to the FortiGate client. Whenever you configure a unique identifier (local ID) on a FortiGate dialup client, you must enable aggressive mode on the FortiGate dialup server and also specify the identifier as a peer ID on the FortiGate dialup server. | Null |
| localid-type {auto ¦ fqdn ¦ user-fqdn ¦ keyid ¦ address ¦ asn1dn} | Select the type of localid: auto — select type automatically fqdn — Fully Qualified Domain Name user-fqdn — Use User Fully Qualified Domain Name keyid — Use Key Identifier ID address — Use IP address ID asn1dn — Use ASN.1 Distinguished Name ID | auto |

Fortinet Technologies Inc.                                                                Page 774                                     FortiOS™ - CLI Reference for FortiOS 5.0

| Variable | Description | Default |
| --- | --- | --- |
| mode {aggressive ¦ main} | Enter aggressive or main (ID Protection) mode. Both modes establish a secure channel. In main mode, identifying information is hidden. Main mode is typically used when both VPN peers have static IP addresses. In aggressive mode, identifying information is exchanged in the clear. Aggressive mode is typically used when a remote peer or dialup client has a dynamic IP address. You must enable aggressive mode when the remote FortiGate unit has a dynamic IP address, or the remote VPN peer or client will be authenticated using an identifier (local ID). This is available if ike-version is 1. | main |
| mode-cfg {enable ¦ disable} | Enable IKE Configuration Method so that compatible clients can configure themselves with settings that the FortiGate unit provides. This is available if type is dynamic. | disable |
| mode-cfg-ip-version {4¦6} | Select whether an IKE Configuration Method client receives an IPv4 or IPv6 IP address. This is available if mode-cfg and assign-ip are enabled. | 4 |
| monitor <phase1> | Optionally, this IPSec interface can act as a backup for another (primary) IPSec interface. Enter the name of the primary interface. The backup interface is used only while the primary interface is out of service. dpd must be enabled. A primary interface can have only one backup interface and cannot act as a backup for another interface. | Null. |
| monitor-hold-down-delay <seconds_int> | Enter the number of seconds to delay returning traffic to the primary interface from backup after the primary interface becomes stable again. Range: 0 to 31 536 000 seconds. | 0 |
| nattraversal {enable ¦ disable} | Enable NAT traversal if you expect the IPSec VPN traffic to go through a gateway that performs NAT. If no NAT device is detected, enabling NAT traversal has no effect. Both ends of the VPN must have the same NAT traversal setting. If you enable NAT traversal you can set the keepalive frequency. | enable |
| negotiate-timeout <seconds_int> | Enter how long in seconds the FortiGate unit will wait for the IKE SA to be negotiated. Range: 1 to 300 seconds. | 30 |
| npu-offload {enable ¦ disable} | Enable or disable offload of VPN session to NPU. | enable |

Fortinet Technologies Inc.                                                                Page 775                                     FortiOS™ - CLI Reference for FortiOS 5.0

| Variable | Description | Default |
| --- | --- | --- |
| peer <CA_certificate_name> | This field is available when authmethod is set to rsa-signature and peertype is set to peer. Enter the name of the peer (CA) certificate that will be used to authenticate remote VPN clients or peers. Use the command config user peer to add peer certificates. Peer certificates must be added to the FortiGate configuration before they can be cross-referenced. For more information, see “user peer” on page 717. | Null |
| peerid <peer_id> | This field is available when peertype is set to one. Enter the peer ID that will be used to authenticate remote clients or peers by peer ID. | Null |
| peergrp <certificate_group_name> | This field is available when type is set to dynamic, authmethod is set to rsa- signature, and peertype is set to peergrp. Enter the name of the peer certificate group that will be used to authenticate remote clients or peers. You must create the peer certificate group before the group name can be cross-referenced. For more information, see “user peergrp” on page 719. | Null |
| peertype <authentication_method> | The following attributes are available under the following conditions: • dialup is available when type is set to dynamic and authmethod is set to psk. • peer is available when authmethod is set to rsa-signature. • peergrp is available when type is set to dynamic and authmethod is set to rsa- signature. Enter the method for authenticating remote clients or peers when they connect to the FortiGate unit: • Type any to accept any remote client or peer (peer IDs are not used for authentication purposes). The mode attribute can be set to aggressive or main. You can use this option with RSA Signature authentication. But, for highest security, you should configure a PKI user/group for the peer and set Peer Options to Accept this peer certificate only. | any |

Fortinet Technologies Inc.                                                                Page 776                                     FortiOS™ - CLI Reference for FortiOS 5.0

| Variable | Description • Type one to authenticate either a remote peer or client that has a dynamic IP address and connects using a unique identifier over a dedicated tunnel, or more than one dialup client that connects through the same tunnel using the same (shared) identifier. Use the peerid field to set the peer ID. If more than one dialup client will be connecting using the same (shared) identifier, set mode to aggressive. • Type dialup to authenticate dialup VPN clients that use unique identifiers and preshared keys (or unique preshared keys only) to connect to the VPN through the same VPN tunnel. In this case, you must create a dialup user group for authentication purposes. Use the usrgrp field to set the user group name. If the dialup clients use unique identifiers and preshared keys, set mode to aggressive. If the dialup clients use preshared keys only, set mode to main. • Type peer to authenticate one (or more) certificate holders based on a particular (or shared) certificate. Use the peer field to enter the certificate name. Set mode to aggressive if the remote peer or client has a dynamic IP address. • Type peergrp to authenticate certificate holders that use unique certificates. In this case, you must create a group of certificate holders for authentication purposes. Use the peergrp field to set the certificate group name. The mode attribute can be set to aggressive or main. Set mode to aggressive if the remote peer or client has a dynamic IP address. | Default |
| --- | --- | --- |
| priority <prio> | This value is used to be break ties in selection of dialup routes. In the case that both routes have the same priority, the egress index for the routes will be used to determine the selected route. Set <prio> to a value between 0 and 4 294 967 295. | 0 |
| proposal <encryption_combination> | Select a minimum of one and a maximum of three encryption-message digest combinations for the phase 1 proposal (for example, 3des-md5). The remote peer must be configured to use at least one of the proposals that you define. Use a space to separate the combinations. | aes128-sha1 3des-sha1 |

Fortinet Technologies Inc.                                                                Page 777                                     FortiOS™ - CLI Reference for FortiOS 5.0

| Variable | Description You can choose any of the following abbreviated symmetric key encryption algorithms: • des — Digital Encryption Standard, a 64-bit block algorithm that uses a 56-bit key. • 3des — Triple-DES, in which plain text is encrypted three times by three keys. • aes128 — A 128-bit block algorithm that uses a 128-bit key. • aes192 — A 128-bit block algorithm that uses a 192-bit key. • aes256 — A 128-bit block algorithm that uses a 256-bit key. • aria128 — A 128-bit Korean block algorithm that uses a 128-bit key. • aria192 — A 128-bit Korean block algorithm that uses a 192-bit key. • aria256 — A 128-bit Korean block algorithm that uses a 256-bit key. • seed — A 128-bit Korean block algorithm that uses a 128-bit key. The ARIA and seed algorithms are not available on some models. You can select any of the following message digests to check the authenticity of messages during an encrypted session: • md5 — Message Digest 5, the hash algorithm developed by RSA Data Security. • sha1— Secure Hash Algorithm 1, which produces a 160-bit message digest. • sha256 — Secure Hash Algorithm 2, which produces a 256-bit message digest. • sha384 — Secure Hash Algorithm 2, which produces a 384-bit message digest. • sha512 — Secure Hash Algorithm 2, which produces a 512-bit message digest. | Default |
| --- | --- | --- |
| psksecret <preshared_key> | This field is available when authmethod is set to psk. Enter the pre-shared key. The pre-shared key must be the same on the remote VPN gateway or client and should only be known by network administrators. The key must consist of at least 6 printable characters. For optimum protection against currently known attacks, the key should consist of a minimum of 16 randomly chosen alphanumeric characters. | * (No default.) |

Fortinet Technologies Inc.                                                                Page 778                                     FortiOS™ - CLI Reference for FortiOS 5.0

| Variable | Description | Default |
| --- | --- | --- |
| remote-gw <address_ipv4> remote-gw6 <address_ipv6> | This field is available when type is set to static. Enter the static IP address of the remote VPN peer. remote-gw6 is available when ip-version is 6. remote-gw is available when ip-version is 4. | 0.0.0.0 for IPv4 :: for IPv6 |
| remotegw-ddns <domain_name> | This field is available when type is set to ddns and ip-version is set to 4. Enter the identifier of the remote peer (for example, a fully qualified domain name). Use this setting when the remote peer has a static domain name and a dynamic IP address (the IP address is obtained dynamically from an ISP and the remote peer subscribes to a dynamic DNS service). | Null |
| rsa-certificate <server_certificate> | This field is available when authmethod is set to rsa-signature. Enter the name of the signed personal certificate for the FortiGate unit. You must install the server certificate before you enter the server certificate name. For more information, see “vpn certificate local” on page 990. | Null |
| save-password {enable ¦ disable} | Enable or disable client saving Xauth user name and password. | disable |
| send-cert-chain {enable ¦ disable} | Enable or disable sending of the certificate chain, rather than a single certificate. | enable |
| split-include-service <service_group_name> | Select the service types that the client can reach through the VPN. This information is sent to the client as part of IKE Configuration Method. | Null |
| type <remote_gw_type> | Enter the connection type of the remote gateway: • If the remote VPN peer has a static IP address, type static. Use the remotegw field to enter the IP address. • If the remote VPN peer has a dynamically assigned IP address (DHCP or PPPoE), type dynamic. • If the remote VPN peer has a dynamically assigned IP address and subscribes to a dynamic DNS service, type ddns. Use the remotegw-ddns field to enter the domain name of the remote VPN peer. This option is not available if ip-version is 6. | static |
| unity-support {enable ¦ disable} | Enable support for Cisco Unity IKE Configuration Method extensions in either a server or a client. This is available for IKEv1 only. | enable |

Fortinet Technologies Inc.                                                                Page 779                                     FortiOS™ - CLI Reference for FortiOS 5.0

| Variable | Description | Default |
| --- | --- | --- |
| usrgrp <group_name> | This field is available when type is set to dynamic, authmethod is set to psk, and peertype is set to dialup. Enter the name of the group of dialup VPN clients to authenticate. The user group must be added to the FortiGate configuration before it can be cross- referenced here. For more information, see “user group” on page 707, “user ldap” on page 711, “user local” on page 714, and “user radius” on page 720. | Null |
| xauthtype <XAuth_type> | Optionally configure XAuth (eXtended Authentication): • Type disable to disable XAuth. • Type client to configure the FortiGate unit to act as an XAuth client. Use the authuser field to add the XAuth user name and password. • Type auto, pap, or chap to configure the FortiGate unit as an XAuth server. These options are available only when type is dynamic. Use the authusrgrp field to specify the user group containing members that will be authenticated using XAuth. | disable |
| xauthexpire {on-disconnect ¦ on-rekey} | Choose when the authentication with XAUTH expires: • on-disconnect — when the tunnel closes • on-rekey — when the phase 1 encryption key expires | on-disconnect |
| config ipv4-exclude-range and config ipv6-exclude-range Variables This subcommand is available only when mode-cfg is enabled. |
| start-ip <ipaddr> | Enter the start of the exclude range. | No default. |
| end-ip <ipaddr> | Enter the end of the exclude range. | No default. |

Fortinet Technologies Inc.                                                                Page 780                                     FortiOS™ - CLI Reference for FortiOS 5.0

ipsec phase2

Use this command to add or edit an IPSec tunnel-mode phase 2 configuration. The FortiGate unit uses the tunnel-mode phase 2 configuration to create and maintain an IPSec VPN tunnel with a remote VPN peer (the VPN gateway or client).

The phase 2 configuration consists of a name for the VPN tunnel, the name of an existing phase 1 configuration, the proposal settings (encryption and authentication algorithms) and DH group used for phase 2. For phase 2 to be successful, the FortiGate unit and the remote VPN peer must be configured with compatible proposal settings.

Syntax

config vpn ipsec phase2 edit <tunnel_name>

set add-route {enable | disable}

set auto-negotiate {enable | disable}

set dhcp-ipsec {enable | disable}

set dhgrp {1 | 2 | 5 | 14}

set dst-addr-type <type>

set dst-end-ip <address_ipv4>

set dst-name <address_name>

set dst-port <dest_port_number> set dst-start-ip <address_ipv4> set dst-subnet <address_ipv4mask>

set encapsulation {tunnel-mode | transport-mode}

set keepalive {enable | disable} set keylife-type <keylife_type> set keylifekbs <kb_integer>

set keylifeseconds <seconds>

set pfs {enable | disable}

set phase1name <gateway_name> set proposal <encrypt_digest> set protocol <protocol_integer> set replay {enable | disable}

set route-overlap {overlap_option}

set selector-match <match_type>

set single-source {enable | disable} set src-addr-type <ip_source_name> set src-end-ip <address_ipv4>

set src-name <address_name>

set src-port <src_port_number> set src-start-ip <address_ipv4> set src-subnet <address_ipv4mask> set use-natip {enable | disable}

end

The phase1name field is required. All other fields are optional.

| Variable | Description | Default |
| --- | --- | --- |
| edit <tunnel_name> | Enter a name for the tunnel. | No default. |
| add-route {enable ¦ disable} | Enable only if you are running a dynamic routing protocol (RIP, OSPF, or BGP) and want the routes to be propagated to routing peers. | disable |
| auto-negotiate {enable ¦ disable} | Enable to negotiate the phase 2 security association (SA) automatically, even if there is no traffic. This repeats every five seconds until it succeeds. You can use this option on a dialup peer to ensure that the tunnel is available for peers at the server end to initiate traffic to the dialup peer. Otherwise, the tunnel does not exist until the dialup peer initiates traffic. | disable |
| dhcp-ipsec {enable ¦ disable} | This field is available when phase1name names a dialup gateway configuration. Enable dhcp-ipsec if the FortiGate unit acts as a dialup server and FortiGate DHCP relay will be used to assign VIP addresses to FortiClient dialup clients. The DHCP relay parameters must be configured separately. If you configure the DHCP server to assign IP addresses based on RADIUS user group attributes, you must also set the peertype to dialup and specify the usrgrp in vpn ipsec phase1. For information about how to configure a DHCP server on a FortiGate interface, see “system dhcp server” on page 497. For information about FortiGate DHCP relay, see “system interface” on page 550. If the FortiGate unit acts as a dialup server and you manually assigned FortiClient dialup clients VIP addresses that match the network behind the dialup server, select Enable to cause the FortiGate unit to act as a proxy for the dialup clients. | disable |
| dhgrp {1 ¦ 2 ¦ 5 ¦ 14} | Type 1, 2, 5, or 14 to select the Diffie-Hellman group to propose for Phase 2 of the IPSec VPN connection. Both VPN peers must use the same DH Group. | 5 |

| Variable | Description | Default |
| --- | --- | --- |
| dst-addr-type <type> | Enter the type of destination address that corresponds to the recipient(s) or network behind the remote VPN peer or FortiGate dialup client: • To specify the IP address of a server or host, type ip. Enter the IP address using the dst-start-ip field. • To specify a range of IP addresses, type range. Enter the starting and ending addresses using the dst- start-ip, and dst-end-ip fields. • To specify a network address, type subnet. Enter the network address using the dst-subnet field. • To specify a firewall address or address group, type name. Enter the address or address group name using the dst-name field. You must also select the name option for src-addr-type. You should not use this option if ike-version is 1. IKEv1 does not support the use of multiple addresses in selectors. Instead, use the default 0.0.0.0/0 subnet selector and rely on the firewall policy to limit destination addresses. | subnet |
| dst-end-ip <address_ipv4> | This field is available when dst-addr-type is set to range. This field is not available if phase1name names a configuration that enables mode-cfg. Enter the highest destination IP address in the range of IP addresses. | 0.0.0.0 |
| dst-name <address_name> | This field is available when dst-addr-type is set to name. Enter the name of a firewall address or address group. | No default. |
| dst-port <dest_port_number> | Enter the port number that the remote VPN peer or FortiGate dialup client uses to transport traffic related to the specified service (see protocol). The range is 1 to 65535. To specify all ports, type 0. | 0 |
| dst-start-ip <address_ipv4> | This field is available when dst-addr-type is set to range. Enter the lowest destination IP address in the range of IP addresses. | 0.0.0.0 |
| dst-subnet <address_ipv4mask> | Enter the IP address and network mask that identifies the private network behind the remote VPN peer or FortiGate dialup client. | 0.0.0.0 0.0.0.0 |
| encapsulation {tunnel-mode ¦ transport-mode} | Select encapsulation: tunnel-mode — Encrypt both payload data and headers. transport-mode — Encrypt only the payload data. This is used when combining IPsec with another encapsulation, such as L2TP. | tunnel-mode |
| keepalive {enable ¦ disable} | Enable to automatically negotiate a new phase 2 security association (SA) before the current SA expires, keeping the tunnel up. Otherwise, a new SA is negotiated only if there is traffic. | disable |

Fortinet Technologies Inc.                                                                Page 783                                     FortiOS™ - CLI Reference for FortiOS 5.0

| Variable | Description | Default |
| --- | --- | --- |
| keylife-type <keylife_type> | Set when the phase 2 key expires. When the key expires, a new key is generated without interrupting service. • To make the key expire after a period of time has expired and after an amount of data is transmitted, type both. • To make the key expire after an amount of data is transmitted, type kbs. Use the keylifekbs field to set the amount of data that is transmitted. • To make the key expire after a number of seconds elapses, type seconds. Use the keylifeseconds field to set the amount of time that elapses. | seconds |
| keylifekbs <kb_integer> | This field is available when keylife-type is set to kbs or both. Set the number of Kbits of data to transmit before the phase 2 key expires. The range is 5120 to 4 294 967 295 Kbits. | 5120 |
| keylifeseconds <seconds> | This field is available when keylife-type is set to seconds or both. Set the number of seconds to elapse before the phase 2 key expires. seconds can be 120 to 172800 seconds. | 1800 |
| pfs {enable ¦ disable} | Optionally, enable or disable perfect forward secrecy (PFS). PFS ensures that each key created during Phase 2 is unrelated to keys created during Phase 1 or to other keys created during Phase 2. PFS may cause minor delays during key generation. | enable |
| phase1name <gateway_name> | Enter a phase 1 gateway configuration name. You must add the phase 1 gateway definition to the FortiGate configuration before it can be cross-referenced. | Null |
| proposal <encrypt_digest> | Enter a minimum of one and a maximum of three encryption-message digest combinations (for example, 3des-md5). The remote peer must be configured to use at least one of the proposals that you define. Use a space to separate the combinations. You can enter any encryption-message digest combination except null-null. Here is an explanation of the abbreviated encryption algorithms: • null— Do not use an encryption algorithm. • des — Digital Encryption Standard, a 64-bit block algorithm that uses a 56-bit key. • 3des — Triple-DES, in which plain text is encrypted three times by three keys. • aes128 — A 128-bit block algorithm that uses a 128-bit key. • aes192 — A 128-bit block algorithm that uses a 192-bit key. • aes256 — A 128-bit block algorithm that uses a 256-bit key. | aes128-sha1 3des-sha1 |

Fortinet Technologies Inc.                                                                Page 784                                     FortiOS™ - CLI Reference for FortiOS 5.0

| Variable | Description • aria128 — A 128-bit Korean block algorithm that uses a 128-bit key. • aria192 — A 128-bit Korean block algorithm that uses a 192-bit key. • aria256 — A 128-bit Korean block algorithm that uses a 256-bit key. • seed — A 128-bit Korean block algorithm that uses a 128-bit key. The ARIA and seed algorithms are not available on some models. You can enter any of the following message digests to check the authenticity of messages during an encrypted session: • null — Do not use a message digest. • md5 — Message Digest 5, the hash algorithm developed by RSA Data Security. • sha1— Secure Hash Algorithm 1, which produces a 160-bit message digest. • sha256 — Secure Hash Algorithm 2, which produces a 256-bit message digest. | Default |
| --- | --- | --- |
| protocol <protocol_integer> | This field is available when selector is set to specify. Enter the IP protocol number for the service. The range is 1 to 255. To specify all services, type 0. | 0 |
| replay {enable ¦ disable} | Optionally, enable or disable replay detection. Replay attacks occur when an unauthorized party intercepts a series of IPSec packets and replays them back into the tunnel. Enable replay detection to check the sequence number of every IPSec packet to see if it has been received before. If packets arrive out of sequence, the FortiGate units discards them. You can configure the FortiGate unit to send an alert email when it detects a replay packet. See “alertemail” on page 49. | enable |
| route-overlap {overlap_option} | Specify how FortiGate unit handles multiple dialup users with the same IP source address. Set overlap_option to one of the following: allow — allow overlapping routes use-new — delete the old route and add the new route use-old — use the old route and do not add the new route | use-new |

Fortinet Technologies Inc.                                                                Page 785                                     FortiOS™ - CLI Reference for FortiOS 5.0

| Variable | Description | Default |
| --- | --- | --- |
| selector-match <match_type> | The peer’s IPSec selectors are compared to FortiGate phase 2 selectors, which are any of src-start-ip / src-end-ip, src-subnet, dst-subnet, dst-start- ip / dst-end-ip. The match_type value can be one of: exact — peer’s selector must match exactly subset — peer’s selector can be a subset of this selector auto — use exact or subset match as needed (default) Note: This field is configured automatically when upgrading a FortiOS version 2.80 VPN to version 3.0. You should not set this field when configuring a new VPN. This field does not apply to IKEv2 connections. | auto |
| single-source {enable ¦ disable} | Enable if src-addr-type is name and hosts on the internal network will initiate communication sessions with remote dialup clients. | disable |
| src-addr-type <ip_source_name> | If the FortiGate unit is a dialup server, enter the type of source address that corresponds to the local sender(s) or network behind the FortiGate dialup server: • To specify the IP address of a server or host, type ip. Enter the IP address using the src-start-ip field. • To specify a range of IP addresses, type range. Enter the starting and ending addresses using the src- start-ip and src-end-ip fields. • To specify a network address, type subnet. Enter the network address using the src-subnet field. • To specify a firewall address or address group, type name. Enter the address or address group name using the src-name field. You must also select the name option for dst-addr-type. You should not use this option if ike-version is 1. IKEv1 does not support the use of multiple addresses in selectors. Instead, use the default 0.0.0.0/0 subnet selector and rely on the firewall policy to limit source addresses. If the FortiGate unit is a dialup client, src-addr-type must refer to the server(s), host(s), or private network behind the FortiGate dialup client. | subnet |
| src-end-ip <address_ipv4> | This field is available when src-addr-type is set to range. Enter the highest source IP address in the range of IP addresses. | 0.0.0.0 |
| src-name <address_name> | This field is available when src-addr-type is set to name. Enter the name of a firewall address or address group. | No default. |

Fortinet Technologies Inc.                                                                Page 786                                     FortiOS™ - CLI Reference for FortiOS 5.0

| Variable | Description | Default |
| --- | --- | --- |
| src-port <src_port_number> | If the FortiGate unit is a dialup server, enter the port number that the FortiGate dialup server uses to transport traffic related to the specified service (see protocol). If the FortiGate unit is a dialup client, enter the port number that the FortiGate dialup client uses to transport traffic related to the specified service. The src-port range is 1 to 65535. To specify all ports, type 0. | 0 |
| src-start-ip <address_ipv4> | This field is available when src-addr-type is set to range. Enter the lowest source IP address in the range of IP addresses. | 0.0.0.0 |
| src-subnet <address_ipv4mask> | If the FortiGate unit is a dialup server, enter the IP address and network mask that identifies the private network behind the FortiGate dialup server. If the FortiGate unit is a dialup client, enter the IP address and network mask that identifies the private network behind the FortiGate dialup client. | 0.0.0.0 0.0.0.0 |
| use-natip {enable ¦ disable} | By default, when outbound NAT is used, the FortiGate unit public interface IP address is the source selector. If you disable use-natip, the source selector is as specified in src-start-ip / src-end-ip or src-subnet. Note: This field is configured automatically when upgrading a FortiOS version 2.80 VPN to version 3.0. You should not set this field when configuring a new VPN. | enable |

Fortinet Technologies Inc.                                                                Page 787                                     FortiOS™ - CLI Reference for FortiOS 5.0

ipsec phase2-interface

Use this command to add a phase 2 configuration for a route-based (interface mode) IPSec tunnel or edit an existing interface-mode phase 2 configuration. This command is available only in NAT/Route mode.

Syntax

config vpn ipsec phase2-interface edit <tunnel_name>

set auto-negotiate {enable | disable}

set dhcp-ipsec {enable | disable}

set dhgrp {1 | 2 | 5 | 14}

set dst-addr-type <type>

set dst-end-ip <address_ipv4> set dst-end-ip6 <address_ipv6> set dst-name <address_name>

set dst-port <dest_port_number> set dst-start-ip <address_ipv4> set dst-start-ip6 <address_ipv6> set dst-subnet <address_ipv4mask>

set dst-subnet6 <address_ipv6mask>

set encapsulation {tunnel-mode | transport-mode}

set keepalive {enable | disable} set keylife-type <keylife_type> set keylifekbs <kb_integer>

set keylifeseconds <seconds>

set pfs {enable | disable}

set phase1name <gateway_name> set proposal <encrypt_digest> set protocol <protocol_integer> set replay {disable | enable}

set route-overlap {overlap_option} set single-source {disable | enable} set src-addr-type <ip_source_name> set src-end-ip <address_ipv4>

set src-end-ip6 <address_ipv6>

set src-name <address_name>

set src-port <src_port_number> set src-start-ip <address_ipv4> set src-start-ip6 <address_ipv6> set src-subnet <address_ipv4mask>

set src-subnet6 <address_ipv6mask>

end

The phase1name field is required. All other fields are optional.

| Variable | Description | Default |
| --- | --- | --- |
| edit <tunnel_name> | Enter a name for the phase 2 tunnel configuration. | No default. |
| auto-negotiate {enable ¦ disable} | Enable to negotiate the phase 2 security association (SA) automatically, even if there is no traffic. This repeats every five seconds until it succeeds. You can use this option on a dialup peer to ensure that the tunnel is available for peers at the server end to initiate traffic to the dialup peer. Otherwise, the tunnel does not exist until the dialup peer initiates traffic. | disable |
| dhcp-ipsec {enable ¦ disable} | This field is available when phase1name names a dialup gateway configuration. This field is not available if phase1name names a configuration that enables mode-cfg. Enable dhcp-ipsec if the FortiGate unit acts as a dialup server and FortiGate DHCP relay will be used to assign VIP addresses to FortiClient dialup clients. The DHCP relay parameters must be configured separately. If you configure the DHCP server to assign IP addresses based on RADIUS user group attributes, you must also set the peertype to dialup and specify the usrgrp in vpn ipsec phase1. For information about how to configure a DHCP server on a FortiGate interface, see “system dhcp server” on page 497. For information about FortiGate DHCP relay, see “system interface” on page 550. If the FortiGate unit acts as a dialup server and you manually assigned FortiClient dialup clients VIP addresses that match the network behind the dialup server, select Enable to cause the FortiGate unit to act as a proxy for the dialup clients. | disable |
| dhgrp {1 ¦ 2 ¦ 5 ¦ 14} | Type 1, 2, 5, or 14 to select the Diffie-Hellman group to propose for Phase 2 of the IPSec VPN connection. Both VPN peers must use the same DH Group. | 5 |

| Variable | Description | Default |
| --- | --- | --- |
| dst-addr-type <type> | Enter the type of destination address that corresponds to the recipient(s) or network behind the remote VPN peer or FortiGate dialup client: • To specify the IPv4 IP address of a server or host, type ip. Enter the IP address using the dst-start-ip field. • To specify the IPv6 IP address of a server or host, type ip6. Enter the IP address using the dst-start-ip6 field. • To specify a range of IPv4 IP addresses, type range. Enter the starting and ending addresses using the dst-start-ip and dst-end-ip fields. • To specify a range of IPv6 IP addresses, type range6. Enter the starting and ending addresses using the dst-start-ip6 and dst-end-ip6 fields. • To specify an IPv4 network address, type subnet. Enter the network address using the dst-subnet field. • To specify an IPv6 network address, type subnet6. Enter the network address using the dst-subnet field. • To specify an address defined in a firewall address or address group, type name. Enter the address name using the dst-name field. You must also select the name option for src-addr-type. This is available only for IPv4 addresses. You should not use this option if ike-version is 1. IKEv1 does not support the use of multiple addresses in selectors. Instead, use the default 0.0.0.0/0 subnet selector and rely on the firewall policy to limit destination addresses. This field is not available if phase1name names a configuration that enables mode-cfg. | subnet |
| dst-end-ip <address_ipv4> | This field is available when dst-addr-type is set to range. This field is not available if phase1name names a configuration that enables mode-cfg. Enter the highest destination IP address in the range of IP addresses. | 0.0.0.0 |
| dst-end-ip6 <address_ipv6> | This field is available when dst-addr-type is set to range6. This field is not available if phase1name names a configuration that enables mode-cfg. Enter the highest destination IP address in the range of IP addresses. | :: |
| dst-name <address_name> | This field is available when dst-addr-type is set to name. This field is not available if phase1name names a configuration that enables mode-cfg. Enter the firewall address or address group name. | No default. |

Fortinet Technologies Inc.                                                                Page 790                                     FortiOS™ - CLI Reference for FortiOS 5.0

| Variable | Description | Default |
| --- | --- | --- |
| dst-port <dest_port_number> | Enter the port number that the remote VPN peer or FortiGate dialup client uses to transport traffic related to the specified service (see protocol). The range is 1 to 65535. To specify all ports, type 0. This field is not available if phase1name names a configuration that enables mode-cfg. | 0 |
| dst-start-ip <address_ipv4> | This field is available when dst-addr-type is set to range. This field is not available if phase1name names a configuration that enables mode-cfg. Enter the lowest destination IP address in the range of IP addresses. | 0.0.0.0 |
| dst-start-ip6 <address_ipv6> | This field is available when dst-addr-type is set to range6. This field is not available if phase1name names a configuration that enables mode-cfg. Enter the lowest destination IP address in the range of IP addresses. | :: |
| dst-subnet <address_ipv4mask> | Enter the IPv4 IP address and network mask that identifies the private network behind the remote VPN peer or FortiGate dialup client. This field is not available if phase1name names a configuration that enables mode-cfg. | 0.0.0.0 0.0.0.0 |
| dst-subnet6 <address_ipv6mask> | Enter the IPv6 IP address and network mask that identifies the private network behind the remote VPN peer or FortiGate dialup client. This field is not available if phase1name names a configuration that enables mode-cfg. | ::/0 |
| encapsulation {tunnel-mode ¦ transport-mode} | Select encapsulation: tunnel-mode — Encrypt both payload data and headers. transport-mode — Encrypt only the payload data. This is used when combining IPsec with another encapsulation, such as GRE. | tunnel-mode |
| keepalive {enable ¦ disable} | Enable to automatically negotiate a new phase 2 security association (SA) before the current SA expires, keeping the tunnel up. Otherwise, a new SA is negotiated only if there is traffic. | disable |

Fortinet Technologies Inc.                                                                Page 791                                     FortiOS™ - CLI Reference for FortiOS 5.0

| Variable | Description | Default |
| --- | --- | --- |
| keylife-type <keylife_type> | Set when the phase 2 key expires. When the key expires, a new key is generated without interrupting service. • To make the key expire after a period of time has expired and after an amount of data is transmitted, type both. • To make the key expire after an amount of data is transmitted, type kbs. Use the keylifekbs field to set the amount of data that is transmitted. • To make the key expire after a number of seconds elapses, type seconds. Use the keylifeseconds field to set the amount of time that elapses. | seconds |
| keylifekbs <kb_integer> | This field is available when keylife-type is set to kbs or both. Set the number of KBits of data to transmit before the phase 2 key expires. The range is 5120 to 4 294 967 295 KBits. | 5120 |
| keylifeseconds <seconds> | This field is available when keylife-type is set to seconds or both. Set the number of seconds to elapse before the phase 2 key expires. seconds can be 120 to 172800 seconds. | 1800 |
| pfs {enable ¦ disable} | Optionally, enable or disable perfect forward secrecy (PFS). PFS ensures that each key created during Phase 2 is unrelated to keys created during Phase 1 or to other keys created during Phase 2. PFS may cause minor delays during key generation. | enable |
| phase1name <gateway_name> | Enter a phase 1 gateway configuration name. You must add the phase 1 gateway definition to the FortiGate configuration before it can be cross- referenced. | Null. |

Fortinet Technologies Inc.                                                                Page 792                                     FortiOS™ - CLI Reference for FortiOS 5.0

| Variable | Description | Default |
| --- | --- | --- |
| proposal <encrypt_digest> | Enter a minimum of one and a maximum of three encryption-message digest combinations (for example, 3des-md5). The remote peer must be configured to use at least one of the proposals that you define. Use a space to separate the combinations. You can enter any encryption-message digest combination except null-null. Here is an explanation of the abbreviated encryption algorithms: • null — Do not use an encryption algorithm. • des — Digital Encryption Standard, a 64-bit block algorithm that uses a 56-bit key. • 3des — Triple-DES, which encrypts data three times by three keys. • aes128 — A 128-bit block algorithm that uses a 128-bit key. • aes192—- A 128-bit block algorithm that uses a 192-bit key. • aes256 — A 128-bit block algorithm that uses a 256-bit key. • aria128 — A 128-bit Korean block algorithm that uses a 128-bit key. • aria192 — A 128-bit Korean block algorithm that uses a 192-bit key. • aria256 — A 128-bit Korean block algorithm that uses a 256-bit key. • seed — A 128-bit Korean block algorithm that uses a 128-bit key. The ARIA and seed algorithms are not available on some models. You can enter any of the following message digests to check the authenticity of messages during an encrypted session: • null — Do not use a message digest. • md5 — Message Digest 5, the hash algorithm developed by RSA Data Security. • sha1 — Secure Hash Algorithm 1, which produces a 160-bit message digest. • sha256 — Secure Hash Algorithm 2, which produces a 256-bit message digest. | aes128-sha1 3des-sha1 |
| protocol <protocol_integer> | This field is available when selector is set to specify. Enter the IP protocol number for the service. The range is 1 to 255. To specify all services, type 0. | 0 |

Fortinet Technologies Inc.                                                                Page 793                                     FortiOS™ - CLI Reference for FortiOS 5.0

| Variable | Description | Default |
| --- | --- | --- |
| replay {disable ¦ enable} | Optionally, enable or disable replay detection. Replay attacks occur when an unauthorized party intercepts a series of IPSec packets and replays them back into the tunnel. Enable replay detection to check the sequence number of every IPSec packet to see if it has been received before. If packets arrive out of sequence, the FortiGate units discards them. You can configure the FortiGate unit to send an alert email when it detects a replay packet. See “alertemail” on page 49. | enable |
| route-overlap {overlap_option} | Specify how FortiGate unit handles multiple dialup users with the same IP source address. Set overlap_option to one of the following: • allow — allow overlapping routes • use-new — delete the old route and add the new route • use-old — use the old route and do not add the new route | use-new |
| single-source {disable ¦ enable} | Enable or disable all FortiClient dialup clients to connect using the same phase 2 tunnel definition. | disable |

Fortinet Technologies Inc.                                                                Page 794                                     FortiOS™ - CLI Reference for FortiOS 5.0

| Variable | Description | Default |
| --- | --- | --- |
| src-addr-type <ip_source_name> | If the FortiGate unit is a dialup server, enter the type of source address that corresponds to the local sender(s) or network behind the FortiGate dialup server: • To specify the IPv4 IP address of a server or host, type ip. Enter the IP address using the src- start-ip field. • To specify the IPv6 IP address of a server or host, type ip6. Enter the IP address using the src- start-ip6 field. • To specify a range of IPv4 IP addresses, type range. Enter the starting and ending addresses using the src-start-ip and src-end-ip fields. • To specify a range of IPv6 IP addresses, type range6. Enter the starting and ending addresses using the src-start-ip6 and src-end-ip6 fields. • To specify an IPv4 network address, type subnet. Enter the network address using the src-subnet field. • To specify an IPv6 network address, type subnet6. Enter the network address using the src-subnet6 field. • To specify an address defined in a firewall address or address group, type name. Enter the address name using the src-name field. You must also select the name option for dst-addr-type. This is available only for IPv4 addresses. You should not use this option if ike-version is 1. IKEv1 does not support the use of multiple addresses in selectors. Instead, use the default 0.0.0.0/0 subnet selector and rely on the firewall policy to limit source addresses. If the FortiGate unit is a dialup client, src-addr-type must refer to the server(s), host(s), or private network behind the FortiGate dialup client. This field is not available if phase1name names a configuration that enables mode-cfg. | subnet |
| src-end-ip <address_ipv4> | This field is available when src-addr-type is set to range. This field is not available if phase1name names a configuration that enables mode-cfg. Enter the highest source IP address in the range of IP addresses. | 0.0.0.0 |
| src-end-ip6 <address_ipv6> | This field is available when src-addr-type is set to range6. This field is not available if phase1name names a configuration that enables mode-cfg. Enter the highest source IP address in the range of IP addresses. | :: |

Fortinet Technologies Inc.                                                                Page 795                                     FortiOS™ - CLI Reference for FortiOS 5.0

| Variable | Description | Default |
| --- | --- | --- |
| src-name <address_name> | This field is available when src-addr-type is set to name. This field is not available if phase1name names a configuration that enables mode-cfg. Enter the firewall address or address group name. |  |
| src-port <src_port_number> | If the FortiGate unit is a dialup server, enter the port number that the FortiGate dialup server uses to transport traffic related to the specified service (see protocol). If the FortiGate unit is a dialup client, enter the port number that the FortiGate dialup client uses to transport traffic related to the specified service. The src-port range is 1 to 65535. To specify all ports, type 0. This field is not available if phase1name names a configuration that enables mode-cfg. | 0 |
| src-start-ip <address_ipv4> | This field is available when src-addr-type is set to range. This field is not available if phase1name names a configuration that enables mode-cfg. Enter the lowest source IP address in the range of IP addresses. | 0.0.0.0 |
| src-start-ip6 <address_ipv6> | This field is available when src-addr-type is set to range6. This field is not available if phase1name names a configuration that enables mode-cfg. Enter the lowest source IP address in the range of IP addresses. | :: |
| src-subnet <address_ipv4mask> | If the FortiGate unit is a dialup server, enter the IPv4 IP address and network mask that identifies the private network behind the FortiGate dialup server. If the FortiGate unit is a dialup client, enter the IP address and network mask that identifies the private network behind the FortiGate dialup client. This field is not available if phase1name names a configuration that enables mode-cfg. | 0.0.0.0 0.0.0.0 |
| src-subnet6 <address_ipv6mask> | If the FortiGate unit is a dialup server, enter the IPv6 IP address and network mask that identifies the private network behind the FortiGate dialup server. If the FortiGate unit is a dialup client, enter the IP address and network mask that identifies the private network behind the FortiGate dialup client. This field is not available if phase1name names a configuration that enables mode-cfg. | ::/0 |

Fortinet Technologies Inc.                                                                Page 796                                     FortiOS™ - CLI Reference for FortiOS 5.0

l2tp

Use this command to enable L2TP and specify a local address range to reserve for remote L2TP clients. When a remote L2TP client connects to the internal network through a L2TP VPN, the client is assigned an IP address from the specified range.

L2TP clients must authenticate with the FortiGate unit when a L2TP session starts. To support L2TP authentication on the FortiGate unit, you must define the L2TP users who need access and then add them to a user group. For more information, see “user group” on page 707, “user ldap” on page 711, “user local” on page 714, and “user radius” on page 720.

You need to define a firewall policy to control services inside the L2TP tunnel. For more information, see “firewall” on page 96. When you define the firewall policy:

•  Create an “external -> internal” policy.

•  Set the source address to match the L2TP address range.

•  Set the destination address to reflect the private address range of the internal network behind the local FortiGate unit.

•  Set the policy service(s) to match the type(s) of traffic that L2TP users may generate.

•  Set the policy action to accept.

•  Enable NAT if required.

FortiGate units support L2TP with Microsoft Point-to-Point Encryption (MPPE) encryption only. Later implementations of Microsoft L2TP for Windows use IPSec and require certificates for authentication and encryption. If you want to use Microsoft L2TP with IPSec to connect to a FortiGate unit, the IPSec and certificate elements must be disabled on the remote client. For more information, see the Disabling Microsoft L2TP for IPSec article in the Fortinet Knowledge Center.

Syntax

config vpn l2tp

set eip <address_ipv4>

set sip <address_ipv4>

set status {enable | disable}

set usrgrp <group_name>

end

You can configure L2TP VPNs on FortiGate units that run in NAT/Route mode. The commands are available in NAT/Route mode only. When you configure an L2TP address range for the first time, you must enter a starting IP address, an ending IP address, and a user group.

| Variable | Description | Default |
| --- | --- | --- |
| eip <address_ipv4> | The ending IP address of the L2TP address range. | 0.0.0.0 |
| sip <address_ipv4> | The starting IP address of the L2TP address range. | 0.0.0.0 |

Fortinet Technologies Inc.                                                                Page 797                                     FortiOS™ - CLI Reference for FortiOS 5.0

| Variable | Description | Default |
| --- | --- | --- |
| status {enable ¦ disable} | Enable or disable L2TP VPN. | disable |
| usrgrp <group_name> | This field is available when status is set to enable. Enter the name of the user group for authenticating L2TP clients. The user group must be added to the FortiGate configuration before it can be specified here. For more information, see “user group” on page 707, “user ldap” on page 711, “user local” on page 714, and “user radius” on page 720. | Null |

Fortinet Technologies Inc.                                                                Page 798                                     FortiOS™ - CLI Reference for FortiOS 5.0

pptp

Use this command to enable PPTP and specify a local address range to reserve for remote PPTP clients. When a remote PPTP client connects to the internal network through a PPTP VPN, the client is assigned an IP address from the specified range or from the server defined in the PPTP user group.

PPTP clients must authenticate with the FortiGate unit when a PPTP session starts. To support PPTP authentication on the FortiGate unit, you must define the PPTP users who need access and then add them to a user group. For more information, see “user group” on page 707, “user ldap” on page 711, “user local” on page 714, “user radius” on page 720, “user peer” on

page 717, and “user peergrp” on page 719.

You need to define a firewall policy to control services inside the PPTP tunnel. For more information, see “firewall” on page 96. When you define the firewall policy:

•  Create an “external -> internal” policy.

•  Set the source address to match the PPTP address range.

•  Set the destination address to reflect the private address range of the internal network behind the local FortiGate unit.

•  Set the policy service(s) to match the type(s) of traffic that PPTP users may generate.

•  Set the policy action to accept.

•  Enable NAT if required.

When you intend to use the FortiGate unit as a PPTP gateway, you can select a PPTP client IP from a local address range or use the server defined in the PPTP user group. You select which method to use for IP address retrieval and, in the case of the user group server, provide the IP address and the user group.

The FortiGate unit retrieves the Framed-IP-Address (the actual IP address of the client) from the RADIUS accounting start/stop message when ip-mode is set to usrgrp.

Syntax

config vpn pptp

set eip <address_ipv4>

set ip-mode {range | usrgrp} set local-ip <address_localip> set sip <address_ipv4>

set status {enable | disable}

set usrgrp <group_name>

end

You can configure PPTP VPNs on FortiGate units that run in NAT/Route mode. The commands are available in NAT/Route mode only. When you configure a PPTP address range for the first time, you must enter a starting IP address, an ending IP address, and a user group.

Fortinet Technologies Inc.                                                                Page 799                                     FortiOS™ - CLI Reference for FortiOS 5.0

| Variable | Description | Default |
| --- | --- | --- |
| eip <address_ipv4> | The ending address of the PPTP address range. | 0.0.0.0 |
| ip-mode {range ¦ usrgrp} | Select one of: range — Assign user IP addresses from the IP address range of configured by sip and eip. usrgrp — Retrieve the IP address from the user group used to authenticate the user. Select the user group in usrgrp. | range |
| local-ip <address_localip> | Enter the IP address to be used for the peer’s remote IP on the PPTP client side. | 0.0.0.0 |
| sip <address_ipv4> | The starting address of the PPTP IP address range. | 0.0.0.0 |
| status {enable ¦ disable} | Enable or disable PPTP VPN. | disable |
| usrgrp <group_name> | This field is available when ip-mode is set to usrgrp. Enter the name of the user group for authenticating PPTP clients. The user group must be added to the FortiGate configuration before it can be specified here. For more information, see “user group” on page 707, “user ldap” on page 711, “user local” on page 714, “user radius” on page 720, “user peer” on page 717, and “user peergrp” on page 719 | Null |

Fortinet Technologies Inc.                                                                Page 800                                     FortiOS™ - CLI Reference for FortiOS 5.0

ssl settings

Use this command to configure basic SSL VPN settings including interface idle-timeout values and SSL encryption preferences. If required, you can also enable the use of digital certificates for authenticating remote clients.

You can optionally specify the IP address of any Domain Name Service (DNS) server and/or Windows Internet Name Service (WINS) server that resides on the private network behind the FortiGate unit. The DNS and/or WINS server will find the IP addresses of other computers whenever a connected SSL VPN user sends an email message or browses the Internet.

You can configure SSL VPNs on FortiGate units that run in NAT/Route mode. The commands are available in NAT/Route mode only.

Syntax

config vpn ssl settings

set algorithm <cipher_suite>

set allow-ssl-big-buffer {enable | disable}

set allow-ssl-client-renegotiation {enable | disable} set allow-ssl-insert-empty-fragment {enable | disable} set auth-timeout <auth_seconds>

set auto-tunnel-policy {enable | disable}

set auto-tunnel-static-route {enable | disable}

set deflate-compression-level <int>

set deflate-min-data-size <int> set dns-server1 <address_ipv4> set dns-server2 <address_ipv4> set dns-suffix <domain_str>

set force-two-factor-auth {enable | disable}

set force-utf8-login {enable | disable} set http-compression {enable | disable} set http-only-cookie {enable | disable} set idle-timeout <idle_seconds>

set port <port_int>

set port-precedence {enable | disable}

set reqclientcert {enable | disable}

set route-source-interface {enable | disable}

set servercert <server_cert_name>

set sslv2 {enable | disable}

set sslv3 {enable | disable}

set sslvpn-enable {enable | disable}

set tlsv1-0 {enable | disable} set tlsv1-1 {enable | disable} set tlsv1-2 {enable | disable}

set tunnel-ip-pools <pool1_name ...pooln_name>

set url-obscuration {enable | disable}

set wins-server1 <address_ipv4>

set wins-server2 <address_ipv4>

end

When you configure the timeout settings, if you set the authentication timeout

(auth-timeout) to 0, then the remote client does not have to re-authenticate again unless they log out of the system. In order to fully take advantage of this setting, the value for

idle-timeout has to be set to 0 also, so the client does not timeout if the maximum idle time is reached. If the idle-timeout is not set to the infinite value, the system will log out if it reaches the limit set, regardless of the auth-timeout setting.

Set the sslvpn-enable attribute to enable to view all possible settings. The

tunnel-ip-pools field is required for tunnel-mode access only. All other fields are optional.

| Variable | Description | Default |
| --- | --- | --- |
| algorithm <cipher_suite> | This field is available when sslvpn-enable is set to enable. Enter one of the following options to determine the level of SSL encryption to use. The web browser on the remote client must be capable of matching the level that you specify: • To use any cipher suite, type low. • To use a 128-bit or greater cipher suite, type default. • To use a cipher suite that is greater than 128 bits, type high. | default |
| allow-ssl-big-buffer {enable ¦ disable} | The default setting (disable) reduces memory use by 16kbytes per connection. | disable |
| allow-ssl-client- renegotiation {enable ¦ disable} | Enable or disable renegotiation if tunnel goes down. SSL renegotiation feature could be used for DOS attack. | disable |
| allow-ssl-insert-empty- fragment {enable ¦ disable} | Internet Explorer 6 and earlier might not work well with the default setting (enable). The setting can be changed, but reduces security. | enable |
| auth-timeout <auth_seconds> | This field is available when sslvpn-enable is set to enable. Enter the period of time (in seconds) to control how long an authenticated connection will remain connected. When this time expires, the system forces the remote client to authenticate again. Range is 10 to 259,200 seconds (3 days). Use the value of 0 to indicate no timeout. | 28800 |
| auto-tunnel-policy {enable ¦ disable} | Enable automatic creation of policies for SSLVPN. | enable |
| auto-tunnel-static-route {enable ¦ disable} | Enable automatic creation of static routes for SSLVPN. | enable |
| deflate-compression- level <int> | Set the compression level. Range is 1 (least compression) to 9 (most compression). Higher compression reduces the volume of data but requires more processing time. This field is available when http-compression is enabled. | 6 |
| deflate-min-data-size <int> | Set the minimum amount of data that will trigger compression. Smaller amounts are not compressed. Range is 200 to 65 535 bytes. This field is available when http-compression is enabled. | 300 |

| Variable | Description | Default |
| --- | --- | --- |
| dns-server1 <address_ipv4> | Enter the IP address of the primary DNS server that SSL VPN clients will be able to access after a connection has been established. If required, you can specify a secondary DNS server through the dns-server2 attribute. | 0.0.0.0 |
| dns-server2 <address_ipv4> | Enter the IP address of a secondary DNS server if required. | 0.0.0.0 |
| dns-suffix <domain_str> | Enter the DNS suffix. Maximum length 253 characters. | null |
| force-two-factor-auth {enable ¦ disable} | Enable to require PKI (peer) users to authenticate by password in addition to certificate authentication. If this is enabled, only PKI users with two-factor authentication enabled will be able to log on to the SSL VPN. | disable |
| force-utf8-login {enable ¦ disable} | Enable to use UTF-8 encoding for the login page. This might be necessary when using LDAP to authenticate users. | disable |
| http-compression {enable ¦ disable} | Enable use of compression between the FortiGate unit and the client web browser. You can adjust the fields deflate-compression-level and deflate-min-data-size to tune performance. | disable |
| http-only-cookie {enable ¦ disable} | Disable only if a web site is having trouble with the tunnel mode Java Applet. | enable |
| idle-timeout <idle_seconds> | This field is available when sslvpn-enable is set to enable. Enter the period of time (in seconds) to control how long the connection can remain idle before the system forces the remote user to log in again. The range is from 10 to 259 200 seconds. Use the value of 0 to indicate no timeout. | 300 |
| port <port_int> | Enter the SSL VPN access port. Range 1 - 65 535. The port is usable only when sslvpn-enable is set to enable. When vdoms are enabled, this setting is per VDOM. | 10443 |
| port-precedence {enable ¦ disable} | Enable to give SSLVPN higher priority than HTTPS if both are enabled on the same port. | enable |
| reqclientcert {enable ¦ disable} | This field is available when sslvpn-enable is set to enable. Disable or enable the use of group certificates for authenticating remote clients. | disable |
| route-source-interface {enable ¦ disable} | This field is available when sslvpn-enable is set to enable. Enable to allow the SSL VPN connection to bypass routing and bind to the incoming interface. | disable |

Fortinet Technologies Inc.                                                                Page 803                                     FortiOS™ - CLI Reference for FortiOS 5.0

| Variable | Description | Default |
| --- | --- | --- |
| servercert <server_cert_name> | This field is available when sslvpn-enable is set to enable. Enter the name of the signed server certificate that the FortiGate unit will use to identify itself during the SSL handshake with a web browser when the web browser connects to the login page. The server certificate must already be loaded into the FortiGate configuration. If you do not specify a server certificate, the FortiGate unit offers its factory installed (self-signed) certificate from Fortinet to remote clients when they connect. | self-sign |
| sslv2 {enable ¦ disable} | This field is available when sslvpn-enable is set to enable. Disable or enable SSL version 2 encryption. | disable |
| sslv3 {enable ¦ disable} | This field is available when sslvpn-enable is set to enable. Disable or enable SSL version 3 encryption. | enable |
| sslvpn-enable {enable ¦ disable} | Disable or enable remote-client access. | disable |
| tlsv1-0 {enable ¦ disable} | Enable or disable TLS 1.0 cryptographic protocol. | enable |
| tlsv1-1 {enable ¦ disable} | Enable or disable TLS 1.1 cryptographic protocol. | enable |
| tlsv1-2 {enable ¦ disable} | Enable or disable TLS 1.2 cryptographic protocol. | enable |
| tunnel-ip-pools <pool1_name ...pooln_name> | Enter the firewall addresses that represent the ranges of IP addresses reserved for remote clients. This field is available when sslvpn-enable is set to enable. | No default. |
| url-obscuration {enable ¦ disable} | This field is available when sslvpn-enable is set to enable. Enable to encrypt the host name of the url in the display (web address) of the browser for web mode only. This is a requirement for ICSA ssl vpn certification. Also, if enabled, bookmark details are not visible (field is blank.). | disable |
| wins-server1 <address_ipv4> | Enter the IP address of the primary WINS server that SSL VPN clients will be able to access after a connection has been established. If required, you can specify a secondary WINS server through the wins-server2 attribute. | 0.0.0.0 |
| wins-server2 <address_ipv4> | Enter the IP address of a secondary WINS server if required. | 0.0.0.0 |

Fortinet Technologies Inc.                                                                Page 804                                     FortiOS™ - CLI Reference for FortiOS 5.0

ssl web  host-check-software

Use this command to define security software for selection in the host-check-policy field of the vpn ssl web portal command.

Syntax

config vpn ssl web host-check-software edit <software_name>

set guid <guid>

set type {av | fw}}

set version <version_str>

config check-item-list edit <id_int>

set action {deny | require}

set md5s <md5_str>

set target {file | process | registry} set type {file | process | registry} set version <version-str>

end

end

| Variable | Description | Default |
| --- | --- | --- |
| <software_name> | Enter a name to identify the software. The name does not need to match the actual application name. |  |
| set guid <guid> | Enter the globally unique identifier (GUID) for the host check application. The GUID is usually in the form xxxxxxxx-xxxx-xxxx-xxxx-xxxxxxxxxxx, where each x is a hexadecimal digit. Windows uses GUIDs to identify applications in the Windows Registry. | No default. |
| set type {av ¦ fw}} | Select the software type: antivirus (av) or firewall (fw). If the software does both, create two entries, one where type is av and one where type is fw. | av |
| set version <version_str> | Enter the software version. | No default. |
| check-item-list variables |
| <id_int> | Enter an ID number for this entry. |  |
| set action {deny ¦ require} | Select one of require — If the item is found, the client meets the check item condition. deny — If the item is found, the client is considered to not meet the check item condition. Use this option if it is necessary to prevent use of a particular security product. | require |
| set md5s <md5_str> | If type is file or process, enter one or more known MD5 signatures for the application executable file.You can use a third-party utility to calculate MD5 signatures or hashes for any file. You can enter multiple signatures to match multiple versions of the application. |  |

Fortinet Technologies Inc.                                                                Page 805                                     FortiOS™ - CLI Reference for FortiOS 5.0

| Variable | Description | Default |
| --- | --- | --- |
| set target {file ¦ process ¦ registry} | Enter information as follows: If type is file, enter the full path to the file. If type is process, enter the application’s executable file name. If type is registry, enter the registry item. | No default. |
| set type {file ¦ process ¦ registry} | Select how to check for the application: • file — Look for a file. This could be the application’s executable file or any other file that would confirm the presence of the application. Set target to the full path to the file. Where applicable, you can use environment variables enclosed in percent (%) marks. For example, %ProgramFiles%\Fortinet\FortiClient\Fo rtiClient.exe. • process — Look for the application as a running process. Set target to the application’s executable file name. • registry — Search for a Windows Registry entry. Set target to the registry item, for example HKLM\SOFTWARE\Fortinet\FortiClient\Mis c. | file |
| set version <version-str> | Enter the version of the application. | No default. |

Fortinet Technologies Inc.                                                                Page 806                                     FortiOS™ - CLI Reference for FortiOS 5.0

ssl web  portal

The SSL VPN Service portal allows you to access network resources through a secure channel using a web browser. FortiGate administrators can configure log in privileges for system users and which network resources are available to the users, such as HTTP/HTTPS, telnet, FTP, SMB/CIFS, VNC, RDP and SSH.

The portal configuration determines what the system user sees when they log in to the FortiGate. Both the system administrator and the system user have the ability to customize the SSL VPN portal.

There are three pre-defined default web portal configurations available:

•  full-access: Includes all widgets available to the user - Session Information, Connection Tool,

Bookmarks, and Tunnel Mode.

•  tunnel-access: Includes Session Information and Tunnel Mode widgets.

•  web-access: Includes Session Information and Bookmarks widgets.

These pre-defined portal configurations can be edited, including their names.

Syntax

config vpn ssl web portal edit <portal_name>

set allow-access <allow_access>

set allow-user-bookmark {enable | disable}

set auto-prompt-mobile-user {enable | disable}

set cache-cleaner {enable | disable}

set heading <str_heading>

set host-check {av | av-fw | custom | fw | none}

set host-check-interval <seconds>

set host-check-policy <hcpolicy_name>

set limit-user-logins {enable | disable}

set mac-addr-action {allow | deny

set mac-addr-check {enable | disable}

set os-check {enable | disable}

set page-layout <double-column | single-column>

set redir-url <redir_url>

set skip-check-for-unsupported-browser {enable | disable}

set skip-check-for-unsupported-os {enable | disable}

set theme {blue | gray | orange}

set virtual-desktop {enable | disable}

set virtual-desktop-app-list <applist_name>

set virtual-desktop-clipboard-share {enable | disable} set virtual-desktop-desktop-switch {enable | disable} set virtual-desktop-logout-when-browser-close

{enable | disable}

set virtual-desktop-network-share-access {enable | disable}

set virtual-desktop-printing {enable | disable}

set virtual-desktop-removable-media-access {enable | disable}

config mac-addr-check-rule edit <rule_name>

set mac-addr-list <mac_list>

set mac-addr-mask <int>

end

config os-check-list {windows-2000 | windows-vista | windows-xp

| windows-7 | windows-8}

set action {allow | check-up-to-date | deny} set latest-patch-level {disable | 0 - 255} set tolerance {tolerance_num}

end

config widget

edit id <widget_id>

set name <name_str>

set type <widget_type>

set auto-connect {enable | disable}

set column <column_number>

set collapse {enable | disable}

set dns-server1 <ip4_addr>

set dns-server2 <ip4_addr>

set allow-apps <service_type_access>

set exclusive-routing {enable | disable}

set ip-mode {range | usrgrp}

set ip-pools {<pool1_name> .. <pooln_name>}

set ipv6-dns-server1 <ip6_addr> set ipv6-dns-server2 <ip6_addr> set ipv6-wins-server1 <ip6_addr> set ipv6-wins-server2 <ip6_addr> set keep-alive {enable | disable}

set save-password {enable | disable}

set split-tunneling {enable | disable}

set split-tunneling-routing-address <address_name>

set wins-server1 <ip4_addr> set wins-server2 <ip4_addr> config bookmarks

edit <bookmark_name>

set additional-params <param_str>

set apptype <service_type>

set url <target_ip>

set host <host_name>

set folder <folder_name>

set description <description_txt>

set full-screen-mode {enable | disable}

set keyboard-layout <locale_str>

set listening-port <port_int>

set logon-user <user-name_str>

set logon-password <password_str>

set remote-port <port_int>

set screen-height <h_int>

end

set screen-width <w_int>

set show-status-window {enable | disable}

set sso {disable | auto}

set sso-credential {sslvpn-login | alternative)

set sso-password <pwd_str>

set sso-username <name_str>

end end

end end

| Variable | Description | Default |
| --- | --- | --- |
| edit <portal_name_str> | Enter a name for the portal. Three pre-defined web portal configurations exist: full-access, tunnel-access, and web- access. | No default. |
| allow-access <allow_access> | Enter a list of the applications allowed in this portal. Separate entries with spaces. Application names are: • citrix for Citrix web server interface • ftp for FTP services. • ping for pinging hosts. • portforward for port forwarding. • rdp for Windows Terminal services. • rdpnative for remote desktop access with native client. • smb for SMB/CIFS (Windows file share) services. • ssh for SSH services. • telnet for telnet services. • vnc for VNC services. • web for HTTP and/or HTTPS services. | No default. |
| allow-user-bookmark {enable ¦ disable} | Allow web portal users to create their own bookmarks. | enable |
| auto-prompt-mobile-user {enable ¦ disable} | Enable to prompt mobile users to download FortiClient Endpoint Security. | enable |
| cache-cleaner {enable ¦ disable} | Enable the FortiGate unit to remove residual information from the remote client computer just before the SSL VPN session ends. This is done with a downloaded ActiveX control or | disable |
| heading <str_heading> | Enter the caption that appears at the top of the web portal home page. | null |

| Variable | Description | Default |
| --- | --- | --- |
| host-check {av ¦ av-fw ¦ custom ¦ fw ¦ none} | Select the type of host checking to perform on endpoints: av — Check for antivirus software recognized by the Windows Security Center. av-fw — Check for both antivirus and firewall software recognized by the Windows Security Center. custom — Check for the software defined in host-check-policy. fw — Check for firewall software recognized by the Windows Security Center. none — Do not perform host checking. | none |
| host-check-interval <seconds> | Enter how often to recheck the host. Range is every 120 seconds to 259 200 seconds. Enter 0 to not recheck the host during the session. This is not available if host-check is none. | 0 |
| host-check-policy <hcpolicy_name> | Select the specific host check software to look for. These applications are defined in the vpn ssl web host-check-software command. This field is available when host-check is custom. | null |
| limit-user-logins {enable ¦ disable} | Enable to allow each user one SSL VPN session at a time. | disable |
| mac-addr-action {allow ¦ deny | Set action for MAC address check: allow or deny connection. | allow |
| mac-addr-check {enable ¦ disable} | Enable or disable MAC address host check. | disable |
| os-check {enable ¦ disable} | Enable the FortiGate unit to determine what action to take depending on what operating system the client has. | disable |
| page-layout <double-column ¦ single-column> | Select the number of columns in the portal display. | single-column |
| redir-url <redir_url> | Enter the URL of the web page which will enable the FortiGate unit to display a second HTML page in a popup window when the web portal home page is displayed. The web server for this URL must reside on the private network behind the FortiGate unit. | null |
| skip-check-for- unsupported-browser {enable ¦ disable} | Skip the host check if the browser doesn’t support it. This field is available if host checking is enabled. | enable |
| skip-check-for- unsupported-os {enable ¦ disable} | Skip the host check if the client operating system doesn’t support it. This field is available if host checking is enabled. | enable |
| theme {blue ¦ gray ¦ orange} | Select the portal display theme (color). | blue |
| virtual-desktop {enable ¦ disable} | Enable the SSL VPN virtual desktop client application. If set to enable on the client, attempts to connect via SSL VPN are refused. | disable |

Fortinet Technologies Inc.                                                                Page 810                                     FortiOS™ - CLI Reference for FortiOS 5.0

| Variable | Description | Default |
| --- | --- | --- |
| virtual-desktop-app-list <applist_name> | Enter the name of the application list to apply to the virtual desktop. See vpn ssl web virtual-desktop- app-list. | Null |
| virtual-desktop-clipboard- share {enable ¦ disable} | Enable or disable sharing of the clipboard with the regular desktop. | disable |
| virtual-desktop-desktop- switch {enable ¦ disable} | Enable or disable switching between virtual and regular desktop. | disable |
| virtual-desktop-logout- when-browser-close {enable ¦ disable} | Enable or disable automatic logout from virtual desktop when browser is closed. | disable |
| virtual-desktop-network- share-access {enable ¦ disable} | Enable or disable network share access from the virtual desktop. | disable |
| virtual-desktop-printing {enable ¦ disable} | Enable or disable printing from the virtual desktop. | disable |
| virtual-desktop-removable- media-access {enable ¦ disable} | Enable or disable accessing removable media such as USB drives from the virtual desktop. | disable |
| config mac-addr-check-rule variables |
| edit <rule_name> | Enter a name for this MAC check rule. |  |
| mac-addr-list <mac_list> | Enter client MAC addresses. | No default. |
| mac-addr-mask <int> | Set the size of the netmask in bits. Range 1-48. | 48 |
| config os-check-list variables Available when set os-check is set to check-up-to-date. |
| action {allow ¦ check-up-to-date ¦ deny} | Specify how to perform the patch level check. • allow - any level is permitted • check-up-to-date - some patch levels are permitted, make selections for latest-patch- level and tolerance • deny - do not permit access for any version of this OS | allow |
| latest-patch-level {disable ¦ 0 - 255} | Specify the latest allowed patch level. Available when action is set to enable. | Win2000: 4 WinXP: 2 |
| tolerance {tolerance_num} | Specify the lowest allowable patch level tolerance. Equals latest-patch-level minus tolerance and above. Available when action is check-up-to-date. | 0 |
| Widget variables |  |  |
| id <widget_id> | Enter the unique ID number of the widget. | No default. |
| name <name_str> | Enter the name for the widget. Maximum 36 characters. | null |
| type <widget_type> | Enter the type of widget: bookmark, forticlient-download, history, info, tool or tunnel. | bookmark |
| auto-connect {enable ¦ disable} | Enable or disable FortiClient automatic connection to this portal. | disable |

Fortinet Technologies Inc.                                                                Page 811                                     FortiOS™ - CLI Reference for FortiOS 5.0

| Variable | Description | Default |
| --- | --- | --- |
| column <column_number> | Enter the number of columns in the widget display: one or two. This is available if page-layout is double- column. | one |
| collapse {enable ¦ disable} | Enable the widget to expand in the web portal view. Allows user to make changes to the widget view/configuration. | disable |
| dns-server1 <ip4_addr> dns-server2 <ip4_addr> | Specify primary and secondary DNS servers. This is available if type is tunnel. | 0.0.0.0 0.0.0.0 |
| allow-apps <service_type_access> | If type is bookmark, select the types of bookmarks the user can create. If type is tool, select the types of services that the user can access with this widget. Separate entries with spaces. • citrix for Citrix web server interface • ftp for FTP services • ping for pinging hosts (tool only) • portforward for port forwarding • rdp for Windows Terminal services • rdpnative for remote desktop access with native client • smb for SMB/CIFS (Windows file share) services • ssh for SSH services • telnet for telnet services • vnc for VNC services • web for HTTP and/or HTTPS services | No default. |
| exclusive-routing {enable ¦ disable} | Enable to force traffic between the client and the client’s local network to pass through the SSL VPN tunnel. This can enhance security. By default, an SSL VPN with split-tunneling disabled does not affect traffic between the client and the client’s local network, even though all other traffic is routed through the SSL VPN tunnel. exclusive-routing is available only when split-tunneling is disabled. | disable |
| ip-mode {range ¦ usrgrp} | Select the mode by which the IP address is assigned to the user: Available only if tunnel-status is enabled. | range |
| ip-pools {<pool1_name> .. <pooln_name>} | Enter the names of the IP pools (firewall addresses) that represent IP address ranges reserved for tunnel-mode SSL VPN clients. This is available only if tunnel-status is enabled. |  |

Fortinet Technologies Inc.                                                                Page 812                                     FortiOS™ - CLI Reference for FortiOS 5.0

| Variable | Description | Default |
| --- | --- | --- |
| ipv6-dns-server1 <ip6_addr> ipv6-dns-server2 <ip6_addr> | Specify primary and secondary IPv6 DNS servers. This is available if type is tunnel. | :: :: |
| ipv6-wins-server1 <ip6_addr> ipv6-wins-server2 <ip6_addr> | Specify primary and secondary IPv6 WINS servers. This is available if type is tunnel. | :: :: |
| keep-alive {enable ¦ disable} | Enable or disable keepalive (automatic reconnect) for FortiClient connections to this portal. |  |
| save-password {enable ¦ disable} | Enable or disable FortiClient saving of user password. | disable |
| split-tunneling {enable ¦ disable} | Enable split tunneling. Split tunneling ensures that only the traffic for the private network is sent to the SSL VPN gateway. Internet traffic is sent through the usual unencrypted route. Available only if tunnel-status is enabled. | disable |
| split-tunneling-routing- address <address_name> | Enter the firewall addresses for the destinations that clients will reach through the SSL VPN. The client’s split-tunneling configuration will ensure that the tunnel is used for these destinations only. This is available when split-tunneling is enabled. | No default. |
| wins-server1 <ip4_addr> wins-server2 <ip4_addr> | Specify primary and secondary WINS servers. This is available if type is tunnel. | 0.0.0.0 0.0.0.0 |

Fortinet Technologies Inc.                                                                Page 813                                     FortiOS™ - CLI Reference for FortiOS 5.0

| Variable | Description | Default |
| --- | --- | --- |
| Bookmarks variables Note: config bookmarks is available only when widget type is bookmark. |
| <bookmark_name> | Enter the unique name of the bookmark. Maximum 36 characters. | null |
| additional-params <param_str> | Enter additional parameters the application requires. Available when apptype is citrix, portforward, rdp, or rdpnative. |  |
| apptype <service_type> | Enter the identifier of the service to associate with the bookmark: • Type citrix for Citrix web server interface. • Type ftp for FTP services. • Type portforward for port forwarding. • Type rdp for Windows Terminal services. • Type rdpnative for remote desktop access with native client. • Type smb for SMB/CIFS (Windows file share) services. • Type ssh for SSH services. • Type telnet for telnet services. • Type vnc for VNC services. • Type web for HTTP and/or HTTPS services. | web |
| url <target_ip> | Enter the URL of the web page, if apptype is web or citrix. | No default. |
| host <host_name> | Enter the host name, if apptype is telnet or rdp. Maximum 36 characters. | No default. |
| folder <folder_name> | Enter the remote folder name, if apptype is smb or ftp. The folder name must include the server name, //172.20.120.103/myfolder, for example. | No default. |
| description <description_txt> | Enter a description of the bookmark. Maximum 129 characters. | null |
| full-screen-mode {enable ¦ disable} | Enable or disable full-screen mode. Available when apptype is rdp or rdpnative. | disable |
| keyboard-layout <locale_str> | Enter the keyboard layout for the RDP session. Available when apptype is rdp. | en-us |
| listening-port <port_int> | Enter the listening port number. Available when apptype is portforward. | null |
| logon-user <user-name_str> logon-password <password_str> | Enter the logon credentials for the RDP bookmark. Available when apptype is rdp. | null |
| remote-port <port_int> | Enter the remote port number. Available when apptype is portforward. | null |

Fortinet Technologies Inc.                                                                Page 814                                     FortiOS™ - CLI Reference for FortiOS 5.0

| Variable | Description | Default |
| --- | --- | --- |
| screen-height <h_int> | Enter screen height in pixels. Available when apptype is rdp or rdpnative. | 768 |
| screen-width <w_int> | Enter screen width in pixels. Available when apptype is rdp or rdpnative. | 1024 |
| show-status-window {enable ¦ disable} | Enable or disable the status window. Available when apptype is portforward. | disable |
| sso {disable ¦ auto} | A Single Sign-On (SSO) bookmark automatically enters the login credentials for the bookmark destination. Select one of: disable — This is not an SSO bookmark. auto — SSO bookmark, configure sso-credential. | disable |
| sso-credential {sslvpn-login ¦ alternative) | Select whether the bookmark enters the user’s SSL VPN credentials or alternative credentials defined in sso-username and sso-password. | sslvpn-login |
| sso-password <pwd_str> | Enter alternative password. Available when sso-credential is alternative. | No default. |
| sso-username <name_str> | Enter alternative username. Available when sso-credential is alternative. | No default. |

Fortinet Technologies Inc.                                                                Page 815                                     FortiOS™ - CLI Reference for FortiOS 5.0

ssl web  realm

Use this command to configure SSL VPN realms.

Syntax

config vpn ssl web realm edit <url-path>

set login-page <content_str> set max-concurrent-user <int> set virtual-host <hostname_str>

end end

| Variable | Description | Default |
| --- | --- | --- |
| edit <url-path> | Enter the URL path to access the SSL-VPN login page. Do not include “http://”. | No default. |
| login-page <content_str> | Enter replacement HTML for SSL-VPN login page. | No default. |
| max-concurrent-user <int> | Enter the maximum number of concurrent users allowed. Range 0-65 535. 0 means unlimited. | 0 |
| virtual-host <hostname_str> | Enter the virtual host name for this realm. Optional. Maximum length 255 characters. | No default. |

ssl web  user

Use this command to configure SSL VPN users and their bookmarks.

Syntax

config vpn ssl web user edit <user_name>

config widget

edit <widget_id>

config bookmarks

edit <bookmark_name>

set apptype <service_type>

set description <description_txt>

set sso {disable | auto}

set sso-credential {sslvpn-login | alternative)

set sso-password <pwd_str> set sso-username <name_str> set url <url_str>

config form-data edit <id_int>

set name <fieldname_str>

set value <value_str>

end end

| Variable | Description | Default |
| --- | --- | --- |
| <user_name> | Enter a name for the user. |  |
| apptype <service_type> | Enter the identifier of the service to associate with the bookmark: • Type citrix for Citrix web server interface. • Type ftp for FTP services. • Type portforward for port forwarding. • Type rdp for Windows Terminal services. • Type rdpnative for remote desktop access with native client. • Type smb for SMB/CIFS (Windows file share) services. • Type ssh for SSH services. • Type telnet for telnet services. • Type vnc for VNC services. • Type web for HTTP and/or HTTPS services. | web |
| description <description_txt> | Enter a description of the bookmark. Maximum 129 characters. | null |

| Variable | Description | Default |
| --- | --- | --- |
| sso {disable ¦ auto} | A Single Sign-On (SSO) bookmark automatically enters the login credentials for the bookmark destination. Select one of: disable — This is not an SSO bookmark. auto — SSO bookmark, configure sso-credential. static — SSO bookmark with form data. | disable |
| sso-credential {sslvpn-login ¦ alternative) | Select whether the bookmark enters the user’s SSL VPN credentials or alternative credentials defined in sso-username and sso-password. | sslvpn-login |
| sso-password <pwd_str> | Enter alternative password. Available when sso-credential is alternative. | No default. |
| sso-username <name_str> | Enter alternative username. Available when sso-credential is alternative. | No default. |
| url <url_str> | Enter the URL for this bookmark. | No default. |
| config form-data variables These fields are available when sso is static. |
| edit <id_int> | Enter an identifier. |  |
| name <fieldname_str> | Enter a required login page field name, “User Name” for example. | No default. |
| value <value_str> | Enter the value to enter in the field identified by name. If you are an administrator configuring a bookmark for users: • Enter %usrname% to represent the user’s SSL VPN user name. Enter %passwd% to represent the user’s SSL VPN password. | No default. |

Fortinet Technologies Inc.                                                                Page 818                                     FortiOS™ - CLI Reference for FortiOS 5.0

ssl web  virtual-desktop-app-list

Use this command to create a list of either allowed or blocked applications which you then select when you configure the virtual desktop.

Syntax

config vpn ssl web virtual-desktop-app-list edit <applist_name>

set set action {allow | block}

config apps

edit <app_name>

set md5s <md5_str>

end end

end

| Variable | Description | Default |
| --- | --- | --- |
| <applist_name> | Enter a name for the application control list. |  |
| set action {allow ¦ block} | Set the action for this application control list: allow — Allow the applications on this list and block all others. block — Block the applications on this list and allow all others | allow |
| <app_name> | Enter the name of the application to be added to the application control list. This can be any name and does not have to match the official name of the application. |  |
| set md5s <md5_str> | Enter one or more known MD5 signatures (space-separated) for the application executable file.You can use a third-party utility to calculate MD5 signatures or hashes for any file. You can enter multiple signatures to match multiple versions of the application. | No default. |

Fortinet Technologies Inc.                                                                Page 819                                     FortiOS™ - CLI Reference for FortiOS 5.0

wanopt

Use these commands to configure FortiGate WAN optimization.

auth-group peer

profile

settings ssl-server storage

webcache

Page 820

auth-group

Use this command to configure WAN optimization authentication groups. Add authentication groups to support authentication and secure tunneling between WAN optimization peers.

Syntax

config wanopt auth-group edit <auth_group_name>

set auth-method {cert | psk} set cert <certificate_name> set peer <peer_host_id>

set peer-accept {any | defined | one}

set psk <preshared_key>

end

| Variable | Description | Default |
| --- | --- | --- |
| edit <auth_group_name> | Enter a name for the authentication group. |  |
| auth-method {cert ¦ psk} | Specify the authentication method for the authentication group. Enter cert to authenticate using a certificate. Enter psk to authenticate using a preshared key. | cert |
| cert <certificate_name> | If auth-method is set to cert, select the local certificate to be used by the peers in this authentication group. The certificate must be a local certificate added to the FortiGate unit using the config vpn certificate local command. For more information, see “vpn certificate local” on page 745. |  |
| peer <peer_host_id> | If peer-method is set to one select the name of one peer to add to this authentication group. The peer must have been added to the FortiGate unit using the config wanopt peer command. |  |
| peer-accept {any ¦ defined ¦ one} | Specify whether the authentication group can be used for any peer, only the defined peers that have been added to the FortiGate unit configuration, or just one peer. If you specify one use the peer field to add the name of the peer to the authentication group. | any |
| psk <preshared_key> | If auth-method is set to psk enter a preshared key to be used for the authentication group. |  |

peer

Add WAN optimization peers to a FortiGate unit to identify the FortiGate units that the local FortiGate unit can form WAN optimization tunnels with. A peer consists of a peer name, which is the local host ID of the remote FortiGate unit and an IP address, which is the IP address of the interface that the remote FortiGate unit uses to connect to the local FortiGate unit.

Use the command config wanopt settings to add the local host ID to a FortiGate unit.

Syntax

config wanopt peer edit <peer_name>

set ip <peer_ip_ipv4>

end

| Variable | Description | Default |
| --- | --- | --- |
| edit <peer_name> | Add the local host ID of the remote FortiGate unit. When the remote FortiGate unit connects to the local FortiGate unit to start a WAN optimization tunnel, the WAN optimization setup request include the remote FortiGate unit local host ID. If the local host ID in the setup request matches a peer added to the local FortiGate unit, then the local FortiGate unit can accept WAN optimization tunnel setup requests from the remote FortiGate unit. |  |
| ip <peer_ip_ipv4> | Enter the IP address of the interface that the remote FortiGate unit uses to connect to the local FortiGate unit. Usually this would be the IP address of the interface connected to the WAN. | 0.0.0.0 |

profile

WAN optimization uses profiles to select traffic to be optimized. But, before WAN optimization can accept traffic, the traffic must be accepted by a FortiGate firewall policy. All sessions accepted by a firewall policy that also match a WAN optimization profile are processed by WAN optimization.

To configure WAN optimization you add WAN optimization profiles to the FortiGate units at each end of the tunnel. Firewall policies use the specified WAN optimization profile to determine how to optimize the traffic over the WAN.

The FortiGate unit applies firewall policies to packets before WAN optimization profiles. A WAN

optimization profile is applied to a packet only after the packet is accepted by a firewall policy.

Syntax

config wanopt profile edit <name_str>

set auth-group <auth_group_name> set transparent {enable | disable} config {cifs | ftp | http | mapi | tcp}

set byte-caching {enable | disable}

set byte-caching-opt {mem-only | mem-disk}

set log-traffic {enable | disable}

set port <port_int>[-<port-int>]

set prefer-chunking {fix | dynamic} set secure-tunnel {enable | disable} set ssl {enable | disable}

set status {enable | disable}

set tunnel-non-http {enable | disable}

set tunnel-sharing {express-shared | private | shared}

set unknown-http-version {best-effort | reject | tunnel}

end

| Variable | Description | Default |
| --- | --- | --- |
| edit <name_str> | Enter a name for this profile. |  |
| auth-group <auth_group_name> | Select an authentication group to be used by this profile. Select an authentication group if you want the client and server FortiGate units that use this profile to authenticate with each other before starting a WAN optimization tunnel. You must add the same authentication group to the client and server FortiGate units. The authentication group should have the same name of both FortiGate units and use the same pre- shared key or the same certificate. You can add an authentication group to profiles with auto-detect set to off or active. An authentication group is required if you enable secure-tunnel for the profile. |  |

| Variable | Description | Default |
| --- | --- | --- |
| transparent {enable ¦ disable} | Enable or disable transparent mode for this profile. If you enable transparent mode, WAN optimization keeps the original source address of the packets, so servers appear to receive traffic directly from clients. Routing on the server network should be able to route traffic with client IP addresses to the FortiGate unit. If you do not select transparent mode, the source address of the packets received by servers is changed to the address of the FortiGate unit interface. So servers appear to receive packets from the FortiGate unit. Routing on the server network is simpler in this case because client addresses are not involved, but the server sees all traffic as coming from the FortiGate unit and not from individual clients. | enable |
| config {cifs ¦ ftp ¦ http ¦ mapi ¦ tcp} fields |
| byte-caching {enable ¦ disable} | Enable or disable WAN optimization byte caching for the traffic accepted by this profile. Byte caching is a WAN optimization technique that reduces the amount of data that has to be transmitted across a WAN by caching file data to serve it later as required. Byte caching is available for all protocols. | For TCP, disable For all others, enable |
| byte-caching-opt {mem-only ¦ mem-disk} | Select whether byte-caching optimization uses only memory or both memory and disk. This is available for TCP only. | mem-only |
| log-traffic {enable ¦ disable} | Enable of disable traffic logging. | enable |
| port <port_int>[-<port-int>] | Enter a single port number or port number range for the profile. Only packets whose destination port number matches this port number or port number range will be accepted by and subject to this profile. | 0 |
| prefer-chunking {fix ¦ dynamic} | Select dynamic or fixed data chunking. Dynamic data chunking helps to detect persistent data chunks in a changed file or in an embedded unknown protocol. prefer-chunking is not available for TCP and MAPI. For TCP, if byte-caching-opt is mem-disk, chunking algorithm will be dynamic. For MAPI, only dynamic is used. For other protocols, fix is the default. | Depends on protocol. |

Fortinet Technologies Inc.                                                                Page 824                                     FortiOS™ - CLI Reference for FortiOS 5.0

| Variable | Description | Default |
| --- | --- | --- |
| secure-tunnel {enable ¦ disable} | Enable or disable using AES-128bit-CBC SSL to encrypt and secure the traffic in the WAN optimization tunnel. The FortiGate units use FortiASIC acceleration to accelerate SSL decryption and encryption of the secure tunnel. The secure tunnel uses the same TCP port as a non-secure tunnel (TCP port 7810). You can configure secure-tunnel if auto- detect is set to active or off. If you enable secure-tunnel you must also add an auth- group to the profile. | disable |
| ssl {enable ¦ disable} | Enable or disable applying SSL offloading for HTTPS traffic. You use SSL offloading to offload SSL encryption and decryption from one or more HTTP servers. If you enable ssl, you should configure the profile to accept SSL-encrypted traffic, usually by configuring the profile to accept HTTPS traffic by setting port to 443. If you enable SSL you must also use the config wanopt ssl-server command to add an SSL server for each HTTP server that you wan to offload SSL encryption/decryption for. See “wanopt ssl-server” on page 828. You can configure ssl if auto-detect is set to active or off. | disable |
| status {enable ¦ disable} | Enable or disable the profile. | enable |
| tunnel-non-http {enable ¦ disable} | Configure how to process non-HTTP traffic when a profile configured to accept and optimize HTTP traffic accepts a non-HTTP session. This can occur if an application sends non-HTTP traffic using an HTTP destination port. Select disable to drop or tear down non-HTTP sessions accepted by the profile. Select enable to pass non-HTTP sessions through the tunnel without applying protocol optimization, byte-caching, or web caching. TCP protocol optimization is applied to non-HTTP sessions. You can configure tunnel-non-http if proto is set to http and auto-detect is set to active or off. | disable |

Fortinet Technologies Inc.                                                                Page 825                                     FortiOS™ - CLI Reference for FortiOS 5.0

| Variable | Description | Default |
| --- | --- | --- |
| tunnel-sharing {express-shared ¦ private ¦ shared} | Select the tunnel sharing mode for this profile: Select express-shared for profiles that accept interactive protocols such as Telnet. Select private for profiles that accept aggressive protocols such as HTTP and FTP so that these aggressive protocols do not share tunnels with less-aggressive protocols. Select shared for profiles that accept non- aggressive and non-interactive protocols. You can configure tunnel sharing if proto is set to http and auto-detect is set to off. | private |
| unknown-http-version {best-effort ¦ reject ¦ tunnel} | Unknown HTTP sessions are HTTP sessions that don’t comply with HTTP 0.9, 1.0, or 1.1. Configure unknown-http-version to specify how a profile handles HTTP traffic that does not comply with HTTP 0.9, 1.0, or 1.1. Select best-effort to assume all HTTP sessions accepted by the profile comply with HTTP 0.9, 1.0, or 1.1. If a session uses a different HTTP version, WAN optimization may not parse it correctly. As a result the FortiGate unit may stop forwarding the session and the connection may be lost. Select reject to reject or tear down HTTP sessions that do not use HTTP 0.9, 1.0, or 1.1. Select tunnel to pass HTTP traffic that does not use HTTP 0.9, 1.0, or 1.1 without applying HTTP protocol optimization, byte-caching, or web caching. TCP protocol optimization is applied to this HTTP traffic. You can configure unknown-http-version if proto is set to http and auto-detect is set to active or off. | tunnel |

Fortinet Technologies Inc.                                                                Page 826                                     FortiOS™ - CLI Reference for FortiOS 5.0

settings

Use this command to add or change the FortiGate WAN optimization local host ID and to enable traffic logging for WAN optimization and WAN optimization web caching sessions. The local host ID identifies the FortiGate unit to other FortiGate units for WAN optimization. All WAN optimization tunnel startup requests to other FortiGate units include the local host id. The FortiGate unit can only perform WAN optimization with other FortiGate units that have this local host id in their peer list.

Syntax

config wanopt settings

set host-id <host-id-name_str>

set log-traffic {cifs ftp http mapi tcp}

set tunnel-ssl-algorithm {high | medium | low}

end

| Variable | Description | Default |
| --- | --- | --- |
| host-id <host-id-name_str> | Enter the local host ID. | default-id |
| log-traffic {cifs ftp http mapi tcp} | Enable WAN optimization and WAN optimization web caching traffic logging for each type of WAN optimization session. Valid types are: cifs ftp http mapi tcp. Separate each type with a space. To add or remove an option from the list, retype the complete list as required. |  |
| tunnel-ssl-algorithm {high ¦ medium ¦ low} | Select the relative strength of encryption accepted for SSL tunnel negotiation. high encryption allows AES and 3DES. medium encryption allows AES, 3DES, and RC4. low encryption allows AES, 3DES, RC4, and DES. | high |

ssl-server

Use this command to add one or more SSL servers to support WAN optimization SSL offloading. You enable WAN optimization SSL offloading by enabling the ssl field in a WAN optimization rule. WAN optimization supports SSL encryption/decryption  offloading for HTTP servers.

SSL offloading uses the FortiGate unit to encrypt and decrypt SSL sessions.The FortiGate unit intercepts HTTPS traffic from clients and decrypts it before sending it as clear text to the HTTP server. The clear text response from the HTTP server is encrypted by the FortiGate unit and returned to the client. The result should be a performance improvement because SSL encryption is offloaded from the server to the FortiGate unit FortiASIC SSL encryption/decryption  engine.

You must add one WAN optimization SSL server configuration to the FortiGate unit for each HTTP server that you are configuring SSL offloading for. This SSL server configuration must also include the HTTP server CA. You load this certificated into the FortiGate unit as a local certificate using the config vpn certification local command and then add the certificate to the SSL server configuration using the ssl-cert field. The certificate key size must be 1024 or 2048 bits. 4096-bit keys are not supported.

You can configure one WAN optimization rule to offload SSL encryption/decryption for multiple HTTP servers. To do this, the WAN optimization rule source and destination addresses must be configured so that the rule accepts packets destined for all of the HTTP servers that you want offloading for. Then you must add one SSL server configuration for each of the HTTP servers.

Syntax

config wanopt ssl-server edit <ssl-server-name>

set add-header-x-forwarded-proto {enable | disable}

set ip <ssl_server_ip_ipv4>

set port <port_int>

set ssl-mode {full | half}

set ssl-algorithm {low | medium | high}

set ssl-cert <certificate_name>

set ssl-client-renegotiation {allow | deny | secure}

set ssl-dh-bits {1024 | 1536 | 2048 | 768}

set ssl-min-version {ssl-3.0 | tls-1.0}

set ssl-max-version {ssl-3.0 | tls-1.0}

set ssl-send-empty-frags {disable | enable}

set url-rewrite {enable | disable}

end

| Variable | Description | Default |
| --- | --- | --- |
| edit <ssl-server-name> | Enter a name for the SSL server. It can be any name and this name is not used by other FortiGate configurations. |  |
| add-header-x-forwarded-proto {enable ¦ disable} | Optionally add X-Forwarded-Proto header. This is available when ssl-mode is half. | enable |

| Variable | Description | Default |
| --- | --- | --- |
| ip <ssl_server_ip_ipv4> | Enter an IP address for the SSL server. This IP address should be the same as the IP address of the HTTP server that this SSL server will be offloading for. When a session is accepted by a WAN optimization rule with SSL offloading enabled, the destination IP address of the session is matched with this IP address to select the SSL server configuration to use. | 0.0.0.0 |
| port <port_int> | Enter a port number to be used by the SSL server. Usually this would be port 443 for an HTTPS server. When a session is accepted by a WAN optimization rule with SSL offloading enabled, the destination port of the session is matched with this port to select the SSL server configuration to use. | 0 |
| ssl-mode {full ¦ half} | Configure the SSL server to operate in full mode or half mode. Half mode offloads SSL from the backend server to the server-side FortiGate unit. | full |
| ssl-algorithm {low ¦ medium ¦ high} | Set the permitted encryption algorithms for SSL sessions according to encryption strength: low — AES, 3DES, RC4, DES medium — AES, 3DES, RC4 high — AES, 3DES | high |
| ssl-cert <certificate_name> | Select the certificate to be used for this SSL server. The certificate should be the HTTP server CA used by the HTTP server that this SSL server configuration will be offloading for. The certificate must be a local certificate added to the FortiGate unit using the config vpn certificate local command. For more information, see “vpn certificate local” on page 745. The certificate key size must be 1024 or 2048 bits. 4096-bit keys are not supported. |  |
| ssl-client-renegotiation {allow ¦ deny ¦ secure} | Select whether client renegotiation is allowed. The deny option aborts any SSL connection that attempts to renegotiate. The secure option rejects any SSL connection that does not offer an RFC 5746 Secure Renegotiation Indication. | allow |
| ssl-dh-bits {1024 ¦ 1536 ¦ 2048 ¦ 768} | Select the size of the Diffie-Hellman prime used in DHE_RSA negotiation. Larger primes may cause a performance reduction but are more secure. | 1024 |
| ssl-min-version {ssl-3.0 ¦ tls-1.0} | Select the lowest or oldest SSL/TLS version to offer when negotiating. You can set the minimum version to SSL 3.0 or TLS 1.0. TLS 1.0 is more secure that SSL 3.0. | ssl-3.0 |
| ssl-max-version {ssl-3.0 ¦ tls-1.0} | Select the highest or newest SSL/TLS version to offer when negotiating. You can set the maximum version to SSL 3.0 or TLS 1.0. TLS 1.0 is more secure that SSL 3.0. | tls-1.0 |

Fortinet Technologies Inc.                                                                Page 829                                     FortiOS™ - CLI Reference for FortiOS 5.0

| Variable | Description | Default |
| --- | --- | --- |
| ssl-send-empty-frags {disable ¦ enable} | Enable or disable sending empty fragments before sending the actual payload. Sending empty fragments is a technique used to avoid cipher-block chaining (CBC) plaintext attacks if the initiation vector (IV) is known. Also called the CBC IV. Some SSL implementations are not compatible with sending empty fragments. Change ssl-send- empty-frags to disable if required by your SSL implementation. | enable |
| url-rewrite {enable ¦ disable} | Enable to rewrite Location header of HTTP redirection response(3XX response). This is available when ssl-mode is half. | disable |

Fortinet Technologies Inc.                                                                Page 830                                     FortiOS™ - CLI Reference for FortiOS 5.0

storage

Use this command to change the size of WAN optimization storages. A storage defines the maximum size of the byte caching or web caching database added to the storage.

Syntax

config wanopt storage

edit <storage_name_str>

set size <partition_size_int>

set webcache-storage-percentage <int>

end

| Variable | Description | Default |
| --- | --- | --- |
| edit <storage_name_str> | Enter the name of a storage configured using the config system storage command. All FortiGate units with hard disks include a default storage name such as Internal or ASM. |  |
| size <partition_size_int> | Enter the size of the partition in Mbytes. The default depends on the partition size. |  |
| webcache-storage-percentage <int> | Enter the portion, in percent, of the storage that is used for web cache. Remainder is used for wanopt. | 50 |

webcache

Use this command to change how the WAN optimization web cache operates. In most cases the default settings are acceptable. However you may want to change these settings to improve performance or optimize the cache for your configuration.

Syntax

config wanopt webcache

set always-revalidate {enable | disable} set always-revalidate {enable | disable} set cache-cookie {enable | disable}

set cache-expired {enable | disable}

set default-ttl <expiry_time>

set fresh-factor <fresh_percent>

set ignore-conditional {enable | disable} set ignore-ie-reload {enable | disable} set ignore-ims {enable | disable}

set ignore-pnc {enable | disable} set max-object-size <object_size> set max-ttl <expiry_time>

set min-ttl <expiry_time>

set neg-resp-time <response_time> set reval-pnc {enable | disable} config cache-exemption-list

edit <url-id_int>

set url-pattern <url-str>

end

end

| Variable | Description | Default |
| --- | --- | --- |
| always-revalidate {enable ¦ disable} | Enable to always to revalidate the requested cached object with content on the server before serving it to the client. | enable |
| cache-cookie {enable ¦ disable} | Enable caching of cookies. Typically a HTTP response with a cookie contains data for a specific user, so cookie caching is best not done. | disable |
| cache-expired {enable ¦ disable} | Applies only to type-1 objects. When this setting is enabled, type-1 objects that are already expired at the time of acquisition are cached (if all other conditions make the object cachable). When this setting is disabled, already expired type-1 objects become non-cachable at the time of acquisition. | disable |
| default-ttl <expiry_time> | The default expiry time for objects that do not have an expiry time set by the web server. The default expiry time is 1440 minutes (24 hours). | 1440 |
| fresh-factor <fresh_percent> | Set the fresh factor as a percentage. The default is 100, and the range is 1 to 100. For cached objects that don’t have an expiry time, the web cache periodically checks the server to see if the object has expired. The higher the fresh factor the less often the checks occur. | 100 |

| Variable | Description | Default |
| --- | --- | --- |
| ignore-conditional {enable ¦ disable} | Enable or disable controlling the behavior of cache-control header values. HTTP 1.1 provides additional controls to the client over the behavior of caches concerning the staleness of the object. Depending on various Cache-Control headers, the FortiGate unit can be forced to consult the OCS before serving the object from the cache. For more information about the behavior of cache-control header values, see RFC 2616. | disable |
| ignore-ie-reload {enable ¦ disable} | Some versions of Internet Explorer issue Accept / header instead of Pragma nocache header when you select Refresh. When an Accept header has only the / value, the FortiGate unit treats it as a PNC header if it is a type-N object. When this option is enabled, the FortiGate unit ignores the PNC interpretation of the Accept: / header. | enable |
| ignore-ims {enable ¦ disable} | Be default, the time specified by the if-modified-since (IMS) header in the client's conditional request is greater than the last modified time of the object in the cache, it is a strong indication that the copy in the cache is stale. If so, HTTP does a conditional GET to the Overlay Caching Scheme (OCS), based on the last modified time of the cached object. Enable ignore-ims to override this behavior. | disable |
| ignore-pnc {enable ¦ disable} | Typically, if a client sends an HTTP GET request with a pragma no-cache (PNC) or cache-control nocache header, a cache must consult the OCS before serving the content. This means that the FortiGate unit always re-fetches the entire object from the OCS, even if the cached copy of the object is fresh. Because of this, PNC requests can degrade performance and increase server-side bandwidth utilization. However, if ignore-pmc is enabled, then the PNC header from the client request is ignored. The FortiGate unit treats the request as if the PNC header is not present at all. | disable |
| max-object-size <object_size> | Set the maximum object size to cache. The default size is 512000 kbytes (512 Mbytes). This object size determines the maximum object size to store in the web cache. All objects retrieved that are larger than the maximum size are delivered to the client but are not stored in the web cache. Range: 1 to 2 147 483 kBytes. | 512000 |
| max-ttl <expiry_time> | The maximum amount of time an object can stay in the web cache without checking to see if it has expired on the server. The default is 7200 minutes (120 hours or 5 days). | 7200 |
| min-ttl <expiry_time> | The minimum amount of time an object can stay in the web cache before checking to see if it has expired on the server. The default is 5 minutes. | 5 |

Fortinet Technologies Inc.                                                                Page 833                                     FortiOS™ - CLI Reference for FortiOS 5.0

| Variable | Description | Default |
| --- | --- | --- |
| neg-resp-time <response_time> | Set how long in minutes to cache negative responses. The default is 0, meaning negative responses are not cached. The content server might send a client error code (4xx HTTP response) or a server error code (5xx HTTP response) as a response to some requests. If the web cache is configured to cache these negative responses, it returns that response in subsequent requests for that page or image for the specified number of minutes. | 0 |
| reval-pnc {enable ¦ disable} | The pragma-no-cache (PNC) header in a client's request can affect the efficiency of the FortiGate unit from a bandwidth gain perspective. If you do not want to completely ignore PNC in client requests (which you can do by using the ignore PNC option configuration), you can lower the impact of the PNC by enabling reval-pnc. When the reval-pnc is enabled, a client's non-conditional PNC-GET request results in a conditional GET request sent to the OCS if the object is already in the cache. This gives the OCS a chance to return the 304 Not Modified response, consuming less server-side bandwidth, because it has not been forced to return full content even though the contents have not actually changed. By default, the revalidate PNC configuration is disabled and is not affected by changes in the top-level profile. When the Substitute Get for PNC configuration is enabled, the revalidate PNC configuration has no effect. Most download managers make byte-range requests with a PNC header. To serve such requests from the cache, the reval-pnc option should be enabled along with byte-range support. | disable |

config  cache-exemption-list

Configure a cache exemption list. The URLs that are defined in this list will be exempted from caching. The url-pattern can be an internal ip address such as “192.168.1.121” or a web address such as “example.com/test123/321” or a numeric ip address such as “1.1.1.1”.

| Variable | Description | Default |
| --- | --- | --- |
| <url-id_int> | A unique number to identify each URL entry in the list. |  |
| url-pattern <url-str> | The URL added to the list. |  |

Fortinet Technologies Inc.                                                                Page 834                                     FortiOS™ - CLI Reference for FortiOS 5.0

webfilter

Use webfilter commands to add banned words to the banned word list, filter URLs, and configure FortiGuard-Web category filtering.

This chapter contains the following sections:

content

content-header fortiguard

ftgd-local-cat ftgd-local-rating ftgd-warning

ips-urlfilter-cache-setting ips-urlfilter-setting override

override-user profile

search-engine

urlfilter

Page 835

content

Control web content by blocking or exempting words, phrases, or patterns.

For each pattern you can select Block or Exempt. Block, blocks access to a web page that matches with the pattern. Exempt allows access to the web page even if other entries in the list that would block access to the page.

For a page, each time a block match is found values assigned to the pattern are totalled. If a user-defined threshold value is exceeded, the web page is blocked.

Use this command to add or edit and configure options for the Web content filter list. Patterns words can be one word or a text string up to 80 characters long. The maximum number of patterns in the list is 5000.

When a single word is entered, the FortiGate unit checks Web pages for that word. Add phrases by enclosing the phrase in ‘single quotes’. When a phrase is entered, the FortiGate unit checks Web pages for any word in the phrase. Add exact phrases by enclosing the phrases in “quotation marks”. If the phrase is enclosed in quotation marks, the FortiGate checks Web pages for the exact phrase.

Create patterns using wildcards or Perl regular expressions.

Perl regular expression patterns are case sensitive for Web Content Filtering. To make a word or phrase case insensitive, use the regular expression /i. For example, /bad language/i blocks all instances of bad language regardless of case. Wildcard patterns are not case sensitive.

Syntax

config webfilter content edit <entry_number>

set name <list_str>

set comment <comment_str>

config entries

edit <content_str>

set action {block | exempt}

set lang {cyrillic | french | japanese | korean | simch

| spanish | thai | trach | western}

set pattern-type {regexp | wildcard}

set score <score_int>

set status {enable | disable}

end

end

| Variable | Description | Default |
| --- | --- | --- |
| edit <entry_number> | A unique number to identify the banned word list. |  |
| name <list_str> | The name of the banned word list. |  |
| comment <comment_str> | The comment attached to the banned word list. |  |
| edit <content_str> | Enter the content to match. |  |

Fortinet Technologies Inc.                                                                Page 836                                     FortiOS™ - CLI Reference for FortiOS 5.0

| Variable | Description | Default |
| --- | --- | --- |
| action {block ¦ exempt} | Select one of: block If the pattern matches, the Score is added to the total for the web page. The page is blocked if the total score of the web page exceeds the web content block threshold defined in the web filter profile. Exempt If the pattern matches, the web page will not be blocked even if there are matching Block entries. | block |
| lang {cyrillic ¦ french ¦ japanese ¦ korean ¦ simch ¦ spanish ¦ thai ¦ trach ¦ western} | Enter the language character set used for the content. Choose from Cyrillic, French, Japanese, Korean, Simplified Chinese, Spanish, Thai, Traditional Chinese, or Western. | western |
| pattern-type {regexp ¦ wildcard} | Set the pattern type for the content. Choose from regexp or wildcard.Create patterns for banned words using Perl regular expressions or wildcards. | wildcard |
| score <score_int> | A numerical weighting applied to the content. The score values of all the matching words appearing on a web page are added, and if the total is greater than the webwordthreshold value set in the web filter profile, the page is processed according to whether the bannedword option is set with the http command in the web filter profile. The score for banned content is counted once even if it appears multiple times on the web page. | 10 |
| status {enable ¦ disable} | Enable or disable the content entry. | disable |

Fortinet Technologies Inc.                                                                Page 837                                     FortiOS™ - CLI Reference for FortiOS 5.0

content-header

Use this example to filter web content according to the MIME content header. You can use this feature to broadly block content by type. But it is also useful to exempt audio and video streaming files from antivirus scanning. Scanning these file types can be problematic.

The content header list is available in the CLI only.

Syntax

config webfilter content-header edit <entry_number>

set name <list_name>

set comment <comment_str>

config entries edit <regex>

set action {allow | block | exempt}

set category <fortiguard_category>

end

end

| Variable | Description | Default |
| --- | --- | --- |
| edit <entry_number> | A unique number to identify the content header list. |  |
| name <list_name> | The name of the content header list. |  |
| comment <comment_str> | The comment attached to the content header list. |  |
| edit <regex> | Enter a regular expression to match the content header. For example, .*image.* matches image content types. |  |
| action {allow ¦ block ¦ exempt} | Select one of: allow — permit matching content. block — if the pattern matches, the content is blocked. exempt — if the pattern matches, the content is exempted from antivirus scanning. | block |
| category <fortiguard_category> | Enter the FortiGuard category (or categories) to match. To view a list of categories, enter set category ? |  |

fortiguard

Use this command to enable Web filtering by specific categories using FortiGuard-Web URL

filtering.

Syntax

config webfilter fortiguard

set cache-mem-percent <percent_int>

set cache-mode {ttl | db-ver}

set cache-prefix-match {enable | disable}

set close-ports {enable | disable}

set ovrd-auth-cert <str>

set ovrd-auth-hostname <str>

set ovrd-auth-https {enable | disable}

set ovrd-auth-port-http <port_int> set ovrd-auth-port-https <port_int> set reports-status {enable | disable}

set request-packet-size-limit <bytes_int>

end

| Variable | Description | Default |
| --- | --- | --- |
| cache-mem-percent <percent_int> | Change the maximum percentage of memory the cache will use in db-ver mode. Enter a value from 1 to 15 percent. | 2 |
| cache-mode {ttl ¦ db-ver} | Change the cache entry expiration mode. Choices are ttl or db-ver. Using ttl, cache entries are deleted after a number of seconds determined by the cache-ttl setting, or until newer cache entries force the removal of older ones. When set to db-ver, cache entries are kept until the FortiGuard database changes, or until newer cache entries force the removal of older ones. | ttl |
| cache-prefix-match {enable ¦ disable} | Enable and disable prefix matching. If enabled the FortiGate unit attempts to match a packet against the rules in a prefix list starting at the top of the list. For information on prefix lists see “prefix-list, prefix-list6” on page 418. | enable |
| close-ports {enable ¦ disable} | Enable to close ports used for HTTP/HTTPS authentication and disable user overrides. | disable |
| ovrd-auth-cert <str> | Enter a certificate name to use for FortiGuard Web Filter HTTPS override authentication. | Fortinet_Firmware |
| ovrd-auth-hostname <str> | Enter a host name to use for FortiGuard Web Filter HTTPS override authentication. | No default. |
| ovrd-auth-https {enable ¦ disable} | Enable to use HTTPS for override authentication. | disable |
| ovrd-auth-port-http <port_int> | The port to use for FortiGuard Web Filter HTTP override authentication. | 8008 |

| Variable | Description | Default |
| --- | --- | --- |
| ovrd-auth-port-https <port_int> | The port to use for FortiGuard Web filtering HTTPS override authentication. | 8010 |
| reports-status {enable ¦ disable} | Enable or disable FortiGuard Web Filter reports. This feature is available only on FortiGate units with an internal hard disk. | disable |
| request-packet-size-limit <bytes_int> | In some cases, FortiGuard request packets may be dropped due to IP fragmentation. You can set the maximum packet size. Range 576 to 10 000 bytes. Use 0 for the default size, 1100 bytes. | 0 |

Fortinet Technologies Inc.                                                                Page 840                                     FortiOS™ - CLI Reference for FortiOS 5.0

ftgd-local-cat

Use this command to add local categories to the global URL category list. The categories defined here appear in the global URL category list when configuring a web filter profile. Users can rate URLs based on the local categories.

Syntax

config webfilter ftgd-local-cat edit <local_cat_str>

set id <id_int>

end

| Variable | Description | Default |
| --- | --- | --- |
| <local_cat_str> | The description of the local category. |  |
| id <id_int> | The local category unique ID number. | 140 |

ftgd-local-rating

Use this command to rate URLs using local categories.

Users can create user-defined categories then specify the URLs that belong to the category. This allows users to block groups of web sites on a per profile basis. The ratings are included in the global URL list with associated categories and compared in the same way the URL block list is processed.

The user can also specify whether the local rating is used in conjunction with the FortiGuard rating or is used as an override.

Syntax

config webfilter ftgd-local-rating edit <url_str>

set rating [[<category_int>] [group_str]...]

set status {enable | disable}

end

| Variable | Description | Default |
| --- | --- | --- |
| <url_str> | The URL being rated. |  |
| rating [[<category_int>] [group_str]...] | Set categories and/or groups. To remove items from the rating, use the unset command. Enter ‘?’ to print a list of category and group codes with descriptions. |  |
| status {enable ¦ disable} | Enable or disable the local rating. | enable |

ftgd-warning

Use this command to configure FortiGuard-Web filter administrative overrides.

The administrative overrides are backed up with the main configuration and managed by the FortiManager system. The administrative overrides are not cleaned up when they expire and you can reuse these override entries by extending their expiry dates.

Syntax

config webfilter override edit <override_int>

set expires <yyyy/mm/dd hh:mm:ss>

set initiator <user_name>

set ip <ipv4>

set ip6 <ipv6>

set new-profile <profile_str>

set old-profile <profile_str>

set scope {user | user-group | ip | ip6}

set status {enable | disable}

set user <user_str>

set user-group <user_group_str>

end

get webfilter override <override_int>

| Variable | Description | Default |
| --- | --- | --- |
| <override_int> | The unique ID number of the override. |  |
| expires <yyyy/mm/dd hh:mm:ss> | The date and time the override expires. For example, the command to configure an expiry time of 6:45 p.m. on May 22, 2009 would be formatted this way: set expires 2010/05/22 18:45:00 | 15 minutes after the override is created. |
| initiator <user_name> | The user who initiated the override rule. This field is get-only. |  |
| ip <ipv4> | When the scope is ip, enter the IP address for which the override rule applies. | 0.0.0.0 |
| ip6 <ipv6> | When the scope is ip6, enter the IP address for which the override rule applies. | :: |
| new-profile <profile_str> | Specify the new web-filter profile to apply the override. | null |
| old-profile <profile_str> | Specify the web-filter profile for which the override applies. | null |
| scope {user ¦ user-group ¦ ip ¦ ip6} | The scope of the override rule. | user |
| status {enable ¦ disable} | Enable or disable the override rule. | disable |
| user <user_str> | When the scope is user, the user for which the override rule applies. |  |
| user-group <user_group_str> | When the scope is user-group, enter the user group for which the override rule applies. |  |

ips-urlfilter-cache-setting

Use this command to configure the global DNS settings for flow-based URL filtering in conjunction with a border gateway. See also the webfilter ips-urlfilter-cache-setting  command.

Syntax

config webfilter ips-urlfilter-cache-setting set dns-retry-interval <seconds_int>

set extended-ttl <seconds_int>

end

| Variable | Description | Default |
| --- | --- | --- |
| dns-retry-interval <seconds_int> | Set the DNS retry interval. Refresh DNS faster than TTL to capture multiple IPs for hosts. Range 0 to 2 147 483. 0 means use DNS server’s TTL value. | 0 |
| extended-ttl <seconds_int> | Extend the TTL beyond that of the DNS server. Range 0 to 2 147 483. | 0 |

ips-urlfilter-setting

Use this command to set up url filtering (flow-based) in conjunction with a border gateway router.

Syntax

config webfilter ips-urlfilter-setting set device <intf_name>

set distance <dist_int>

set gateway <ip_addr>

end

| Variable | Description | Default |
| --- | --- | --- |
| device <intf_name> | Select the interface that connects to the border router. | No default. |
| distance <dist_int> | Set the administrative distance. Range 1 to 255. | 1 |
| gateway <ip_addr> | Enter the IP address of the border router. | 0.0.0.0 |

override

Use this command to view FortiGuard-Web filter warnings.

When a user attempts to access a web site within a category that is configured with the warning action, the user will received a warning which they have to acknowledge before continuing. You can view all active warnings with the get webfilter override command.

Although the full selection of set commands are offered, you cannot change any of the override     entries. The FortiGate unit will return an error when you enter next or end.

Syntax

config webfilter override

get webfilter override <override_int>

edit <override_int>

set expires <yyyy/mm/dd hh:mm:ss>

set initiator <user_name>

set ip <ipv4>

set ip6 <ipv6>

set new-profile <profile_str>

set old-profile <profile_str>

set scope {user | user-group | ip | ip6}

set status {enable | disable}

set user <user_str>

set user-group <user_group_str>

end

| Variable | Description | Default |
| --- | --- | --- |
| <override_int> | The unique ID number of the override. |  |
| expires <yyyy/mm/dd hh:mm:ss> | The date and time the override expires. For example, the command to configure an expiry time of 6:45 p.m. on May 22, 2009 would be formatted this way: set expires 2010/05/22 18:45:00 | 15 minutes after the override is created. |
| initiator <user_name> | The user who initiated the override rule. This field is get- only. |  |
| ip <ipv4> | When the scope is ip, enter the IP address for which the override rule applies. | 0.0.0.0 |
| ip6 <ipv6> | When the scope is ip6, enter the IP address for which the override rule applies. | :: |
| new-profile <profile_str> | Specify the new web-filter profile to apply the override. | null |
| old-profile <profile_str> | Specify the web-filter profile for which the override applies. | null |
| scope {user ¦ user-group ¦ ip ¦ ip6} | The scope of the override rule. | user |
| status {enable ¦ disable} | Enable or disable the override rule. | disable |

| Variable | Description | Default |
| --- | --- | --- |
| user <user_str> | When the scope is user, the user for which the override rule applies. |  |
| user-group <user_group_str> | When the scope is user-group, enter the user group for which the override rule applies. |  |

Fortinet Technologies Inc.                                                                Page 847                                     FortiOS™ - CLI Reference for FortiOS 5.0

override-user

Use this command to configure FortiGuard-Web filter user overrides.

When a user attempts to access a blocked site, if override is enabled, a link appears on the block page directing the user to an authentication form. The user must provide a correct user name and password or the web site remains blocked. Authentication is based on user groups and can be performed for local, RADIUS, and LDAP users.

Administrators can only view and delete the user overrides entries.

Syntax

config webfilter override-user edit <override_int>

set expires <yyyy/mm/dd hh:mm:ss>

set initiator <user_name>

set ip <ipv4>

set ip6 <ipv6>

set new-profile <profile_str>

set old-profile <profile_str>

set scope {user | user-group | ip | ip6}

set status {enable | disable}

set user <user_str>

set user-group <user_group_str>

end

get webfilter override-user <override_int>

| Variable | Description | Default |
| --- | --- | --- |
| <override_int> | The unique ID number of the override. |  |
| expires <yyyy/mm/dd hh:mm:ss> | The date and time the override expires. For example, the command to configure an expiry time of 6:45 p.m. on May 22, 2009 would be formatted this way: set expires 2010/05/22 18:45:00 | 15 minutes after the override is created. |
| initiator <user_name> | The user who initiated the override rule. This field is get-only. |  |
| ip <ipv4> | When the scope is IP, enter the IP address for which the override rule applies. | 0.0.0.0 |
| ip6 <ipv6> | When the scope is ip6, enter the IP address for which the override rule applies. | :: |
| new-profile <profile_str> | Specify the new web-filter profile to apply the override. | null |
| old-profile <profile_str> | Specify the web-filter profile for which the override applies. | null |
| scope {user ¦ user-group ¦ ip ¦ ip6} | The scope of the override rule. | user |
| status {enable ¦ disable} | Enable or disable the override rule. | disable |

Fortinet Technologies Inc.                                                                Page 848                                     FortiOS™ - CLI Reference for FortiOS 5.0

| Variable | Description | Default |
| --- | --- | --- |
| user <user_str> | When the scope is user, the user for which the override rule applies. |  |
| user-group <user_group_str> | When the scope is user-group, the user group for which the override rule applies. |  |

Fortinet Technologies Inc.                                                                Page 849                                     FortiOS™ - CLI Reference for FortiOS 5.0

profile

Use this command to configure UTM web filtering profiles for firewall policies. Web filtering profiles configure how web filtering and FortiGuard Web Filtering is applied to sessions accepted by a firewall policy that includes the web filter profile.

Syntax

config webfilter profile edit <name_str>

set comment <comment_str>

set extended-utm-log {enable | disable}

set flow-based {enable | disable}

set log-all-urls {enable | disable}

set options {activexfilter | block-invalid-url | contenttype- check | cookiefilter | https-scan | intrinsic | javafilter

| js | jscript | per-user-bwl | rangeblock | unknown | vbs

| wf-cookie | wf-referer}

set ovrd-perm [bannedword-override contenttype-check-override fortiguard-wf-override urlfilter-override]

set post-action {normal | comfort | block}

set web-content-log {enable | disable}

set web-filter-activex-log {enable | disable}

set web-filter-command-block-log {enable | disable}

set web-filter-cookie-log {enable | disable}

set web-filter-cookie-removal-log {enable | disable}

set web-filter-applet-log {enable | disable}

set web-filter-js-log {enable | disable}

set web-filter-jscript-log {enable | disable}

set web-filter-vbs-log {enable | disable}

set web-filter-unknown-log {enable | disable} set web-filter-referer-log {enable | disable} set web-ftgd-err-log {enable | disable}

set web-ftgd-quota-usage {enable | disable} set web-invalid-domain-log {enable | disable} set web-url-log {enable | disable}

config ftgd-wf

set options {connect-request-bypass | error-allow

| ftgd-disable | http-err-detail | rate-image-urls

| rate-server-ip | redir-block | strict-blocking}

set category-override <category_str>

set exempt-quota {all | <category_str>}

set exempt-ssl {all | <category_str>}

Variables for config filters edit <id_str>

set action {authenticate | block | monitor | warning}

set auth-usr-group [group1 ...groupn] set category {category_int group_str} set log {enable | disable}

set warn-duration <dur_string>

end

config quota edit <id>

set category <id>

set duration <dur_str>

set type {time | traffic} set unit {B | GB | KB | MB} set value <int>

end end

config override

set ovrd-dur <###d##h##m>

set ovrd-dur-mode {ask | constant}

set ovrd-scope {ask | ip | user | user-group}

set ovrd-user-group <groupname_str> [<groupname_str>...]

set profile <web_profile>

set profile-attribute <attribute_str>

set profile-type {list | radius}

end config web

set bword-threshold <threshold_int> set bword-table <filter_list_name> set urlfilter-table <url_list_name>

set content-header-list <list_number>

set keyword-match <pattern_str> set log-search {enable | disable} set safe-search {url | header}

set urlfilter-table <url_list_name>

set youtube-edu-filter-id <accountid_int>

end

end

| Variable | Description | Default |
| --- | --- | --- |
| <name_str> | Enter the name of the web filtering profile. |  |
| comment <comment_str> | Optionally enter a description of up to 63 characters of the web filter profile. |  |
| extended-utm-log {enable ¦ disable} | Enable or disable detailed UTM log messages. | disable |
| flow-based {enable ¦ disable} | Enable or disable flow-based web filtering. | disable |

| Variable | Description | Default |
| --- | --- | --- |
| log-all-urls {enable ¦ disable} | Enable to log all URLs, even if FortiGuard is not enabled. extended-utm-log must be enabled. | disable |
| options {activexfilter ¦ block-invalid-url ¦ contenttype-check ¦ cookiefilter ¦ https-scan ¦ intrinsic ¦ javafilter ¦ js ¦ jscript ¦ per-user-bwl ¦ rangeblock ¦ unknown ¦ vbs ¦ wf-cookie ¦ wf-referer} | Select one or more options apply to web filtering. To select more than one, enter the option names separated by a space. Some options are only available for some protocols. activexfilter — block ActiveX plugins. block-invalid-url — block web pages with an invalid domain name. contenttype-check — filter based on the content-type header. cookiefilter — block cookies. https-scan — enable encrypted content scanning for HTTPS traffic. This option is available only on FortiGate units that support encrypted content scanning. intrinsic — block intrinsic scripts. javafilter — block Java applets. js — block JavaScript applets. jscript — block JavaScript applets. per-user-bwl — per-user black/white list. This must also be enabled in system global. rangeblock — block downloading parts of a file that have already been partially downloaded. Selecting this option prevents the unintentional download of virus files hidden in fragmented files. Note that some types of files, such as PDF, fragment files to increase download speed and enabling this option can cause download interruptions. Enabling this option may break certain applications that use the Range Header in the HTTP protocol, such as YUM, a Linux update manager. unknown — block unknown scripts. vbs — block VB scripts. wf-cookie — block the contents of the HTTP header “Cookie”. wf-referer — block the contents of the HTTP header “Referer”. Separate multiple options with a space.To remove an option from the list or add an option to the list, retype the list with the option removed or added. |  |

Fortinet Technologies Inc.                                                                Page 852                                     FortiOS™ - CLI Reference for FortiOS 5.0

| Variable | Description | Default |
| --- | --- | --- |
| ovrd-perm [bannedword-override contenttype-check-overri de fortiguard-wf-override urlfilter-override] | Override permit options: bannedword-override — content block contenttype-check-override — filter based on content-type header override fortiguard-wf-override — FortiGuard Web Filter block override urlfilter-override — web url filter override | null |
| post-action {normal ¦ comfort ¦ block} | Select the action to take with HTTP POST traffic. This option is available for HTTPS normal — do not affect HTTP POST traffic. comfort — use the comfort-interval and comfort- amount http options of the“firewall profile-protocol- options” on page 185 to send comfort bytes to the server in case the client connection is too slow. Select this option to prevent a server timeout when scanning or other filtering tool is turned on. block — block HTTP POST requests. When the post request is blocked the FortiGate unit sends the http- post-block replacement message to the user’s web browser. | normal |
| web-content-log {enable ¦ disable} | Enable or disable logging for web content blocking. | enable |
| web-filter-activex-log {enable ¦ disable} | Enable or disable logging for activex script web filtering. | enable |
| web-filter-command- block-log {enable ¦ disable} | Enable or disable logging of web filter command block messages. | enable |
| web-filter-cookie-log {enable ¦ disable} | Enable or disable logging for cookie script web filtering. | enable |
| web-filter-cookie- removal-log {enable ¦ disable} | Enable or disable logging for web filter cookie blocking. | enable |
| web-filter-applet-log {enable ¦ disable} | Enable or disable logging for applet script web filtering. | enable |
| web-filter-js-log {enable ¦ disable} | Enable or disable logging for web script filtering on javascripts. | enable |
| web-filter-jscript-log {enable ¦ disable} | Enable or disable logging for web script filtering on JScripts. | enable |
| web-filter-sdns-action {redirect ¦ block} | Select the action for FortiGuard DNS-based webfiltering: redirect user to a captive portal or block the connection. | redirect |
| web-filter-sdns-portal <portal_ip> | Enter the captive portal IP address used for users redirected by FortiGuard DNS-based webfiltering. | 0.0.0.0 |
| web-filter-vbs-log {enable ¦ disable} | Enable or disable logging for web script filtering on VBS scripts. | enable |
| web-filter-unknown-log {enable ¦ disable} | Enable or disable logging for web script filtering on unknown scripts. | enable |

Fortinet Technologies Inc.                                                                Page 853                                     FortiOS™ - CLI Reference for FortiOS 5.0

| Variable | Description | Default |
| --- | --- | --- |
| web-filter-referer-log {enable ¦ disable} | Enable or disable logging for webfilter referer block. | enable |
| web-ftgd-err-log {enable ¦ disable} | Enable or disable logging for FortiGuard Web Filtering rating errors. | enable |
| web-ftgd-quota-usage {enable ¦ disable} | Enable or disable logging for FortiGuard Web Filtering daily quota usage. | enable |
| web-invalid-domain-log {enable ¦ disable} | Enable or disable logging for web filtering of invalid domain names. | enable |
| web-url-log {enable ¦ disable} | Enable or disable logging for web URL filtering. | enable |

config  ftgd-wf

Configure FortiGuard Web Filtering options.

For the enable, disable, allow, deny, log, ovrd, ftgd-wf-ssl-exempt options, to view a list of available category codes with their descriptions, enter get, then find entries such as g01 Potentially Liable, 1 Drug Abuse, and c06 Spam URL. Separate multiple codes with a space. To delete entries, use the unset command to delete the entire list.

| Variable | Description | Default |
| --- | --- | --- |
| category-override <category_str> | Enable local categories to take precedence over FortiGuard Web Filtering categories. Enter category numbers or group numbers separated by spaces. | null |
| exempt-quota {all ¦ <category_str>} | Do not stop quota for these categories. |  |
| exempt-ssl {all ¦ <category_str>} | Enter categories to exempt from SSL inspection. |  |
| options {connect-request-bypass ¦ error-allow ¦ ftgd-disable ¦ http-err-detail ¦ rate-image-urls ¦ rate-server-ip ¦ redir-block ¦ strict-blocking} | Select options for FortiGuard web filtering, separating multiple options with a space. connect-request-bypass — (http only) bypass FortiGuard Web Filtering for HTTP sessions to the same address as bypassed HTTPS connections. error-allow — allow web pages with a rating error to pass through. ftgd-disable — disable FortiGuard. http-err-detail — display a replacement message for 4xx and 5xx HTTP errors. If error pages are allowed, malicious or objectionable sites could use these common error pages to circumvent web category blocking. This option does not apply to HTTPS. rate-image-urls — rate images by URL. Blocked images are replaced with blanks. This option does not apply to HTTPS. rate-server-ip — send both the URL and the IP address of the requested site for checking, providing additional security against attempts to bypass the FortiGuard system. |  |

Fortinet Technologies Inc.                                                                Page 854                                     FortiOS™ - CLI Reference for FortiOS 5.0

| Variable | Description redir-block — block HTTP redirects. Many web sites use HTTP redirects legitimately; however, in some cases, redirects may be designed specifically to circumvent web filtering, as the initial web page could have a different rating than the destination web page of the redirect. strict-blocking — block any web pages if any classification or category matches the rating. This option does not apply to HTTPS. To remove an option from the list or add an option to the list, retype the list with the option removed or added. These options take effect only if FortiGuard web filtering is enabled for the protocol. | Default |
| --- | --- | --- |
| Variables for config filters |
| <id_str> | Enter the ID number of the filter. Enter a new number to create a new filter. Enter an existing number to edit a filter. |  |
| action {authenticate ¦ block ¦ monitor ¦ warning} | Enter the action to take for matches. authenticate permits authenticated users to load the web page. block prevents the user from loading the web page. monitor permits the user to load the web page but logs the action. warning requires that the user acknowledge a warning before they can proceed. | block |
| auth-usr-group [group1 ...groupn] | Enter the user groups who are permitted to authenticate. This is available if action is authenticate. | No default. |
| category {category_int group_str} | Enter the categories and groups the filter will examine. You can specify multiple categories and groups by separating them with a space character. | No default. |
| log {enable ¦ disable} | Enable or diable logging for this filter. | enable |
| warn-duration <dur_string> | Set duration (nnhnnmnns, 23h59m59s for example) of warning. This is available when action is warning or authenticated. | 5m |

Fortinet Technologies Inc.                                                                Page 855                                     FortiOS™ - CLI Reference for FortiOS 5.0

config  override

Configure web filtering overrides.

| Variable | Description | Default |
| --- | --- | --- |
| ovrd-dur <###d##h##m> | Enter the FortiGuard Web Filtering override duration in days, hours, and minutes in any combination. For example, 34d, 12h, 20m, 34d23m, 200d12h45m. The maximum is 364d23h59m. | 15m |
| ovrd-dur-mode {ask ¦ constant} | Enter the FortiGuard Web Filtering duration type, one of: constant — as specified in ftgd-wf-ovrd-dur ask — ask for duration when initiating override. ftgd-wf-ovrd-dur is the maximum | constant |
| ovrd-scope {ask ¦ ip ¦ user ¦ user-group} | Enter the scope of the Web Filtering override, one of: ask — ask for scope when initiating an override. ip — override for the initiating IP — user — override for the user user-group — override for a user group | user |
| ovrd-user-group <groupname_str> [<groupname_str>...] | Enter the names of user groups that can be used for FortiGuard Web Filter overrides. Separate multiple names with spaces. | null |
| profile <web_profile> | Enter the web profile name. |  |
| profile-attribute <attribute_str> | Enter the name of the profile attribute to retrieve from the RADIUS server. Available when profile- type is radius. | Login-LAT-service |
| profile-type {list ¦ radius} | Enter list if the override profile chosen from a list. Enter radius if the override profile is determined by a RADIUS server. |  |

config  quota

Configure FortiGuard quotas.

| Variable | Description | Default |
| --- | --- | --- |
| edit <id> | Enter an ID for the quota. | No default. |
| category <id> | Set the category. The category must have action of monitor and must not be in exempt-ssl list. | No default. |
| duration <dur_str> | Set the duration (nnhnnmnns). | 5m |
| type {time ¦ traffic} | Set the quota type: time-based or traffic-based. | time |
| unit {B ¦ GB ¦ KB ¦ MB} | Set the unit for traffic based quota. | MB |
| value <int> | Set the quota numeric value. | 0 |

config  web

Specify the web content filtering the web URL filtering lists to use with the web filtering profile and set other configuration setting such as the web content filter threshold.

| Variable | Description | Default |
| --- | --- | --- |
| bword-threshold <threshold_int> | If the combined scores of the web content filter patterns appearing in a web page exceed the threshold value, the web page is blocked. The rang is 0-2147483647. | 10 |
| bword-table <filter_list_name> | Select the name of the web content filter list to use with the web filtering profile. |  |
| content-header-list <list_number> | Select the content header list. | 0 |
| keyword-match <pattern_str> | Search keywords to log. |  |
| log-search {enable ¦ disable} | Enable or disable logging all search phrases. | disable |
| safe-search {url ¦ header} | Select whether safe search is based on the request URL or header. | Null |
| urlfilter-table <url_list_name> | Select the name of the URL filter list to use with the web filtering profile. | No default. |
| youtube-edu-filter- id <accountid_int> | Enter the account ID for YouTube Education Filter. Available when safe-search is header. | No default. |

search-engine

Use this command to configure search engine definitions. Definitions for well-known search engines are included by default.

Syntax

config webfilter search-engine edit <site_name>

set charset {utf-8 | gb2312}

set hostname <url_regex>

set query <str>

set safesearch {disable | header | url}

set safesearch-str set url <url_str>

end

| Variable | Description | Default |
| --- | --- | --- |
| <site_name> | Enter the name of the search engine. | No default. |
| charset {utf-8 ¦ gb2312} | Select the search engine’s preferred character set. | utf-8 |
| hostname <url_regex> | Enter the regular expression to match the hostname portion of the search URL. For example, .*\.google\..* for Google. | No default. |
| query <str> | Enter the code used to prefix a query. | No default. |
| safesearch {disable ¦ header ¦ url} | Select how to request safe search on this site. disable — site does not support safe search header — selected by search header, e.g. youtube.edu url — selected with a parameter in the URL | disable |
| safesearch-str | Enter the safe search parameter used in the URL. Example: &safe=on This is available if safesearch is url. | No default. |
| url <url_str> | Enter the regular expression to match the search URL. For example ^\/((custom¦search¦images¦videosearch¦webhp)\?) | No default. |

urlfilter

Use this command to control access to specific URLs by adding them to the URL filter list. The FortiGate unit exempts or blocks Web pages matching any specified URLs and displays a replacement message instead.

Configure the FortiGate unit to allow, block, or exempt all pages on a website by adding the top-level URL or IP address and setting the action to allow, block, or exempt.

Block individual pages on a website by including the full path and filename of the web page to block. Type a top-level URL or IP address to block access to all pages on a website. For example, www.example.com or 172.16.144.155 blocks access to all pages at this website.

Type a top-level URL followed by the path and filename to block access to a single page on a website. For example, www.example.com/news.html or 172.16.144.155/news.html blocks the news page on this website.

To block all pages with a URL that ends with example.com, add example.com to the block list. For example, adding example.com blocks access to www.example.com, mail.example.com, www.finance.example.com, and so on.

Use this command to exempt or block all URLs matching patterns created using text and regular expressions (or wildcard characters). For example, example.* matches example.com, example.org, example.net and so on. The FortiGate unit exempts or blocks Web pages that match any configured pattern and displays a replacement message instead.

The maximum number of entries in the list is 5000.

Syntax

config webfilter urlfilter edit <list_int>

set name <list_str>

set comment <comment_str>

set one-arm-ips-urlfilter {enable | disable}

config entries edit <url_str>

set action {allow | block | exempt | monitor}

set exempt {all | activex-java-cookie | av | dlp

| filepattern | fortiguard | web-content}

set status {enable | disable}

set type {simple | regex | wildcard}

end end

| Variable | Description | Default |
| --- | --- | --- |
| <list_int> | A unique number to identify the URL filter list. |  |
| name <list_str> | The name of the URL filter list. |  |
| comment <comment_str> | The comment attached to the URL filter list. |  |
| one-arm-ips-urlfilter {enable ¦ disable} | Enable or disable IPS URL filter. | disable |
| <url_str> | The URL to added to the list. |  |

| Variable | Description | Default |
| --- | --- | --- |
| action {allow ¦ block ¦ exempt ¦ monitor} | The action to take for matches. An allow match exits the URL filter list and checks the other web filters. A block match blocks the URL and no further checking will be done. An exempt match stops all further checking including AV scanning for the current HTTP session, which can affect multiple URLs. A monitor match passes the URL and generates a log message. The request is still subject to other UTM inspections. | exempt |
| exempt {all ¦ activex-java-cookie ¦ av ¦ dlp ¦ filepattern ¦ fortiguard ¦ web-content} | Enter the types of scanning to skip for the exempt URLs: all All of the following options. activex-java-cookie — Allow activeX, Java, and cookies for the URL. av — Do not antivirus scanning for the URL. dlp — Do not apply DLP scanning for the URL. filepattern — Do not apply file pattern filtering for the URL. fortiguard — Do not apply FortiGuard web filtering for the URL. web-content — Do not apply web content filtering for the URL. | all ¦ activex-java-cookie ¦ av ¦ dlp ¦ filepattern ¦ fortiguard ¦ web-content |
| status {enable ¦ disable} | The status of the filter. | enable |
| type {simple ¦ regex ¦ wildcard} | The type of URL filter: simple, regular expression, or wildcard. | simple |

Fortinet Technologies Inc.                                                                Page 860                                     FortiOS™ - CLI Reference for FortiOS 5.0

web-proxy

Use these commands to configure the FortiGate web proxy. You can use the FortiGate web proxy and interface settings to enable explicit HTTP and HTTPS proxying on one or more interfaces. When enabled, the FortiGate unit becomes a web proxy server. All HTTP and HTTPS session received by interfaces with explicit web proxy enabled are intercepted by the explicit web proxy relayed to their destinations.

To use the explicit proxy, users must add the IP address of a FortiGate interface and the explicit proxy port number to the proxy configuration settings of their web browsers.

On FortiGate units that support WAN optimization, you can also enable web caching for the explicit proxy.

explicit

forward-server forward-server-group global

url-match

Page 861

explicit

Use this command to enable the explicit web proxy, and configure the TCP port used by the explicit proxy.

Syntax

config web-proxy explicit

set status {enable | disable}

set ftp-over-http {enable | disable}

set socks {enable | disable}

set http-incoming-port <http_port_int> set https-incoming-port <https_port_int> set ftp-incoming-port <ftp_port_int>

set socks-incoming-port <socks_port_int> set incoming-ip <incoming_interface_ipv4> set incoming-ip6 <incoming_interface_ipv6> set ipv6-status {enable | disable}

set outgoing-ip <outgoing_interface_ipv4> [<outgoing_interface_ipv4> ... <outgoing_interface_ipv4>]

set outgoing-ip6 <outgoing_interface_ipv6> [<outgoing_interface_ipv6> ... <outgoing_interface_ipv6>]

set unknown-http-version {best-effort | reject}

set realm <realm_str>

set sec-default-action {accept | deny}

set pac-file-server-status {enable | disable}

set pac-file-server-port <pac_port_int>

set pac-file-name <pac_file_str> set pac-file-data <pac_file_str> set pac-file-url <url_str>

set ssl-algorithm {low | medium | high}

end

| Variable | Description | Default |
| --- | --- | --- |
| status {enable ¦ disable} | Enable the explicit web proxy for HTTP and HTTPS sessions. | disable |
| ftp-over-http {enable ¦ disable} | Configure the explicit proxy to proxy FTP sessions sent from a web browser. The explicit proxy only supports FTP with a web browser and not with a standalone FTP client. | disable |
| socks {enable ¦ disable} | Configure the explicit proxy to proxy SOCKS sessions sent from a web browser. For information about SOCKS, see RFC 1928. The explicit web proxy supports SOCKs 4 and 5. | disable |
| http-incoming-port <http_port_int> | Enter the port number that HTTP traffic from client web browsers use to connect to the explicit proxy. The range is 0 to 65535. Explicit proxy users must configure their web browser’s HTTP proxy settings to use this port. | 8080 |

Fortinet Technologies Inc.                                                                Page 862                                     FortiOS™ - CLI Reference for FortiOS 5.0

| Variable | Description | Default |
| --- | --- | --- |
| https-incoming-port <https_port_int> | Enter the port number that HTTPS traffic from client web browsers use to connect to the explicit proxy. The range is 0 to 65535. Explicit proxy users must configure their web browser’s HTTPS proxy settings to use this port. The default value of 0 means use the same port as HTTP. | 0 |
| ftp-incoming-port <ftp_port_int> | Enter the port number that FTP traffic from client web browsers use to connect to the explicit proxy. The range is 0 to 65535. Explicit proxy users must configure their web browser’s FTP proxy settings to use this port. The default value of 0 means use the same port as HTTP. | 0 |
| socks-incoming-port <socks_port_int> | Enter the port number that SOCKS traffic from client web browsers use to connect to the explicit proxy. The range is 0 to 65535. Explicit proxy users must configure their web browser’s SOCKS proxy settings to use this port. The default value of 0 means use the same port as HTTP. | 0 |
| incoming-ip <incoming_interface_ipv4> | Enter the IP address of a FortiGate unit interface that should accept sessions for the explicit web proxy. Use this command to restrict the explicit web proxy to only accepting sessions from one FortiGate interface. The destination IP address of explicit web proxy sessions should match this IP address. This field is not available in Transparent mode. | 0.0.0.0 |
| incoming-ip6 <incoming_interface_ipv6> | Enter the IPv6 address of a FortiGate unit interface that should accept sessions for the explicit web proxy. Use this command to restrict the explicit web proxy to only accepting sessions from one FortiGate interface. This is available when ipv6-status is enable. | ::0 |
| ipv6-status {enable ¦ disable} | Enable or disable IPv6 web-proxy operation. | disable |
| outgoing-ip <outgoing_interface_ipv4> [<outgoing_interface_ipv4> ... <outgoing_interface_ipv4>] | Enter the IP address of a FortiGate unit interface that explicit web proxy sessions should exit the FortiGate unit from. Multiple interfaces can be specified. Use this command to restrict the explicit web proxy to only allowing sessions to exit from one FortiGate interface. This IP address becomes the source address of web proxy sessions exiting the FortiGate unit. This field is not available in Transparent mode. | 0.0.0.0 |

Fortinet Technologies Inc.                                                                Page 863                                     FortiOS™ - CLI Reference for FortiOS 5.0

| Variable | Description | Default |
| --- | --- | --- |
| outgoing-ip6 <outgoing_interface_ipv6> [<outgoing_interface_ipv6> ... <outgoing_interface_ipv6>] | Enter the IPv6 address of a FortiGate unit interface that explicit web proxy sessions should exit the FortiGate unit from. Multiple interfaces can be specified. Use this command to restrict the explicit web proxy to only allowing sessions to exit from one FortiGate interface. This IP address becomes the source address of web proxy sessions exiting the FortiGate unit. This field is not available in Transparent mode. | ::0 |
| unknown-http-version {best-effort ¦ reject} | Select the action to take when the proxy server must handle an unknown HTTP version request or message. Choose from either Reject or Best Effort. Best Effort attempts to handle the HTTP traffic as best as it can. Reject treats unknown HTTP traffic as malformed and drops it. The Reject option is more secure. | reject |
| realm <realm_str> | Enter an authentication realm to identify the explicit web proxy. The realm can be any text string of up to 63 characters. If the realm includes spaces enclose it in quotes. When a user authenticates with the explicit proxy the HTTP authentication dialog includes the realm so you can use the realm to identify the explicit web proxy for your users. | default |
| sec-default-action {accept ¦ deny} | Configure the explicit web proxy to block (deny) or accept sessions if firewall policies have note been added for the explicit web proxy. To add firewall policies for the explicit web proxy add a firewall policy and set the source interface to web-proxy. The default setting denies access to the explicit web proxy before adding a firewall policy. If you set this option to accept the explicit web proxy server accepts sessions even if you haven’t defined a firewall policy. | deny |
| pac-file-server-status {enable ¦ disable} | Enable support for proxy auto-config (PAC). With PAC support enabled you can configure a PAC file on the FortiGate unit and distribute the URL of this file to your web browser users. These users can enter this URL as an automatic proxy configuration URL and their browsers will automatically download proxy configuration settings. You can use PAC to provide access to multiple proxy servers and access methods as well as other features. To enable PAC you must edit or replace (by importing) the default PAC file installed in your FortiGate unit. | disable |

Fortinet Technologies Inc.                                                                Page 864                                     FortiOS™ - CLI Reference for FortiOS 5.0

| Variable | Description | Default |
| --- | --- | --- |
| pac-file-server-port <pac_port_int> | Select the port that PAC traffic from client web browsers use to connect to the explicit proxy. The range is 0 to 65535. Explicit proxy users must configure their web browser’s PAC proxy settings to use this port. The default value of 0 means use the same port as HTTP. | 0 |
| pac-file-name <pac_file_str> | Change the name of the PAC file. In most cases you could keep the default name. | proxy.pac |
| pac-file-data <pac_file_str> | Enter the contents of the PAC file made available from the explicit proxy server for PAC support. Enclose the PAC file text in quotes. You can also copy the contents of a PAC text file and paste the contents into the CLI using this option. Enter the command followed by two sets of quotes then place the cursor between the quotes and paste the file content. The maximum PAC file size is 8192 bytes. You can use any PAC file syntax that is supported by your users’s browsers. The FortiGate unit does not parse the PAC file. |  |
| pac-file-url <url_str> | Displays the PAC file URL in the format: http://<interface_ip>: <PAC_port_int>/<pac_file_str> For example, if the interface with the explicit web proxy has IP address 172.20.120.122, the PAC port is the same as the default HTTP explicit proxy port (8080) and the PAC file name is proxy.pac the PAC file URL would be: http://172.20.120.122:8080/proxy.pac If the explicit web proxy is enabled on multiple interfaces there will be multiple PAC URLs. If you have configured an incoming-ip only one PAC file URL is listed that includes the incoming-ip. Distribute this URL to PAC users. You cannot use the pac-file-url option to edit the PAC file URL. |  |
| ssl-algorithm {low ¦ medium ¦ high} | Select the strength of encryption algorithms accepted for deep scan: high: AES, 3DES low: AES, 3DES, RC4, DES medium: AES, 3DES, RC4 | medium |

Fortinet Technologies Inc.                                                                Page 865                                     FortiOS™ - CLI Reference for FortiOS 5.0

forward-server

Use this command to support explicit web proxy forwarding, also called proxy chaining.

Syntax

config web-proxy forward-server edit <server_name_string>

set addr-type {fqdn | ip}

set comment <comment_string>

set fqdn <fqdn_string>

set healthcheck {enable | disable}

set ip <server_ipv4> set monitor <http_url> set port <port_integer>

set server-down-option {block | pass}

end

| Variable | Description | Default |
| --- | --- | --- |
| addr-type {fqdn ¦ ip} | Select whether proxy address is defined by domain name (fqdn) or IP address. | ip |
| comment <comment_string> | Optionally, enter a description. | No default. |
| fqdn <fqdn_string> | Enter the fully qualified domain name of the forwarding web proxy server. Available if addr- type is fqdn. | No default. |
| healthcheck {enable ¦ disable} | Enable or disable proxy server health check. Health checking attempts to connect to a web server to make sure that the remote forwarding server is operating. | disable |
| ip <server_ipv4> | Enter the IP address of the forwarding proxy server. Available if addr-type is ip. | 0.0.0.0 |
| monitor <http_url> | Enter the URL to use for health check monitoring. This would be a URL that the web proxy would attempt to connect to through the forwarding server. If the web proxy can’t connect to this URL it assumes the forwarding server is down. |  |
| port <port_integer> | Enter the port number that the forwarding server expects to receive HTTP sessions on. | 3128 |
| server-down-option {block ¦ pass} | Select the action to take when the forwarding proxy server is down. You can either forward connections to | block |

forward-server-group

Use this command to configure a load-balanced group of web proxy forward servers.

Syntax

config web-proxy forward-server-group edit <fwdsrvr_group_name>

set affinity {enable | disable}

set group-down-option {pass | block}

set ldb-method {least-session | weighted}

config server-list

edit <fwd-srvr-name>

set weight <weight_int>

end

end

| Variable | Description | Default |
| --- | --- | --- |
| affinity {enable ¦ disable} | Enable to attach source-ip's traffic to assigned forward-server until forward-server- affinity-timeout (see web-proxy global). | enable |
| group-down-option {pass ¦ block} | Select action to take if all forward servers are down: pass traffic through or block traffic. | block |
| ldb-method {least-session ¦ weighted} | Select the load-balancing method. | weighted |
| weight <weight_int> | Set weight of this server for load balancing. Range 1 to 100. | 10 |

global

Configure global web-proxy settings that control how the web proxy functions and handles web traffic. In most cases you should not have to change the default settings of this command. If your FortiGate unit is operating with multiple VDOMS these settings affect all VDOMs.

Syntax

config web-proxy global

set add-header-client-ip {enable | disable}

set add-header-via {enable | disable}

set add-header-x-forwarded-for {enable | disable} set add-header-front-end-https {enable | disable} set forward-proxy-auth {enable | disable}

set forward-server-affinity-timeout <minutes_int>

set max-message-length <kBytes> set max-request-length <kBytes> set proxy-fqdn <fqdn>

set strict-web-check {enable | disable}

set tunnel-non-http {enable | disable}

set unknown-http-version {tunnel | best-effort | reject}

end

| Variable | Description | Default |
| --- | --- | --- |
| add-header-client-ip {enable ¦ disable} | Enable to add the client IP to the header of forwarded requests | disable |
| add-header-front-end-https {enable ¦ disable} | Enable to add a front-end-https header to forwarded requests. | disable |
| add-header-via {enable ¦ disable} | Enable to add the via header to forwarded requests. | disable |
| add-header-x-forwarded-for {enable ¦ disable} | Enable to add x-forwarded-for header to forwarded requests. | disable |
| forward-proxy-auth {enable ¦ disable} | In explicit mode, enable to forward proxy authentication headers. By default proxy authentication headers are blocked by the explicit web proxy. You can set this option to enable if you need to allow proxy authentication through the explicit web proxy. This option does not apply to web proxy transparent mode, because in transparent mode, proxy authentication headers are always forwarded by the web proxy. | disable |
| forward-server-affinity- timeout <minutes_int> | The source-ip's traffic will attach to assigned forward-server until timeout. Range: 6 to 60 minutes. | 30 |
| max-message-length <kBytes> | Set the maximum length, in kBytes, of the HTTP message not including body. Range 16 to 256. | 32 |
| max-request-length <kBytes> | Set the maximum length, in kBytes, of the HTTP request line. Range 2 to 64. | 4 |

| Variable | Description | Default |
| --- | --- | --- |
| proxy-fqdn <fqdn> | Set the fully qualified domain name (FQDN) for the proxy. This is the domain that clients connect to. | default.fqdn |
| strict-web-check {enable ¦ disable} | Enable to block web sites that send incorrect headers that do not conform to HTTP 1.1 as described in RFC 2616. Disable to allow and cache websites that send incorrect headers that do not conform to the RFC. This option is disabled by default so that web sites are not blocked. You can enable this option if you want to increase security by blocking sites that do not conform. Enabling this option may block some commonly used websites. | disable |
| tunnel-non-http {enable ¦ disable} | Enable to allow non-HTTP traffic. | enable |
| unknown-http-version {tunnel ¦ best-effort ¦ reject} | Select how to handle traffic if HTTP version is unknown: tunnel — tunnel the traffic best-effort — proceed with best effort reject — reject the traffic | best-effort |

Fortinet Technologies Inc.                                                                Page 869                                     FortiOS™ - CLI Reference for FortiOS 5.0

url-match

Use this command to define URLs for forward-matching or cache exemption.

Syntax

config web-proxy url-match edit <url-pattern>

set cache-exemption {enable | disable}

set comment <comment_str>

set forward-server <name_str> set status {enable | disable} set url-pattern <pattern_str>

end

| Variable | Description | Default |
| --- | --- | --- |
| cache-exemption {enable ¦ disable} | Enable to set a cache exemption list. User defined URLs in the list will be exempted from caching. | disable |
| comment <comment_str> | Optionally enter a comment. |  |
| forward-server <name_str> | Enter the forward server name. |  |
| status {enable ¦ disable} | Enable or disable per-URL pattern web proxy forwarding and cache exemptions. | enable |
| url-pattern <pattern_str> | Enter the URL pattern. |  |

Fortinet Technologies Inc.                                                                Page 870                                     FortiOS™ - CLI Reference for FortiOS 5.0

wireless-controller

Use these commands to create virtual wireless access points that can be associated with multiple physical wireless access points. Clients can roam amongst the physical access points, extending the range of the wireless network.

This chapter describes the following commands:

ap-status global setting timers

vap

wids-profile wtp

wtp-profile

Page 871

ap-status

Use this command to designate detected access points as accepted or rogue or to suppress a rogue AP.

To get information about detected access points, use the get wireless-controller scan

command.

Syntax

config wireless-controller ap-status edit <ap_id>

set bssid <bssid>

set ssid <ssid>

set status {accepted | rogue | suppressed}

end

| Variable | Description | Default |
| --- | --- | --- |
| <ap_id> | Enter a number to identify this access point. | No default. |
| bssid <bssid> | Enter the access point’s BSSID. This is the wireless AP’s wireless MAC address. | 00:00:00:00:00:00 |
| ssid <ssid> | Enter the wireless service set identifier (SSID) or network name for the wireless interface. | No default. |
| status {accepted ¦ rogue ¦ suppressed} | Select the desired status for this AP: accepted or rogue. | rogue |

global

Use this command to configure global settings for physical access points, also known as WLAN Termination Points (WTPs), configured using Control And Provisioning of Wireless Access Points (CAPWAP) protocol.

Syntax

config wireless-controller global

set data-ethernet-II {enable | disable}

set dhcp-option-code <option_int> set discovery-mc-addr <ipv4addr> set local-radio-vdom <vdom_name> set location <string>

set max-clients <int>

set max-retransmit <int> set mesh-eth-type <id_int> set name <string>

set rogue-scan-mac-adjacency <int>

end

| Variable | Description | Default |
| --- | --- | --- |
| data-ethernet-II {enable ¦ disable} | Enable or disable use of Ethernet frame type with 802.3 data tunnel mode. | disable |
| dhcp-option-code <option_int> | Enter DHCP option code. This is available when ac-discovery-type is dhcp. | 138 |
| discovery-mc-addr <ipv4addr> | Enter the IP address for AP discovery. This is available when ac-discovery-type is multicast. | 224.0.1.140 |
| local-radio-vdom <vdom_name> | Select the VDOM to which the FortiWiFi unit’s built- in access point belongs. | root |
| location <string> | Enter the location of your wireless network. | No default. |
| max-clients <int> | Enter the maximum number of clients permitted to connect simultaneously. Enter 0 for no limit. | 0 |
| max-retransmit <int> | Enter the maximum number of retransmissions for tunnel packet. Range 0 to 64. | 3 |
| mesh-eth-type <id_int> | Identifier included in packets. Useful for debugging. | 8755 |
| name <string> | Enter a name for your wireless network. | No default. |
| rogue-scan-mac-adjacency <int> | Enter the maximum numeric difference between an AP’s Ethernet and wireless MAC values to match for rogue detection. Range: 0-7. | 7 |

setting

Use this command to configure VDOM-specific options for the wireless controller.

Syntax

config wireless-controller setting

set ap-auto-suppress {enable | disable} set ap-bgscan-disable-day <day_list_str> set ap-bgscan-disable-end <time_str>

set ap-bgscan-disable-start <time_str>

set ap-bgscan-period <secs_int> set ap-scan {enable | disable} set country <country-code>

set on-wire-scan {enable | disable}

end

| Variable | Description | Default |
| --- | --- | --- |
| ap-auto-suppress {enable ¦ disable} | Enable or disable automatic suppression of detected rogue APs. To enable ap-auto-suppress, first ap-scan and on-wire-scan must be enabled. | disable |
| ap-bgscan-disable-day <day_list_str> | Enter the days of the week when background scanning is disabled. | null |
| ap-bgscan-disable-end <time_str> | Enter the end time (format hh:mm) for disabled background scanning. ap-bgscan-disable-day must be set. | 00:00 |
| ap-bgscan-disable-start <time_str> | Enter the start time (format hh:mm) for disabled background scanning. ap-bgscan-disable-day must be set. | 00:00 |
| ap-bgscan-period <secs_int> | Enter the period in seconds between background scans. | 600 |
| ap-scan {enable ¦ disable} | Enable or disable scanning for other APs available at your location. | disable |
| country <country-code> | Select the country of operation for your wireless network. This affects the radio channels that are available. To view the available country codes, enter set country ? You must set the country before you configure access point (WTP) profiles. | US |
| on-wire-scan {enable ¦ disable} | Enable or disable looking for MAC addresses of unknown APs on the wired network to distinguish rogues from neighbors. Use this in conjunction with ap-scan. | disable |

timers

Use this command to alter global timers for physical access points, also known as WLAN Termination Points (WTPs) configured using Control And Provisioning of Wireless Access Points (CAPWAP) protocol.

Syntax

config wireless-controller timers set client-idle-timeout <seconds> set darrp-optimize <seconds_int> set darrp-wtp-tune <seconds_int> set discovery-interval <seconds> set echo-interval <seconds>

set fake-ap-log <int>

set rogue-ap-log <int>

end

| Variable | Description | Default |
| --- | --- | --- |
| client-idle-timeout <seconds> | Set the timeout period in seconds for inactive clients. Range: 20 to 3600, 0 for no timeout. | 300 |
| darrp-optimize <seconds_int> | Set the DARRP (Dynamic Automatic Radio Resource Provisioning) optimization interval. Range: 0 to 86 400 seconds. | 1800 |
| darrp-wtp-tune <seconds_int> | Set the automatic channel selection interval. Range: 1 to 30 seconds. | 3 |
| discovery-interval <seconds> | Set the period between discovery requests. Range 2 to 180 seconds. | 5 |
| echo-interval <seconds> | Set the interval before WTP sends Echo Request after joining AC. Range 1 to 600 seconds. | 30 |
| fake-ap-log <int> | Set a period, in minutes, for periodic logging of fake APs. | 1 |
| rogue-ap-log <int> | Set a period, in minutes, for periodic logging of rogue APs. | 0 |

vap

Use this command to configure Virtual Access Points.

Syntax

config wireless-controller vap edit <vap_name>

set auth {usergroup | radius}

set broadcast-suppress {arp | dhcp} set broadcast-ssid {enable | disable} set dynamic-vlan {enable | disable} set encrypt {AES | TKIP |  TKIP-AES}

set external-fast-roaming {enable | disable}

set fast-roaming {enable | disable}

set gtk-rekey-intv <secs>

set intra-vap-privacy {enable | disable}

set key <key_str>

set keyindex {1 | 2 | 3 | 4}

set local-authentication {enable | disable}

set local-bridging {enable | disable} set local-switching {enable | disable} set max-clients <int>

set mesh-backhaul {enable | disable}

set me-disable-thresh <limit_int>

set multicast-enhance {enable | disable}

set passphrase <hex_str>

set portal-message-override-group <repl-msg-group_name>

set ptk-rekey-intv <secs>

set radius-server <server_name>

set radius-mac-auth {enable | disable}

set radius-mac-auth-server <srv_str>

set security {captive-portal | open | wep128 | wep64

| wpa-enterprise | wpa-only-enterprise | wpa-only-personal

| wpa-personal | wpa2-only-enterprise | wpa2_only-personal}

set selected-usergroups <groups_str>

set ssid <string>

set usergroup <group_name>

set vdom <vdom_name>

set vlanid <vlan_int>

set vlan-auto {enable | disable}

| Variable | Description | Default |
| --- | --- | --- |
| auth {usergroup ¦ radius} | Select whether WPA-Enterprise authentication uses FortiGate user groups or a RADIUS server. | usergroup |
| broadcast-suppress {arp ¦ dhcp} | Prevent ARP or DHCP messages being carried to other access points carrying the same SSID. | (null) |

| Variable | Description | Default |
| --- | --- | --- |
| broadcast-ssid {enable ¦ disable} | Enable broadcast of the SSID. Broadcasting the SSID enables clients to connect to your wireless network without first knowing the SSID. For better security, do not broadcast the SSID. | enable |
| dynamic-vlan {enable ¦ disable} | Enable dynamic VLAN assignment for users based RADIUS attribute. | disable |
| encrypt {AES ¦ TKIP ¦ TKIP-AES} | Select whether VAP uses AES or TKIP encryption, or accepts both. This is available if security is a WPA type. | AES |
| external-fast-roaming {enable ¦ disable} | Enable or disable pre-authentication with external non-managed AP. | disable |
| fast-roaming {enable ¦ disable} | Enabling fast-roaming enables pre-authentication where supported by clients. | enable |
| gtk-rekey-intv <secs> | Set the WPA re-key interval. Some clients may require a longer interval. For WPA-RADIUS SSID, use ptk-rekey-intv. Range 60 to 864 000 seconds. | 600 |
| intra-vap-privacy {enable ¦ disable} | Enable to block communication between clients of the same AP. | disable |
| key <key_str> | Enter the encryption key that the clients must use. For WEP64, enter 10 hexadecimal digits. For WEP128, enter 26 hexadecimal digits. This is available when security is a WEP type. | No default. |
| keyindex {1 ¦ 2 ¦ 3 ¦ 4} | Many wireless clients can configure up to four WEP keys. Select which key clients must use.with this access point. This is available when security is a WEP type. | 1 |
| local-authentication {enable ¦ disable} | Enable authentication of clients by the FortiAP unit if the wireless controller is unavailable. This applies only if security is a WPA-Personal mode and local-bridging is enabled. | disable |
| local-bridging {enable ¦ disable} | Enable or disable bridging of wireless and Ethernet interfaces on the FortiAP unit. | disable |
| local-switching {enable ¦ disable} | Enable or disable bridging of local VAP interfaces. | enable |
| max-clients <int> | Enter the maximum number of clients permitted to connect simultaneously. Enter 0 for no limit. | 0 |
| mesh-backhaul {enable ¦ disable} | Enable to use this Virtual Access Point as a WiFi mesh backhaul. WiFi clients cannot connect directly to this SSID. | disable |
| me-disable-thresh <limit_int> | Set the multicast enhancement threshold. Range 2 to 256 subscribers. | 64 |
| multicast-enhance {enable ¦ disable} | Enable conversion of multicast to unicast to improve performance. | disable |
| passphrase <hex_str> | Enter the encryption passphrase of 8 to 63 characters. This is available when security is a WPA type and auth is PSK. | No default. |

Fortinet Technologies Inc.                                                                Page 877                                     FortiOS™ - CLI Reference for FortiOS 5.0

| Variable | Description | Default |
| --- | --- | --- |
| portal-message-override- group <repl-msg-group_name> | Enter the replacement message group for this virtual access point. The replacement message group must already exist in system replacemsg-group and its group-type must be captive-portal. This field is available when security is captive-portal. | Null. |
| ptk-rekey-intv <secs> | Set the WPA-RADIUS re-key interval. Some clients may require a longer interval. Range 60 to 864 000 seconds. | 3600 |
| radius-server <server_name> | Enter the RADIUS server used to authenticate users. This is available when auth is radius. | No default. |
| radius-mac-auth {enable ¦ disable} | Enable if you want MAC address authentication of clients. This is independent of other authentication protocols. You will also have to specify radius-mac-auth-server. | disable |
| radius-mac-auth-server <srv_str> | Specify the RADIUS server to use for MAC address authentication. This is available if radius-mac-auth is enabled. | null |
| security {captive-portal ¦ open ¦ wep128 ¦ wep64 ¦ wpa-enterprise ¦ wpa-only-enterprise ¦ wpa-only-personal ¦ wpa-personal ¦ wpa2-only-enterprise ¦ wpa2_only-personal} | Select the security mode for the wireless interface. Wireless users must use the same security mode to be able to connect to this wireless interface. captive-portal — users are authenticated through a captive web portal. open — has no security. Any wireless user can connect to the wireless network. wep128 — 128-bit WEP. To use WEP128 you must enter a Key containing 26 hexadecimal digits (0-9 a-f) and inform wireless users of the key. wep64 — 64-bit web equivalent privacy (WEP). To use WEP64 you must enter a Key containing 10 hexadecimal digits (0-9 a-f) and inform wireless users of the key. wpa-enterprise — WPA-Enterprise security, WPA or WPA2. wpa-only-enterprise — WPA-Enterprise security, WPA only. wpa-only-personal — WPA-Personal security, WPA only. wpa-personal — WPA-Personal security, WPA or WPA2. wpa2-only-enterprise — WPA-Enterprise security, WPA2 only. wpa2-only-personal — WPA-Personal security, WPA2 only. | wpa-personal |

Fortinet Technologies Inc.                                                                Page 878                                     FortiOS™ - CLI Reference for FortiOS 5.0

| Variable | Description | Default |
| --- | --- | --- |
| selected-usergroups <groups_str> | Select the user groups that can authenticate. This is available when security is captive- portal. | No default. |
| ssid <string> | Enter the wireless service set identifier (SSID) or network name for this wireless interface. Users who want to use the wireless network must configure their computers with this network name. | fortinet |
| usergroup <group_name> | Enter the usergroup for WPA-Enterprise authentication when auth is usergroup. | No default. |
| <vap_name> | Enter a name for this Virtual Access Point. | No default. |
| vdom <vdom_name> | Enter the name of the VDOM to which this VAP belongs. | No default. |
| vlanid <vlan_int> | Enter the VLAN ID, if a VLAN will be used. 0 means no VLAN. | 0 |
| vlan-auto {enable ¦ disable} | Enable or disable automatic VLAN assignment for authenticated users of this SSID. This is available if security is WPA Enterprise or captive portal and vlanid is not 0. | disable |

Fortinet Technologies Inc.                                                                Page 879                                     FortiOS™ - CLI Reference for FortiOS 5.0

wids-profile

Use this command to configure Wireless Intrusion Detection (WIDS) profiles.

Syntax

config wireless-controller wids-profile edit <wids-profile_name>

set comment <comment_str>

set asleap-attack {enable | disable}

set assoc-frame-flood {enable | disable} set auth-frame-flood {enable | disable} set deauth-broadcast {enable | disable} set eapol-fail-flood {enable | disable} set eapol-fail-intv <int>

set eapol-fail-thres <int>

set eapol-logoff-flood {enable | disable}

set eapol-logoff-intv <int>

set eapol-logoff-thres <int>

set eapol-pre-fail-flood {enable | disable}

set eapol-pre-fail-intv <int>

set eapol-pre-fail-thres <int>

set eapol-pre-succ-flood {enable | disable}

set eapol-pre-succ-intv <int>

set eapol-pre-succ-thres <int>

set eapol-start-flood {enable | disable}

set eapol-start-intv <int>

set eapol-start-thres <int>

set eapol-succ-flood {enable | disable}

set eapol-succ-intv <int>

set eapol-succ-thres <int>

set invalid-mac-oui {enable | disable}

set long-duration-attack {enable | disable}

set long-duration-thresh <int>

set null-ssid-probe-resp {enable | disable}

set spoofed-deauth {enable | disable}

set weak-wep-iv {enable | disable}

set wireless-bridge {enable | disable}

end

| Variable | Description | Default |
| --- | --- | --- |
| <wids-profile_name> | Enter a name for this WIDS profile. | No default. |
| comment <comment_str> | Optionally, enter a descriptive comment. | No default. |
| asleap-attack {enable ¦ disable} | Enable to detect asleap attack (attempt to crack LEAP security). | disable |
| assoc-frame-flood {enable ¦ disable} | Enable to detect association frame flood attack. | disable |
| auth-frame-flood {enable ¦ disable} | Enable to detect authentication frame flood attack. | disable |

Fortinet Technologies Inc.                                                                Page 880                                     FortiOS™ - CLI Reference for FortiOS 5.0

| Variable | Description | Default |
| --- | --- | --- |
| deauth-broadcast {enable ¦ disable} |  | disable |
| eapol-fail-flood {enable ¦ disable} | Enable to detect EAP FAIL flood attack. | disable |
| eapol-fail-intv <int> | Set EAP FAIL detection interval. | 1 |
| eapol-fail-thres <int> | Set EAP FAIL detection threshold. | 10 |
| eapol-logoff-flood {enable ¦ disable} | Enable to detect EAP LOGOFF flood attack. | disable |
| eapol-logoff-intv <int> | Set EAP LOGOFF detection interval. | 1 |
| eapol-logoff-thres <int> | Set EAP LOGOFF detection threshold. | 10 |
| eapol-pre-fail-flood {enable ¦ disable} | Enable to detect EAP premature FAIL flood attack. | disable |
| eapol-pre-fail-intv <int> | Set EAP premature FAIL detection interval. | 1 |
| eapol-pre-fail-thres <int> | Set EAP premature FAIL detection threshold. | 10 |
| eapol-pre-succ-flood {enable ¦ disable} | Enable to detect EAP premature SUCC flood attack. | disable |
| eapol-pre-succ-intv <int> | Set EAP premature SUCC detection interval. | 1 |
| eapol-pre-succ-thres <int> | Set EAP premature SUCC detection threshold. | 10 |
| eapol-start-flood {enable ¦ disable} | Enable to detect EAP START flood attack. | disable |
| eapol-start-intv <int> | Set EAP START detection interval. | 1 |
| eapol-start-thres <int> | Set EAP START detection threshold. | 10 |
| eapol-succ-flood {enable ¦ disable} | Enable to detect EAP SUCC flood attack. | disable |
| eapol-succ-intv <int> | Set EAP SUCC detection interval. | 1 |
| eapol-succ-thres <int> | Set EAP SUCC detection threshold. | 10 |
| invalid-mac-oui {enable ¦ disable} | Enable to detect use of spoofed MAC addresses. (The first three bytes should indicate a known manufacturer.) | disable |
| long-duration-attack {enable ¦ disable} | Enable for long duration attack detection based on long-duration-thresh. | disable |
| long-duration-thresh <int> | Enter the duration in usec for long-duration attack detection. This is available when long- duration-attack is enable. | 8200 |
| null-ssid-probe-resp {enable ¦ disable} |  | disable |
| spoofed-deauth {enable ¦ disable} | Enable to detect spoofed deathentication packets. | disable |
| weak-wep-iv {enable ¦ disable} | Enable to detect APs using weak WEP encryption. | disable |
| wireless-bridge {enable ¦ disable} | Enable to detect wireless bridge operation, which is suspicious if your network doesn’t use a wireless bridge. | disable |
| Read-only variables (view using get command) |
| used-by |  |

Fortinet Technologies Inc.                                                                Page 881                                     FortiOS™ - CLI Reference for FortiOS 5.0

wtp

Use this command to configure physical access points (APs) for management by the wireless controller, also known as an access controller (AC).

Syntax

config wireless-controller wtp edit <wtp-id>

set admin <admin_status>

set ap-scan {enable | disable}

set auto-power-level {enable | disable}

set auto-power-low <dBm_int> set auto-power-high <dBm_int> set band {2.4GHz | 5GHz}

set coordinate-enable {enable | disable}

set coordinate-x <int>

set coordinate-y <int>

set image-download {enable | disable}

set location <string>

set login-enable {default | enable | disable}

set login-passwd <pwd_string>

set login-passwd-change {default | yes | no}

set mesh-bridge-enable {default | enable | disable}

set name <string>

set power-level <int>

set radio-enable {enable | disable}

set vap-all {enable | disable}

set vaps {vap1 ... vapn>

set wtp-id <id_string>

set wtp-profile <name_string>

end

To retrieve information about a physical access point:

config wireless-controller wtp edit <wtp-id>

get end

Along with the current configuration settings, information such as the current number of clients, is returned. See the read-only variables section of the table below.

Fortinet Technologies Inc.                                                                Page 882                                     FortiOS™ - CLI Reference for FortiOS 5.0

| Variable | Description | Default |
| --- | --- | --- |
| edit <wtp-id> | Enter the ID for the AP unit. | No default. |
| admin <admin_status> | Set to one of the following: discovered — This is the setting for APs that have discovered this AC and registered themselves. To use such an AP, select enable. disable — Do not manage this AP. enable — Manage this AP. | enable |
| ap-scan {enable ¦ disable} | Enable or disable rogue AP scanning. | enable |
| auto-power-level {enable ¦ disable} | Enable or disable automatic power-level adjustment to prevent co-channel interference. | disable |
| auto-power-low <dBm_int> | Set automatic power level low limit, in dBm. Range 0 to 17dBm. | 10 |
| auto-power-high <dBm_int> | Set automatic power level high limit, in dBm. Range 0 to 17dBm. | 17 |
| band {2.4GHz ¦ 5GHz} | Select 2.4GHz or 5GHz band. Applies when automatic profile is used. | 2.4GHz |
| coordinate-enable {enable ¦ disable} | Enable AP unit coordinates. | disable |
| coordinate-x <int> coordinate-y <int> | Enter x and y coordinates for AP. This is available if coordinate-enable is enabled. | 0,0 |
| image-download {enable ¦ disable} | Enable or disable downloading of firmware to the AP unit. | enable |
| location <string> | Optionally, enter the location of this AP. | No default. |
| login-enable {default ¦ enable ¦ disable} | Enable or disable AP telnet login. Set to default to control the AP telnet login capability with the TELNET_ALLOW setting on the AP unit. | default |
| login-passwd <pwd_string> | Set the AP unit login password. This is available if login-passwd-change is yes. | No default. |
| login-passwd-change {default ¦ yes ¦ no} | Select whether to change AP unit login password. Select default to change the AP unit password back to its default. | no |
| mesh-bridge-enable {default ¦ enable ¦ disable} | Enable to create a bridge between the AP unit’s WiFi interface and its Ethernet interface. Set to default to use the setting configured on the FortiAP unit. | disable |
| name <string> | Enter a name to identify this access point. | No default. |
| power-level <int> | Set radio power level. Range is 0 (minimum) to 100 (maximum). The maximum power level is set to the regulatory maximum for your region, as determined by your selection in the country field of wireless- controller setting. | 100 |
| radio-enable {enable ¦ disable} | Enable or disable radio operation. | enable |
| vap-all {enable ¦ disable} | Enable to inherit all VAPs. Disable to select VAPs. | enable |

Fortinet Technologies Inc.                                                                Page 883                                     FortiOS™ - CLI Reference for FortiOS 5.0

| Variable | Description | Default |
| --- | --- | --- |
| vaps {vap1 ... vapn> | Set the virtual access points carried on this physical access point. This is used only when wtp-profile is not set. | No default. |
| wtp-id <id_string> | Enter the ID of the AP unit. | No default. |
| wtp-profile <name_string> | Enter the name of the wtp profile to apply to this access point. | No default. |
| Read-only variables (view using get command) |
| base-bssid base-bssid-2 | The wireless MAC address of each radio. |
| client-count | The number of clients connected to this managed access point. |
| connection-state | Shows “connected” if FortiAP is connected, otherwise “idle”. |
| image-download- progress | Shows 0-100% progress during FortiAP image upload. |
| join-time | Date and time that the managed AP connected to the controller. |
| last-failure | Last error message concerning this managed AP. |
| last-failure-param | Additional information about the last error. |
| last-failure-time | Date and time of last error message. |
| local-ipv4-address | The IP address assigned to the AP. |
| max-vaps max-vaps-2 | The maximum number of SSIDs supported on each radio. |
| oper-chan oper-chan-2 | The current operating channel of each radio. |
| region-code | The region-code (country) currently set on the FortiAP unit. |
| software-version | The build number of the FortiAP firmware, e.g.:FAP22A-v4.0-build212 |

Fortinet Technologies Inc.                                                                Page 884                                     FortiOS™ - CLI Reference for FortiOS 5.0

wtp-profile

Use this command to define an access point profile (wtp profile).

Syntax

config wireless-controller wtp-profile edit <name_string>

set ap-country <country-code>

set comment <comment_string>

set dtls-policy {clear-text | dtls-enabled}

set handoff-rssi <rssi_int>

set handof-sta-thresh <thresh_int>

set max-clients <int>

set preferred-oper-mode {LE | SN}

config deny-mac-list edit <mac_id>

set mac <mac>

end

config platform

set type <type_string>

end

config radio-1

set ap-auto-suppress {enable | disable}

set ap-bgscan {enable | disable}

set ap-bgscan-disable-day <day_list_str>

set ap-bgscan-disable-end <time_str> set ap-bgscan-disable-start <time_str> set ap-bgscan-period <secs_int>

set auto-power-level {enable | disable}

set auto-power-low <dBm_int>

set auto-power-high <dBm_int>

set band {802.11a | 802.11b | 802.11g | 802.11n | 802.11n-5G}

set beacon-interval <integer> set channel <channels_string> set darrp {enable | disable} set dtim <int>

set frag-threshold <int>

set max-supported-mcs <mcs_int>

set mode <mode_string> set power-level <dBm> set rts-threshold <int>

set short-guard-interval {enable | disable}

set station-locate {enable | disable}

set vaps {vap1 ... vapn>

end

config radio-2

set ap-auto-suppress {enable | disable}

set ap-bgscan {enable | disable}

set ap-bgscan-disable-day <day_list_str>

set ap-bgscan-disable-end <time_str> set ap-bgscan-disable-start <time_str> set ap-bgscan-period <secs_int>

set auto-power-level {enable | disable}

set auto-power-low <dBm_int>

set auto-power-high <dBm_int>

set band {802.11a | 802.11b | 802.11g | 802.11n | 802.11n-5G}

set beacon-interval <integer>

set channel <channels_string>

set channel-bonding {enable | disable}

set darrp {enable | disable}

set dtim <int>

set frag-threshold <int>

set max-supported-mcs <mcs_int>

set mode <mode_string> set power-level <dBm> set rts-threshold <int>

set short-guard-interval {enable | disable}

set vaps {vap1 ... vapn>

end end

| Variable | Description | Default |
| --- | --- | --- |
| ap-country <country-code> | Set the country in which this AP will operate. To list available country codes, enter set ap-country ? | US |
| comment <comment_string> | Optionally, enter a description. | No default. |
| dtls-policy {clear-text ¦ dtls-enabled} | Select whether CAPWAP protocol uses clear-text or DTLS encryption. | clear-text |
| handoff-rssi <rssi_int> | Enter the minimum RSSI value for handoff. | 25 |
| handof-sta-thresh <thresh_int> | Enter the threshold value for AP handoff. | 30 |
| max-clients <int> | Enter the maximum number of clients this AP supports. Use 0 for no limit. | 0 |
| preferred-oper-mode {LE ¦ SN} | Select the preferred operating mode: • LE — local MAC and 802.3 frame tunnel mode • SN — split MAC and 802.11 frame tunnel mode | LE |
| config deny-mac-list variables |  |
| <mac_id> | Enter a number to identify this entry. | No default. |
| mac <mac> | Enter the wireless MAC address to deny. | No default. |

| Variable | Description | Default |
| --- | --- | --- |
| config platform variables |
| type <type_string> | Enter the AP hardware type: 112B FortiAP-112B 11C FortiAP-11C 14C FortiAP-14C 210B FortiAP-210B 220A FortiAP-220A 220B FortiAP-220B 222B FortiAP-222B 223B FortiAP-223B 3320B FortiAP-320B 60C FortiWiFi-20C/40C/60C/60CM/60CA 80CM-81CM FortiWiFi-80CM/81CM | 220B |
| config radio-1, config radio-2 variables |
| ap-auto-suppress {enable ¦ disable} | Enable or disable automatic suppression of detected rogue APs. This is available only if mode is monitor. | disable |
| ap-bgscan {enable ¦ disable} | Enable or disable background scanning. Note: Scanning can reduce performance. | disable |
| ap-bgscan-disable-day <day_list_str> | Enter the days of the week when background scanning is disabled. | null |
| ap-bgscan-disable-end <time_str> | Enter the end time (format hh:mm) for disabled background scanning. ap-bgscan-disable-day must be set. | 00:00 |
| ap-bgscan-disable-start <time_str> | Enter the start time (format hh:mm) for disabled background scanning. ap-bgscan-disable-day must be set. | 00:00 |
| ap-bgscan-period <secs_int> | Enter the period in seconds between background scans. | 600 |
| auto-power-level {enable ¦ disable} | Enable or disable automatic power-level adjustment to prevent co-channel interference. | disable |
| auto-power-low <dBm_int> | Set automatic power level low limit, in dBm. Range 0 to 17dBm. | 10 |
| auto-power-high <dBm_int> | Set automatic power level high limit, in dBm. Range 0 to 17dBm. | 17 |
| band {802.11a ¦ 802.11b ¦ 802.11g ¦ 802.11n ¦ 802.11n-5G} | Enter the wireless band to use. Available bands depend on the capabilities of the radio. 802.11n-5G is 802.11n on the 5GHz band. | No default. |
| beacon-interval <integer> | Set the interval between beacon packets. Access Points broadcast beacons or Traffic Indication Messages (TIM) to synchronize wireless networks. In an environment with high interference, decreasing the beacon-interval might improve network performance. In a location with few wireless nodes, you can increase this value. | 100 |

Fortinet Technologies Inc.                                                                Page 887                                     FortiOS™ - CLI Reference for FortiOS 5.0

| Variable | Description | Default |
| --- | --- | --- |
| channel <channels_string> | Enter a list of the radio channels your access point can use. Separate the channel numbers with spaces. The AP will use the least busy of the listed channels. To determine which channels are available for your selected radio band and geography, enter set channel ? | No default. |
| channel-bonding {enable ¦ disable} | Available for config radio-2 only. | disable |
| darrp {enable ¦ disable} | Enable Distributed Automatic Radio Resource Provisioning. | disable |
| dtim <int> | Set the interval for Delivery Traffic Indication Message (DTIM). Range is 1 to 255. | 1 |
| frag-threshold <int> | Set the maximum packet size that can be sent without fragmentation. Range is 800 to 2346 bytes. | 2346 |
| max-supported-mcs <mcs_int> | Range 0 - 31. | 15 |
| mode <mode_string> | Select one of the following modes for the access point: ap — Radio provides wireless Access Point service. monitor — Radio performs scanning only. disable — Radio is not used. | ap |
| power-level <dBm> | Set transmitter power level in dBm. Range 0 to 17. | 17 |
| rts-threshold <int> | Set the packet size for RTS transmissions. Range 256 to 2346 bytes. | 2346 |
| short-guard-interval {enable ¦ disable} | Optionally, enabling this option might increase the data rate. | disable |
| station-locate {enable ¦ disable} | Enable station location for all clients, associated or not. | disable |
| vaps {vap1 ... vapn> | Set the virtual access points carried on this physical access point. | No default. |
| wids-profile <wids-profile_name> | Enter the WIDS profile name. | No default. |

Fortinet Technologies Inc.                                                                Page 888                                     FortiOS™ - CLI Reference for FortiOS 5.0

execute

The execute commands perform immediate operations on the FortiGate unit, including:

•  Maintenance operations, such as back up and restore the system configuration, reset the configuration to factory settings, update antivirus and attack definitions, set the date and time.

•  Network operations, such as view and clear DHCP leases, clear arp table entries, use ping or traceroute to diagnose network problems.

•  View and delete log messages. Delete old log files.

•  Generate certificate requests and install certificates for VPN authentication.

This chapter contains the following sections:

backup batch

bypass-mode carrier-license central-mgmt cfg reload

cfg save

clear system arp table

cli check-template-status cli status-msg-only

client-reputation date

disk

disk raid

dhcp lease-clear dhcp lease-list

disconnect-admin-session enter

factoryreset factoryreset2 formatlogdisk forticarrier-license forticlient fortiguard-log fortisandbox test-

connectivity

fortitoken fortitoken-mobile fsso refresh

ha disconnect

ha ignore-hardware-revision ha manage

ha synchronize

interface dhcpclient-renew interface pppoe-reconnect log client-reputation-report

log convert-oldlogs log delete-all

log delete-oldlogs log delete-rolled log display

log filter

log fortianalyzer test-connectivity log list

log rebuild-sqldb log recreate-sqldb log-report reset

log roll

log upload-progress modem dial

modem hangup modem trigger mrouter clear netscan

pbx ping

ping-options, ping6-options ping6

policy-packet-capture  delete-all reboot

report

report-config reset restore

revision

router clear bfd session router clear bgp

router clear ospf process router restart

send-fds-statistics

set system session filter set-next-reboot

sfp-mode-sgmii

shutdown ssh

sync-session tac report telnet

time traceroute tracert6 update-ase update-av update-geo-ip update-ips update-now

update-src-vis upd-vd-license upload

usb-device usb-disk

vpn certificate ca vpn certificate crl vpn certificate local

vpn certificate remote vpn ipsec tunnel down vpn ipsec tunnel up vpn sslvpn del-all

vpn sslvpn del-tunnel vpn sslvpn del-web vpn sslvpn list

wireless-controller delete-wtp-image wireless-controller list-wtp-image wireless-controller reset-wtp

wireless-controller restart-acd wireless-controller restart-wtpd wireless-controller upload-wtp-image

Page 889

backup

Back up the FortiGate configuration files, logs, or IPS user-defined signatures file to a TFTP or FTP server, USB disk, or a management station. Management stations can either be a FortiManager unit, or FortiGuard Analysis and Management Service. For more information, see “system fortiguard” on page 512 or “system central-management” on page 490.

When virtual domain configuration is enabled (in system global, vdom-admin is enabled), the content of the backup file depends on the administrator account that created it.

•  A backup of the system configuration from the super admin account contains the global settings and the settings for all of the VDOMs. Only the super admin can restore the configuration from this file.

•  When you back up the system configuration from a regular administrator account, the backup file contains the global settings and the settings for the VDOM to which the administrator belongs. Only a regular administrator account can restore the configuration from this file.

Syntax

execute backup config flash <comment>

execute backup config ftp <filename_str> <server_ipv4[:port_int] | server_fqdn[:port_int]> [<username_str> [<password_str>]] [<backup_password_str>]

execute backup config management-station <comment_str>

execute backup config tftp <filename_str> <server_ipv4> [<backup_password_str>]

execute backup config usb <filename_str> [<backup_password_str>]

execute backup config usb-mode [<backup_password_str>]

execute backup full-config ftp <filename_str> <server_ipv4[: port_int] | server_fqdn[:port_int]> [<username_str> [<password_str>]] [<backup_password_str>]

execute backup full-config tftp <filename_str> <server_ipv4> [<backup_password_str>]

execute backup full-config usb <filename_str> [<backup_password_str>]

execute backup ipsuserdefsig ftp <filename_str> <server_ipv4[: port_int] | server_fqdn[:port_int]> [<username_str> [<password_str>]]

execute backup ipsuserdefsig tftp tftp <filename_str> <server_ipv4>

execute backup {disk | memory} alllogs ftp <server_ipv4[:port_int] |

server_fqdn[:port_int]> [<username_str> <password_str>]

execute backup {disk | memory} alllogs tftp <server_ipv4>

execute backup {disk | memory} log ftp <server_ipv4[:port_int] |

server_fqdn[:port_int]> <username_str> <password_str> {app-ctrl

| event | ids | im | spam | virus | voip | webfilter}

execute backup {disk | memory} log {ftp | tftp} <server_ipv4> netscan

Fortinet Technologies Inc.                                                                Page 890                                     FortiOS™ - CLI Reference for FortiOS 5.0

| Variable | Description |
| --- | --- |
| config flash <comment> | Back up the system configuration to the flash disk. Optionally, include a comment. |
| config ftp <filename_str> <server_ipv4[: port_int] ¦ server_fqdn[:port_int]> [<username_str> [<password_str>]] [<backup_password_str>] | Back up the system configuration to an FTP server. Optionally, you can specify a password to protect the saved data. |
| config management-station <comment_str> | Back up the system configuration to a configured management station. If you are adding a comment, do not add spaces, underscore characters (_), or quotation marks (“ “) or any other punctuation marks. For example, uploadedthetransparentmodeconfigfortheaccoun tingdepartmentwilluploadonadailybasis. The comment you enter displays in both the portal website and FortiGate web-based manager (System > Maintenance > Revision). |
| config tftp <filename_str> <server_ipv4> [<backup_password_str>] | Back up the system configuration to a file on a TFTP server. Optionally, you can specify a password to protect the saved data. |
| config usb <filename_str> [<backup_password_str>] | Back up the system configuration to a file on a USB disk. Optionally, you can specify a password to protect the saved data. |
| config usb-mode [<backup_password_str>] | Back up the system configuration to a USB disk. Optionally, you can specify a password to protect the saved data. |
| full-config ftp <filename_str> <server_ipv4[: port_int] ¦ server_fqdn[:port_int]> [<username_str> [<password_str>]] [<backup_password_str>] | Back up the full system configuration to a file on an FTP server. You can optionally specify a password to protect the saved data. |
| full-config tftp <filename_str> <server_ipv4> [<backup_password_str>] | Back up the full system configuration to a file on a TFTP server. You can optionally specify a password to protect the saved data. |
| full-config usb <filename_str> [<backup_password_str>] | Back up the full system configuration to a file on a USB disk. You can optionally specify a password to protect the saved data. |
| ipsuserdefsig ftp <filename_str> <server_ipv4[:port_int] ¦ server_fqdn[: port_int]> [<username_str> [<password_str>]] | Backup IPS user-defined signatures to a file on an FTP server. |
| ipsuserdefsig tftp tftp <filename_str> <server_ipv4> | Back up IPS user-defined signatures to a file on a TFTP server. |
| {disk ¦ memory} alllogs ftp <server_ipv4[: port_int] ¦ server_fqdn[:port_int]> [<username_str> <password_str>] | Back up either all memory or all hard disk log files for this VDOM to an FTP server. The disk option is available on FortiGate models that log to a hard disk. The file name has the form: <log_file_name>_<VDOM>_<date>_<time> |

Fortinet Technologies Inc.                                                                Page 891                                     FortiOS™ - CLI Reference for FortiOS 5.0

| Variable | Description |
| --- | --- |
| {disk ¦ memory} alllogs tftp <server_ipv4> | Back up either all memory or all hard disk log files for this VDOM to a TFTP server. he disk option is available on FortiGate models that log to a hard disk. The file name has the form: <log_file_name>_<VDOM>_<date>_<time> |
| {disk ¦ memory} log ftp <server_ipv4[: port_int] ¦ server_fqdn[:port_int]> <username_str> <password_str> {app-ctrl ¦ event ¦ ids ¦ im ¦ spam ¦ virus ¦ voip ¦ webfilter} | Back up the specified type of log file from either hard disk or memory to an FTP server. he disk option is available on FortiGate models that log to a hard disk. |
| {disk ¦ memory} log tftp <server_ipv4> {app-ctrl ¦ event ¦ ids ¦ im ¦ spam ¦ virus ¦ voip ¦ webfilter} | Back up the specified type of log file from either hard disk or memory to an FTP server. The disk option is available on FortiGate models that log to a hard disk. |
| {disk ¦ memory} log {ftp ¦ tftp} <server_ipv4> netscan | Back up the specified type of log file from either hard disk or memory to FTP or TFTP server. The disk option is available on FortiGate models that log to a hard disk. |

Example

This example shows how to backup the FortiGate unit system configuration to a file named

fgt.cfg on a TFTP server at IP address 192.168.1.23.

execute backup config tftp fgt.cfg 192.168.1.23

batch

Execute a series of CLI commands.

execute batch commands are controlled by the Maintenance (mntgrp) access control     group.

Syntax

execute batch [<cmd_cue>]

where <cmd_cue> is one of:

•  end — exit session and run the batch commands

•  lastlog — read the result of the last batch commands

•  start — start batch mode

•  status — batch mode status reporting if batch mode is running or stopped

Example

To start batch mode:

execute batch start

Enter batch mode...

To enter commands to run in batch mode:

config system global set refresh 5

end

To execute the batch commands:

execute batch end

Exit and run batch commands...

bypass-mode

Use this command to manually switch a FortiGate-600C or FortiGate-1000C into bypass mode. This is available in transparent mode only. If manually switched to bypass mode, the unit remains in bypass-mode until bypass mode is disabled.

Syntax

execute bypass-mode {enable | disable}

carrier-license

Use this command to enter a l FortiOS Carrier license key if you have installed a FortiOS Carrier build on a FortiGate unit and need to enter a license key to enable FortiOS Carrier functionality.

Contact Fortinet Support for more information about this command.

Syntax

execute carrier-license <license_key>

| Variable | Description |
| --- | --- |
| <license_key> | Enter the FortiOS Carrier license key supplied by Fortinet. |

central-mgmt

Update Central Management Service account information. Also used receive configuration file updates from an attached FortiManager unit.

Syntax

execute central-mgmt set-mgmt-id <management_id>

execute central-mgmt register-device <fmg-serial-number>

<fmg-register-password> <fgt-user-name> <fgt-password>

execute central-mgmt unregister-device <fmg-serial-number>

set-mgmt-id is used to change or initially set the management ID, or your account number for

Central Management Services. This account ID must be set for the service to be enabled.

register-device registers the FortiGate unit with a specific FortiManager unit specified by serial number. You must also specify the administrator name and password that the FortiManager unit uses to log on to the FortiGate unit.

unregister-device removes the FortiGate unit from the specified FortiManager unit’s device list.

update is used to update your Central Management Service contract with your new management account ID. This command is to be used if there are any changes to your management service account.

Example

If you are registering with the Central Management Service for the first time, and your account number is 123456, you would enter the following:

execute central-mgmt set-mgmt-id 123456

cfg  reload

Use this command to restore the saved configuration when the configuration change mode is manual or revert. This command has no effect if the mode is automatic, the default. The set cfg-save command in system global sets the configuration change mode.

When you reload the saved system configuration, the your session ends and the FortiGate unit restarts.

In the default configuration change mode, automatic, CLI commands become part of the saved unit configuration when you execute them by entering either next or end.

In manual mode, commands take effect but do not become part of the saved configuration unless you execute the execute cfg save command. When the FortiGate unit restarts, the saved configuration is loaded. Configuration changes that were not saved are lost.

The revert mode is similar to manual mode, except that configuration changes are saved automatically if the administrative session is idle for more than a specified timeout period. This provides a way to recover from an erroneous configuration change, such as changing the IP address of the interface you are using for administration. You set the timeout in

system global using the set cfg-revert-timeout command.

Syntax

execute cfg reload

Example

This is sample output from the command when successful:

# execute cfg reload

configs reloaded. system will reboot.This is sample output from the command when not in runtime-only configuration mode:

# execute cfg reload

no config to be reloaded.

cfg  save

Use this command to save configuration changes when the configuration change mode is manual or revert. If the mode is automatic, the default, all changes are added to the saved configuration as you make them and this command has no effect. The set cfg-save command in system global sets the configuration change mode.

In manual mode, commands take effect but do not become part of the saved configuration unless you execute the execute cfg save command. When the FortiGate unit restarts, the saved configuration is loaded. Configuration changes that were not saved are lost.

The revert mode is similar to manual mode, except that configuration changes are reverted automatically if the administrative session is idle for more than a specified timeout period. This provides a way to recover from an erroneous configuration change, such as changing the IP address of the interface you are using for administration. To change the timeout from the default of 600 seconds, go to system global and use the set cfg-revert-timeout command.

Syntax

execute cfg save

Example

This is sample output from the command:

# execute cfg save config saved.

This is sample output when not in runtime-only configuration mode. It also occurs when in runtime-only configuration mode and no changes have been made:

# execute cfg save

no config to be saved.

clear system arp table

Clear all the entries in the arp table.

Syntax

execute clear system arp table

cli check-template-status

Reports the status of the secure copy protocol (SCP) script template.

Syntax

execute cli check-template-status

cli status-msg-only

Enable or disable displaying standardized CLI error output messages. If executed, this command stops other debug messages from displaying in the current CLI session. This command is used for compatibility with FortiManager.

Syntax

execute cli status-msg-only [enable | disable]

| Variable | Description | Default |
| --- | --- | --- |
| status-msg-only [enable ¦ disable] | Enable or disable standardized CLI error output messages. Entering the command without enable or disable disables displaying standardized output. | enable |

client-reputation

Use these commands to retrieve or remove client reputation information.

Syntax

To erase all client reputation data

execute client-reputation erase

To retrieve client reputation host count

execute client-reputation host-count <rows>

To retrieve client reputation host details

execute client-reputation host detail <host>

To retrieve client reputation host summary

execute client-reputation host summary <host>

To purge old data

execute client-reputation purge

To view the top n records

execute client-reputation <n | all>

date

Get or set the system date.

Syntax

execute date [<date_str>]

date_str has the form yyyy-mm-dd, where

•  yyyy is the year and can be 2001 to 2037

•  mm is the month and can be 01 to 12

•  dd is the day of the month and can be 01 to 31

If you do not specify a date, the command returns the current system date. Shortened values, such as ‘06’ instead of ‘2006’ for the year or ‘1’ instead of ‘01’ for month or day, are not valid.

Example

This example sets the date to 17 September 2004:

execute date 2004-09-17

disk

Use this command to list and format hard disks installed in FortiGate units or individual partitions on these hard disks.

Syntax

execute disk format <partition1_ref_int> [...<partitionn_ref_int>]

execute disk list

| Variable | Description |
| --- | --- |
| format | Format the referenced disk partitions or disks. Separate reference numbers with spaces. If you enter a partition reference number the disk partition is formatted. If you enter a disk reference number the entire disk and all of its partitions are formatted. |
| list | List the disks and partitions and the reference number for each one. |
| <ref_int> | Disk (device) or partition reference number. |

The execute disk format command formats the specified partitions or disks and then reboots the system if a reboot is required.

In most cases you need to format the entire disk only if there is a problem with the partition. Formatting the partition removes all data from the partition. Formatting the disk removes all data from the entire disk and creates a single partition on the disk.

Examples

Use the following command to list the disks and partitions.

execute disk list

| Device I1 | 29.9 GB | ref: 256 | SUPER TALENT (IDE) |
| --- | --- | --- | --- |
| partition 1 | 29.9 GB | ref: 257 | label: 224E6EE7177E1652 |

In this example (for a FortiGate-51B), the disk (device) reference number is 256 and the reference number for the single partition is 257.

Enter the following command to format the partition.

execute disk format 257

After a confirmation message the FortiGate unit formats the partition and restarts. This can take a few minutes.

Enter the following command to format the entire disk.

execute disk format 256

After a confirmation message the FortiGate unit formats the disk, restores the original partition, and restarts. This can take a few minutes.

disk  raid

Use this command to view information about and change the raid settings on FortiGate units that support RAID.

Syntax

execute disk raid disable execute disk raid rebuild

execute disk raid rebuild-level {Raid-0 | Raid-1 | Raid-5}

execute disk raid status

| Variable | Description |
| --- | --- |
| disable | Disable raid for the FortiGate unit. |
| rebuild | Rebuild RAID on the FortiGate unit at the same RAID level. You can only execute this command if a RAID error has been detected. Changing the RAID level takes a while and deletes all data on the disk array. |
| rebuild-level {Raid-0 ¦ Raid-1 ¦ Raid-5} | Change the RAID level on the FortiGate unit. |
| status | Display information about the RAID disk array in the FortiGate unit. |

Examples

Use the following command to display information about the RAID disk array in a FortiGate-

82C.

execute disk raid status

RAID Level: Raid-1

RAID Status: OK RAID Size: 1000GB

| Disk | 1: | OK | Used | 1000GB |
| --- | --- | --- | --- | --- |
| Disk | 2: | OK | Used | 1000GB |
| Disk | 3: | OK | Used | 1000GB |
| Disk | 4: | Unavailable | Not-Used | 0GB |

dhcp  lease-clear

Clear all DHCP address leases.

Syntax

For IPv4:

execute dhcp lease-clear

For IPv6

execute dhcp6 lease-clear

dhcp  lease-list

Display DHCP leases on a given interface

Syntax

For IPv4:

execute dhcp lease-list [interface_name]

For IPv6:

execute dhcp6 lease-list [interface_name]

If you specify an interface, the command lists only the leases issued on that interface. Otherwise, the list includes all leases issued by DHCP servers on the FortiGate unit.

If there are no DHCP leases in user on the FortiGate unit, an error will be returned.

disconnect-admin-session

Disconnect an administrator who is logged in.

Syntax

execute disconnect-admin-session <index_number>

To determine the index of the administrator that you want to disconnect, view the list of logged- in administrators by using the following command:

execute disconnect-admin-session ? The list of logged-in administrators looks like this: Connected:

INDEX   USERNAME     TYPE      FROM               TIME

0       admin        WEB       172.20.120.51      Mon Aug 14 12:57:23

2006

1       admin2       CLI       ssh(172.20.120.54) Mon Aug 14 12:57:23

2006

Example

This example shows how to disconnect the logged administrator admin2 from the above list.

execute disconnect-admin-session 1

enter

Use this command to go from global commands to a specific virtual domain (VDOM). Only available when virtual domains are enabled and you are in config global.

After you enter the VDOM, the prompt will not change from “(global)”. However you will be in the VDOM with all the commands that are normally available in VDOMs.

Syntax

execute enter <vdom>

Use “?” to see a list of available VDOMs.

factoryreset

Reset the FortiGate configuration to factory default settings.

Syntax

execute factoryreset

This procedure deletes all changes that you have made to the FortiGate configuration and reverts the system to its original configuration, including resetting interface addresses.

factoryreset2

Reset the FortiGate configuration to factory default settings except VDOM and interface settings.

Syntax

execute factoryreset2

formatlogdisk

Format the FortiGate hard disk to enhance performance for logging.

Syntax

execute formatlogdisk

In addition to deleting logs, this operation will erase all other data on the disk, including system configuration, quarantine files, and databases for antivirus and IPS.

forticarrier-license

Use this command to perform a FortiCarrier license upgrade.

Syntax

execute forticarrier-license <activation-code>

forticlient

Use these commands to manage FortiClient licensing.

Syntax

To view FortiClient license information

execute forticlient info

To show current FortiClient count

execute forticlient list <connection_type>

where <connection_type> is one of:

•  0 - IPsec

•  1 - SSLVPN

•  2 - NAC (Endpoint Security)

•  3 - WAN optimization

•  4 - Test

To upgrade  FortiClient licenses

execute forticlient upgrade <license_key_str>

fortiguard-log

Use this to manage FortiGuard Analysis and Management Service (FortiCloud) operation.

Syntax

To create a FortiCloud account

execute fortiguard-log create-account

To activity FortiCloud certification

execute fortiguard-log certification

To retrieve the FortiCloud agreement

execute fortiguard-log agreement

To log in to a FortiCloud account

execute fortiguard-log login <account-id> <password>

To update the FortiGuard Analysis and Management Service contract

execute fortiguard-log update

fortisandbox test-connectivity

Use this command to query FortiSandbox connection status.

Syntax

execute fortisandbox test-connectivity

fortitoken

Use these commands to activate and synchronize a FortiToken device. FortiToken devices are used in two-factor authentication of administrator and user account logons. The device generates a random six-digit code that you enter during the logon process along with user name and password.

Before they can be used to authenticate account logins, FortiToken devices must be activated with the FortiGuard service. When successfully activated, the status of the FortiToken device will change from New to Active.

Synchronization is sometimes needed due to the internal clock drift of the FortiToken device. It is not unusual for new FortiToken units to require synchronization before being put into service. Synchronization is accomplished by entering two sequential codes provided by the FortiToken.

Syntax

To activate  one or more FortiToken devices

execute fortitoken activate <serial_number> [serial_number2 ... serial_numbern]

To import FortiToken OTP seeds

execute fortitoken import <seeds_file> <seeds_file_preshared_key>

To synchronize a FortiToken device

execute fortitoken sync <serial_number> <code> <next code>

fortitoken-mobile

Use these commands to activate and synchronize a FortiToken Mobile card. FortiToken Mobile cards are used in two-factor authentication of administrator and user account logons. The FortiGate unit sends a random six-digit code to the mobile device by email or SMS that the user enters during the logon process along with user name and password.

Syntax

To import the FortiToken Mobile card serial number

execute fortitoken-mobile import <activation_code>

To poll a FortiToken Mobile token state

execute fortitoken-mobile poll

To provision a FortiToken Mobile token

execute fortitoken-mobile provision <token_serial_number>

fsso  refresh

Use this command to manually refresh user group information from Directory Service servers connected to the FortiGate unit using the Fortinet Single Sign On (FSSO) agent.

Syntax

execute fsso refresh

ha disconnect

Use this command to disconnect a FortiGate unit from a functioning cluster. You must specify the serial number of the unit to be disconnected. You must also specify an interface name and assign an IP address and netmask to this interface of the disconnected unit. You can disconnect any unit from the cluster even the primary unit. After the unit is disconnected the cluster responds as if the disconnected unit has failed. The cluster may renegotiate and may select a new primary unit.

To disconnect the unit from the cluster, the execute ha disconnect command sets the HA mode of the disconnected unit to standalone. In addition, all interface IP addresses of the disconnected unit are set to 0.0.0.0. The interface specified in the command is set to the IP address and netmask that you specify in the command. In addition all management access to this interface is enabled. Once the FortiGate unit is disconnected you can use SSH, telnet, HTTPS, or HTTP to connect to and manage the FortiGate unit.

Syntax

execute ha disconnect <cluster-member-serial_str> <interface_str>

<address_ipv4> <address_ipv4mask>

| Variable | Description |
| --- | --- |
| cluster-member-serial_str | The serial number of the cluster unit to be disconnected. |
| interface_str | The name of the interface to configure. The command configures the IP address and netmask for this interface and also enables all management access for this interface. |

Example

This example shows how to disconnect a cluster unit with serial number FGT5002803033050. The internal interface of the disconnected unit is set to IP address 1.1.1.1 and netmask

255.255.255.0.

execute ha disconnect FGT5002803033050 internal 1.1.1.1 255.255.255.0

ha ignore-hardware-revision

Use this command to set ignore-hardware-revision status.

Syntax

To view ignore-hardware-revision status

execute ha ignore-hardware-revision status

To set ignore-hardware-revision status

execute ha ignore-hardware-revision {enable | disable}

ha manage

Use this command from the CLI of a FortiGate unit in an HA cluster to log into the CLI of another unit in the cluster. Usually you would use this command from the CLI of the primary unit to log into the CLI of a subordinate unit. However, if you have logged into a subordinate unit CLI, you can use this command to log into the primary unit CLI, or the CLI of another subordinate unit.

You can use CLI commands to manage the cluster unit that you have logged into. If you make changes to the configuration of any cluster unit (primary or subordinate unit) these changes are synchronized to all cluster units.

Syntax

execute ha manage <cluster-index>

| Variable | Description |
| --- | --- |
| cluster-index | The cluster index is assigned by the FortiGate Clustering Protocol according to cluster unit serial number. The cluster unit with the highest serial number has a cluster index of 0. The cluster unit with the second highest serial number has a cluster index of 1 and so on. Enter ? to list the cluster indexes of the cluster units that you can log into. The list does not show the unit that you are already logged into. |

Example

This example shows how to log into a subordinate unit in a cluster of three FortiGate units. In this example you have already logged into the primary unit. The primary unit has serial number FGT3082103000056. The subordinate units have serial numbers FGT3012803021709 and FGT3082103021989.

execute ha manage ?

<id>    please input slave cluster index.

<0>     Subsidary unit FGT3012803021709

<1>     Subsidary unit FGT3082103021989

Type 0 and press enter to connect to the subordinate unit with serial number FGT3012803021709. The CLI prompt changes to the host name of this unit. To return to the primary unit, type exit.

From the subordinate unit you can also use the execute ha manage command to log into the primary unit or into another subordinate unit. Enter the following command:

execute ha manage ?

<id>    please input slave cluster index.

<1>     Subsidary unit FGT3082103021989

<2>     Subsidary unit FGT3082103000056

Type 2 and press enter to log into the primary unit or type 1 and press enter to log into the other subordinate unit. The CLI prompt changes to the host name of this unit.

ha synchronize

Use this command from a subordinate unit in an HA cluster to manually synchronize its configuration with the primary unit. Using this command you can synchronize the following:

•  Configuration changes made to the primary unit (normal system configuration, firewall configuration, VPN configuration and so on stored in the FortiGate configuration file),

You can also use the start and stop fields to force the cluster to synchronize its configuration or to stop a synchronization process that is in progress.

Syntax

execute ha synchronize {config| start | stop}

| Variable | Description |
| --- | --- |
| config | Synchronize the FortiGate configuration. |
| start | Start synchronizing the cluster configuration. |
| stop | Stop the cluster from completing synchronizing its configuration. |

interface dhcpclient-renew

Renew the DHCP client for the specified DHCP interface and close the CLI session. If there is no DHCP connection on the specified port, there is no output.

Syntax

execute interface dhcpclient-renew <port>

Example

This is the output for renewing the DHCP client on port1 before the session closes:

# execute interface dhcpclient-renew port1 renewing dhcp lease on port1

interface pppoe-reconnect

Reconnect to the PPPoE service on the specified PPPoE interface and close the CLI session. If there is no PPPoE connection on the specified port, there is no output.

Syntax

execute interface pppoe-reconnect <port>

log client-reputation-report

Use these commands to control client-reputation log actions.

Syntax

To accept  a host so that it has its own baselines

execute log client-reputation-report accept <policy-id> <host>

To clear all auto-profile data

execute log client-reputation-report clear

To ignore a host, removing  it from the abnormal list

execute log client-reputation-report ignore <policy-id> <host>

To refresh the data of one option  result

execute log client-reputation-report refresh <policy-id> <option>

<action>

•  <option> is one of bandwidth, session, failconn, geo, or app

•  <action> is one of data, baseline, or data_baseline (both data and baseline)

To get baseline/average information of one option

execute log client-reputation-report result baseline <policy-id>

<option>

•  <option> is one of bandwidth, session, or failconn

To get hourly data of a host visiting  a country  or using an application

execute log client-reputation-report result details {hourly | total}

<policy-id> <option> <name> <host>

•  <option> is geo or app

•  <name> is the name of the country or application

To list abnormal hosts of one or all options

execute log client-reputation-report result list <policy-id> <option>

•  <option> is geo, app, or all

To list periodical data of one host of one option

execute log client-reputation-report result period <policy-id>

<option> <host> <periods>

•  <option> is one of bandwidth, session, failconn, geo, or app

•  <periods> is number of periods to list

To list the top 10 abnormal hosts of one option

execute log client-reputation-report result top10 <policy-id>

<option>

•  <option> is one of bandwidth, session, failconn, geo, or app

To run reports immediately

execute log client-reputation-report run <policy-id>

log convert-oldlogs

Use this command to convert old compact logs to the new format. This command is available only if you have upgraded from an earlier version of FortiOS and have old compact logs on your system.

Syntax

execute log convert-oldlogs

log delete-all

Use this command to clear all log entries in memory and current log files on hard disk. If your FortiGate unit has no hard disk, only log entries in system memory will be cleared. You will be prompted to confirm the command.

Syntax

execute log delete-all

log delete-oldlogs

Use this command to delete old compact logs. This command is available only if you have upgraded from an earlier version of FortiOS and have old compact logs on your system.

Syntax

execute log delete-oldlogs

log delete-rolled

Use this command to delete rolled log files.

Syntax

execute log delete-rolled <category> <start> <end>

| Variable | Description |
| --- | --- |
| <category> | Enter the category of rolled log files that you want to delete: • traffic • event • virus • webfilter • attack • spam • content • im • voip • dlp • app-crtl The <category> must be one of the above categories. The FortiGate unit can only delete one category at a time. |
| <start> | Enter the number of the first log to delete. If you are deleting multiple rolled log files, you must also enter a number for end. The <start> and <end> values represent the range of rolled log files to delete. If <end> is not specified, only the <start> log number is deleted. |
| <end> | Enter the number of the last log to delete, if you are deleting multiple rolled log files. The <start> and <end> values represent the range of rolled log files to delete. If <end> is not specified, only the <start> log number is deleted. |

Example

The following deletes all event rolled logs from 1 to 50.

execute log delete-rolled event 1 50

log display

Use this command to display log messages that you have selected with the execute log filter command.

Syntax

execute log display

The console displays the first 10 log messages. To view more messages, run the command again. You can do this until you have seen all of the selected log messages. To restart viewing the list from the beginning, use the commands

execute log filter start-line 1 execute log display

You can restore the log filters to their default values using the command

execute log filter reset

log filter

Use this command to select log messages for viewing or deletion. You can view one log category on one device at a time. Optionally, you can filter the messages to select only specified date ranges or severities of log messages. For traffic logs, you can filter log messages by source or destination IP address.

Commands are cumulative. If you omit a required variable, the command displays the current setting.

Use as many execute log filter commands as you need to define the log messages that you want to view.

execute log filter category <category_name> execute log filter device {disk | memory} execute log filter dump

execute log filter field <name>

execute log filter ha-member <unitsn_str>

execute log filter reset

execute log filter rolled_number <number> execute log filter start-line <line_number> execute log filter view-lines <count>

| Variable | Description | Default |
| --- | --- | --- |
| category <category_name> | Enter the type of log you want to select. For SQL logging and memory logging, one of: • utm • netscan • content • event • traffic For other logging, one of: • netscan • traffic • event • virus • webfilter • spam • attack • content • dlp • app-crtl | event |
| device {disk ¦ memory} | Device where the logs are stored. | disk |
| dump | Display current filter settings. | No default. |
| field <name> | Press Enter to view the fields that are available for the associated category. Enter the fields you want, using commas to separate multiple fields. | No default. |

| Variable | Description | Default |
| --- | --- | --- |
| ha-member <unitsn_str> | Select logs from the specified HA cluster member. Enter the serial number of the unit. |  |
| reset | Execute this command to reset all filter settings. | No default. |
| rolled_number <number> | Select logs from rolled log file. 0 selects current log file. | 0 |
| start-line <line_number> | Select logs starting at specified line number. | 1 |
| view-lines <count> | Set lines per view. Range: 5 to 1000 | 10 |

Fortinet Technologies Inc.                                                                Page 933                                     FortiOS™ - CLI Reference for FortiOS 5.0

log fortianalyzer test-connectivity

Use this command to test the connection to the FortiAnalyzer unit. This command is available only when FortiAnalyzer is configured.

Syntax

execute log fortianalyzer test-connectivity

Example

When FortiAnalyzer is connected, the output looks like this:

FortiAnalyzer Host Name: FortiAnalyzer-800B FortiGate Device ID: FG50B3G06500085

Registration: registered

Connection: allow

Disk Space (Used/Allocated): 468/1003 MB Total Free Space: 467088 MB

Log: Tx & Rx

Report: Tx & Rx

Content Archive: Tx & Rx

Quarantine: Tx & Rx

When FortiAnalyzer is not connected, the output is: Connect Error

log list

You can view the list of current and rolled log files on the console. The list shows the file name, size and timestamp.

Syntax

execute log list <category>

<category> must be one of: traffic, event, virus, webfilter, attack, spam,

content, im, voip, dlp, and app-ctrl.

| Example |  |
| --- | --- |
| The output looks like this: |  |
| elog | 8704 | Fri | March | 6 | 14:24:35 | 2009 |
| elog.1 | 1536 | Thu | March | 5 | 18:02:51 | 2009 |
| elog.2 | 35840 | Wed | March | 4 | 22:22:47 | 2009 |

At the end of the list, the total number of files in the category is displayed. For example:

501 event log file(s) found.

log rebuild-sqldb

Use this command to rebuild the SQL database from log files.

If run in the VDOM context, only this VDOM’s SQL database is rebuilt. If run in the global context, the SQL database is rebuilt for all VDOMs.

If SQL logging is disabled, this command is unavailable.

Syntax

execute log rebuild-sqldb

log recreate-sqldb

Use this command to recreate SQL log database.

If SQL logging is disabled, this command is unavailable.

Syntax

execute log recreate-sqldb

log-report reset

Use this command to delete all logs, archives and user configured report templates.

Syntax

execute log-report reset

log roll

Use this command to roll all log files.

Syntax

execute log roll

log upload-progress

Use this command to display the progress of the latest log upload.

Syntax

execute log upload-progress

modem dial

Dial the modem.

The dial command dials the accounts configured in config system modem until it makes a connection or it has made the maximum configured number of redial attempts.

This command can be used if the modem is in Standalone mode.

Syntax

execute modem dial

modem hangup

Hang up the modem.

This command can be used if the modem is in Standalone mode.

Syntax

execute modem hangup

modem trigger

This command sends a signal to the modem daemon, which causes the state machine to re- evaluate its current state. If for some reason the modem should be connected but isn't, then it will trigger a redial. If the modem should not be connected but is, this command will cause the modem to disconnect.

Syntax

execute modem trigger

mrouter clear

Clear multicast routes, RP-sets, IGMP membership records or routing statistics.

Syntax

Clear IGMP memberships:

execute mrouter clear igmp-group {{<group-address>} <interface- name>}

execute mrouter clear igmp-interface <interface-name>

Clear multicast routes:

execute mrouter clear <route-type> {<group-address>

{<source-address>}}

Clear PIM-SM RP-sets learned from the bootstrap router (BSR):

execute mrouter clear sparse-mode-bsr

Clear statistics:

execute mrouter clear statistics {<group-address>

{<source-address>}}

| Variable | Description |
| --- | --- |
| <interface-name> | Enter the name of the interface on which you want to clear IGMP memberships. |
| <group-address> | Optionally enter a group address to limit the command to a particular group. |
| <route-type> | Enter one of: • dense-routes - clear only PIM dense routes • multicast-routes - clear all types of multicast routes • sparse-routes - clear only sparse routes |
| <source-address> | Optionally, enter a source address to limit the command to a particular source address. You must also specify group-address. |

netscan

Use this command to start and stop the network vulnerability scanner and perform related functions.

Syntax

execute netscan import execute netscan list execute netscan start scan execute netscan status execute netscan stop

Variable           Description

import                Import hosts discovered on the last asset discovery scan. list                      List the hosts discovered on the last asset discover scan. start scan            Start configured vulnerability scan.

status                  Display the status of the current network vulnerability scan.

stop                    Stop the current network vulnerability scan.

pbx

Use this command to view active channels and to delete, list or upload music files for when music is playing while a caller is on hold.

Syntax

execute pbx active-call <list>

execute pbx extension <list>

execute pbx ftgd-voice-pkg {sip-trunk}

execute pbx music-on-hold {delete | list | upload}

execute pbx prompt upload ftp <file.tgz> <ftp_server_address>[:port] [<username>] [password>]

execute pbx prompt upload tftp <file.tgz> <ftp_server_address>[:port] [<username>] [password>]

execute pbx prompt upload usb <file.tgz> <ftp_server_address>[:port] [<username>] [password>]

execute pbx restore-default-prompts execute pbx sip-trunk list

| Variables | Description |
| --- | --- |
| active-call <list> | Enter to display a list of the active calls being processed by the FortiGate Voice unit. |
| extension <list> | Enter to display the status of all extensions with SIP phones that have connected to the FortiGate Voice unit. |
| ftgd-voice-pkg {sip-trunk} | Enter to retrieve FortiGuard voice package sip trunk information. |
| music-on-hold {delete ¦ list ¦ upload} | Enter to either delete, list or upload music on hold files. You can upload music on hold files using FTP, TFTP, or from a USB drive plugged into the FortiGate Voice unit. |
| prompt upload ftp <file.tgz> <ftp_server_address>[:port] [<username>] [password>] | Upload new pbx voice prompt files using FTP. The voice prompt files should be added to a tar file and zipped. This file would usually have the extension tgz. You must include the filename, FTP server address (domain name of IPv4 address) and if required the username and password for the server. |
| prompt upload tftp <file.tgz> <ftp_server_address>[:port] [<username>] [password>] | Upload new pbx voice prompt files using TFTP. The voice prompt files should be added to a tar file and zipped. This file would usually have the extension tgz. You must include the filename and TFTP server IP address. |
| prompt upload usb <file.tgz> <ftp_server_address>[:port] [<username>] [password>] | Upload new pbx voice prompt files from a USB drive plugged into the FortiGate Voice unit. The voice prompt files should be added to a tar file and zipped. This file would usually have the extension tgz. You must include the filename. |
| restore-default-prompts | Restore default English voicemail and other PBX system prompts. Use this command if you have changed the default prompts and want to restore the default settings. |
| sip-trunk list | Enter to display the status of all SIP trunks that have been added to the FortiGate Voice configuration. |

Example command output

Enter the following command to view active calls:

execute pbx active-call

| Call-From | Call-To | Durationed |
| --- | --- | --- |
| 6016 | 6006 | 00:00:46 |

Enter the following command to display the status of all extensions

execute pbx extension list

Extension  Host                 Dialplan

6052      Unregister          company-default

6051      Unregister          company-default

6050      Unregister          company-default

6022      Unregister          company-default

6021/6021 172.30.63.34        company-default

6020      Unregister          company-default

Enter the following command to display the status of all SIP trunks

execute pbx sip-trunk list

ping

Send an ICMP echo request (ping) to test the network connection between the FortiGate unit and another network device.

Syntax

execute ping {<address_ipv4> | <host-name_str>}

<host-name_str> should be an IP address, or a fully qualified domain name.

Example

This example shows how to ping a host with the IP address 172.20.120.16.

#execute ping 172.20.120.16

PING 172.20.120.16 (172.20.120.16): 56 data bytes

64 bytes from 172.20.120.16: icmp_seq=0 ttl=128 time=0.5 ms

64 bytes from 172.20.120.16: icmp_seq=1 ttl=128 time=0.2 ms

64 bytes from 172.20.120.16: icmp_seq=2 ttl=128 time=0.2 ms

64 bytes from 172.20.120.16: icmp_seq=3 ttl=128 time=0.2 ms

64 bytes from 172.20.120.16: icmp_seq=4 ttl=128 time=0.2 ms

--- 172.20.120.16 ping statistics ---

5 packets transmitted, 5 packets received, 0% packet loss round-trip min/avg/max = 0.2/0.2/0.5 ms

ping-options, ping6-options

Set ICMP echo request (ping) options to control the way ping tests the network connection between the FortiGate unit and another network device.

Syntax

execute ping-options data-size <bytes> execute ping-options df-bit {yes | no} execute ping-options pattern <2-byte_hex> execute ping-options repeat-count <repeats>

execute ping-options source {auto | <source-intf_ip>}

execute ping-options timeout <seconds> execute ping-options tos <service_type> execute ping-options ttl <hops>

execute ping-options validate-reply {yes | no}

execute ping-options view-settings

| Variable | Description | Default |
| --- | --- | --- |
| data-size <bytes> | Specify the datagram size in bytes. | 56 |
| df-bit {yes ¦ no} | Set df-bit to yes to prevent the ICMP packet from being fragmented. Set df-bit to no to allow the ICMP packet to be fragmented. | no |
| pattern <2-byte_hex> | Used to fill in the optional data buffer at the end of the ICMP packet. The size of the buffer is specified using the data_size parameter. This allows you to send out packets of different sizes for testing the effect of packet size on the connection. | No default. |
| repeat-count <repeats> | Specify how many times to repeat ping. | 5 |
| source {auto ¦ <source- intf_ip>} | Specify the FortiGate interface from which to send the ping. If you specify auto, the FortiGate unit selects the source address and interface based on the route to the <host-name_str> or <host_ip>. Specifying the IP address of a FortiGate interface tests connections to different network segments from the specified interface. | auto |
| timeout <seconds> | Specify, in seconds, how long to wait until ping times out. | 2 |
| tos <service_type> | Set the ToS (Type of Service) field in the packet header to provide an indication of the quality of service wanted. • lowdelay = minimize delay • throughput = maximize throughput • reliability = maximize reliability • lowcost = minimize cost | 0 |
| ttl <hops> | Specify the time to live. Time to live is the number of hops the ping packet should be allowed to make before being discarded or returned. | 64 |
| validate-reply {yes ¦ no} | Select yes to validate reply data. | no |
| view-settings | Display the current ping-option settings. | No default. |

Example

Use the following command to increase the number of pings sent.

execute ping-options repeat-count 10

Use the following command to send all pings from the FortiGate interface with IP address

192.168.10.23.

execute ping-options source 192.168.10.23

ping6

Send an ICMP echo request (ping) to test the network connection between the FortiGate unit and an IPv6 capable network device.

Syntax

execute ping6 {<address_ipv6> | <host-name_str>}

Example

This example shows how to ping a host with the IPv6 address 12AB:0:0:CD30:123:4567:

89AB:CDEF.

execute ping6 12AB:0:0:CD30:123:4567:89AB:CDEF

policy-packet-capture delete-all

Use this command to delete captured packets.

Syntax

execute policy-packet-capture delete-all

You will be asked to confirm that you want delete the packets.

reboot

Restart the FortiGate unit.

Abruptly powering off your FortiGate unit may corrupt its configuration. Using the reboot and shutdown options here or in the web-based manager ensure proper shutdown procedures are followed to prevent any loss of configuration.

Syntax

execute reboot <comment “comment_string”>

<comment “comment_string”> allows you to optionally add a message that will appear in the hard disk log indicating the reason for the reboot. If the message is more than one word it must be enclosed in quotes.

Example

This example shows the reboot command with a message included.

execute reboot comment “December monthly maintenance”

report

Use these commands to manage reports.

Syntax

To flash report  caches:

execute report flash-cache

To recreate  the report  database:

execute report recreate-db

To generate a report:

execute report run [<layout_name>["start-time" "end-time"]]

The start and end times have the format yyyy-mm-dd hh:mm:ss

report-config reset

Use this command to reset report templates to the factory default. Logs are not deleted.

If SQL logging is disabled, this command is unavailable.

Syntax

execute report-config reset

restore

Use this command to

•  restore the configuration from a file

•  change the FortiGate firmware

•  change the FortiGate backup firmware

•  restore an IPS custom signature file

When virtual domain configuration is enabled (in system global, vdom-admin is enabled), the content of the backup file depends on the administrator account that created it.

•  A backup of the system configuration from the super admin account contains the global settings and the settings for all of the VDOMs. Only the super admin account can restore the configuration from this file.

•  A backup file from a regular administrator account contains the global settings and the settings for the VDOM to which the administrator belongs. Only a regular administrator account can restore the configuration from this file.

Syntax

execute restore ase ftp <filename_str> <server_ipv4[:port_int]

| server_fqdn[:port_int]> [<username_str> <password_str>] execute restore ase tftp <filename_str> <server_ipv4[:port_int]> execute restore av ftp <filename_str> <server_ipv4[:port_int]

| server_fqdn[:port_int]> [<username_str> <password_str>]

execute restore av tftp <filename_str> <server_ipv4[:port_int]>

execute restore config flash <revision>

execute restore config ftp <filename_str> <server_ipv4[:port_int]

| server_fqdn[:port_int]> [<username_str> <password_str>] [<backup_password_str>]

execute restore config management-station {normal | template

| script} <rev_int>

execute restore config tftp <filename_str> <server_ipv4> [<backup_password_str>]

execute restore config usb <filename_str> [<backup_password_str>]

execute restore config usb-mode [<backup_password_str>] execute restore forticlient tftp <filename_str> <server_ipv4> execute restore image flash <revision>

execute restore image ftp <filename_str> <server_ipv4[:port_int]

| server_fqdn[:port_int]> [<username_str> <password_str>]

execute restore image management-station <version_int> execute restore image tftp <filename_str> <server_ipv4> execute restore image usb <filename_str>

execute restore ips ftp <filename_str> <server_ipv4[:port_int]

| server_fqdn[:port_int]> [<username_str> <password_str>]

execute restore ips tftp <filename_str> <server_ipv4>

execute restore ipsuserdefsig ftp <filename_str> <server_ipv4[:

port_int] | server_fqdn[:port_int]> [<username_str>

<password_str>]

execute restore ipsuserdefsig tftp <filename_str> <server_ipv4>

execute restore secondary-image ftp <filename_str> <server_ipv4[:

port_int] | server_fqdn[:port_int]> [<username_str>

<password_str>]

execute restore secondary-image tftp <filename_str> <server_ipv4>

execute restore secondary-image usb <filename_str>

execute restore src-vis <src-vis-pkgfile>

execute restore vcm {ftp | tftp} <filename_str> <server_ipv4>

execute restore vmlicense {ftp | tftp} <filename_str> <server_ipv4>

| Variable | Description |
| --- | --- |
| ase ftp <filename_str> <server_ipv4[:port_int] ¦ server_fqdn[:port_int]> [<username_str> <password_str>] | Restore the antispam engine. Download the restore file from an FTP server. The user and password to access the FTP server are only necessary if the server requires them |
| ase tftp <filename_str> <server_ipv4[:port_int]> | Restore the antispam engine. Download the restore file from a TFTP server. |
| av ftp <filename_str> <server_ipv4[:port_int] ¦ server_fqdn[:port_int]> [<username_str> <password_str>] | Download the antivirus database file from an FTP server to the FortiGate unit. |
| av tftp <filename_str> <server_ipv4[:port_int]> | Download the antivirus database file from a TFTP server to the FortiGate unit. |
| config flash <revision> | Restore the specified revision of the system configuration from the flash disk. |
| config ftp <filename_str> <server_ipv4[:port_int] ¦ server_fqdn[:port_int]> [<username_str> <password_str>] [<backup_password_str>] | Restore the system configuration from an FTP server. The new configuration replaces the existing configuration, including administrator accounts and passwords. If the backup file was created with a password, you must specify the password. |
| config management-station {normal ¦ template ¦ script} <rev_int> | Restore the system configuration from the central management server. The new configuration replaces the existing configuration, including administrator accounts and passwords. rev_int is the revision number of the saved configuration to restore. Enter 0 for the most recent revision. |
| config tftp <filename_str> <server_ipv4> [<backup_password_str>] | Restore the system configuration from a file on a TFTP server. The new configuration replaces the existing configuration, including administrator accounts and passwords. If the backup file was created with a password, you must specify the password. |
| config usb <filename_str> [<backup_password_str>] | Restore the system configuration from a file on a USB disk. The new configuration replaces the existing configuration, including administrator accounts and passwords. If the backup file was created with a password, you must specify the password. |

| Variable | Description |
| --- | --- |
| config usb-mode [<backup_password_str>] | Restore the system configuration from a USB disk. The new configuration replaces the existing configuration, including administrator accounts and passwords. When the USB drive is removed, the FortiGate unit needs to reboot and revert to the unit’s existing configuration. If the backup file was created with a password, you must specify the password. |
| forticlient tftp <filename_str> <server_ipv4> | Download the FortiClient image from a TFTP server to the FortiGate unit. The filename must have the format: FortiClientSetup_versionmajor.versionminor.build.exe. For example, FortiClientSetup.4.0.377.exe. |
| image flash <revision> | Restore specified firmware image from flash disk. |
| image ftp <filename_str> <server_ipv4[:port_int] ¦ server_fqdn[:port_int]> [<username_str> <password_str>] | Download a firmware image from an FTP server to the FortiGate unit. The FortiGate unit reboots, loading the new firmware. This command is not available in multiple VDOM mode. |
| image management-station <version_int> | Download a firmware image from the central management station. This is available if you have configured a FortiManager unit as a central management server. This is also available if your account with FortiGuard Analysis and Management Service allows you to upload firmware images. |
| image tftp <filename_str> <server_ipv4> | Download a firmware image from a TFTP server to the FortiGate unit. The FortiGate unit reboots, loading the new firmware. This command is not available in multiple VDOM mode. |
| image usb <filename_str> | Download a firmware image from a USB disk to the FortiGate unit. The FortiGate unit reboots, loading the new firmware. |
| ips ftp <filename_str> <server_ipv4[:port_int] ¦ server_fqdn[:port_int]> [<username_str> <password_str>] | Download the IPS database file from an FTP server to the FortiGate unit. |
| ips tftp <filename_str> <server_ipv4> | Download the IPS database file from a TFTP server to the FortiGate unit. |
| ipsuserdefsig ftp <filename_str> <server_ipv4[:port_int] ¦ server_fqdn[:port_int]> [<username_str> <password_str>] | Restore IPS custom signature file from an FTP server. The file will overwrite the existing IPS custom signature file. |
| ipsuserdefsig tftp <filename_str> <server_ipv4> | Restore an IPS custom signature file from a TFTP server. The file will overwrite the existing IPS custom signature file. |
| secondary-image ftp <filename_str> <server_ipv4[:port_int] ¦ server_fqdn[:port_int]> [<username_str> <password_str>] | Download a firmware image from an FTP server as the backup firmware of the FortiGate unit. Available on models that support backup firmware images. |

Fortinet Technologies Inc.                                                                Page 958                                     FortiOS™ - CLI Reference for FortiOS 5.0

| Variable | Description |
| --- | --- |
| secondary-image tftp <filename_str> <server_ipv4> | Download a firmware image from a TFTP server as the backup firmware of the FortiGate unit. Available on models that support backup firmware images. |
| secondary-image usb <filename_str> | Download a firmware image from a USB disk as the backup firmware of the FortiGate unit. The unit restarts when the upload is complete. Available on models that support backup firmware images. |
| src-vis <src-vis-pkgfile> | Download source visibility signature package. |
| vcm {ftp ¦ tftp} <filename_str> <server_ipv4> | Restore VCM engine/plugin from an ftp or tftp server. |
| vmlicense {ftp ¦ tftp} <filename_str> <server_ipv4> | Restore VM license (VM version of product only). |

Example

This example shows how to upload a configuration file from a TFTP server to the FortiGate unit and restart the FortiGate unit with this configuration. The name of the configuration file on the TFTP server is backupconfig. The IP address of the TFTP server is 192.168.1.23.

execute restore config tftp backupconfig 192.168.1.23

revision

Use these commands to manage configuration and firmware image files on the local disk.

Syntax

To delete a configuration file

execute revision delete config <revision>

To delete a firmware image file

execute revision delete image <revision>

To list the configuration files

execute revision list config

To delete a firmware image file

execute revision list image

router clear bfd session

Use this command to clear bi-directional forwarding session.

Syntax

execute router clear bfd session <src_ip> <dst_ip> <interface>

| Variable | Description |
| --- | --- |
| <src_ip> | Select the source IP address of the session. |
| <dst_ip> | Select the destination IP address of the session. |
| <interface> | Select the interface for the session. |

router clear bgp

Use this command to clear BGP peer connections.

Syntax

execute router clear bgp all [soft] [in | out]

execute router clear bgp as <as_number> [soft] [in | out] execute router clear bgp dampening {ip_address | ip/netmask} execute router clear bgp external {in prefix-filter} [soft] [in |

out]

execute router clear bgp flap-statistics {ip_address | ip/netmask}

execute router clear bgp ip <ip_address> [soft] [in | out]

| Variable | Description |
| --- | --- |
| all | Clear all BGP peer connections. |
| as <as_number> | Clear BGP peer connections by AS number. |
| dampening {ip_address ¦ ip/netmask} | Clear route flap dampening information for peer or network. |
| external {in prefix-filter} | Clear all external peers. |
| ip <ip_address> | Clear BGP peer connections by IP address. |
| peer-group | Clear all members of a BGP peer-group. |
| [in ¦ out] | Optionally limit clear operation to inbound only or outbound only. |
| flap-statistics {ip_address ¦ ip/netmask} | Clear flap statistics for peer or network. |
| soft | Do a soft reset that changes the configuration but does not disturb existing sessions. |

router clear ospf  process

Use this command to clear and restart the OSPF router.

Syntax

IPv4:

execute router clear ospf process

IPv6:

execute router clear ospf6 process

router restart

Use this command to restart the routing software.

Syntax

execute router restart

send-fds-statistics

Use this command to send an FDS statistics report now, without waiting for the FDS statistics report interval to expire.

Syntax

execute send-fds-statistics

set system session filter

Use these commands to define the session filter for get system session commands.

Syntax

To clear the filter settings

execute set system session filter clear

{all|dport|dst|duration|expire|policy|proto|sport|src|vd}

To specify  destination port

execute set system session filter dport <port_range>

To specify  destination IP address

execute set system session filter dst <ip_range>

To specify  duration

execute set system session filter duration <duration_range>

To specify  expiry

execute set system session filter expire <expire_range>

To list the filter settings

execute set system session filter list

To invert a filter setting

execute set system session filter negate

{dport|dst|duration|expire|policy|proto|sport|src|vd}

To specify  firewall policy ID

execute set system session filter policy <policy_range>

To specify  protocol

execute set system session filter proto <protocol_range>

To specify  source port

execute set system session filter sport <port_range>

To specify  source IP address

execute set system session filter src <ip_range>

To specify  virtual domain

execute set system session filter vd <vdom_index>

| Variable | Description |
| --- | --- |
| <duration_range> | The start and end times, separated by a space. |
| <expire_range> | The start and end times, separated by a space. |
| <ip_range> | The start and end IP addresses, separated by a space. |
| <policy_range> | The start and end policy numbers, separated by a space. |
| <port_range> | The start and end port numbers, separated by a space. |

| Variable | Description |
| --- | --- |
| <protocol_range> | The start and end protocol numbers, separated by a space. |
| <vdom_index> | The VDOM index number. -1 means all VDOMs. |

Fortinet Technologies Inc.                                                                Page 967                                     FortiOS™ - CLI Reference for FortiOS 5.0

set-next-reboot

Use this command to start the FortiGate unit with primary or secondary firmware after the next reboot. Available on models that can store two firmware images. By default, the FortiGate unit loads the firmware from the primary partition.

VDOM administrators do not have permission to run this command. It must be executed by a super administrator.

Syntax

execute set-next-reboot {primary | secondary}

sfp-mode-sgmii

Change the SFP mode for an NP2 card to SGMII. By default when an AMC card is inserted the

SFP mode is set to SERDES mode by default.

If a configured NP2 card is removed and re-inserted, the SFP mode goes back to the default.

In these situations, the sfpmode-sgmii command will change the SFP mode from SERDES to

SGMII for the interface specified.

Syntax

execute sfpmode-sgmii <interface>

<interface> is the NP2 interface where you are changing the SFP mode.

shutdown

Shut down the FortiGate unit now. You will be prompted to confirm this command.

Abruptly powering off your FortiGate unit may corrupt its configuration. Using the reboot and shutdown options here or in the web-based manager ensure proper shutdown procedures are followed to prevent any loss of configuration.

Syntax

execute shutdown [comment <comment_string>]

comment is optional but you can use it to add a message that will appear in the event log message that records the shutdown. The comment message of the does not appear on the Alert Message console. If the message is more than one word it must be enclosed in quotes.

Example

This example shows the reboot command with a message included.

execute shutdown comment “emergency facility shutdown”

An event log message similar to the following is recorded:

2009-09-08 11:12:31 critical admin 41986 ssh(172.20.120.11) shutdown User admin shutdown the device from ssh(172.20.120.11). The reason is 'emergency facility shutdown'

ssh

Use this command to establish an ssh session with another system.

Syntax

execute ssh <destination>

<destination> - the destination in the form user@ip or user@host.

Example

execute ssh admin@172.20.120.122

To end an ssh session, type exit:

FGT-6028030112 # exit

Connection to 172.20.120.122 closed. FGT-8002805000 #

sync-session

Use this command to force a session synchronization.

Syntax

execute sync-session

tac  report

Use this command to create a debug report to send to Fortinet Support. Normally you would only use this command if requested to by Fortinet Support.

Syntax

execute tac report

telnet

Use telnet client. You can use this tool to test network connectivity.

Syntax

execute telnet <telnet_ipv4>

<telnet_ipv4> is the address to connect with. Type exit to close the telnet session.

time

Get or set the system time.

Syntax

execute time [<time_str>]

time_str has the form  hh:mm:ss, where

•  hh is the hour and can be 00 to 23

•  mm is the minutes and can be 00 to 59

•  ss is the seconds and can be 00 to 59

If you do not specify a time, the command returns the current system time.

You are allowed to shorten numbers to only one digit when setting the time. For example both

01:01:01 and 1:1:1 are allowed.

Example

This example sets the system time to 15:31:03:

execute time 15:31:03

traceroute

Test the connection between the FortiGate unit and another network device, and display information about the network hops between the device and the FortiGate unit.

Syntax

execute traceroute {<ip_address> | <host-name>}

Example

This example shows how to test the connection with http://docs.forticare.com. In this example the traceroute command times out after the first hop indicating a possible problem.

#execute traceoute docs.forticare.com

traceroute to docs.forticare.com (65.39.139.196), 30 hops max, 38 byte packets

1  172.20.120.2 (172.20.120.2)  0.324 ms  0.427 ms  0.360 ms

2  * * *

If your FortiGate unit is not connected to a working DNS server, you will not be able to connect to remote host-named locations with traceroute.

tracert6

Test the connection between the FortiGate unit and another network device using IPv6 protocol, and display information about the network hops between the device and the FortiGate unit.

Syntax

tracert6 [-Fdn] [-f first_ttl] [-i interface] [-m max_ttl] [-s src_addr] [-q nprobes] [-w waittime] [-z sendwait]

host [paddatalen]

| Variable | Description |
| --- | --- |
| -F | Set Don’t Fragment bit. |
| -d | Enable debugging. |
| -n | Do not resolve numeric address to domain name. |
| -f <first_ttl> | Set the initial time-to-live used in the first outgoing probe packet. |
| -i <interface> | Select interface to use for tracert. |
| -m <max_ttl> | Set the max time-to-live (max number of hops) used in outgoing probe packets. |
| -s <src_addr> | Set the source IP address to use in outgoing probe packets. |
| -q <nprobes> | Set the number probes per hop. |
| -w <waittime> | Set the time in seconds to wait for response to a probe. Default is 5. |
| -z <sendwait> | Set the time in milliseconds to pause between probes. |
| host | Enter the IP address or FQDN to probe. |
| <paddatalen> | Set the packet size to use when probing. |

update-ase

Use this command to manually initiate the antispam engine and rules update.

Syntax

execute update-ase

update-av

Use this command to manually initiate the virus definitions and engines update. To update both virus and attack definitions, use the execute update-now command.

Syntax

execute update-av

update-geo-ip

Use this command to obtain an update to the IP geography database from FortiGuard.

Syntax

execute update-geo-ip

update-ips

Use this command to manually initiate the Intrusion Prevention System (IPS) attack definitions and engine update. To update both virus and attack definitions, use the execute update-now command.

Syntax

execute update-ips

update-now

Use this command to manually initiate both virus and attack definitions and engine updates. To initiate only virus or attack definitions, use the execute update-av or execute update- ids command respectively.

Syntax

execute update-now

update-src-vis

Use this command to trigger an FDS update of the source visibility signature package.

Syntax

execute update-src-vis

upd-vd-license

Use this command to enter a Virtual Domain (VDOM) license key.

If you have a FortiGate- unit that supports VDOM licenses, you can purchase a license key from Fortinet to increase the maximum number of VDOMs to 25, 50, 100 or 500. By default, FortiGate units support a maximum of 10 VDOMs.

Available on FortiGate models that can be licensed for more than 10 VDOMs.

Syntax

execute upd-vd-license <license_key>

| Variable | Description |
| --- | --- |
| <license_key> | The license key is a 32-character string supplied by Fortinet. Fortinet requires your unit serial number to generate the license key. |

upload

Use this command to upload system configurations and firmware images to the flash disk from

FTP, TFTP, or USB sources.

Syntax

To upload configuration files:

execute upload config ftp <filename_str> <comment> <server_ipv4[: port_int] | server_fqdn[:port_int]> [<username_str> [<password_str>]] [<backup_password_str>]

execute upload config tftp <filename_str> <comment> <server_ipv4>

execute upload config usb <filename_str> <comment>

To upload firmware image files:

execute upload image ftp <filename_str> <comment> <server_ipv4[: port_int] | server_fqdn[:port_int]> [<username_str> [<password_str>]]

execute upload image tftp <filename_str> <comment> <server_ipv4>

execute upload image usb <filename_str> <comment>

To upload report  image files:

execute upload report-img ftp <filename_str> <server_ipv4[:port_int]

| server_fqdn[:port_int]> [<username_str> [<password_str>]]

execute upload report-img tftp <filename_str> <server_ipv4>

| Variable | Description |
| --- | --- |
| <comment> | Comment string. |
| <filename_str> | Filename to upload. |
| <server_fqdn[:port_int]> | Server fully qualified domain name and optional port. |
| <server_ipv4[:port_int]> | Server IP address and optional port number. |
| <username_str> | Username required on server. |
| <password_str> | Password required on server. |
| <backup_password_str> | Password for backup file. |

usb-device

Use these commands to manage FortiExplorer IOS devices.

Syntax

List connected FortiExplorer IOS devices

execute usb-device list

Disconnect FortiExplorer IOS devices

execute usb-device disconnect

usb-disk

Use these commands to manage your USB disks.

Syntax

execute usb-disk delete <filename>

execute usb-disk format execute usb-disk list

execute usb-disk rename <old_name> <new_name>

| Variable | Description |
| --- | --- |
| delete <filename> | Delete the named file from the USB disk. |
| format | Format the USB disk. |
| list | List the files on the USB disk. |
| rename <old_name> <new_name> | Rename a file on the USB disk. |

vpn certificate ca

Use this command to import a CA certificate from a TFTP or SCEP server to the FortiGate unit, or to export a CA certificate from the FortiGate unit to a TFTP server.

Before using this command you must obtain a CA certificate issued by a CA.

Digital certificates are used to ensure that both participants in an IPSec communications session are trustworthy, prior to an encrypted VPN tunnel being set up between the participants. The CA certificate is the certificate that the FortiGate unit uses to authenticate itself to other devices.

VPN peers must use digital certificates that adhere to the X.509 standard.

Digital certificates are not required for configuring FortiGate VPNs. Digital certificates are an advanced feature provided for the convenience of system administrators. This manual assumes the user has prior knowledge of how to configure digital certificates for their implementation.

Syntax

execute vpn certificate ca export tftp <certificate-name_str>

<file-name_str> <tftp_ip>

execute vpn certificate ca import auto <ca_server_url>

<ca_identifier_str>

execute vpn certificate ca import tftp <file-name_str> <tftp_ip>

| Variable | Description |
| --- | --- |
| import | Import the CA certificate from a TFTP server to the FortiGate unit. |
| export | Export or copy the CA certificate from the FortiGate unit to a file on the TFTP server. Type ? for a list of certificates. |
| <certificate-name_str> | Enter the name of the CA certificate. |
| <file-name_str> | Enter the file name on the TFTP server. |
| <tftp_ip> | Enter the TFTP server address. |
| auto | Retrieve a CA certificate from a SCEP server. |
| tftp | Import the CA certificate to the FortiGate unit from a file on a TFTP server (local administrator PC). |
| <ca_server_url> | Enter the URL of the CA certificate server. |
| <ca_identifier_str> | CA identifier on CA certificate server (optional). |

Examples

Use the following command to import the CA certificate named trust_ca to the FortiGate unit from a TFTP server with the address  192.168.21.54.

execute vpn certificate ca import trust_ca 192.168.21.54

vpn certificate crl

Use this command to get a CRL via LDAP, HTTP, or SCEP protocol, depending on the auto- update configuration.

In order to use the command execute vpn certificate crl, the authentication servers must already be configured.

Digital certificates are used to ensure that both participants in an IPSec communications session are trustworthy, prior to an encrypted VPN tunnel being set up between the participants. The CA certificate is the certificate that the FortiGate unit uses to authenticate itself to other devices.

VPN peers must use digital certificates that adhere to the X.509 standard.

Digital certificates are not required for configuring FortiGate VPNs. Digital certificates are an advanced feature provided for the convenience of system administrators. This manual assumes the user has prior knowledge of how to configure digital certificates for their implementation.

Syntax

execute vpn certificate crl import auto <crl-name>

| Variable | Description |
| --- | --- |
| import | Import the CRL from the configured LDAP, HTTP, or SCEP authentication server to the FortiGate unit. |
| <crl-name> | Enter the name of the CRL. |
| auto | Trigger an auto-update of the CRL from the configured LDAP, HTTP, or SCEP authentication server. |

vpn certificate local

Use this command to generate a local certificate, to export a local certificate from the FortiGate unit to a TFTP server, and to import a local certificate from a TFTP server to the FortiGate unit.

Digital certificates are used to ensure that both participants in an IPSec communications session are trustworthy, prior to an encrypted VPN tunnel being set up between the participants. The local certificate is the certificate that the FortiGate unit uses to authenticate itself to other devices.

When you generate a certificate request, you create a private and public key pair for the local FortiGate unit. The public key accompanies the certificate request. The private key remains confidential.

When you receive the signed certificate from the CA, use the vpn certificate local

command to install it on the FortiGate unit.

VPN peers must use digital certificates that adhere to the X.509 standard.

Digital certificates are not required for configuring FortiGate VPNs. Digital certificates are an advanced feature provided for the convenience of system administrators. This manual assumes the user has prior knowledge of how to configure digital certificates for their implementation.

Syntax - generate

execute vpn certificate local generate <certificate-name_str>

<key-length> {<host_ip> | <domain-name_str> | email-addr_str>} [<optional_information>]

| Variable | Description |
| --- | --- |
| <certificate-name_str> | Enter a name for the certificate. The name can contain numbers (0- 9), uppercase and lowercase letters (A-Z, a-z), and the special characters - and _. Other special characters and spaces are not allowed. |
| <host_ip> |  |
| {<host_ip> ¦ <domain-name_str> ¦ email-addr_str>} | Enter the host IP address (host_ip), the domain name (domain-name_str), or an email address (email-addr_str) to identify the FortiGate unit being certified. Preferably use an IP address or domain name. If this is impossible (such as with a dialup client), use an e-mail address. For host_ip, enter the IP address of the FortiGate unit. For domain-name_str, enter the fully qualified domain name of the FortiGate unit. For email-addr_str, enter an email address that identifies the FortiGate unit. If you specify a host IP or domain name, use the IP address or domain name associated with the interface on which IKE negotiations will take place (usually the external interface of the local FortiGate unit). If the IP address in the certificate does not match the IP address of this interface (or if the domain name in the certificate does not match a DNS query of the FortiGate unit’s IP), then some implementations of IKE may reject the connection. Enforcement of this rule varies for different IPSec products. |

| Variable | Description |
| --- | --- |
| <key-length> | Enter 1024, 1536 or 2048 for the size in bits of the encryption key. |
| [<optional_information>] | Enter optional_information as required to further identify the certificate. See “Optional information variables” on page 991 for the list of optional information variables. You must enter the optional variables in order that they are listed in the table. To enter any optional variable you must enter all of the variables that come before it in the list. For example, to enter the organization_name_str, you must first enter the country_code_str, state_name_str, and city_name_str. While entering optional variables, you can type ? for help on the next required variable. |

Optional  information variables

| Variable | Description |
| --- | --- |
| <country_code_str> | Enter the two-character country code. Enter execute vpn certificates local generate <name_str> country followed by a ? for a list of country codes. The country code is case sensitive. Enter null if you do not want to specify a country. |
| <state_name_str> | Enter the name of the state or province where the FortiGate unit is located. |
| <city_name_str> | Enter the name of the city, or town, where the person or organization certifying the FortiGate unit resides. |
| <organization-name_str> | Enter the name of the organization that is requesting the certificate for the FortiGate unit. |
| <organization-unit_name_str> | Enter a name that identifies the department or unit within the organization that is requesting the certificate for the FortiGate unit. |
| <email_address_str> | Enter a contact e-mail address for the FortiGate unit. |
| <ca_server_url> | Enter the URL of the CA (SCEP) certificate server that allows auto-signing of the request. |
| <challenge_password> | Enter the challenge password for the SCEP certificate server. |

Example - generate

Use the following command to generate a local certificate request with the name

branch_cert, the domain name www.example.com and a key size of 1536.

execute vpn certificate local generate branch_cert 1536 www.example.com

Syntax - import/export

execute vpn certificate local import tftp <file-name_str> <tftp_ip>

execute vpn certificate local export tftp <certificate-name_str>

<file-name_str> <tftp_ip>

| Variable | Description |
| --- | --- |
| import | Import the local certificate from a TFTP server to the FortiGate unit. |
| export | Export or copy the local certificate from the FortiGate unit to a file on the TFTP server. Type ? for a list of certificates. |
| <certificate-name_str> | Enter the name of the local certificate. |
| <tftp_ip> | Enter the TFTP server address. |
| <file-name_str> | Enter the file name on the TFTP server. |
| list | List local certificates. |

Examples - import/export

Use the following command to export the local certificate request generated in the above example from the FortiGate unit to a TFTP server. The example uses the file name testcert for the downloaded file and the TFTP server address 192.168.21.54.

execute vpn certificate local export branch_cert testcert

192.168.21.54

Use the following command to import the signed local certificate named branch_cert to the

FortiGate unit from a TFTP server with the address 192.168.21.54.

execute vpn certificate local import branch_cert 192.168.21.54

vpn certificate remote

Use this command to import a remote certificate from a TFTP server, or export a remote certificate from the FortiGate unit to a TFTP server. The remote certificates are public certificates without a private key. They are used as OCSP (Online Certificate Status Protocol) server certificates.

Syntax

execute vpn certificate remote import tftp <file-name_str> <tftp_ip>

execute vpn certificate remote export tftp <certificate-name_str>

<file-name_str> <tftp_ip>

| Field/variable | Description |
| --- | --- |
| import | Import the remote certificate from the TFTP server to the FortiGate unit. |
| export | Export or copy the remote certificate from the FortiGate unit to a file on the TFTP server. Type ? for a list of certificates. |
| <certificate-name_str> | Enter the name of the public certificate. |
| <file-name_str> | Enter the file name on the TFTP server. |
| <tftp_ip> | Enter the TFTP server address. |
| tftp | Import/export the remote certificate via a TFTP server. |

vpn ipsec tunnel down

Use this command to shut down an IPsec VPN tunnel.

Syntax

execute vpn ipsec tunnel down <phase2> [<phase1> <phase2_serial>]

where:

•  <phase2> is the phase 2 name

•  <phase1> is the phase 1 name

•  <phase2_serial> is the phase 2 serial number

<phase1> is required on a dial-up tunnel.

vpn ipsec tunnel up

Use this command to activate an IPsec VPN tunnel.

Syntax

execute vpn ipsec tunnel up <phase2> [<phase1> <phase2_serial>]

where:

•  <phase2> is the phase 2 name

•  <phase1> is the phase 1 name

•  <phase2_serial> is the phase 2 serial number

This command cannot activate a dial-up tunnel.

vpn sslvpn del-all

Use this command to delete all SSL VPN connections in this VDOM.

Syntax

execute vpn sslvpn del-all

vpn sslvpn del-tunnel

Use this command to delete an SSL tunnel connection.

Syntax

execute vpn sslvpn del-tunnel <tunnel_index>

<tunnel_index> identifies which tunnel to delete if there is more than one active tunnel.

vpn sslvpn del-web

Use this command to delete an active SSL VPN web connection.

Syntax

execute vpn sslvpn del-web <web_index>

<web_index> identifies which web connection to delete if there is more than one active connection.

vpn sslvpn list

Use this command to list current SSL VPN tunnel connections.

Syntax

execute vpn sslvpn list {web | tunnel}

wireless-controller delete-wtp-image

Use this command to delete all firmware images for WLAN Termination Points (WTPs), also known as physical access points.

Syntax

execute wireless-controller delete-wtp-image

wireless-controller list-wtp-image

Use this command to list all firmware images for WLAN Termination Points (WTPs), also known as WiFi physical access points.

Syntax

execute wireless-controller list-wtp-image

| Example output |  |
| --- | --- |
| WTP Images on AC: ImageName | ImageSize(B) | ImageInfo ImageMTime |
| FAP22A-IMG.wtp | 3711132 | FAP22A-v4.0-build212 Mon Jun 6 |

12:26:41 2011

wireless-controller reset-wtp

Use this command to reset a physical access point (WTP).

If the FortiGate unit has a more recent version of the FortiAP firmware, the FortiAP unit will download and install it. Use the command execute wireless-controller upload-wtp-image to upload FortiAP firmware to the FortiGate unit.

Syntax

execute wireless-controller reset-wtp {<serialNumber_str> | all}

where <serialNumber_str> is the FortiWiFi unit serial number. Use the all option to reset all APs.

wireless-controller restart-acd

Use this command to restart the wireless-controller daemon.

Syntax

execute wireless-controller restart-acd

wireless-controller restart-wtpd

Use this command to restart the wireless access point daemon.

Syntax

execute wireless-controller restart-wtpd

wireless-controller upload-wtp-image

Use this command to upload a FortiWiFi firmware image to the FortiGate unit. Wireless APs controlled by this wireless controller can download the image as needed. Use the execute wireless-controller reset-wtp command to trigger FortiAP units to update their firmware.

Syntax

FTP:

execute wireless-controller upload-wtp-image ftp <filename_str>

<server_ipv4[:port_int]> [<username_str> <password_str>]

TFTP:

execute wireless-controller upload-wtp-image tftp <filename_str>

<server_ipv4>

get

The get commands retrieve information about the operation and performance of your FortiGate unit.

This chapter contains the following sections:

endpoint-control app-detect firewall dnstranslation firewall iprope appctrl

firewall iprope list firewall proute, proute6 firewall service predefined firewall shaper

grep

gui console status gui topology status hardware cpu hardware memory hardware nic hardware npu hardware status

ips decoder status ips rule status

ips session ipsec tunnel ips view-map

netscan settings pbx branch-office pbx dialplan

pbx did

pbx extension

pbx ftgd-voice-pkg pbx global

pbx ringgrp pbx sip-trunk pbx voice-menu

report database schema

router info bfd neighbor router info bgp

router info gwdetect router info isis

router info kernel router info multicast router info ospf router info protocols router info rip

router info routing-table router info vrrp

router info6 bgp router info6 interface router info6 kernel router info6 ospf router info6 protocols router info6 rip

router info6 routing-table system admin list

system admin status system arp

system auto-update

system central-management system checksum

system cmdb status

system fortianalyzer-connectivity system fortiguard-log-service status system fortiguard-service status system ha-nonsync-csum

system ha status system info admin ssh system info admin status

system interface physical system mgmt-csum

system performance firewall system performance status system performance top system session list

system session status

system session-helper-info list system session-info

system source-ip

system startup-error-log system status

test

user adgrp

vpn ike gateway

vpn ipsec tunnel details vpn ipsec tunnel name vpn ipsec stats crypto vpn ipsec stats tunnel vpn ssl monitor

vpn status l2tp vpn status pptp vpn status ssl

webfilter ftgd-statistics webfilter status

wireless-controller rf-analysis wireless-controller scan wireless-controller status wireless-controller vap-status wireless-controller wlchanlistlic wireless-controller wtp-status

endpoint-control app-detect

Use this command to retrieve information about predefined application detection signatures for

Endpoint NAC.

Syntax

get endpoint-control app-detect predefined-category status get endpoint-control app-detect predefined-group status

get endpoint-control app-detect predefined-signature status get endpoint-control app-detect predefined-vendor status

Example output (partial)

get endpoint-control app-detect predefined-category status

FG200A2907500558 # get endpoint-control app-detect predefined-category status

name: "Anti-Malware Software" id: 1

group: 1

name: "Authentication and Authorization" id: 2

group: 1

name: "Encryption, PKI" id: 3

group: 1

name: "Firewalls" id: 4

group: 1

get endpoint-control app-detect predefined-group status

FG200A2907500558 # get endpoint-control app-detect predefined-group status

name: "Security" id: 1

name: "Multimedia" id: 2

name: "Communication" id: 3

name: "Critical Functions" id: 4

get endpoint-control app-detect predefined-signature status

FG200A2907500558 # get endpoint-control app-detect predefined-signature status

name: "Apache HTTP Server" id: 256

category: 26 vendor: 149

name: "RealPlayer (32-bit)" id: 1

category: 10 vendor: 68

name: "VisualSVN Server" id: 257

category: 26 vendor: 162

name: "QQ2009" id: 2

category: 14 vendor: 78

get endpoint-control app-detect predefined-vendor status

FG200A2907500558 # get endpoint-control app-detect predefined-vendor status

name: "Access Remote PC (www.access-remote-pc.com)" id: 3

name: "ACD Systems, Ltd." id: 4

name: "Adobe Systems Incorporated" id: 5

name: "Alen Soft" id: 6

firewall dnstranslation

Use this command to display the firewall DNS translation table.

Syntax

get firewall dnstranslation

firewall iprope appctrl

Use this command to list all application control signatures added to an application control list and display a summary of the application control configuration.

Syntax

get firewall iprope appctrl {list | status}

Example output

In this example, the FortiGate unit includes one application control list that blocks the FTP

application.

get firewall iprope appctrl list

app-list=app_list_1/2000 other-action=Pass

app-id=15896      list-id=2000  action=Block

get firewall iprope appctrl status appctrl table 3 list 1 app 1 shaper 0

firewall iprope list

Use this command to list all of the FortiGate unit iprope firewall policies. Optionally include a group number in hexidecimal format to display a single policy. Policies are listed in FortiOS format.

Syntax

get firewall iprope list [<group_number_hex>]

Example output

get firewall iprope list 0010000c

policy flag (8000000): pol_stats

flag2 (20): ep_block shapers: / per_ip=

imflag: sockport: 1011 action: redirect index: 0

schedule() group=0010000c av=00000000 au=00000000 host=0 split=00000000 chk_client_info=0x0 app_list=0 misc=0 grp_info=0 seq=0 hash=0 npu_sensor_id=0

tunnel=

zone(1): 0 ->zone(1): 0 source(0):

dest(0):

source wildcard(0): destination wildcard(0): service(1):

[6:0x8:1011/(0,65535)->(80,80)]

nat(0):

mms: 0 0

firewall proute, proute6

Use these commands to list policy routes.

Syntax

For IPv4 policy routes:

get firewall proute

For IPv6 policy routes:

get firewall proute6

Example output

get firewall proute

list route policy info(vf=root):

iff=5 src=1.1.1.0/255.255.255.0 tos=0x00 tos_mask=0x00 dst=0.0.0.0/0.0.0.0 protocol=80 port=1:65535

oif=3 gwy=1.2.3.4

firewall service predefined

Use this command to retrieve information about predefined services. If you do not specify a

<service_name> the command lists all of the pre-defined services.

Syntax

get firewall service predefined [<service_name>]

Example output

get firewall service predefined FTP

name                : FTP icmpcode            : icmptype            :

protocol            : TCP/UDP/SCTP

protocol-number     : 6 sctpport-range      :

tcpport-range       : 21:0-65535 udpport-range       :

get firewall service predefined SIP

name                : SIP icmpcode            : icmptype            :

protocol            : TCP/UDP/SCTP

protocol-number     : 17 sctpport-range      : tcpport-range       :

udpport-range       : 5060:0-65535

get firewall service predefined AOL

name                : AOL icmpcode            : icmptype            :

protocol            : TCP/UDP/SCTP

protocol-number     : 6 sctpport-range      :

tcpport-range       : 5190-5194:0-65535 udpport-range       :

firewall shaper

Use these command to retrieve information about traffic shapers.

Syntax

To get information about per-ip  traffic shapers

get firewall shaper per-ip

To get information about shared traffic shapers

get firewall shaper traffic-shaper

grep

In many cases the get and show (and diagnose) commands may produce a large amount of output. If you are looking for specific information in a large get or show command output you can use the grep command to filter the output to only display what you are looking for. The grep command is based on the standard UNIX grep, used for searching text output based on regular expressions.

Information about how to use grep and regular expressions is available from the Internet. For example, see http://www.opengroup.org/onlinepubs/009695399/utilities/grep.html.

Syntax

{get | show| diagnose} | grep <regular_expression>

Example output

Use the following command to display the MAC address of the FortiGate unit internal interface:

get hardware nic internal | grep Current_HWaddr

Current_HWaddr                  00:09:0f:cb:c2:75

Use the following command to display all TCP sessions in the session list and include the session list line number in the output

get system session list | grep -n tcp

19:tcp     1110   10.31.101.10:1862 172.20.120.122:30670

69.111.193.57:1469 -

27:tcp  3599 10.31.101.10:2061 -         10.31.101.100:22 -

38:tcp     3594   10.31.101.10:4780 172.20.120.122:49700

172.20.120.100:445 -

43:tcp     3582   10.31.101.10:4398 172.20.120.122:49574

24.200.188.171:48726 -

Use the following command to display all lines in HTTP replacement message commands that contain URL (upper or lower case):

show system replacemsg http | grep -i url

set buffer "<HTML><BODY>The page you requested has been blocked because it contains a banned word. URL =

%%PROTOCOL%%%%URL%%</BODY></HTML>" config system replacemsg http "url-block"

set buffer "<HTML><BODY>The URL you requested has been blocked. URL = %%URL%%</BODY></HTML>"

config system replacemsg http "urlfilter-err"

.

.

.

gui console status

Display information about the CLI console.

Syntax

get gui console status

Example

The output looks like this:

Preferences:

User: admin

Colour scheme (RGB): text=FFFFFF, background=000000

Font: style=monospace, size=10pt

History buffer=50 lines, external input=disabled

gui topology status

Display information about the topology viewer database. The topology viewer is available only if the Topology widget has been added to a customized web-based manager menu layout.

Syntax

get gui topology status

Example output

Preferences:

Canvas dimensions (pixels): width=780, height=800

Colour scheme (RGB): canvas=12ff08, lines=bf0f00, exterior=ddeeee

Background image: type=none, placement: x=0, y=0

Line style: thickness=2

Custom background image file: none

Topology element database:

FortiGate  : x=260, y=340

Office: x=22, y=105

ISPnet: x=222, y=129

Text  : x=77, y=112: "Ottawa"

Text  : x=276, y=139: "Internet"

hardware cpu

Use this command to display detailed information about all of the CPUs in your FortiGate unit.

Syntax

get hardware cpu

Example output

get hardware npu legacy list

No npu ports are found

620_ha_1 # get hardware cpu processor       : 0

vendor_id       : GenuineIntel cpu family      : 6

model           : 15

model name      : Intel(R) Core(TM)2 Duo CPU     E4300  @ 1.80GHz stepping        : 13

cpu MHz         : 1795.545 cache size      : 64 KB fdiv_bug        : no hlt_bug         : no f00f_bug        : no coma_bug        : no

fpu             : yes fpu_exception   : yes cpuid level     : 10 wp              : yes

flags	: fpu vme de pse tsc msr pae mce cx8 apic sep mtrr pge mca cmov pat pse36 clflush dts acpi mmx fxsr sse sse2 ss ht tm pbe lm pni monitor ds_cpl tm2 est

bogomips        : 3578.26

processor       : 1

vendor_id       : GenuineIntel cpu family      : 6

model           : 15

model name      : Intel(R) Core(TM)2 Duo CPU     E4300  @ 1.80GHz stepping        : 13

cpu MHz         : 1795.545 cache size      : 64 KB fdiv_bug        : no hlt_bug         : no f00f_bug        : no coma_bug        : no

fpu             : yes fpu_exception   : yes cpuid level     : 10

wp              : yes

flags	: fpu vme de pse tsc msr pae mce cx8 apic sep mtrr pge mca cmov pat pse36 clflush dts acpi mmx fxsr sse sse2 ss ht tm pbe lm pni monitor ds_cpl tm2 est

bogomips        : 3578.26

hardware memory

Use this command to display information about FortiGate unit memory use including the total, used, and free memory.

Syntax

get hardware memory

Example output

get hardware memory

total:    used:    free:  shared: buffers:  cached: shm: Mem:  3703943168 348913664 3355029504        0   192512 139943936

137314304

hardware nic

Use this command to display hardware and status information about each FortiGate interface. The hardware information includes details such as the driver name and version and chip revision. Status information includes transmitted and received packets, and different types of errors.

Syntax

get hardware nic <interface_name>

| Variable | Description |
| --- | --- |
| <interface_name> | A FortiGate interface name such as port1, wan1, internal, etc. |

Example output

get hardware nic port9

Chip_Model         FA2/ISCP1B-v3/256MB FPGA_REV_TAG       06101916

Driver Name        iscp1a/b-DE Driver Version     0.1

Driver Copyright   Fortinet Inc.

Link               down Speed              N/A Duplex             N/A State              up

Rx_Packets         0

Tx_Packets         0

Rx_Bytes           0

Tx_Bytes           0

Current_HWaddr     00:09:0f:77:09:68

Permanent_HWaddr   00:09:0f:77:09:68

Frame_Received     0

Bad Frame Received 0

Tx Frame           0

Tx Frame Drop      0

Receive IP Error   0

FIFO Error         0

Small PktBuf Left  125

Normal PktBuf Left 1021

Jumbo PktBuf Left  253

NAT Anomaly        0

hardware npu

Use this command to display information about the network processor unit (NPU) hardware installed in a FortiGate unit. The NPUs can be built-in or on an installed AMC module.

Syntax

get hardware npu legacy {list | session <device_name_str> | setting

<device_name_str>}

get hardware npu np1 {list | status}

get hardware npu np2 {list | performance <device_id_int> | status

<device_id_int>}

get hardware npu np4 {list | status <device_id_int>}

get hardware npu sp {list | status}

Example output

get hardware npu np1 list

ID          Interface

0           port9 port10

get hardware npu np1 status

ISCP1A 10ee:0702

RX SW Done 0 MTP 0x00000000

desc_size  = 0x00001000 count    = 0x00000100 nxt_to_u   = 0x00000000 nxt_to_f = 0x00000000

Total Number of Interfaces: 2

Number of Interface In-Use: 2

Interface[0] Tx done: 0

desc_size  = 0x00004000 count    = 0x00000100 nxt_to_u   = 0x00000000 nxt_to_f = 0x00000000

TX timeout = 0x00000000 BD_empty = 0x00000000

HRx Packets= 0x00000000 HTXBytes = 0x00000000 HRXBytes = 0x00000000

Interface[1] Tx done: 0

desc_size  = 0x00004000 count    = 0x00000100 nxt_to_u   = 0x00000000 nxt_to_f = 0x00000000

TX timeout = 0x00000000 BD_empty = 0x00000000

HRx Packets= 0x00000000 HTXBytes = 0x00000000 HRXBytes = 0x00000000

NAT Information:

head       = 0x00000001 tail     = 00000001

ISCP1A Performance [Top]:

Nr_int   : 0x00000000      INTwoInd  : 0x00000000     RXwoDone  :

0x00000000

PKTwoEnd  : 0x00000000     PKTCSErr  : 0x00000000

PKTidErr : 0x00000000      PHY0Int   : 0x00000000     PHY1INT   :

0x00000000

CSUMOFF  : 0x00000000      BADCSUM   : 0x00000000     MSGINT    :

0x00000000

IPSEC    : 0x00000000      IPSVLAN   : 0x00000000     SESMISS   :

0x00000000

TOTUP    : 0x00000000      RSVD MEMU : 0x00000010

MSG Performance:

QLEN:   0x00001000(QW) HEAD: 0x00000000

Performance:

TOTMSG: 0x00000000 BADMSG: 0x00000000 TOUTMSG: 0x00000000 QUERY:

0x00000000

NULLTK: 0x00000000

NAT Performance: BYPASS (Enable) BLOCK (Disable)

IRQ    : 00000001 QFTL   : 00000000 DELF  : 00000000 FFTL  : 00000000

OVTH   : 00000001 QRYF   : 00000000 INSF  : 00000000 INVC  : 00000000

ALLO   : 00000000 FREE   : 00000000 ALLOF : 00000000 BPENTR: 00000000

BKENTR: 00000000

PBPENTR: 00000000 PBKENTR: 00000000 NOOP  : 00000000 THROT :

00000000(0x002625a0)

SWITOT : 00000000 SWDTOT : 00000000 ITDB  : 00000000 OTDB  : 00000000

SPISES : 00000000 FLUSH  : 00000000

APS (Disabled) information:

MODE: BOTH UDPTH 255 ICMPTH 255 APSFLAGS: 0x00000000

IPSEC Offload Status: 0x58077dcb

get hardware npu np2 list

ID       PORTS

--       -----

0        amc-sw1/1

0        amc-sw1/2

0        amc-sw1/3

0        amc-sw1/4

ID       PORTS

--       -----

1        amc-dw2/1

ID       PORTS

--       -----

2        amc-dw2/2

get hardware npu np2 status 0

NP2 Status

ISCP2 f7750000 (Neighbor 00000000) 1a29:0703 256MB Base f8aad000 DBG

0x00000000

RX SW Done 0 MTP 0x0 desc_alloc = f7216000

desc_size  = 0x2000 count    = 0x100 nxt_to_u   = 0x0 nxt_to_f = 0x0

Total Interfaces: 4 Total Ports: 4

Number of Interface In-Use: 4

Interface f7750100 netdev 81b1e000 0 Name amc-sw1-1

PHY: Attached

LB Mode 0 LB IDX 0/1 LB Ports: f7750694, 00000000, 00000000, 00000000

Port f7750694 Id 0 Status Down ictr 4 desc = 8128c000

desc_size  = 0x00001000 count     = 0x00000100 nxt_to_u   = 0x00000000 nxt_to_f = 0x00000000

Intf f7750100

Interface f7750264 netdev 81b2cc00 1 Name amc-sw1-2

PHY: Attached

LB Mode 0 LB IDX 0/1 LB Ports: f7750748, 00000000, 00000000, 00000000

Port f7750748 Id 1 Status Down ictr 0 desc = 81287000

desc_size  = 0x00001000 count     = 0x00000100 nxt_to_u   = 0x00000000 nxt_to_f = 0x00000000

Intf f7750264

Interface f77503c8 netdev 81b2c800 2 Name amc-sw1-3

PHY: Attached

LB Mode 0 LB IDX 0/1 LB Ports: f77507fc, 00000000, 00000000, 00000000

Port f77507fc Id 2 Status Down ictr 0 desc = 81286000

desc_size  = 0x00001000 count     = 0x00000100 nxt_to_u   = 0x00000000 nxt_to_f = 0x00000000

Intf f77503c8

Interface f775052c netdev 81b2c400 3 Name amc-sw1-4

PHY: Attached

LB Mode 0 LB IDX 0/1 LB Ports: f77508b0, 00000000, 00000000, 00000000

Port f77508b0 Id 3 Status Down ictr 0 desc = 81281000

desc_size  = 0x00001000 count     = 0x00000100 nxt_to_u   = 0x00000000 nxt_to_f = 0x00000000

Intf f775052c

NAT Information:

cmdq_qw    = 0x2000 cmdq     = 82160000 head       = 0x1 tail     = 0x1

APS (Enabled) information:

Session Install when TMM TSE OOE: Disable Session Install when TMM TAE OOE: Disable IPS anomaly check policy: Follow config MSG Base = 82150000 QL = 0x1000 H = 0x0

hardware status

Report information about the FortiGate unit hardware including FortiASIC version, CPU type, amount of memory, flash drive size, hard disk size (if present), USB flash size (if present), network card chipset, and WiFi chipset (FortiWifi models). This information can be useful for troubleshooting, providing information about your FortiGate unit to Fortinet Support, or confirming the features that your FortiGate model supports.

Syntax

get hardware status

Example output

Model name: Fortigate-620B ASIC version: CP6

ASIC SRAM: 64M

CPU: Intel(R) Core(TM)2 Duo CPU     E4300  @ 1.80GHz

RAM: 2020 MB

Compact Flash: 493 MB /dev/sda Hard disk: 76618 MB /dev/sdb USB Flash: not available

Network Card chipset: Broadcom 570x Tigon3 Ethernet Adapter

(rev.0x5784100)

ips decoder status

Displays all the port settings of all the IPS decoders.

Syntax

get ips decoder status

Example output

# get ips decoder status decoder-name: "back_orifice"

decoder-name: "dns_decoder" port_list: 53

decoder-name: "ftp_decoder" port_list: 21

decoder-name: "http_decoder" decoder-name: "im_decoder"

decoder-name: "imap_decoder" port_list: 143

Ports are shown only for decoders with configurable port settings.

ips rule  status

Displays current configuration information about IPS rules.

Syntax

get ips rule status

Example output

# get ips rule status rule-name: "IP.Land" rule-id: 12588

rev: 2.464 action: pass status: disable log: enable

log-packet: disable severity: 3.high service: All

location: server, client os: All

application: All

rule-name: "IP.Loose.Src.Record.Route.Option" rule-id: 12805

rev: 2.464 action: pass status: disable log: enable

log-packet: disable severity: 2.medium service: All

location: server, client os: All

application: All

ips session

Displays current IPS session status.

Syntax

get ips session

Example output

get ips session

SYSTEM:

memory capacity            279969792 memory used                5861008 recent pps\bps             0\0K session in-use             0

TCP:  in-use\active\total  0\0\0

UDP:  in-use\active\total  0\0\0

ICMP: in-use\active\total  0\0\0

ipsec tunnel

List the current IPSec VPN tunnels and their status.

Syntax

To view details of all IPsec tunnels:

get ipsec tunnel details

To list IPsec tunnels by name:

get ipsec tunnel name

To view a summary  of IPsec tunnel information:

get ipsec tunnel summary

ips view-map

Use this command to view the policies examined by IPS. This is mainly used for debugging. If there is no ips view map, it means IPS is not used or enabled.

Syntax

get ips view-map <id>

Example output

id                  : 1 id-policy-id        : 0 policy-id           : 2 vdom-id             : 0

which               : firewall

| Variable | Description |
| --- | --- |
| id | IPS policy ID |
| id-policy-id | Identity-based policy ID (0 means none) |
| policy-id | Policy ID |
| vdom-id | VDOM, identified by ID number |
| which | Type of policy id: firewall, firewall6, sniffer, sniffer6, interface, interface6 |

netscan settings

Use this command to display tcp and udp ports that are scanned by the current scan mode.

Syntax

get netscan settings

Example output

scan-mode : full

tcp-ports : 1-65535 udp-ports : 1-65535

pbx branch-office

Use this command to list the configured branch offices.

Syntax

get pbx branch-office

Example output

== [ Branch 15 ]

name: Branch 15

== [ Branch 12 ]

name: Branch 12

pbx dialplan

Use this command to list the configured dial plans.

Syntax

get pbx dialplan

Example output

== [ company-default ]

name: company-default

== [ inbound ]

name: inbound

pbx did

Use this command to list the configured direct inward dial (DID) numbers.

Syntax

get pbx did

Example output

== [ Operator ]

name: Operator

== [ Emergency ]

name: Emergency

pbx extension

Use this command to list the configured extensions.

Syntax

get pbx extension

Example output

== [ 6555 ]

extension: 6555

== [ 6777 ]

extension: 6777

== [ 6111 ]

extension: 6111

pbx ftgd-voice-pkg

Use this command to display the current FortiGate Voice service package status.

Syntax

get pbx ftgd-voice-pkg status

Example output

Status: Activated

Total 1 Packages:

Package Type: B, Credit Left: 50.00, Credit Used: 0.00, Expiration Date: 2011-01-01 12:00:00

Total 1 Dids:

12345678901

Total 1 Efaxs:

12345678902

Total 0 Tollfrees:

pbx global

Use this command to display the current global pbx settings.

Syntax

get pbx global

Example output

block-blacklist     : enable country-area        : USA country-code        : 1

efax-check-interval : 5 extension-pattern   : 6XXX

fax-admin-email     : faxad@example.com

ftgd-voice-server   : service.fortivoice.com local-area-code     : 408

max-voicemail       : 60 outgoing-prefix     : 9 ring-timeout        : 20 rtp-hold-timeout    : 0 rtp-timeout         : 60 voicemail-extension : *97

pbx ringgrp

Use this command to display the currently configured ring groups.

Syntax

get pbx ringgrp

Example output

== [ 6001 ]

name: 6001

== [ 6002 ]

name: 6002

pbx sip-trunk

Use this command to display the currently configured SIP trunks.

Syntax

get pbx sip-trunk

Example output

== [   FtgdVoice_1 ]

name:   FtgdVoice_1

pbx voice-menu

Use this command to display the current voice menu and recorder extension configuration.

Syntax

get pbx voice-menu

Example output

comment             : general password            : *

press-0:

ring-group          : 6001

type                : ring-group press-1:

type                : voicemail press-2:

type                : directory press-3:

type                : none press-4:

type                : none press-5:

type                : none press-6:

type                : none press-7:

type                : none press-8:

type                : none press-9:

type                : none recorder-exten      : *30

report database schema

Use this command to display the FortiGate SQL reporting database schema.

Syntax

get report database schema

router info  bfd neighbor

Use this command to list state information about the neighbors in the bi-directional forwarding table.

Syntax

get router info bfd neighbour

router info  bgp

Use this command to display information about the BGP configuration.

Syntax

get router info bgp <keyword>

| <keyword> | Description |
| --- | --- |
| cidr-only | Show all BGP routes having non-natural network masks. |
| community | Show all BGP routes having their COMMUNITY attribute set. |
| community-info | Show general information about the configured BGP communities, including the routes in each community and their associated network addresses. |
| community-list | Show all routes belonging to configured BGP community lists. |
| dampening {dampened-paths ¦ flap-statistics ¦ parameters} | Display information about dampening: • Type dampened-paths to show all paths that have been suppressed due to flapping. • Type flap-statistics to show flap statistics related to BGP routes. • Type parameters to show the current dampening settings. |
| filter-list | Show all routes matching configured AS-path lists. |
| inconsistent-as | Show all routes associated with inconsistent autonomous systems of origin. |
| memory | Show the BGP memory table. |
| neighbors [<address_ipv4> ¦ <address_ipv4> advertised-routes ¦ <address_ipv4> received prefix-filter ¦ <address_ipv4> received-routes ¦ <address_ipv4> routes] | Show information about connections to TCP and BGP neighbors. |
| network [<address_ipv4mask>] | Show general information about the configured BGP networks, including their network addresses and associated prefixes. |
| network-longer-prefixes <address_ipv4mask> | Show general information about the BGP route that you specify (for example, 12.0.0.0/14) and any specific routes associated with the prefix. |
| paths | Show general information about BGP AS paths, including their associated network addresses. |
| prefix-list <name> | Show all routes matching configured prefix list <name>. |
| quote-regexp <regexp_str> | Enter the regular expression to compare to the AS_PATH attribute of BGP routes (for example, ^730$) and enable the use of output modifiers (for example, include, exclude, and begin) to search the results. |
| regexp <regexp_str> | Enter the regular expression to compare to the AS_PATH attribute of BGP routes (for example, ^730$). |

| <keyword> | Description |
| --- | --- |
| route-map | Show all routes matching configured route maps. |
| scan | Show information about next-hop route scanning, including the scan interval setting. |
| summary | Show information about BGP neighbor status. |

Example output

get router info bgp memory

Memory type                          Alloc count   Alloc bytes

=================================== ============= ===============

bgp proto specifc allocations :         9408 B bgp generic allocations       :       196333 B bgp total allocations         :       205741 B

router info  gwdetect

Use this command to view the status of gateway detection.

Syntax

get router info gwdetect

router info  isis

Use this command to display information about the FortiGate ISIS.

Syntax

get router info isis interface get router info isis neighbor

get router info isis is-neighbor get router info isis database

get router info isis route

get router info isis topology

router info  kernel

Use this command to display the FortiGate kernel routing table. The kernel routing table displays information about all of the routes in the kernel.

Syntax

get router info kernel [<routing_type_int>]

router info  multicast

Use this command to display information about a Protocol Independent Multicasting (PIM)

configuration. Multicast routing is supported in the root virtual domain only.

Syntax

get router info multicast <keywords>

| <keywords> | Description |
| --- | --- |
| igmp | Show Internet Group Management Protocol (IGMP) membership information according to one of these qualifiers: • Type groups [{<interface-name> ¦ <group-address>}] to show IGMP information for the multicast group(s) associated with the specified interface or multicast group address. • Type groups-detail [{<interface-name> ¦ <group- address>}] to show detailed IGMP information for the multicast group(s) associated with the specified interface or multicast group address. • Type interface [<interface-name>] to show IGMP information for all multicast groups associated with the specified interface. |
| pim dense-mode | Show information related to dense mode operation according to one of these qualifiers: • Type interface to show information about PIM-enabled interfaces. • Type interface-detail to show detailed information about PIM- enabled interfaces. • Type neighbor to show the current status of PIM neighbors. • Type neighbor-detail to show detailed information about PIM neighbors. • Type next-hop to show information about next-hop PIM routers. • Type table [<group-address>][<source-address>] to show the multicast routing table entries associated with the specified multicast group address and/or multicast source address. |
| pim sparse-mode | Show information related to sparse mode operation according to one of these qualifiers: • Type bsr-info to show Boot Strap Router (BSR) information. • Type interface to show information about PIM-enabled interfaces. • Type interface-detail to show detailed information about PIM- enabled interfaces. • Type neighbor to show the current status of PIM neighbors. • Type neighbor-detail to show detailed information about PIM neighbors. • Type next-hop to show information about next-hop PIM routers. • Type rp-mapping to show Rendezvous Point (RP) information. • Type table [<group-address>][<source-address>] to show the multicast routing table entries associated with the specified multicast group address and/or multicast source address. |

| <keywords> | Description |
| --- | --- |
| table [<group-address>] [<source-address>] | Show the multicast routing table entries associated with the specified multicast group address and/or multicast source address. |
| table-count [<group-address>] [<source-address>] | Show statistics related to the specified multicast group address and/or multicast source address. |

Fortinet Technologies Inc.                                                               Page 1050                                    FortiOS™ - CLI Reference for FortiOS 5.0

router info  ospf

Use this command to display information about the FortiGate OSPF configuration and/or the Link-State Advertisements (LSAs) that the FortiGate unit obtains and generates. An LSA identifies the interfaces of all OSPF-enabled routers in an area, and provides information that enables OSPF-enabled routers to select the shortest path to a destination.

Syntax

get router info ospf <keyword>

| <keyword> | Description |
| --- | --- |
| border-routers | Show OSPF routing table entries that have an Area Border Router (ABR) or Autonomous System Boundary Router (ASBR) as a destination. |
| database <qualifier> | Show information from the OSPF routing database according to the of these qualifiers. Some qualifiers require a target that can be one of the following values: • Type adv_router <address_ipv4> to limit the information to LSAs originating from the router at the specified IP address. • Type self-originate <address_ipv4> to limit the information to LSAs originating from the FortiGate unit. |
|  | adv-router <address_ipv4> | Type adv-router <address_ipv4> to show ospf Advertising Router link states for the router at the given IP address. |
|  | asbr-summary <target> | Type asbr-summary to show information about ASBR summary LSAs. |
|  | brief | Type brief to show the number and type of LSAs associated with each OSPF area. |
|  | external <target> | Type external to show information about external LSAs. |
|  | max-age | Type max-age to show all LSAs in the MaxAge list. |
|  | network <target> | Type network to show information about network LSAs. |
|  | nssa-external <target> | Type nssa-external to show information about not-so-stubby external LSAs. |
|  | opaque-area <address_ipv4> | Type opaque-area <address_ipv4> to show information about opaque Type 10 (area-local) LSAs (see RFC 2370). |
|  | opaque-as <address_ipv4> | Type opaque-as <address_ipv4> to show information about opaque Type 11 LSAs (see RFC 2370), which are flooded throughout the AS. |
|  | opaque-link <address_ipv4> | Type opaque-link <address_ipv4> to show information about opaque Type 9 (link-local) LSAs (see RFC 2370). |
|  | router <target> | Type router to show information about router LSAs. |
|  | self-originate | Type self-originate to show self-originated LSAs. |
|  | summary <target> | Type summary to show information about summary LSAs. |
| interface [<interface_name>] | Show the status of one or all FortiGate interfaces and whether OSPF is enabled on those interfaces. |

Fortinet Technologies Inc.                                                               Page 1051                                    FortiOS™ - CLI Reference for FortiOS 5.0

| <keyword> | Description |
| --- | --- |
| neighbor [all ¦ <neighbor_id> ¦ detail ¦ detail all ¦ interface <address_ipv4>] | Show general information about OSPF neighbors, excluding down- status neighbors: • Type all to show information about all neighbors, including down-status neighbors. • Type <neighbor_id> to show detailed information about the specified neighbor only. • Type detail to show detailed information about all neighbors, excluding down-status neighbors. • Type detail all to show detailed information about all neighbors, including down-status neighbors. • Type interface <address_ipv4> to show neighbor information based on the FortiGate interface IP address that was used to establish the neighbor’s relationship. |
| route | Show the OSPF routing table. |
| status | Show general information about the OSPF routing processes. |
| virtual-links | Show information about OSPF virtual links. |

Fortinet Technologies Inc.                                                               Page 1052                                    FortiOS™ - CLI Reference for FortiOS 5.0

router info  protocols

Use this command to show the current states of active routing protocols. Inactive protocols are not displayed.

Syntax

get router info protocols

Routing Protocol is "rip"

Sending updates every 30 seconds with +/-50%

Timeout after 180 seconds, garbage collect after 120 seconds Outgoing update filter list for all interface is not set Incoming update filter list for all interface is not set Default redistribution metric is 1

Redistributing:

Default version control: send version 2, receive version 2

Interface        Send  Recv   Key-chain

Routing for Networks:

Routing Information Sources:

Gateway          Distance  Last Update  Bad Packets  Bad Routes

Distance: (default is 120)

Routing Protocol is "ospf 0"

Invalid after 0 seconds, hold down 0, flushed after 0

Outgoing update filter list for all interfaces is Incoming update filter list for all interfaces is Redistributing:

Routing for Networks:

Routing Information Sources: Gateway        Distance     Last Update

Distance: (default is 110) Address         Mask            Distance

List

Routing Protocol is "bgp 5"

IGP synchronization is disabled

Automatic route summarization is disabled

Default local-preference applied to incoming route is 100

Redistributing: Neighbor(s):

Address AddressFamily FiltIn FiltOut DistIn DistOut RouteMapIn

RouteMapOut Weight

192.168.20.10 unicast

router info  rip

Use this command to display information about the RIP configuration.

Syntax

get router info rip <keyword>

| <keyword> | Description |
| --- | --- |
| database | Show the entries in the RIP routing database. |
| interface [<interface_name>] | Show the status of the specified FortiGate unit interface <interface_name> and whether RIP is enabled. If interface is used alone it lists all the FortiGate unit interfaces and whether RIP is enabled on each. |

router info  routing-table

Use this command to display the routes in the routing table.

Syntax

get router info routing-table <keyword>

| <keyword> | Description |
| --- | --- |
| all | Show all entries in the routing table. |
| bgp | Show the BGP routes in the routing table. |
| connected | Show the connected routes in the routing table. |
| database | Show the routing information database. |
| details [<address_ipv4mask>] | Show detailed information about a route in the routing table, including the next-hop routers, metrics, outgoing interfaces, and protocol-specific information. |
| ospf | Show the OSPF routes in the routing table. |
| rip | Show the RIP routes in the routing table. |
| static | Show the static routes in the routing table. |

router info  vrrp

Use this command to display information about the VRRP configuration.

Syntax

get router info vrrp

Example output

Interface: port1, primary IP address: 9.1.1.2

VRID: 1

vrip: 9.1.1.254, priority: 100, state: BACKUP adv_interval: 1, preempt: 1, start_time: 3 vrdst: 0.0.0.0

router info6 bgp

Use this command to display information about the BGP IPv6 configuration.

Syntax

get router info6 bgp <keyword>

| <keyword> | Description |
| --- | --- |
| community | Show all BGP routes having their COMMUNITY attribute set. |
| community-list | Show all routes belonging to configured BGP community lists. |
| dampening {dampened-paths ¦ flap-statistics ¦ parameters} | Display information about dampening: • Type dampened-paths to show all paths that have been suppressed due to flapping. • Type flap-statistics to show flap statistics related to BGP routes. • Type parameters to show the current dampening settings. |
| filter-list | Show all routes matching configured AS-path lists. |
| inconsistent-as | Show all routes associated with inconsistent autonomous systems of origin. |
| neighbors [<address_ipv6mask> | Show information about connections to TCP and BGP neighbors. |
| network [<address_ipv6mask>] | Show general information about the configured BGP networks, including their network addresses and associated prefixes. |
| network-longer-prefixes <address_ipv6mask> | Show general information about the BGP route that you specify (for example, 12.0.0.0/14) and any specific routes associated with the prefix. |
| paths | Show general information about BGP AS paths, including their associated network addresses. |
| prefix-list <name> | Show all routes matching configured prefix list <name>. |
| quote-regexp <regexp_str> | Enter the regular expression to compare to the AS_PATH attribute of BGP routes (for example, ^730$) and enable the use of output modifiers (for example, include, exclude, and begin) to search the results. |
| regexp <regexp_str> | Enter the regular expression to compare to the AS_PATH attribute of BGP routes (for example, ^730$). |
| route-map | Show all routes matching configured route maps. |
| summary | Show information about BGP neighbor status. |

router info6 interface

Use this command to display information about IPv6 interfaces.

Syntax

get router info6 interface <interface_name>

Example output

The command returns the status of the interface and the assigned IPv6 address.

dmz2                       [administratively down/down]

2001:db8:85a3:8d3:1319:8a2e:370:7348 fe80::209:fff:fe04:4cfd

router info6 kernel

Use this command to display the FortiGate kernel routing table. The kernel routing table displays information about all of the routes in the kernel.

Syntax

get router info6 kernel

router info6 ospf

Use this command to display information about the OSPF IPv6 configuration.

Syntax

get router info6 ospf

router info6 protocols

Use this command to display information about the configuration of all IPv6 dynamic routing protocols.

Syntax

get router info6 protocols

router info6 rip

Use this command to display information about the RIPng configuration.

Syntax

get router info6 rip

router info6 routing-table

Use this command to display the routes in the IPv6 routing table.

Syntax

get router info6 routing-table <item>

where <item> is one of the following:

| Variable | Description |
| --- | --- |
| <ipv6_ip> | Destination IPv6 address or prefix. |
| bgp | Show BGP routing table entries. |
| connected | Show connected routing table entries. |
| database | Show routing information base. |
| ospf | Show OSPF routing table entries. |
| rip | Show RIP routing table entries. |
| static | Show static routing table entries. |

system admin  list

View a list of all the current administration sessions.

Syntax

get system admin list

| Example output |  |
| --- | --- |
| # get system admin list username local device | remote | started |
| admin sshv2 port1:172.20.120.148:22 | 172.20.120.16:4167 | 2006-08- |

09 12:24:20

admin    https  port1:172.20.120.148:443 172.20.120.161:56365 2006-08-

09 12:24:20

admin    https  port1:172.20.120.148:443 172.20.120.16:4214   2006-08-

09 12:25:29

| username | Name of the admin account for this session |
| --- | --- |
| local | The protocol this session used to connect to the FortiGate unit. |
| device | The interface, IP address, and port used by this session to connect to the FortiGate unit. |
| remote | The IP address and port used by the originating computer to connect to the FortiGate unit. |
| started | The time the current session started. |

system admin  status

View the status of the currently logged in admin and their session.

Syntax

get system admin status

Example

The output looks like this:

# get system admin status username: admin

login local: sshv2

login device: port1:172.20.120.148:22 login remote: 172.20.120.16:4167

login vdom: root

login started: 2006-08-09 12:24:20 current time: 2006-08-09 12:32:12

| username | Name of the admin account currently logged in. |
| --- | --- |
| login local | The protocol used to start the current session. |
| login device | The login information from the FortiGate unit including interface, IP address, and port number. |
| login remote | The computer the user is logging in from including the IP address and port number. |
| login vdom | The virtual domain the admin is current logged into. |
| login started | The time the current session started. |
| current time | The current time of day on the FortiGate unit |

system arp

View the ARP table entries on the FortiGate unit.

This command is not available in multiple VDOM mode.

Syntax

get system arp

| Example output |  |
| --- | --- |
| # get system arp Address | Age(min) | Hardware Addr | Interface |
| 172.20.120.16 | 0 | 00:0d:87:5c:ab:65 | internal |
| 172.20.120.138 | 0 | 00:08:9b:09:bb:01 | internal |

system auto-update

Use this command to display information about the status FortiGuard updates on the FortiGate unit.

Syntax

get system auto-update status get system auto-update versions

Example output

get system auto-update status

FDN availability:  available at Thu Apr  1 08:22:58 2010

Push update: disable

Scheduled update: enable

Update daily:   8:22

Virus definitions update: enable IPS definitions update: enable Server override: disable

Push address override: disable

Web proxy tunneling: disable

system central-management

View information about the Central Management System configuration.

Syntax

get system central-management

Example

The output looks like this:

FG600B3908600705 # get system central-management status              : enable

type                : fortimanager auto-backup         : disable schedule-config-restore: enable schedule-script-restore: enable allow-push-configuration: enable allow-pushd-firmware: enable

allow-remote-firmware-upgrade: enable allow-monitor       : enable

fmg                 : 172.20.120.161 vdom                : root

authorized-manager-only: enable

serial-number       : "FMG-3K2404400063"

system checksum

View the checksums for global, root, and all configurations. These checksums are used by HA

to compare the configurations of each cluster unit.

Syntax

get system checksum status

Example output

# get system checksum status

global: 7a 87 3c 14 93 bc 98 92 b0 58 16 f2 eb bf a4 15 root: bb a4 80 07 42 33 c2 ff f1 b5 6e fe e4 bb 45 fb all: 1c 28 f1 06 fa 2e bc 1f ed bd 6b 21 f9 4b 12 88

system cmdb  status

View information about cmdbsvr on the FortiGate unit. FortiManager uses some of this information.

Syntax

get system cmdb status

Example output

# get system cmdb status version: 1

owner id: 18

update index: 6070

config checksum: 12879299049430971535 last request pid: 68

last request type: 29 last request: 78

| Variable | Description |
| --- | --- |
| version | Version of the cmdb software. |
| owner id | Process ID of the cmdbsvr daemon. |
| update index | The updated index shows how many changes have been made in cmdb. |
| config checksum | The config file version used by FortiManager. |
| last request pid | The last process to access the cmdb. |
| last requst type | Type of the last attempted access of cmdb. |
| last request | The number of the last attempted access of cmdb. |

system fortianalyzer-connectivity

Display connection and remote disk usage information about a connected FortiAnalyzer unit.

Syntax

get fortianalyzer-connectivity status

Example output

# get system fortianalyzer-connectivity status

Status: connected

Disk Usage: 0%

system fortiguard-log-service status

Command returns information about the status of the FortiGuard Log & Analysis Service including license and disk information.

Syntax

get system fortiguard-log-service status

Example output

# get system fortiguard-log-service status

FortiGuard Log & Analysis Service

Expire on: 20071231

Total disk quota: 1111 MB Max daily volume: 111 MB Current disk quota usage: n/a

system fortiguard-service status

COMMAND REPLACED. Command returns information about the status of the FortiGuard service including the name, version late update, method used for the last update and when the update expires. This information is shown for the AV Engine, virus definitions, attack definitions, and the IPS attack engine.

Syntax

get system fortiguard-service status

Example output

NAME            VERSION LAST UPDATE        METHOD   EXPIRE

AV Engine          2.002   2006-01-26 19:45:00  manual    2006-06-12

system ha-nonsync-csum

FortiManager uses this command to obtain a system checksum.

Syntax

get system ha-nonsync-csum

system ha status

Use this command to display information about an HA cluster. The command displays general HA configuration settings. The command also displays information about how the cluster unit that you have logged into is operating in the cluster.

Usually you would log into the primary unit CLI using SSH or telnet. In this case the get system ha status command displays information about the primary unit first, and also displays the HA state of the primary unit (the primary unit operates in the work state). However, if you log into the primary unit and then use the execute ha manage command to log into a subordinate unit, (or if you use a console connection to log into a subordinate unit) the get system status command displays information about this subordinate unit first, and also displays the HA state of this subordinate unit. The state of a subordinate unit is work for an active-active cluster and standby for an active-passive cluster.

For a virtual cluster configuration, the get system ha status command displays information about how the cluster unit that you have logged into is operating in virtual cluster 1 and virtual cluster 2. For example, if you connect to the cluster unit that is the primary unit for virtual cluster 1 and the subordinate unit for virtual cluster 2, the output of the get system ha status command shows virtual cluster 1 in the work state and virtual cluster 2 in the standby state. The get system ha status command also displays additional information about virtual cluster 1 and virtual cluster 2.

Syntax

get system ha status

The command display includes the following fields. For more information see the examples that follow.

| Variable | Description |
| --- | --- |
| Model | The FortiGate model number. |
| Mode | The HA mode of the cluster: a-a or a-p. |
| Group | The group ID of the cluster. |
| Debug | The debug status of the cluster. |
| ses_pickup | The status of session pickup: enable or disable. |
| load_balance | The status of the load-balance-all field: enable or disable. Displayed for active-active clusters only. |
| schedule | The active-active load balancing schedule. Displayed for active-active clusters only. |
| Master Slave | Master displays the device priority, host name, serial number, and actual cluster index of the primary (or master) unit. Slave displays the device priority, host name, serial number, and actual cluster index of the subordinate (or slave, or backup) unit or units. The list of cluster units changes depending on how you log into the CLI. Usually you would use SSH or telnet to log into the primary unit CLI. In this case the primary unit would be at the top the list followed by the other cluster units. If you use execute ha manage or a console connection to log into a subordinate unit CLI, and then enter get system ha status the subordinate unit that you have logged into appears at the top of the list of cluster units. |

| Variable | Description |
| --- | --- |
| number of vcluster | The number of virtual clusters. If virtual domains are not enabled, the cluster has one virtual cluster. If virtual domains are enabled the cluster has two virtual clusters. |
| vcluster 1 | The HA state (hello, work, or standby) and HA heartbeat IP address of the cluster unit that you have logged into in virtual cluster 1. If virtual domains are not enabled, vcluster 1 displays information for the cluster. If virtual domains are enabled, vcluster 1 displays information for virtual cluster 1. The HA heartbeat IP address is 10.0.0.1 if you are logged into a the primary unit of virtual cluster 1 and 10.0.0.2 if you are logged into a subordinate unit of virtual cluster 1. vcluster 1 also lists the primary unit (master) and subordinate units (slave) in virtual cluster 1. The list includes the operating cluster index and serial number of each cluster unit in virtual cluster 1. The cluster unit that you have logged into is at the top of the list. If virtual domains are not enabled and you connect to the primary unit CLI, the HA state of the cluster unit in virtual cluster 1 is work. The display lists the cluster units starting with the primary unit. If virtual domains are not enabled and you connect to a subordinate unit CLI, the HA state of the cluster unit in virtual cluster 1 is standby. The display lists the cluster units starting with the subordinate unit that you have logged into. If virtual domains are enabled and you connect to the virtual cluster 1 primary unit CLI, the HA state of the cluster unit in virtual cluster 1 is work. The display lists the cluster units starting with the virtual cluster 1 primary unit. If virtual domains are enabled and you connect to the virtual cluster 1 subordinate unit CLI, the HA state of the cluster unit in virtual cluster 1 is standby. The display lists the cluster units starting with the subordinate unit that you are logged into. In a cluster consisting of two cluster units operating without virtual domains enabled all clustering actually takes place in virtual cluster 1. HA is designed to work this way to support virtual clustering. If this cluster was operating with virtual domains enabled, adding virtual cluster 2 is similar to adding a new copy of virtual cluster 1. Virtual cluster 2 is visible in the get system ha status command output when you add virtual domains to virtual cluster 2. |

Fortinet Technologies Inc.                                                               Page 1076                                    FortiOS™ - CLI Reference for FortiOS 5.0

| Variable | Description |
| --- | --- |
| vcluster 2 | vcluster 2 only appears if virtual domains are enabled. vcluster 2 displays the HA state (hello, work, or standby) and HA heartbeat IP address of the cluster unit that you have logged into in virtual cluster 2. The HA heartbeat IP address is 10.0.0.2 if you are logged into the primary unit of virtual cluster 2 and 10.0.0.1 if you are logged into a subordinate unit of virtual cluster 2. vcluster 2 also lists the primary unit (master) and subordinate units (slave) in virtual cluster 2. The list includes the cluster index and serial number of each cluster unit in virtual cluster 2. The cluster unit that you have logged into is at the top of the list. If you connect to the virtual cluster 2 primary unit CLI, the HA state of the cluster unit in virtual cluster 2 is work. The display lists the cluster units starting with the virtual cluster 2 primary unit. If you connect to the virtual cluster 2 subordinate unit CLI, the HA state of the cluster unit in virtual cluster 2 is standby. The display lists the cluster units starting with the subordinate unit that you are logged into. |

Fortinet Technologies Inc.                                                               Page 1077                                    FortiOS™ - CLI Reference for FortiOS 5.0

system info  admin  ssh

Use this command to display information about the SSH configuration on the FortiGate unit such as:

•  the SSH port number

•  the interfaces with SSH enabled

•  the hostkey DSA fingerprint

•  the hostkey RSA fingerprint

Syntax

get system info admin ssh

Example output

# get system info admin ssh

SSH v2 is enabled on port 22

SSH is enabled on the following 1 interfaces:

internal

SSH hostkey DSA fingerprint = cd:e1:87:70:bb:f0:9c:7d:e3:7b:73:f7:44:

23:a5:99

SSH hostkey RSA fingerprint = c9:5b:49:1d:7c:ba:be:f3:9d:39:33:4d:48:

9d:b8:49

system info  admin  status

Use this command to display administrators that are logged into the FortiGate unit.

Syntax

get system info admin status

Example

This shows sample output.

| Index | User name | Login | type | From |
| --- | --- | --- | --- | --- |
| 0 | admin | CLI |  | ssh(172.20.120.16) |
| 1 | admin | WEB |  | 172.20.120.16 |

| Index | The order the administrators logged in. |
| --- | --- |
| User name | The name of the user account logged in. |
| Login type | Which interface was used to log in. |
| From | The IP address this user logged in from. |

Related topics

•  get system info admin ssh

system interface physical

Use this command to list information about the unit’s physical network interfaces.

Syntax

get system interface physical

The output looks like this:

# get system interface physical

== [onboard]

==[dmz1]

mode: static

ip: 0.0.0.0 0.0.0.0 status: down

speed: n/a

==[dmz2]

mode: static

ip: 0.0.0.0 0.0.0.0 status: down

speed: n/a

==[internal]

mode: static

ip: 172.20.120.146 255.255.255.0 status: up

speed: 100

==[wan1]

mode: pppoe

ip: 0.0.0.0 0.0.0.0 status: down

speed: n/a

==[wan2]

mode: static

ip: 0.0.0.0 0.0.0.0 status: down

speed: n/a

==[modem]

mode: static

ip: 0.0.0.0 0.0.0.0 status: down

speed: n/a

system mgmt-csum

FortiManager uses this command to obtain checksum information from FortiGate units.

Syntax

get system mgmt-csum {global | vdom | all}

where

global retrieves global object checksums vdom retrieves VDOM object checksums all retrieves all object checksums.

system performance firewall

Use this command to display packet distribution and traffic statistics information for the

FortiGate firewall.

Syntax

get system performance firewall packet-distribution get system performance firewall statistics

| Variable | Description |
| --- | --- |
| packet-distribution | Display a list of packet size ranges and the number of packets of each size accepted by the firewall since the system restarted. You can use this information to learn about the packet size distribution on your network. |
| statistics | Display a list of traffic types (browsing, email, DNS etc) and the number of packets and number of payload bytes accepted by the firewall for each type since the FortiGate unit was restarted. |

Example output

get system performance firewall packet-distribution getting packet distribution statistics...

0 bytes - 63 bytes: 655283 packets

64 bytes - 127 bytes: 1678278 packets

128 bytes - 255 bytes: 58823 packets

256 bytes - 383 bytes: 70432 packets

384 bytes - 511 bytes: 1610 packets

512 bytes - 767 bytes: 3238 packets

768 bytes - 1023 bytes: 7293 packets

1024 bytes - 1279 bytes: 18865 packets

1280 bytes - 1500 bytes: 58193 packets

> 1500 bytes: 0 packets

get system performance firewall statistics getting traffic statistics...

Browsing: 623738 packets, 484357448 bytes

DNS: 5129187383836672 packets, 182703613804544 bytes

E-Mail: 23053606 packets, 2 bytes

FTP: 0 packets, 0 bytes Gaming: 0 packets, 0 bytes IM: 0 packets, 0 bytes

Newsgroups: 0 packets, 0 bytes P2P: 0 packets, 0 bytes Streaming: 0 packets, 0 bytes

TFTP: 654722117362778112 packets, 674223966126080 bytes

VoIP: 16834455 packets, 10 bytes

Generic TCP: 266287972352 packets, 8521215115264 bytes

Generic UDP: 0 packets, 0 bytes Generic ICMP: 0 packets, 0 bytes Generic IP: 0 packets, 0 bytes

system performance status

Use this command to display FortiGate CPU usage, memory usage, network usage, sessions, virus, IPS attacks, and system up time.

Syntax

get system performance status

| Variable | Description |
| --- | --- |
| CPU states | The percentages of CPU cycles used by user, system, nice and idle categories of processes. These categories are: • user -CPU usage of normal user-space processes • system -CPU usage of kernel • nice - CPU usage of user-space processes having other-than- normal running priority • idle - Idle CPU cycles Adding user, system, and nice produces the total CPU usage as seen on the CPU widget on the web-based system status dashboard. |
| Memory states | The percentage of memory used. |
| Average network usage | The average amount of network traffic in kbps in the last 1, 10 and 30 minutes. |
| Average sessions | The average number of sessions connected to the FortiGate unit over the list 1, 10 and 30 minutes. |
| Virus caught | The number of viruses the FortiGate unit has caught in the last 1 minute. |
| IPS attacks blocked | The number of IPS attacks that have been blocked in the last 1 minute. |
| Uptime | How long since the FortiGate unit has been restarted. |

Example output

# get system performance status

CPU states: 0% user 0% system 0% nice 100% idle

Memory states: 18% used

Average network usage: 0 kbps in 1 minute, 0 kbps in 10 minutes, 1 kbps in 30 minutes

Average sessions: 5 sessions in 1 minute, 6 sessions in 10 minutes, 5 sessions in 30 minutes

Virus caught: 0 total in 1 minute

IPS attacks blocked: 0 total in 1 minute

Uptime: 9days, 22 hours, 0 minutes

system performance top

Use this command to display the list of processes running on the FortiGate unit (similar to the

Linux top command).

You can use the following commands when get system performance top is running:

• Press Q or Ctrl+C to quit.

• Press P to sort the processes by the amount of CPU that the processes are using.

• Press M to sort the processes by the amount of memory that the processes are using.

Syntax

get system performance top [<delay_int>] <max_lines_int>]]

| Variable | Description |
| --- | --- |
| <delay_int> | The delay, in seconds, between updating the process list. The default is 5 seconds. |
| <max_lines_int> | The maximum number of processes displayed in the output. The default is 20 lines. |

system session list

Command returns a list of all the sessions active on the FortiGate unit. or the current virtual domain if virtual domain mode is enabled.

Syntax

get system session list

Example output

| PROTO NAT | EXPIRE SOURCE DESTINATION | SOURCE- DESTINATION-NAT |
| --- | --- | --- |
| tcp | 0 | 127.0.0.1:1083 - 127.0.0.1:514 - |
| tcp | 0 | 127.0.0.1:1085 - 127.0.0.1:514 - |
| tcp | 10 | 127.0.0.1:1087 - 127.0.0.1:514 - |
| tcp | 20 | 127.0.0.1:1089 - 127.0.0.1:514 - |
| tcp | 30 | 127.0.0.1:1091 - 127.0.0.1:514 - |
| tcp | 40 | 127.0.0.1:1093 - 127.0.0.1:514 - |
| tcp | 60 | 127.0.0.1:1097 - 127.0.0.1:514 - |
| tcp | 70 | 127.0.0.1:1099 - 127.0.0.1:514 - |
| tcp | 80 | 127.0.0.1:1101 - 127.0.0.1:514 - |
| tcp | 90 | 127.0.0.1:1103 - 127.0.0.1:514 - |
| tcp | 100 | 127.0.0.1:1105 - 127.0.0.1:514 - |
| tcp | 110 | 127.0.0.1:1107 - 127.0.0.1:514 - |
| tcp | 103 | 172.20.120.16:3548 - 172.20.120.133:22 - |
| tcp | 3600 | 172.20.120.16:3550 - 172.20.120.133:22 - |
| udp | 175 | 127.0.0.1:1026 - 127.0.0.1:53 - |
| tcp | 5 | 127.0.0.1:1084 - 127.0.0.1:514 - |
| tcp | 5 | 127.0.0.1:1086 - 127.0.0.1:514 - |
| tcp | 15 | 127.0.0.1:1088 - 127.0.0.1:514 - |
| tcp | 25 | 127.0.0.1:1090 - 127.0.0.1:514 - |
| tcp | 45 | 127.0.0.1:1094 - 127.0.0.1:514 - |
| tcp | 59 | 127.0.0.1:1098 - 127.0.0.1:514 - |
| tcp | 69 | 127.0.0.1:1100 - 127.0.0.1:514 - |
| tcp | 79 | 127.0.0.1:1102 - 127.0.0.1:514 - |
| tcp | 99 | 127.0.0.1:1106 - 127.0.0.1:514 - |
| tcp | 109 | 127.0.0.1:1108 - 127.0.0.1:514 - |
| tcp | 119 | 127.0.0.1:1110 - 127.0.0.1:514 - |

| Variable | Description |
| --- | --- |
| PROTO | The transfer protocol of the session. |
| EXPIRE | How long before this session will terminate. |
| SOURCE | The source IP address and port number. |
| SOURCE-NAT | The source of the NAT. ‘-’ indicates there is no NAT. |
| DESTINATION | The destination IP address and port number. |
| DESTINATION-NAT | The destination of the NAT. ‘-’ indicates there is no NAT. |

system session status

Use this command to display the number of active sessions on the FortiGate unit, or if virtual domain mode is enabled it returns the number of active sessions on the current VDOM. In both situations it will say ‘the current VDOM.

Syntax

get system session status

Example output

The total number of sessions for the current VDOM: 3100

system session-helper-info list

Use this command to list the FortiGate session helpers and the protocol and port number configured for each one.

Syntax

get system sesion-helper-info list

Example output

list builtin help module:

mgcp dcerpc rsh pmap

dns-tcp dns-udp rtsp pptp

sip mms tns h245 h323 ras tftp ftp

list session help:

help=pmap, protocol=17 port=111 help=rtsp, protocol=6 port=8554 help=rtsp, protocol=6 port=554 help=pptp, protocol=6 port=1723 help=rtsp, protocol=6 port=7070 help=sip, protocol=17 port=5060 help=pmap, protocol=6 port=111 help=rsh, protocol=6 port=512 help=dns-udp, protocol=17 port=53 help=tftp, protocol=17 port=69 help=tns, protocol=6 port=1521 help=mgcp, protocol=17 port=2727 help=dcerpc, protocol=17 port=135 help=rsh, protocol=6 port=514 help=ras, protocol=17 port=1719 help=ftp, protocol=6 port=21 help=mgcp, protocol=17 port=2427 help=dcerpc, protocol=6 port=135 help=mms, protocol=6 port=1863 help=h323, protocol=6 port=1720

system session-info

Use this command to display session information.

Syntax

get system session-info expectation get system session-info full-stat get system session-info list

get system session-info statistics get system session-info ttl

| Variable | Description |
| --- | --- |
| expectation | Display expectation sessions. |
| full-stat | Display detailed information about the FortiGate session table including a session table and expect session table summary, firewall error statistics, and other information. |
| list | Display detailed information about all current FortiGate sessions. For each session the command displays the protocol number, traffic shaping information, policy information, state information, statistics and other information. |
| statistics | Display the same information as the full-stat command except for the session table and expect session table summary. |
| ttl | Display the current setting of the config system session-ttl command including the overall session timeout as well as the timeouts for specific protocols. |

Example output

get system session-info statistics

misc info:               session_count=15 exp_count=0 clash=0 memory_tension_drop=0 ephemeral=1/32752 removeable=14

delete=0, flush=0, dev_down=0/0 firewall error stat: error1=00000000

error2=00000000 error3=00000000 error4=00000000 tt=00000000 cont=00000000 ids_recv=00000000 url_recv=00000000 av_recv=00000000 fqdn_count=00000001 tcp reset stat:

syncqf=0 acceptqf=0 no-listener=227 data=0 ses=0 ips=0 global: ses_limit=0 ses6_limit=0 rt_limit=0 rt6_limit=0

system source-ip

Use this command to list defined source-IPs.

Syntax

get system source-ip

Example output

# get sys source-ip status

The following services force their communication to use a specific source IP address:

service=NTP source-ip=172.18.19.101 service=DNS source-ip=172.18.19.101

vdom=root service=RADIUS name=server-pc25 source-ip=10.1.100.101 vdom=root service=TACACS+ name=tac_plus_pc25 source-ip=10.1.100.101 vdom=root service=FSAE name=pc26 source-ip=172.18.19.101

vdom=V1 service=RADIUS name=pc25-Radius source-ip=172.16.200.101 vdom=V1 service=TACACS+ name=pc25-tacacs+ source-ip=172.16.200.101 vdom=V1 service=FSAE name=pc16 source-ip=172.16.200.101

system startup-error-log

Use this command to display information about system startup errors. This command only displays information if an error occurs when the FortiGate unit starts up.

Syntax

get system startup-error-log

system status

Use this command to display system status information including:

•  FortiGate firmware version, build number and branch point

•  virus and attack definitions version

•  FortiGate unit serial number and BIOS version

•  log hard disk availability

•  host name

•  operation mode

•  virtual domains status: current VDOM, max number of VDOMs, number of NAT and TP mode

VDOMs and VDOM status

•  current HA status

•  system time

•  the revision of the WiFi chip in a FortiWiFi unit

Syntax

get system status

Example output

Version: Fortigate-620B v4.0,build0271,100330 (MR2) Virus-DB: 11.00643(2010-03-31 17:49)

Extended DB: 11.00643(2010-03-31 17:50) Extreme DB: 0.00000(2003-01-01 00:00) IPS-DB: 2.00778(2010-03-31 12:55)

FortiClient application signature package: 1.167(2010-04-01 10:11) Serial-Number: FG600B3908600705

BIOS version: 04000006

Log hard disk: Available

Hostname: 620_ha_1

Operation Mode: NAT

Current virtual domain: root

Max number of virtual domains: 10

Virtual domains status: 1 in NAT mode, 0 in TP mode

Virtual domain configuration: disable

FIPS-CC mode: disable

Current HA mode: a-p, master Distribution: International Branch point: 271

Release Version Information: MR2

System time: Thu Apr  1 15:27:29 2010

test

Use this command to display information about FortiGate applications and perform operations on FortiGate applications. You can specify an application name and a test level. Enter ? to display the list of applications. The test level performs various functions depending on the application but can include displaying memory usage, dropping connections and restarting the application.

The test levels are different for different applications. In some cases when you enter the command and include an application name but no test level (or an invalid test level) the command output includes a list of valid test levels.

Syntax

get test <application_name_str> <test_level_int>

Example output

get test http

Proxy Worker 0 - http

[0:H] HTTP Proxy Test Usage

[0:H]

[0:H]     2: Drop all connections

[0:H]    22: Drop max idle connections [0:H]   222: Drop all idle connections [0:H]     4: Display connection stat [0:H]    44: Display info per connection

[0:H]   444: Display connections per state

[0:H]  4444: Display per-VDOM statistics

[0:H] 44444: Display information about idle connections

[0:H]    55: Display tcp info per connection

get test http 4

HTTP Common

Current Connections                                   0/8032

HTTP Stat

Bytes sent                                            0 (kb) Bytes received                                        0 (kb) Error Count (alloc)                                   0

Error Count (accept)                                  0

Error Count (bind)                                    0

Error Count (connect)                                 0

Error Count (socket)                                  0

Error Count (read)                                    0

Error Count (write)                                   0

Error Count (retry)                                   0

Error Count (poll)                                    0

Error Count (scan reset)                              0

Error Count (urlfilter wait)                          0

Last Error                                            0

Web responses clean                                   0

Web responses scan errors                             0

Web responses detected                                0

Web responses infected with worms                     0

Web responses infected with viruses                   0

Web responses infected with susp                      0

Web responses file blocked                            0

Web responses file exempt                             0

Web responses bannedword detected                     0

Web requests oversize pass                            0

Web requests oversize block                           0

URL  requests exempt                                  0

URL  requests blocked                                 0

URL  requests passed                                  0

URL  requests submit error                            0

URL  requests rating error                            0

URL  requests rating block                            0

URL  requests rating allow                            0

URL  requests infected with worms                     0

Web  requests detected                                0

Web  requests file blocked                            0

Web  requests file exempt                             0

POST requests clean                                   0

POST requests scan errors                             0

POST requests infected with viruses                   0

POST requests infected with susp                      0

POST requests file blocked                            0

POST requests bannedword detected                     0

POST requests oversize pass                           0

POST requests oversize block                          0

Web request  backlog drop                             0

Web response backlog drop                             0

HTTP Accounting

setup_ok=0 setup_fail=0 conn_ok=0 conn_inp=0 urlfilter=0/0/0 uf_lookupf=0

scan=0 clt=0 srv=0

user  adgrp

Use this command to list Directory Service user groups.

Syntax

get user adgrp [<dsgroupname>]

If you do not specify a group name, the command returns information for all Directory Service groups. For example:

== [ DOCTEST/Cert Publishers ]

name: DOCTEST/Cert Publishers    server-name: DSserv1

== [ DOCTEST/Developers ]

name: DOCTEST/Developers    server-name: DSserv1

== [ DOCTEST/Domain Admins ]

name: DOCTEST/Domain Admins    server-name: DSserv1

== [ DOCTEST/Domain Computers ]

name: DOCTEST/Domain Computers    server-name: DSserv1

== [ DOCTEST/Domain Controllers ]

name: DOCTEST/Domain Controllers    server-name: DSserv1

== [ DOCTEST/Domain Guests ]

name: DOCTEST/Domain Guests    server-name: DSserv1

== [ DOCTEST/Domain Users ]

name: DOCTEST/Domain Users    server-name: DSserv1

== [ DOCTEST/Enterprise Admins ]

name: DOCTEST/Enterprise Admins    server-name: DSserv1

== [ DOCTEST/Group Policy Creator Owners ]

name: DOCTEST/Group Policy Creator Owners    server-name: DSserv1

== [ DOCTEST/Schema Admins ]

name: DOCTEST/Schema Admins    server-name: DSserv1

If you specify a Directory Service group name, the command returns information for only that group. For example:

name                : DOCTEST/Developers server-name         : ADserv1

The server-name is the name you assigned to the Directory Service server when you configured it in the user fsae command.

vpn ike gateway

Use this command to display information about FortiGate IPsec VPN IKE gateways.

Syntax

get vpn ike gateway [<gateway_name_str>]

vpn ipsec tunnel details

Use this command to display information about IPsec tunnels.

Syntax

get vpn ipsec tunnel details

vpn ipsec tunnel name

Use this command to display information about a specified IPsec VPN tunnel.

Syntax

get vpn ipsec tunnel name <tunnel_name_str>

vpn ipsec stats crypto

Use this command to display information about the FortiGate hardware and software crypto configuration.

Syntax

get vpn ipsec stats crypto

Example output

get vpn ipsec stats crypto

IPsec crypto devices in use: CP6 (encrypted/decrypted):

null:   0      0 des:    0      0

3des:   0      0 aes:    0      0

CP6 (generated/validated): null:	0      0 md5:	0      0 sha1:	0      0 sha256: 0      0

SOFTWARE (encrypted/decrypted):

null:   0      0 des:    0      0

3des:   0      0 aes:    0      0

SOFTWARE (generated/validated):

null:   0      0 md5:    0      0 sha1: 0    0 sha256: 0      0

vpn ipsec stats tunnel

Use this command to view information about IPsec tunnels.

Syntax

get vpn ipsec stats tunnel

Example output

#get vpn ipsec stats tunnel tunnels

total: 0 static/ddns: 0 dynamic: 0 manual: 0

errors: 0 selectors

total: 0 up: 0

vpn ssl monitor

Use this command to display information about logged in SSL VPN users and current SSL VPN

sessions.

Syntax

get vpn ssl monitor

Example output

vpn status l2tp

Use this command to display information about L2TP tunnels.

Syntax

get vpn status l2tp

vpn status pptp

Use this command to display information about PPTP tunnels.

Syntax

get vpn status pptp

vpn status ssl

Use this command to display SSL VPN tunnels and to also verify that the FortiGate unit includes the CP6 or greater FortiASIC device that supports SSL acceleration.

Syntax

get vpn status ssl hw-acceleration-status get vpn status ssl list

| Variable | Description |
| --- | --- |
| hw-acceleration-status | Display whether or not the FortiGate unit contains a FortiASIC device that supports SSL acceleration. |
| list | Display information about all configured SSL VPN tunnels. |

webfilter ftgd-statistics

Use this command to display FortiGuard Web Filtering rating cache and daemon statistics.

Syntax

get webfilter ftgd-statistics

Example output

get webfilter ftgd-statistics

Rating Statistics:

=====================

DNS failures                     :          0

DNS lookups                      :          0

Data send failures               :          0

Data read failures               :          0

Wrong package type               :          0

Hash table miss                  :          0

Unknown server                   :          0

Incorrect CRC                    :          0

Proxy request failures           :          0

Request timeout                  :          0

Total requests                   :          0

Requests to FortiGuard servers   :          0

Server errored responses         :          0

Relayed rating                   :          0

Invalid profile                  :          0

Allowed                          :          0

Blocked                          :          0

Logged                           :          0

Errors                           :          0

Cache Statistics:

=====================

Maximum memory                   :          0

Memory usage                     :          0

Nodes                            :          0

Leaves                         :          0

Prefix nodes                   :          0

Exact nodes                    :          0

| Requests : | 0 |
| --- | --- |
| Misses : | 0 |
| Hits : | 0 |
| Prefix hits : | 0 |
| Exact hits : | 0 |

| No cache directives : | 0 |
| --- | --- |
| Add after prefix : | 0 |
| Invalid DB put : | 0 |
| DB updates : | 0 |

| Percent full : | 0% |
| --- | --- |
| Branches : | 0% |
| Leaves : | 0% |
| Prefix nodes : | 0% |
| Exact nodes : | 0% |

| Miss rate : | 0% |
| --- | --- |
| Hit rate : | 0% |
| Prefix hits : | 0% |
| Exact hits : | 0% |

webfilter status

Use this command to display FortiGate Web Filtering rating information.

Syntax

get webfilter status [<refresh-rate_int>]

wireless-controller rf-analysis

Use this command to show information about RF conditions at the access point.

Syntax

get wireless-controller rf-analysis [<wtp_id>]

Example output

# get wireless-controller rf-analysis

<wtp-id>    wtp id

FWF60C3G11004319 (global) # get wireless-controller rf-analysis

WTP: FWF60C-WIFI0  0-127.0.0.1:15246

channel    rssi-total   rf-score     overlap-ap   interfere-ap

1      418          1            24           26

2      109          5            0            34

3      85           7            1            34

4      64           9            0            35

5      101          6            1            35

6      307          1            8            11

7      82           7            0            16

8      69           8            1            15

9      42           10           0            15

10      53           10           0            14

11      182          1            5            6

12      43           10           0            6

13      20           10           0            5

14      8            10           0            5

Controller: FWF60C3G11004319-0 channel	rssi_total

1      418

2      109

3      85

4      64

5      101

6      307

7      82

8      69

9      42

10      53

11      182

12      43

13      20

14      8

wireless-controller scan

Use this command to view the list of access points detected by wireless scanning.

Syntax

get wireless-controller scan

Example output

CMW SSID    BSSID            CHAN RATE S:N  INT CAPS ACT LIVE AGE WIRED

UNN         00:0e:8f:24:18:6d  64 54M  16:0  100 Es  N 62576 1668

?

UNN ftiguest 00:15:55:23:d8:62 157 130M   6:0  100 EPs N 98570 2554

?

wireless-controller status

Use this command to view the numbers of wtp sessions and clients.

Syntax

get wireless-controller status

Example output

# get wireless-controller status

Wireless Controller  : wtp-session-count: 1 client-count	: 1/0

wireless-controller vap-status

Use this command to view information about your SSIDs.

Syntax

get wireless-controller vap-status

Example output

# get wireless-controller vap-status

WLAN: mesh.root

name             : mesh.root vdom             : root

ssid             : fortinet.mesh.root status           : up

mesh backhaul    : yes

ip               : 0.0.0.0

mac              : 00:ff:0a:57:95:ca station info     : 0/0

WLAN: wifi

name             : wifi vdom             : root ssid             : ft-mesh status           : up

mesh backhaul    : yes

ip               : 10.10.80.1

mac              : 00:ff:45:e1:55:81 station info     : 1/0

wireless-controller wlchanlistlic

Use this command to display a list of the channels allowed in your region, including

•  the maximum permitted power for each channel

•  the channels permitted for each wireless type (802.11n, for example) The list is in XML format.

Syntax

get wireless-controller wlchanlistlic

Sample output

country name: UNITED STATES2, country code:841, iso name:US

channels on 802.11A band without channel bonding:

| channel= 36 | maxRegTxPower= | 23 | maxTxPower= | 63/2 | minTxPower= | 63/2 |
| --- | --- | --- | --- | --- | --- | --- |
| channel= 40 | maxRegTxPower= | 23 | maxTxPower= | 63/2 | minTxPower= | 63/2 |
| channel= 44 | maxRegTxPower= | 23 | maxTxPower= | 63/2 | minTxPower= | 63/2 |
| channel= 48 | maxRegTxPower= | 23 | maxTxPower= | 63/2 | minTxPower= | 63/2 |
| channel=149 | maxRegTxPower= | 30 | maxTxPower= | 63/2 | minTxPower= | 63/2 |
| channel=153 | maxRegTxPower= | 30 | maxTxPower= | 63/2 | minTxPower= | 63/2 |
| channel=157 | maxRegTxPower= | 30 | maxTxPower= | 63/2 | minTxPower= | 63/2 |
| channel=161 | maxRegTxPower= | 30 | maxTxPower= | 63/2 | minTxPower= | 63/2 |
| channel=165 | maxRegTxPower= | 30 | maxTxPower= | 63/2 | minTxPower= | 63/2 |

channels on 802.11B band without channel bonding:

| channel= | 1 | maxRegTxPower= | 27 | maxTxPower= | 63/2 | minTxPower= | 63/2 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| channel= | 2 | maxRegTxPower= | 27 | maxTxPower= | 63/2 | minTxPower= | 63/2 |
| channel= | 3 | maxRegTxPower= | 27 | maxTxPower= | 63/2 | minTxPower= | 63/2 |
| channel= | 4 | maxRegTxPower= | 27 | maxTxPower= | 63/2 | minTxPower= | 63/2 |
| channel= | 5 | maxRegTxPower= | 27 | maxTxPower= | 63/2 | minTxPower= | 63/2 |
| channel= | 6 | maxRegTxPower= | 27 | maxTxPower= | 63/2 | minTxPower= | 63/2 |
| channel= | 7 | maxRegTxPower= | 27 | maxTxPower= | 63/2 | minTxPower= | 63/2 |
| channel= | 8 | maxRegTxPower= | 27 | maxTxPower= | 63/2 | minTxPower= | 63/2 |
| channel= | 9 | maxRegTxPower= | 27 | maxTxPower= | 63/2 | minTxPower= | 63/2 |
| channel= | 10 | maxRegTxPower= | 27 | maxTxPower= | 63/2 | minTxPower= | 63/2 |
| channel= | 11 | maxRegTxPower= | 27 | maxTxPower= | 63/2 | minTxPower= | 63/2 |

channels on 802.11G band without channel bonding:

| channel= | 10 | maxRegTxPower= 27 | maxTxPower= 63/2 | minTxPower= | 63/2 |
| --- | --- | --- | --- | --- | --- |
| channel= | 11 | maxRegTxPower= 27 | maxTxPower= 63/2 | minTxPower= | 63/2 |

channels on 802.11N 2.4GHz band without channel bonding:

| channel= | 1 | maxRegTxPower= | 27 | maxTxPower= | 63/2 | minTxPower= | 63/2 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| channel= | 2 | maxRegTxPower= | 27 | maxTxPower= | 63/2 | minTxPower= | 63/2 |
| channel= | 3 | maxRegTxPower= | 27 | maxTxPower= | 63/2 | minTxPower= | 63/2 |
| channel= | 4 | maxRegTxPower= | 27 | maxTxPower= | 63/2 | minTxPower= | 63/2 |
| channel= | 5 | maxRegTxPower= | 27 | maxTxPower= | 63/2 | minTxPower= | 63/2 |
| channel= | 6 | maxRegTxPower= | 27 | maxTxPower= | 63/2 | minTxPower= | 63/2 |
| channel= | 7 | maxRegTxPower= | 27 | maxTxPower= | 63/2 | minTxPower= | 63/2 |
| channel= | 8 | maxRegTxPower= | 27 | maxTxPower= | 63/2 | minTxPower= | 63/2 |
| channel= | 9 | maxRegTxPower= | 27 | maxTxPower= | 63/2 | minTxPower= | 63/2 |
| channel= | 10 | maxRegTxPower= | 27 | maxTxPower= | 63/2 | minTxPower= | 63/2 |
| channel= | 11 | maxRegTxPower= | 27 | maxTxPower= | 63/2 | minTxPower= | 63/2 |

channels on 802.11N 2.4GHz band with channel bonding plus:

| channel= | 1 | maxRegTxPower= | 27 | maxTxPower= | 63/2 | minTxPower= | 63/2 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| channel= | 2 | maxRegTxPower= | 27 | maxTxPower= | 63/2 | minTxPower= | 63/2 |
| channel= | 3 | maxRegTxPower= | 27 | maxTxPower= | 63/2 | minTxPower= | 63/2 |
| channel= | 4 | maxRegTxPower= | 27 | maxTxPower= | 63/2 | minTxPower= | 63/2 |
| channel= | 5 | maxRegTxPower= | 27 | maxTxPower= | 63/2 | minTxPower= | 63/2 |
| channel= | 6 | maxRegTxPower= | 27 | maxTxPower= | 63/2 | minTxPower= | 63/2 |
| channel= | 7 | maxRegTxPower= | 27 | maxTxPower= | 63/2 | minTxPower= | 63/2 |

channels on 802.11N 2.4GHz band with channel bonding minus:

| channel= | 5 | maxRegTxPower= | 27 | maxTxPower= | 63/2 | minTxPower= | 63/2 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| channel= | 6 | maxRegTxPower= | 27 | maxTxPower= | 63/2 | minTxPower= | 63/2 |
| channel= | 7 | maxRegTxPower= | 27 | maxTxPower= | 63/2 | minTxPower= | 63/2 |
| channel= | 8 | maxRegTxPower= | 27 | maxTxPower= | 63/2 | minTxPower= | 63/2 |
| channel= | 9 | maxRegTxPower= | 27 | maxTxPower= | 63/2 | minTxPower= | 63/2 |
| channel= | 10 | maxRegTxPower= | 27 | maxTxPower= | 63/2 | minTxPower= | 63/2 |
| channel= | 11 | maxRegTxPower= | 27 | maxTxPower= | 63/2 | minTxPower= | 63/2 |

channels on 802.11N 5GHz band without channel bonding:

| channel= 36 | maxRegTxPower= | 23 | maxTxPower= | 63/2 | minTxPower= | 63/2 |
| --- | --- | --- | --- | --- | --- | --- |
| channel= 40 | maxRegTxPower= | 23 | maxTxPower= | 63/2 | minTxPower= | 63/2 |
| channel= 44 | maxRegTxPower= | 23 | maxTxPower= | 63/2 | minTxPower= | 63/2 |
| channel= 48 | maxRegTxPower= | 23 | maxTxPower= | 63/2 | minTxPower= | 63/2 |
| channel=149 | maxRegTxPower= | 30 | maxTxPower= | 63/2 | minTxPower= | 63/2 |
| channel=153 | maxRegTxPower= | 30 | maxTxPower= | 63/2 | minTxPower= | 63/2 |
| channel=157 | maxRegTxPower= | 30 | maxTxPower= | 63/2 | minTxPower= | 63/2 |
| channel=161 | maxRegTxPower= | 30 | maxTxPower= | 63/2 | minTxPower= | 63/2 |
| channel=165 | maxRegTxPower= | 30 | maxTxPower= | 63/2 | minTxPower= | 63/2 |

channels on 802.11N 5GHz band with channel bonding all:

| channel= 48 | maxRegTxPower= | 23 | maxTxPower= | 63/2 | minTxPower= | 63/2 |
| --- | --- | --- | --- | --- | --- | --- |
| channel=149 | maxRegTxPower= | 30 | maxTxPower= | 63/2 | minTxPower= | 63/2 |
| channel=153 | maxRegTxPower= | 30 | maxTxPower= | 63/2 | minTxPower= | 63/2 |
| channel=157 | maxRegTxPower= | 30 | maxTxPower= | 63/2 | minTxPower= | 63/2 |
| channel=161 | maxRegTxPower= | 30 | maxTxPower= | 63/2 | minTxPower= | 63/2 |

wireless-controller wtp-status

Syntax

get wireless-controller wtp-status

Example output

# get wireless-controller wtp-status

WTP: FAP22B3U11005354  0-192.168.3.110:5246 wtp-id	: FAP22B3U11005354 region-code	:

name             :

mesh-uplink      : mesh

mesh-downlink    : disabled mesh-hop-count   : 1

parent-wtp-id    :

software-version :

local-ipv4-addr  : 0.0.0.0

board-mac        : 00:00:00:00:00:00

join-time        : Mon Apr  2 10:23:32 2012 connection-state : Disconnected

image-download-progress: 0 last-failure     : 0 -- N/A last-failure-param:

last-failure-time: N/A Radio 1            : Monitor Radio 2            : Ap

country-name     : NA country-code     : N/A client-count     : 0

base-bssid       : 00:00:00:00:00:00 max-vaps         : 7

oper-chan        : 0

Radio 3            : Not Exist

WTP: FWF60C-WIFI0  0-127.0.0.1:15246 wtp-id	: FWF60C-WIFI0 region-code	: ALL

name             :

mesh-uplink      : ethernet mesh-downlink    : enabled mesh-hop-count   : 0

parent-wtp-id    :

software-version : FWF60C-v5.0-build041 local-ipv4-addr  : 127.0.0.1

board-mac        : 00:09:0f:fe:cc:56

join-time        : Mon Apr  2 10:23:35 2012 connection-state : Connected

image-download-progress: 0 last-failure     : 0 -- N/A

last-failure-param:

last-failure-time: N/A Radio 1            : Ap

country-name     : US country-code     : N/A client-count     : 1

base-bssid       : 00:0e:8e:3b:63:99 max-vaps         : 7

oper-chan        : 1

Radio 2            : Not Exist

Radio 3            : Not Exist

tree

The tree command displays FortiOS config CLI commands in a tree structure called the configuration tree. Each configuration command forms a branch of the tree.

Syntax

tree [branch] [sub-branch]

You can enter the tree command from the top of the configuration tree the command displays the complete configuration tree. Commands are displayed in the order that they are processed when the FortiGate unit starts up. For example, the following output shows the first 10 lines of tree command output:

tree

--  -- system -- [vdom] --*name (12)

+- vcluster-id (0,0)

|- <global> -- language

|- gui-ipv6

|- gui-voip-profile

|- gui-lines-per-page (20,1000)

|- admintimeout (0,0)

|- admin-concurrent

|- admin-lockout-threshold (0,0)

|- admin-lockout-duration (1,2147483647)

|- refresh (0,2147483647)

|- interval (0,0)

|- failtime (0,0)

|- daily-restart

|- restart-time

...

You can include a branch name with the tree command to view the commands in that branch:

tree user

-- user -- [radius] --*name (36)

|- server (64)

|- secret

|- secondary-server (64)

|- secondary-secret

|- all-usergroup

|- use-management-vdom

|- nas-ip

|- radius-port (0,0)

+- auth-type

|- [tacacs+] --*name (36)

...

You can include a branch and sub branch name with the tree command to view the commands in that sub branch:

tree user local

-- [local] --*name (36)

|- status

|- type

|- passwd

|- ldap-server (36)

|- radius-server (36)

+- tacacs+-server (36)

...

If you enter the tree command from inside the configuration tree the command displays the tree for the current command:

config user ldap tree

-- [ldap] --*name (36)

|- server (64)

|- cnid (21)

|- dn (512)

|- port (1,65535)

|- type

|- username (512)

|- password

|- filter (512 xss)

|- secure

|- ca-cert (64)

|- password-expiry-warning

|- password-renewal

+- member-attr (64)

You can use the tree command to view the number of characters that are allowed in a configuration parameter text string. For example, firewall address names can contain up to 64 characters. When you add a firewall address to the web-based manager you are limited to entering 64 characters in the firewall

address name field. From the CLI you can do the following to confirm that the firewall address name field allows 64 characters.

config firewall address tree

-- [address] --*name (64)

|- subnet

|- type

|- start-ip

|- end-ip

|- fqdn (256)

|- cache-ttl (0,86400)

|- wildcard

|- comment (64 xss)

|- associated-interface (16)

+- color (0,32)

Note that the tree command output also shows the number of characters allowed for other firewall address name settings. For example, the fully-qualified domain name (fqdn) field can contain up to 256 characters.

Fortinet Technologies Inc.                                                               Page 1119                                 FortiOS™ - CLI Reference for FortiOS 5.0v3

# Text boxes

| Name Host Username | Account-Type | State |
| --- | --- | --- |
| Provider_1 192.169.20.1 +5555555 | Static | N/A |

| Swap: | 0 | 0 |  | 0 |
| --- | --- | --- | --- | --- |
| MemTotal: |  | 3617132 | kB |  |
| MemFree: |  | 3276396 | kB |  |
| MemShared: |  | 0 | kB |  |
| Buffers: |  | 188 | kB |  |
| Cached: |  | 136664 | kB |  |
| SwapCached: |  | 0 | kB |  |
| Active: |  | 22172 | kB |  |
| Inactive: |  | 114740 | kB |  |
| HighTotal: |  | 1703936 | kB |  |
| HighFree: |  | 1443712 | kB |  |
| LowTotal: |  | 1913196 | kB |  |
| LowFree: |  | 1832684 | kB |  |
| SwapTotal: |  | 0 | kB |  |
| SwapFree: |  | 0 | kB |  |

| BGP structure : | 2 | 1408 |
| --- | --- | --- |
| BGP VR structure : | 2 | 104 |
| BGP global structure : | 1 | 56 |
| BGP peer : | 2 | 3440 |
| BGP as list master : | 1 | 24 |
| Community list handler : | 1 | 32 |
| BGP Damp Reuse List Array : | 2 | 4096 |
| BGP table : | 62 | 248 |
| ----------------------------------- | ------------- | --------------- |
| Temporary memory : | 4223 | 96095 |
| Hash : | 7 | 140 |
| Hash index : | 7 | 28672 |
| Hash bucket : | 11 | 132 |
| Thread master : | 1 | 564 |
| Thread : | 4 | 144 |
| Link list : | 32 | 636 |
| Link list node : | 24 | 288 |
| Show : | 1 | 396 |
| Show page : | 1 | 4108 |
| Show server : | 1 | 36 |
| Prefix IPv4 : | 10 | 80 |
| Route table : | 4 | 32 |
| Route node : | 63 | 2772 |
| Vector : | 2180 | 26160 |
| Vector index : | 2180 | 18284 |
| Host config : | 1 | 2 |
| Message of The Day : | 1 | 100 |
| IMI Client : | 1 | 708 |
| VTY master : | 1 | 20 |
| VTY if : | 11 | 2640 |
| VTY connected : | 5 | 140 |
| Message handler : | 2 | 120 |
| NSM Client Handler : | 1 | 12428 |
| NSM Client : | 1 | 1268 |
| Host : | 1 | 64 |
| Log information : | 2 | 72 |
| Context : | 1 | 232 |
| ----------------------------------- | ------------- | --------------- |

| 08:00:00 Virus Definitions | 6.513 | 2006-06-02 | 22:01:00 | manual | 2006-06-12 |
| --- | --- | --- | --- | --- | --- |
| 08:00:00 |  |  |  |  |  |
| Attack Definitions 08:00:00 | 2.299 | 2006-06-09 | 19:19:00 | manual | 2006-06-12 |
| IPS Attack Engine 08:00:00 | 1.015 | 2006-05-09 | 23:29:00 | manual | 2006-06-12 |

| channel= | 1 | maxRegTxPower= | 27 | maxTxPower= | 63/2 | minTxPower= | 63/2 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| channel= | 2 | maxRegTxPower= | 27 | maxTxPower= | 63/2 | minTxPower= | 63/2 |
| channel= | 3 | maxRegTxPower= | 27 | maxTxPower= | 63/2 | minTxPower= | 63/2 |
| channel= | 4 | maxRegTxPower= | 27 | maxTxPower= | 63/2 | minTxPower= | 63/2 |
| channel= | 5 | maxRegTxPower= | 27 | maxTxPower= | 63/2 | minTxPower= | 63/2 |
| channel= | 6 | maxRegTxPower= | 27 | maxTxPower= | 63/2 | minTxPower= | 63/2 |